## Slide 1
The History and Evolution of the GOES-R Advanced Baseline Imager
  Timothy J. Schmit (tim.j.schmit@noaa.gov)
NOAA/NESDIS/Satellite Applications and Research
Advanced Satellite Products Branch (ASPB)
Madison, WI
UW-Madison
AMS Annual Meeting
11th History Symposium
January 8, 2013
Austin, TX

## Slide 2: Co-authors: James J. Gurka, Mathew M. Gunshor, W. P. Menzel, J. Phillips
Special Thanks to:
S. Ackerman, W. L. Smith, Sr., R. Heymann, N. Rao, B. Baum, M. Griffin, A. Heidinger, J. Gurka, E. Prins, G. S. Wade, F. Mosher, G. Ellrod, J. Sieglaff, A. J. Schreiner, J. Li, M. Weinreb, S. Bachmeier, K. Strabala, J. Otkin, J. Feltz, J. Gerth, A. Huang, C. Velden, K. Bah, J. P. Nelson, C. Hayden, D. W. Martin, D. Hillger, D. Wade, D. Chesters, J. L. Schmit

## Slide 3: Outline
Early GOES
  First 3 Generations
Current GOES
  Fourth Generation
GOES-R ABI
  Fifth Generation
Summary
Lockheed Martin

## Slide 4: GOES History
GOES-13/14/15
Launched
2005
2009
2010
Better navigation and calibration.
No eclipse outages.
Better spatial resolutions for the 6.5 um on GOES-12+ and the 13.3 um band on GOES-14/15.
Operational Sounder
GOES-8/12
Launched
1994
1995
1997
2000
2001
3-axis stabilized.
Imager Bands: 4 IR; 1 visible.
Operational Sounder
(18 IR bands)
GOES-R/S+
Planned Launch
2015
2017
2020
2025
Faster coverage.
16 Imager Bands.
Improved spatial.
No sounder.
GLM
GOES-4/7
Launched
1980
1981
1983
1987
VISSR–VAS visible, 12 IR. MSI (visible, IRW, and 2 additional IR channels)
GOES-1/3
Launched
1975
1977 1978
One visible and one infrared .
Operational.
1G 2G 3G 4G 5G
Notes: The circles represent an estimate of the impact of GOES on regional scale numerical models.

## Slide 5: Mission Planning
STAR very involved during the early GOES-R series development. This includes: formulation studies for both ABI and Advanced Baseline Sounder (ABS), ABI band selection and modification, etc.
Originally ABI was only 8 spectral bands, now it is 16. All ABI bands were modified with input from STAR and it’s Cooperative Institutes.
ABI/ABS Requirements.
circa 1999/2000
Notes: Significant remaining scientific challenges for the specific science topic
Next step(s)
  Instruments (current/future), techniques, testbed, transition, …
Path into applications/operations
  Who will use it and how
  How will it get out to the real world

## Slide 6: 1 0.52 – 0.72 0.62 Visible Daytime clouds, fog 8 1.3 – 1.9 1.6 Near IR Daytime clouds/snow, water/ice clouds 2 3.8 – 4.0 3.9 Shortwave IR Nighttime low clouds, fog, fire detection 3 6.5 – 7.0 6.75 Water Vapor 1 Upper tropospheric flow, winds 6 7.0 – 7.5 7.25 Water Vapor 2 Mid tropospheric flow, winds 4 10.2 – 11.2 10.7 IR Window 3 Clouds, low-level water vapor, fog, winds 5 11.5 – 12.5 12.0 IR Window 4 Low-level water vapor, volcanic ash 7 13.2 – 13.8 13.5 Carbon Dioxide Cloud-top parameters, heights for winds
ABI - 8
# Wavelengths Description Primary Use
Range (m) Center
ABI – circa 1999
(8 total bands, most spectrally wide)
Based on a NWS 1999 requirements document
Notes: These 8 bands represent the current GOES imager “six” and 1.6 and 7.2 um bands.

## Slide 7: 0.59 – 0.69 0.64 Visible Daytime cloud, smoke, fog 0.81 ­ 0.91 0.86* Solar window Daytime cloud, NDVI, fog, aerosol, ocean studies 1.36 - 1.39 1.375* Near IR Daytime thin cirrus detection 1.58 – 1.64 1.61 Near IR Daytime clouds/snow, water/ice clouds 3.8 – 4.0 3.9 Shortwave IR Nighttime low clouds, fog, fire detection 5.7 – 6.6 6.15 Water Vapor 1 Upper tropospheric flow, winds 6.8 – 7.2 7.0 Water Vapor 2 Mid tropospheric flow, winds 8.3 – 8.7 8.5* IR Window 1 Sulfuric acid aerosols, cloud phase 10.1 – 10.6 10.35* IR Window 2 Cloud particle size, sfc properties 10.8 – 11.6 11.2 IR Window 3 Clouds, low-level water vapor, fog, winds, SST 11.8 – 12.8 12.3 IR Window 4 Low-level water vapor, volcanic ash, SST 13.0 – 13.6 13.3 Carbon Dioxide Cloud-top parameters, heights for winds
Proposed ABI (8 or 12) channels
Wavelengths Description Primary Use
Range (m) Center
* proposed additional channel to baseline of eight channels.
Notes: As originally proposed by the National Weather Service, the ABI was to have a minimum of 8 spectral channels. The selected channels were close to the five channels on the GOES-8 -10 imagers ( 0.64, 3.9, 6.15, 11.2, and 12.3 m) supplemented with a snow/cloud discriminating 1.6 m channel, a mid-tropospheric 7.0 um water vapor channel, and a cloud height determining 13.3 m channel. Two additional channels were proposed to expand the capabilities closer to meeting NWS requirements and to enhance opportunities for weather and climate research and applications; the IR windows at 8.5 m and 10.35 m offer improved moisture, cloud, aerosol, and surface sensing capabilities. In addition some of the ABI-8 spectral widths were modified to complement other satellite spectral channels and to capitalize on experience gained with the MODIS Airborne Simulator (MAS). To round out an ABI-12, another visible channel at 0.86 m was added to help with the detection of aerosols and vegetation and a near infrared channel at 1.38 m to detect very thin cirrus in the upper troposphere.
The addition of the 8.5 m enables detection of volcanic cloud with sulfuric acid aerosols and thin cirrus in conjunction with the 11.2 m channel as well as determination of cloud micro-physical properties with the 11.2 and 12.3 m channels. This includes a more accurate delineation of ice from water clouds during the day or night.
The addition of the 10.35 m improves determination of micro-physical properties of clouds with the 11.2 and 12.3 m channels; this includes a more accurate determination of cloud particle size during the day and night. Also, the observation of surface properties (such as SST) is improved using the 10.35m along with the 8.6, 11.2, and 12.3 m channels. Finally, there is more sensitivity to low level moisture with the additional split windows.
The 0.86 m channel provides synergy with the AVHRR/3, as it is similar its channel 2. This channel is used for determining vegetation amount, aerosols and ocean/land studies. Characterizing aerosols and their optical properties is essential for improving a number of satellite products, for example SST, ocean color and surface temperatures. This channel also enables very localized vegetation stress monitoring, fire danger monitoring, and albedo retrieval.
The 1.38 m channel is copied from one on MODIS. It does not see into the lower troposphere due to water vapor sensitivity and thus it provides excellent daytime sensitivity to very thin cirrus. This will aid several products relying on clear skies in the infrared windows, for example SST.

## Slide 8
IR channels on the current GOES and the proposed ABI
UW-Madison/CIMSS
Based on a NWS 1999 requirements document
Notes: This figure, generated by Mat Gunshor, shows the spectral coverage of the current GOES Imager (in red) and that proposed in the IR region for the ABI (Advanced Baseline Imager) (in green). A sample high spectral resolution earth-emitted spectra is also plotted (in blue). It’s apparent that the ABI has advantages over the current GOES Imager. For example, a 13.3 um band for cloud heights, two water vapor bands instead of one, and a band covering at the 8.5 um region (for cloud phase).

## Slide 9
Current GOES Imagers
MSG/Sounder
MODIS/MTG/etc
ABI Bands (proposed 18)
Notes: Band pass are approximate

## Slide 10: ATS-III November 18, 1967
The spin scan cloud camera provided full disk visible images of the earth and its cloud cover every 20 minutes.
Note the ‘natural color’ image from the 3 visible spectral bands.
Notes: Natural color images from the geo perspective are possible, as demonstrated in 1967.

## Slide 11
Options 3b. 2.6.6 VIIRS Compatibility Study
The Contractor shall assess the impact of modifying the Spectral Response Envelope of the reflective channels to be consistent with the current VIIRS design. The required changes are:
a) Move the 0.47 um channel to 0.488 um with a nominal bandwidth of 0.02 um,
b) Change the 0.64 um channel nominal bandwidth to 0.08 um,
c) Move the 0.86 um channel to 0.865 um with a nominal bandwidth of 0.039 um,
d) Move the 1.38 um channel to 1.378 um with a nominal bandwidth of 0.015 um,
e) Move the 2.26 um channel to 2.25 um with a nominal bandwidth of 0.050 um.

## Slide 12
a) Move the 0.47 um channel to 0.488 um with a nominal bandwidth of 0.02 um, [No, need shorter wavelength for better scattering. VIIRS has 2 bands in this region!]
b) Change the 0.64 um channel nominal bandwidth to 0.08 um, [OK, but also shift center to 0.645 um to match HES-CW.]
c) Move the 0.86 um channel to 0.859 um with a nominal bandwidth of 0.039 um, [OK, but width of 0.039 and 0.04 um so similar the same performance may be the same!]
d) Move the 1.38 um channel to 1.378 um with a nominal bandwidth of 0.015 um, [OK, if noise is still OK!]
e) Move the 2.26 um channel to 2.25 um with a nominal bandwidth of 0.050 um. [Actually change to 2.13 um to match MODIS, VIIRS and MTG!]

## Slide 13
ABI 6.2 um, 7.0 um, and 7.4 um bands
Effects of changing central wavenumber
Current ABI Bandwidth
Possible ABI shifted Bandwidth
7.0 um band
6.8 um - 7.2 um
7.4 um band
7.3 um - 7.5 um
7.34 um band
7.24 um - 7.44 um
6.95 um band
6.75 um - 7.15 um
6.2 um band
5.7 um - 6.6 um
6.2 um band adjusted
5.77 um - 6.6 um

## Slide 14
ABI 7.4 um Band
ABI 7.4 um
“ABI 7.34 um”

## Slide 15
GOES-R ABI detects some SO2 plumes
Water Vapor Band Difference convolved from AIRS data
sees SO2 plume from Montserrat Island, West Indies. High-spectral AIRS sees a larger brightness temperature difference.
ABI 7.34 μm - 6.95 μm
SO2 Plume
AIRS 7.8 μm – 7.43 μm
High-spectral sounder data gives a much greater brightness temperature difference (by almost a factor of 2) than broad-band instruments.
Notes: Current GOES can detect an ash cloud, but not the SO2. Note different color scales!

## Slide 16: Other considerations
Other bands considered on the ABI:
  a 0.55 um band, similar to MODIS for the generation of ‘natural color’ images.
  a 3.7 um band for better night-time cloud detection
It also should be noted that the ABI was designed to have a companion high-spectral infrared sounder. This is why the ABI only has one CO2 band.

## Slide 17: ABI bands 1-6
Notes: Final column added: heritage. The ABI band 1 was suggested by Dr. Fred Mosher at a GOES Users' Conference.
The ABI band 3 was suggested by the late Dr. C. Rao (of the then ORA).
Some of these bands have been shifted to more closely match those on the VIIRS.

## Slide 18
The ABI visible and near-IR bands have many uses.
Visible and near-IR channels on the ABI
Haze
Clouds
Veg.
Cirrus
Part. size
Snow, Phase
Notes: Note how ABI bands 2 and 3 might indicate vegetation. ABI bands 2 and 5 (or 6) depict snow.
Schmit, T. J., M. M. Gunshor, W. P. Menzel, J. J. Gurka, J. Li, and A. S. Bachmeier, 2005: Introducing the next-generation Advanced Baseline Imager on GOES-R. Bull. Amer. Meteor. Soc., 86, 1079-1096.

## Slide 19
AVIRIS: Linden_haze_0.439_0.498um (simulated ABI band 1)
Smoke
The 0.47 um band was added, in part, due to a request from Fred Mosher, then of the AWC
Notes: AVIRIS (Airborne Visible/Infrared Imaging Spectrometer)
Simulated by convolving mock ABI spectral response functions with either AVIRIS data.
This band was chosen to better monitor daytime smoke, etc.

## Slide 20
Linden_0.577_0.696_um (simulated ABI band 2)
Notes: Simulated by convolving mock ABI spectral response functions with either AVIRIS data.

## Slide 21
01 September 2000-- Pre-burning
MODIS Detects Burn Scars in Louisiana
CIMSS, UW
Burn Scars
Scars (dark regions) caused by biomass burning in early September are
evident in MODIS 250 m NIR channel 2 (0.85 μm) imagery on the 17th.
MODIS Data from GSFC DAAC
17 September 2000-- Post-burning
ABI will allow for diurnal characterizations of burn areas, this has implications for re-growth patterns.
Notes: Figures from Chris Moeller, of CIMSS. The traditional visible 0.6um band does not show the burn scars (not shown).

## Slide 22
1.88 m (or 1.38 m) is helpful for contrail detection
Examples from MAS (Chs 2, 10, 16).
Contrail detection is important when estimating many surface parameters.
There is also interest in the climate change community.
Notes: MODIS Airborne Simulator. The image is 1.88 um, but that’s similar to the physics as the band chosen for the ABI.

## Slide 23
Snow
MODIS 1.6 µm -- Snow is darker.
Notes: Image from A. Heidnger of ASPB.

## Slide 24
Snow
MODIS 0.65 µm -- Snow is bright (but so are clouds).
Notes: Image from A. Heidnger of ASPB.

## Slide 25: ABI bands 7-16
Notes: The ABI band 10 was modified to better depict upper-level SO2. (G. Ellrod and others)
The ABI band 11 was suggested by Steve Ackerman (CIMSS), based on HIRS experience.
The ABI band 13 was suggested by W. P. Menzel (then NOAA NESDIS).

## Slide 26
Nocturnal Fog/Stratus Over the Northern Plains
ABI image (from MODIS) shows greater detail in structure of fog.
“ABI” 4 minus 11 μm Difference
Notes: Note the ABI (from MODIS) image is better spatial resolution and better signal-to-noise ratio then the GOES-10 imager.
Schmit, T. J., M. M. Gunshor, W. P. Menzel, J. J. Gurka, J. Li, and A. S. Bachmeier, 2005: Introducing the next-generation Advanced Baseline Imager on GOES-R. Bull. Amer. Meteor. Soc., 86, 1079-1096.

## Slide 27
ABI image (from MODIS) shows greater detail in structure of fog.
GOES-10 4 minus 11 μm Difference
Nocturnal Fog/Stratus Over the Northern Plains
Notes: Schmit, T. J., M. M. Gunshor, W. P. Menzel, J. J. Gurka, J. Li, and A. S. Bachmeier, 2005: Introducing the next-generation Advanced Baseline Imager on GOES-R. Bull. Amer. Meteor. Soc., 86, 1079-1096.

## Slide 28
GOES-12 and GOES-R ABI
Simulation of Grand Prix Fire/Southern California
GOES-12
GOES-12
GOES-R ABI
GOES-R ABI
Notes: Here are two different fires from J. Feltz of CIMSS (using mcidas-v). What we can see is a more defined peak in the higher resolution data and it is easier to pick out individual hotspots. In addition, the higher saturation temperature of the ABI allows us to see that the fire is around 370K. ABI is simulated from MODIS.

## Slide 29
GOES-R ABI will detect SO2 plumes
Water Vapor Band Difference convolved from AIRS data
sees SO2 plume from Montserrat Island, West Indies
Current GOES Imager can not
detect SO2
Current GOES Imager
No skill in monitoring
ABI 7.34 μm – 13.3 μm
SO2 Plume
Figure courtesy of Kris Karnauskas
Notes: Current GOES can detect an ash cloud, but not the SO2 signature. The ABI can, if the plume is large and high enough.
Image on Right from:
Schmit, T. J., M. M. Gunshor, W. P. Menzel, J. J. Gurka, J. Li, and A. S. Bachmeier, 2005: Introducing the next-generation Advanced Baseline Imager on GOES-R. Bull. Amer. Meteor. Soc., 86, 1079-1096.

## Slide 30
USING GOES-R TO HELP MONITOR UPPER LEVEL SO2
Anthony J. Schreiner*, Timothy J. Schmit#, Jun Li*, Gary P. Ellrod#, Mat Gunshor*
*CIMSS #NOAA/NESDIS
Simulated GOES-R ABI
Image Difference
Plume
Simulated IR spectrums for “normal” and “SO2 enriched” atmosphere and spectral response functions
Difference and GOES-R ABI SRF
TOMS
Carn
The 7.3 um band was spectrally modified to better detect upper-level SO2. This was, in part, due to a suggestion of G. Ellrod.

## Slide 31
Simulated
ABI
(11-12 μm)
One day after the Mt. Cleveland eruption
20 February 2001, 8:45 UTC
Volcanic Ash Plume: 11-12 and 8.5-11 μm images
UW/CIMSS
Simulated
ABI
(8.5-11 μm)
Notes: One of uses of the 8.5 um is better ash detection.

## Slide 32: ABI -- 8.5 m Based on MODIS used with ABI window channels to separate water from ice clouds
The 8.5 um band was added, in part, due to a request in the late 1980s from Steve Ackerman, CIMSS.
Notes: Another use of the 8.5 um band is a day and night cloud-top phase product.

## Slide 33
Aerosol/Dust Optical Thickness Retrieval
Results from SEVIRI@EUMETSAT
Figure courtesy of J. Li and P. Zhang
In general, GOES-R products will be more quantitative that current GOES.
Notes: The 8.5 um is also very helpful for dust detection.

## Slide 34
0.64 m
0.86 m
1.38 m
1.61 m
2.26 m
3.9 m
6.19 m
6.95 m
7.34 m
0.47 m
8.5 m
9.61 m
10.35 m
11.2 m
12.3 m
13.3 m
AWG Proxy ABI Simulations of Hurricane Katrina
NOAA/NESDIS STAR and GOES-R Imagery Team
Notes: As shown in mcidas-v

## Slide 35
The ABI visible and near-IR bands have many uses.
Aerosols, Insolation
Clouds, Snow
Vegetation, Imagery
Cloud mask, Suspended matter
Cloud Particle size
Snow, Phase
Visible and near-IR channels on the ABI
Sample use only, many other uses
Notes: Schmit, T. J., M. M. Gunshor, W. P. Menzel, J. J. Gurka, J. Li, and A. S. Bachmeier, 2005: Introducing the next-generation Advanced Baseline Imager on GOES-R. Bull. Amer. Meteor. Soc., 86, 1079-1096.

## Slide 36
ABI has many more bands than the current operational GOES imagers.
The IR channels on the ABI
Clouds, Stability Indices
Rainfall, Aerosol
SST, Fires, Radiances
Hurricane, Imagery
Cloud Phase, SST
Ozone, Downward Radiation
SO2, Radiances
Winds, WV profiling
TPW, Rainfall rate
Fires, Fog
Sample use only, many other uses
Notes: Schmit, T. J., M. M. Gunshor, W. P. Menzel, J. J. Gurka, J. Li, and A. S. Bachmeier, 2005: Introducing the next-generation Advanced Baseline Imager on GOES-R. Bull. Amer. Meteor. Soc., 86, 1079-1096.

## Slide 37: GOES-R ABI Weighting Functions
ABI has only 1 CO2 band.
Notes: This figure was generated by M. Gunshor, of CIMSS.

## Slide 38: ABI Band “Champions”
CWL | Band # | Champion
0.47 | 1 | Fred Mosher
0.64 | 2 | Vern Suomi
0.86 | 3 | Nagaraja Rao
1.38 | 4 | Bo-Cai Gao
1.61 | 5 | L. Stowe
2.25 | 6 | M. King
3.9 | 7 | Vern Suomi
6.16 | 8 | Pierre Morel
6.93 | 9 | W. L. Smith
7.34 | 10 | Gary Ellrod
8.5 | 11 | S. Ackerman
9.61 | 12 | Art Neuendorffer
10.33 | 13 | W. P. Menzel
11.2 | 14 | Vern Suomi
12.3 | 15 | Vern Suomi
13.3 | 16 | W. L. Smith

## Slide 39: Ackerman memo (1989)
8 micrometer…very useful in detecting …cirrus information … microphysical properties

## Slide 40: GOES Fly-out Schedule
http://www.goes-r.gov/

## Slide 41: The Advanced Baseline Imager:
ABI Current
Spectral Coverage
16 bands 5 bands
Spatial resolution
0.64 mm Visible 0.5 km Approx. 1 km
Other Visible/near-IR 1.0 km n/a
Bands (>2 mm) 2 km Approx. 4 km
Spatial coverage
Full disk 4 per hour Scheduled (3 hrly)
CONUS 12 per hour ~4 per hour
Mesoscale Every 30 sec n/a
Visible (reflective bands)
On-orbit calibration Yes No
Notes: The ABI allows more bands, finer spatial resolution, faster refresh rates and on-orbit calibration of all bands!

## Slide 42: Approximate spectral and spatial resolutions of US GOES Imagers
~ Band Center (um) | GOES-6/7 | GOES-8/11 | GOES-12/N | GOES-O/P | GOES-R+
0.47 |  |  |  |  | 
0.64 |  |  |  |  | 
0.86 |  |  |  |  | 
1.6 |  |  |  |  | 
1.38 |  |  |  |  | 
2.2 |  |  |  |  | 
3.9 |  |  |  |  | 
6.2 |  |  |  |  | 
6.5/6.7/7 | 14km |  |  |  | 
7.3 |  |  |  |  | 
8.5 |  |  |  |  | 
9.7 |  |  |  |  | 
10.35 |  |  |  |  | 
11.2 |  |  |  |  | 
12.3 |  |  |  |  | 
13.3 |  |  |  |  | 
8
4
2
Visible
Near-IR
Infrared
Box size represents detector size
“MSI mode”
Notes: 0.40 inches = 4km; 0.80 inches = 8km
MSI is Multi-Spectral Imaging Mode (dashed boxes)
This does not show other improvements: SNR, MTF, bit-depth, navigation, coverage rates, etc.

## Slide 43: Imager Coverage in ~30 minutes
 | Current Imager (Rapid Scan mode) | Future Imager (“Flex” mode)
Full Disk | 0 | 2
Northern Hemi | 1 | -
CONUS | 3 | 6
Mesoscale | 0 | 60
Full Disk
N. Hemisphere
CONUS
Mesoscale

## Slide 44: GOES-R like intervals
Notes: .mov version

## Slide 45: GOES Outages -- approximate hours/year
0400 UTC
0500 UTC
0600 UTC
Outage
during
landfall
Satellite Series | KOZ, Eclipse and Stray Light (spring and fall) | Housekeeping, SEM calibration, Maneuvers and Yaw-flip
GOES-8 thru -12 | 420 | 211
GOES-13/14/15 (may be reduced) | 220 | 107
GOES-R ABI | ~6 - 40 | ~2 - 6
Hurricane
Ivan
Improved stray light performance with the ABI.
Notes: 2004, Hurricane Ivan.

## Slide 46
Improved products could be realized from combinations of ABI and HES (Hyperspectral Environmental Suite) data
ABI
HES
Surface
emissivity
Spectral
coverage
Spectral resolution
Temporal
resolution
Spatial
resolution
Cloud
clearing
cira 2004
HES cancelled in 2006

## Slide 47: GOES-R main instruments
Images courtesy of SOHO EIT, a joint NASA/ESA program
Space Weather/Solar
ABI covers the earth 5X faster than current Imager
ABI – Advanced Baseline Imager
Geostationary Lightning Mapper
Unique Payload Services
No Sounder
SEISS
SUVI
EXIS
Magnetometer

## Slide 48: GOES-R Series Overview
No dedicated Sounder
Advanced Baseline Imager (ABI)
Geostationary Lightning Mapper (GLM)
Space Weather
  Space Environmental In-Situ Suite (SEISS)
  Solar Ultra Violet Imager (SUVI)
  Extreme Ultra Violet/X-Ray Irradiance Sensor (EXIS)
  Magnetometer
Communications
  GOES Rebroadcast (GRB)
  Low Rate Information Transmissions (LRIT)
  Emergency Managers Weather Information Network (EMWIN)
  Search and Rescue (SAR)
  Data Collection System (DCS)
Notes:   Advanced Baseline Imager (ABI) Earth-viewing
  Geostationary Lightning Mapper (GLM) Earth-viewing
  Solar Ultra-Violet Imager (SUVI) Sun-viewing
  EUVS and XRS Irradiance Sensors (EXIS) Sun-viewing
  Space Environment In-Situ Suite (SEISS) Space-viewing
  Magnetometer (MAG) Space-viewing

## Slide 49: GOES-R
Folks who named the instruments
Goodman
Coakley
Hawkins
?
Schmit
Notes: Graphic from LM

## Slide 50: Summary
The ABI on GOES-R will improve over the current instrument in many aspects (spatial, temporal, spectral, etc.).
The great amount of information from the GOES-R will offer a continuation of current products and new products.
The ABI builds on previous experience and instruments.
The ABI has already had a long history, even before launch.
Contact information: tim.j.schmit@noaa.gov

## Slide 51: Acknowledgements
The authors would like to thank the entire GOES and GOES-R teams; both within the government, industry and academia.
The views, opinions, and findings contained in this presentation are those of the authors and should not be construed as an official National Oceanic and Atmospheric Administration or U.S. Government position, policy, or decision.

## Slide 52: Web page
www.goes-r.gov

## Slide 53: Links
  http://www.goes-r.gov
  http://www.meted.ucar.edu/index.htm
  http://cimss.ssec.wisc.edu/goes_r/proving-ground.html
  http://cimss.ssec.wisc.edu/goes_r/proving-ground/nssl_abi/nssl_abi_rt.html
  http://cimss.ssec.wisc.edu/goes/abi/
  http://cimss.ssec.wisc.edu/goes/blog/
  http://www.ssec.wisc.edu/data/geo/
  http://cimss.ssec.wisc.edu/goes/srsor/GOES-14_SRSOR.html

## Slide 54: GOES-R ABI Products
Advanced Baseline Imager (ABI)
Aerosol Detection (Including Smoke and Dust) Aerosol Optical Depth (AOD) Clear Sky Masks Cloud and Moisture Imagery Cloud Optical Depth Cloud Particle Size Distribution Cloud Top Height Cloud Top Phase Cloud Top Pressure Cloud Top Temperature Derived Motion Winds Derived Stability Indices Downward Shortwave Radiation: Surface Fire/Hot Spot Characterization Hurricane Intensity Estimation Land Surface Temperature (Skin) Legacy Vertical Moisture Profile Legacy Vertical Temperature Profile Radiances Rainfall Rate/QPE Reflected Shortwave Radiation: TOA Sea Surface Temperature (Skin) Snow Cover Total Precipitable Water Volcanic Ash: Detection and Height
Baseline Products
Advanced Baseline Imager (ABI)
Absorbed Shortwave Radiation: Surface Aerosol Particle Size Aircraft Icing Threat Cloud Ice Water Path Cloud Layers/Heights Cloud Liquid Water Cloud Type Convective Initiation Currents Currents: Offshore Downward Longwave Radiation: Surface Enhanced “V”/Overshooting Top Detection Flood/Standing Water Ice Cover Low Cloud and Fog Ozone Total Probability of Rainfall Rainfall Potential Sea and Lake Ice: Age Sea and Lake Ice: Concentration Sea and Lake Ice: Motion Snow Depth (Over Plains) SO2 Detection Surface Albedo Surface Emissivity Tropopause Folding Turbulence Prediction Upward Longwave Radiation: Surface Upward Longwave Radiation: TOA Vegetation Fraction: Green Vegetation Index Visibility
Future Capabilities

## Slide 55: Pseudo-Natural Color