## Slide 1
Preparing Users for the Advanced Baseline Imager (ABI) on GOES-R
  Timothy J. Schmit (tim.j.schmit@noaa.gov)
NOAA/NESDIS/StAR Advanced Satellite Products Branch (ASPB)
M. Gunshor, K. Bah, J. Gerth, B. Pierce,
Madison, WI
and S. J. Goodman
GOES-R Program Office (GPO)
UW-Madison
11th Annual Symposium on New Generation Operational Environmental Satellite Systems
January 6, 2015

## Slide 2: Outline
Background/Instrument
  8 to 16 spectral bands, scan options, etc.
Simulations
  triplets, WES, WRF Chem, NSSL-WRF
Education/Training
  COMET, VISIT, WF, webapps, papers, conferences, web pages, short courses
Other sensors
  AVIRIS, MAS, MODIS, SEVIRI, VIIRS, AHI, and SRSOR (GOES-14)
Lockheed Martin

## Slide 3: 1 0.52 – 0.72 0.62 Visible Daytime clouds, fog 8 1.3 – 1.9 1.6 Near IR Daytime clouds/snow, water/ice clouds 2 3.8 – 4.0 3.9 Shortwave IR Nighttime low clouds, fog, fire detection 3 6.5 – 7.0 6.75 Water Vapor 1 Upper tropospheric flow, winds 6 7.0 – 7.5 7.25 Water Vapor 2 Mid tropospheric flow, winds 4 10.2 – 11.2 10.7 IR Window 3 Clouds, low-level water vapor, fog, winds 5 11.5 – 12.5 12.0 IR Window 4 Low-level water vapor, volcanic ash 7 13.2 – 13.8 13.5 Carbon Dioxide Cloud-top parameters, heights for winds
ABI - 8
# Wavelengths Description Primary Use
Range (m) Center
ABI – circa 1999
(8 total bands, most spectrally wide)
Notes: These 8 bands represent the current GOES imager “six” and 1.6 and 7.2 um bands.

## Slide 4: ABI bands 1-6
6 visible or near infrared bands on the ABI, compared to only one on today’s imager
Notes: Final column added: heritage. The ABI band 1 was suggested by Dr. Fred Mosher at a GOES Users' Conference.
The ABI band 3 was suggested by the late Dr. C. Rao (of the then ORA).
Some of these bands have been shifted to more closely match those on the VIIRS.

## Slide 5: ABI bands 7-16
10 infrared bands on the ABI, compared to four on today’s imager
Notes: The ABI band 10 was modified to better depict upper-level SO2. (G. Ellrod and others)
The ABI band 11 was suggested by Steve Ackerman (CIMSS), based on HIRS experience.
The ABI band 13 was suggested by W. P. Menzel (then NOAA NESDIS).

## Slide 6: Baseline ABI Scan Modes
Scan mode (3) or ‘flex mode’ for the ABI:
- Full disk every 15 minutes + 5 min CONUS
+ 1-min mesoscales (2 locations).
[Scan mode (4) or ‘Continuous Full Disk’ (CFD) is a full disk every 5 min]
Notes: CONUS image is the shifted center point.

## Slide 7: Baseline Mode 3 “Time-Time” chart
Covers 15 minutes
Note many more star looks, especially IR stars.
Notes: Copy and pasted from excel. Pasted as a picture. Resized to 44% by 44% of original. Arrange -> Align -> Align Center & Align Middle

## Slide 8: Baseline Time-Time Mode 4
This is the Continuous Full Disk (every 5 min) mode
Covers 15 minutes

## Slide 9
Exploratory ABI Scan Modes
At some point, other ABI scan mode could be possible. Although, this requires an upgrade to the ground system.
  The ABI instrument is capable of supporting other scan modes.
Use the ‘white space’ (or idle time) of when the ABI instrument is not scanning in mode 3 (‘flex’):
  increase to an ‘extended CONUS’ image.
  or
  Consider a full disk scan every 10 min (along with CONUS and meso-scale sectors). This would sync with the geo global constellation (EUMETSAT, AHI, AMI, AGRI, etc.).

## Slide 10: ABI CONUS Sector Size
Working on extending the ABI CONUS size to better address operational needs (and use time when the ABI instrument would be idle)
This would need a ground system upgrade
Other scan modes are being explored, e.g., full disk every 10 min + CONUS + mesoscales.
Current CONUS Sector for ABI
Proposed CONUS Sector for ABI
Mode 3
Mode “3a”

## Slide 11: Draft “Mode 6” with 10-min FD
Only proposed.
In 10-min:
  1 Full Disk
  2 CONUS
  20 Meso-scale
The 10-min Full Disk would offer synergy with other geos and improved AMVs outside of CONUS, plus still allow for meso-scale observations.
This draft mode 6 ideally could be tested during PLPT (Post Launch Products Test).
This mode should be easier to implement at the Ground System, since the scan sectors are the same size/locations as in mode 3.
Notes: Copy and pasted from excel. Pasted as a picture. Resized to 44% by 44% of original. Arrange -> Align -> Align Center & Align Middle

## Slide 12: Outline
Background/Instrument
  8 to 16 spectral bands, scan options, etc.
Simulations
  triplets, WES, WRF Chem, NSSL-WRF
Education/Training
  COMET, VISIT, WF, webapps, papers, conferences, web pages, short courses
Other sensors
  AVIRIS, MAS, MODIS, SEVIRI, VIIRS, AHI, and SRSOR (GOES-14)
Lockheed Martin

## Slide 13: In ABI FGF (75W)

## Slide 14: In ABI FGF (89.5W)
SSEC

## Slide 15: In ABI FGF (137W)
SSEC

## Slide 16: ABI WES
Contains simulated ABI for all bands for a June-2006 convective storm (CONUS and mesoscale), Hurricane Katrina, band differences, a WES (Weather Event Simulator) guide, etc.
http://cimss.ssec.wisc.edu/goes/abi/loops/WES_for_GOES-R_ABI_2011_Version.pdf

## Slide 17: Near Realtime WRF Chem ABI runs
http://cimss.ssec.wisc.edu/goes_r/proving-ground/wrf_chem_abi/wrf_chem_abi.html

## Slide 18
Synthetic Retrieval
Truth
Synthetic Retrieval - Truth
Total Precip Water (TPW) Validation

## Slide 19: Outline
Background/Instrument
  8 to 16 spectral bands, scan options, etc.
Simulations
  triplets, WES, WRF Chem, NSSL-WRF
Education/Training
  COMET, VISIT, WF, webapps, papers, conferences, web pages, short courses
Other sensors
  AVIRIS, MAS, MODIS, SEVIRI, VIIRS, AHI, and SRSOR (GOES-14)
Lockheed Martin

## Slide 20
http://cimss.ssec.wisc.edu/wxfest/

## Slide 21
http://cimss.ssec.wisc.edu/goes/applets/overview.html

## Slide 24
http://cimss.ssec.wisc.edu/goes/webapps/bandapp/overview.html

## Slide 25
http://cimss.ssec.wisc.edu/goes/webapps/bandapp/overview.html

## Slide 26
http://cimss.ssec.wisc.edu/goes/webapps/bandapp/overview.html

## Slide 27
Land
http://cimss.ssec.wisc.edu/goes/webapps/bandapp/overview.html

## Slide 28
http://cimss.ssec.wisc.edu/goes/webapps/bandapp/overview.html
Cloud

## Slide 29
ABI Band Fact Sheets
http://www.goes-r.gov/education/ABI-bands-quick-info.html

## Slide 30: Outline
Background/Instrument
  8 to 16 spectral bands, scan options, etc.
Simulations
  triplets, WES, WRF Chem, NSSL-WRF
Education/Training
  COMET, VISIT, WF, webapps, papers, conferences, web pages, short courses
Other sensors
  AVIRIS, MAS, MODIS, SEVIRI, VIIRS, AHI, and SRSOR (GOES-14)
Lockheed Martin

## Slide 31: MODIS Airborne Simulator (MAS) April 26, 1996
Note the cirrus clouds in the center image

## Slide 32
JMA’s AHI: 0.47 um
Notes: December 18, 2014

## Slide 33
JMA’s AHI: 0.52 um

## Slide 34
JMA’s AHI: 0.64 um

## Slide 35
JMA’s AHI: 0.86 um

## Slide 36
JMA’s AHI: 1.6 um

## Slide 37
JMA’s AHI: 2.3 um

## Slide 38
JMA’s AHI: 3.9 um

## Slide 39
JMA’s AHI: 6.2 um

## Slide 40
JMA’s AHI: 6.9 um

## Slide 41
JMA’s AHI: 7.3 um

## Slide 42
JMA’s AHI: 8.6 um

## Slide 43
JMA’s AHI: 9.6 um

## Slide 44
JMA’s AHI: 10.4 um

## Slide 45
JMA’s AHI: 11.2 um

## Slide 46
JMA’s AHI: 12.4 um

## Slide 47
JMA’s AHI: 13.3 um
http://www.jma.go.jp/jma/jma-eng/satellite/news.html
http://cimss.ssec.wisc.edu/goes/blog/archives/category/himawari-8 http://cimss.ssec.wisc.edu/goes/webapps/bandapp/overview_ahi_first_light.html

## Slide 48: GOES-14 Super Rapid Scan Operations to Prepare for GOES-R (SRSOR)
SRSOR plans for 2015 include May 18-June 12, and August 10-22:
  http://cimss.ssec.wisc.edu/goes/srsor2015/GOES-14_SRSOR.html
  Data during parts of 2012 (Hurricane Sandy, convection), 2013 (CA Rim Fire, convection) and 2014 (Hurricane Marie, convection):
  http://cimss.ssec.wisc.edu/goes/srsor/GOES-14_SRSOR.html
  http://cimss.ssec.wisc.edu/goes/srsor2013/GOES-14_SRSOR.html
  http://cimss.ssec.wisc.edu/goes/srsor2014/GOES-14_SRSOR.html
GOES-14 provided very unique data and offered a glimpse into the possibilities that will be provided by the ABI on GOES-R in one minute mesoscale imagery
GOES-14 visible image showing rapid convective development

## Slide 49
Thank you!
For more information visit www.goes-r.gov