## Slide 1
Preparing Users for the Advanced Baseline Imager (ABI) on GOES-R
  Timothy J. Schmit (tim.j.schmit@noaa.gov)
NOAA/NESDIS/StAR Advanced Satellite Products Branch (ASPB)
M. Gunshor, K. Bah, J. Gerth, B. Pierce,
Madison, WI
and S. J. Goodman
GOES-R Program Office (GPO)
UW-Madison
11th Annual Symposium on New Generation Operational Environmental Satellite Systems
January 6, 2015

## Slide 2: Outline
Background/Instrument
  8 to 16 spectral bands, scan options, etc.
Simulations
  triplets, WES, WRF Chem, NSSL-WRF
Education/Training
  COMET, VISIT, Weighting Functions, webapps, papers, conferences, web pages, short courses
Other sensors
  AVIRIS, MAS, MODIS, SEVIRI, VIIRS, AHI, and SRSOR (GOES-14)
Lockheed Martin

## Slide 3: 1 0.52 – 0.72 0.62 Visible Daytime clouds, fog 8 1.3 – 1.9 1.6 Near IR Daytime clouds/snow, water/ice clouds 2 3.8 – 4.0 3.9 Shortwave IR Nighttime low clouds, fog, fire detection 3 6.5 – 7.0 6.75 Water Vapor 1 Upper tropospheric flow, winds 6 7.0 – 7.5 7.25 Water Vapor 2 Mid tropospheric flow, winds 4 10.2 – 11.2 10.7 IR Window 3 Clouds, low-level water vapor, fog, winds 5 11.5 – 12.5 12.0 IR Window 4 Low-level water vapor, volcanic ash 7 13.2 – 13.8 13.5 Carbon Dioxide Cloud-top parameters, heights for winds
ABI - 8
# Wavelengths Description Primary Use
Range (m) Center
ABI – circa 1999
(8 total bands, most spectrally wide)
Notes: These 8 bands represent the current GOES imager “six” and 1.6 and 7.2 um bands.

## Slide 4: ABI bands 1-6
6 visible or near infrared bands on the ABI, compared to only one on today’s imager
Notes: Final column added: heritage. The ABI band 1 was suggested by Dr. Fred Mosher at a GOES Users' Conference.
The ABI band 3 was suggested by the late Dr. C. Rao (of the then ORA).
Some of these bands have been shifted to more closely match those on the VIIRS.

## Slide 5: ABI bands 7-16
10 infrared bands on the ABI, compared to four on today’s imager
Notes: The ABI band 10 was modified to better depict upper-level SO2. (G. Ellrod and others)
The ABI band 11 was suggested by Steve Ackerman (CIMSS), based on HIRS experience.
The ABI band 13 was suggested by W. P. Menzel (then NOAA NESDIS).

## Slide 6: Baseline ABI Scan Modes
Scan mode (3) or ‘flex mode’ for the ABI:
- Full disk every 15 minutes + 5 min CONUS
+ 1-min mesoscales (2 locations).
[Scan mode (4) or ‘Continuous Full Disk’ (CFD) is a full disk every 5 min]
Notes: CONUS image is the shifted center point.

## Slide 7: Baseline Mode 3 “Time-Time” chart
Covers 15 minutes
“White space” represents time the instrument is not scanning.
Mode 3 is the ‘flex’ mode.
Notes: Copy and pasted from excel. Pasted as a picture. Resized to 44% by 44% of original. Arrange -> Align -> Align Center & Align Middle

## Slide 8: Baseline Time-Time Mode 4
This is the Continuous Full Disk (every 5 min) mode
Covers 15 minutes

## Slide 9
Exploratory ABI Scan Modes
At some point, other ABI scan mode could be possible. Although, this requires an upgrade to the ground system.
  - The ABI instrument is capable of supporting other scan modes.
Use the ‘white space’ (or idle time) of when the ABI instrument is not scanning in mode 3 (‘flex’):
  increase to an ‘extended (larger) CONUS’ image.
  or
  Consider a full disk scan every 10 min, along with CONUS and meso-scale sectors. (under study)
  This would sync with the geo global constellation (EUMETSAT, AHI, AMI, AGRI, etc.).

## Slide 10: Outline
Background/Instrument
  8 to 16 spectral bands, scan options, etc.
Simulations
  triplets, WES, WRF Chem, NSSL-WRF
Education/Training
  COMET, VISIT, Weighting Functions, webapps, papers, conferences, web pages, short courses
Other sensors
  AVIRIS, MAS, MODIS, SEVIRI, VIIRS, AHI, and SRSOR (GOES-14)
Lockheed Martin

## Slide 11: In ABI FGF (75W)

## Slide 12: In ABI FGF (89.5W)
SSEC

## Slide 13: In ABI FGF (137W)
SSEC

## Slide 14: ABI WES
Contains simulated ABI for all bands for a June-2006 convective storm (CONUS and mesoscale), Hurricane Katrina, band differences, a WES (Weather Event Simulator) guide, etc.
http://cimss.ssec.wisc.edu/goes/abi/loops/WES_for_GOES-R_ABI_2011_Version.pdf

## Slide 15: Near Realtime WRF Chem ABI runs
http://cimss.ssec.wisc.edu/goes_r/proving-ground/wrf_chem_abi/wrf_chem_abi.html

## Slide 16
Synthetic Retrieval
Truth
Synthetic Retrieval - Truth
Total Precip Water (TPW) Validation

## Slide 17: Outline
Background/Instrument
  8 to 16 spectral bands, scan options, etc.
Simulations
  triplets, WES, WRF Chem, NSSL-WRF
Education/Training
  COMET, VISIT, Weighting Functions, webapps, papers, conferences, web pages, short courses
Other sensors
  AVIRIS, MAS, MODIS, SEVIRI, VIIRS, AHI, and SRSOR (GOES-14)
Lockheed Martin
Notes: Weighting Functions web page: http://cimss.ssec.wisc.edu/goes/wf/ABI/

## Slide 18
http://cimss.ssec.wisc.edu/wxfest/

## Slide 19
http://cimss.ssec.wisc.edu/goes/applets/overview.html

## Slide 20
http://cimss.ssec.wisc.edu/goes/applets/overview.html

## Slide 21
http://cimss.ssec.wisc.edu/goes/applets/overview.html

## Slide 22
http://cimss.ssec.wisc.edu/goes/webapps/bandapp/overview.html

## Slide 23
http://cimss.ssec.wisc.edu/goes/webapps/bandapp/overview.html

## Slide 24
http://cimss.ssec.wisc.edu/goes/webapps/bandapp/overview.html

## Slide 25
Land
http://cimss.ssec.wisc.edu/goes/webapps/bandapp/overview.html

## Slide 26
http://cimss.ssec.wisc.edu/goes/webapps/bandapp/overview.html
Cloud

## Slide 27
ABI Band Fact Sheets
http://www.goes-r.gov/education/ABI-bands-quick-info.html
New band introduced each month.

## Slide 28: Outline
Background/Instrument
  8 to 16 spectral bands, scan options, etc.
Simulations
  triplets, WES, WRF Chem, NSSL-WRF
Education/Training
  COMET, VISIT, Weighting Functions, webapps, papers, conferences, web pages, short courses
Other sensors
  AVIRIS, MAS, MODIS, SEVIRI, VIIRS, AHI, and SRSOR (GOES-14)
Lockheed Martin

## Slide 29: MODIS Airborne Simulator (MAS) April 26, 1996
Note the cirrus clouds in the center image

## Slide 30
JMA’s AHI: 0.47 um
Notes: December 18, 2014

## Slide 31
JMA’s AHI: 0.52 um

## Slide 32
JMA’s AHI: 0.64 um

## Slide 33
JMA’s AHI: 0.86 um

## Slide 34
JMA’s AHI: 1.6 um

## Slide 35
JMA’s AHI: 2.3 um

## Slide 36
JMA’s AHI: 3.9 um

## Slide 37
JMA’s AHI: 6.2 um

## Slide 38
JMA’s AHI: 6.9 um

## Slide 39
JMA’s AHI: 7.3 um

## Slide 40
JMA’s AHI: 8.6 um

## Slide 41
JMA’s AHI: 9.6 um

## Slide 42
JMA’s AHI: 10.4 um

## Slide 43
JMA’s AHI: 11.2 um

## Slide 44
JMA’s AHI: 12.4 um

## Slide 45
JMA’s AHI: 13.3 um
http://www.jma.go.jp/jma/jma-eng/satellite/news.html
http://cimss.ssec.wisc.edu/goes/blog/archives/category/himawari-8 http://cimss.ssec.wisc.edu/goes/webapps/bandapp/overview_ahi_first_light.html

## Slide 46: GOES-14 Super Rapid Scan Operations to Prepare for GOES-R (SRSOR)
SRSOR plans for 2015 include May 18-June 12, and August 10-22:
  http://cimss.ssec.wisc.edu/goes/srsor2015/GOES-14_SRSOR.html
  Data during parts of 2012 (Hurricane Sandy, convection), 2013 (CA Rim Fire, convection) and 2014 (Hurricane Marie, convection):
  http://cimss.ssec.wisc.edu/goes/srsor/GOES-14_SRSOR.html
  http://cimss.ssec.wisc.edu/goes/srsor2013/GOES-14_SRSOR.html
  http://cimss.ssec.wisc.edu/goes/srsor2014/GOES-14_SRSOR.html
GOES-14 provided very unique data and offered a glimpse into the possibilities that will be provided by the ABI on GOES-R in one minute mesoscale imagery
GOES-14 visible image showing rapid convective development

## Slide 47
Thank you!
For more information visit www.goes-r.gov