## Slide 1
The Pre-launch History of the Advanced Baseline Imager (ABI) on GOES-R
  Timothy J. Schmit (tim.j.schmit@noaa.gov)
NOAA/NESDIS/Satellite Applications and Research
Advanced Satellite Products Branch (ASPB)
Madison, WI
Mat Gunshor, Jim Gurka, Paul Menzel
UW-Madison
12th Annual Symposium on New Generation Operational Environmental Satellite Systems
AMS Annual Meeting
New Orleans, LA
January 11, 2016

## Slide 2: Outline
Lockheed Martin
GOES-R series ABI
  Overview
  Spectral
  Spatial
  Temporal
ABS
Summary

## Slide 3: The Advanced Baseline Imager:
ABI Current
Spectral Coverage
16 bands 5 bands
Spatial resolution
0.64 mm Visible 0.5 km Approx. 1 km
Other Visible/near-IR 1.0 km n/a
Bands (>2 mm) 2 km Approx. 4 km
Spatial coverage
Full disk Every 15 min Scheduled (3 hrly)
CONUS Every 5 min ~4 per hour
Mesoscale Every 30 sec n/a
Visible (reflective bands)
On-orbit calibration Yes No
Notes: The ABI allows more bands, finer spatial resolution, faster refresh rates and on-orbit calibration of all bands!

## Slide 4: Advanced Baseline Imager
5
4
3
X
Faster coverage (5-minute full disk vs. 25-minute)
X
Improved spatial resolution
(2 km IR vs. 4 km)
X
More spectral bands (16 on ABI vs. 5 on the current imager)
Notes: Slide from J. Gerth, CIMSS.

## Slide 5: ABI spectral bands 1-6
2 visible bands and 4 near infrared bands on the ABI, compared to only one on today’s imager
Approximate:
Notes: Final column added: heritage. The ABI band 1 was suggested by Dr. Fred Mosher at a GOES Users' Conference.
The ABI band 3 was suggested by the late Dr. C. Rao (of the then ORA).
Some of these bands have been shifted to more closely match those on the VIIRS.

## Slide 6: ABI spectral bands 7-16
10 infrared bands on the ABI, compared to four on today’s imager
Approximate:
Notes: The ABI band 10 was modified to better depict upper-level SO2. (G. Ellrod and others)
The ABI band 11 was suggested by Steve Ackerman (CIMSS), based on HIRS experience.
The ABI band 13 was suggested by W. P. Menzel (then NOAA NESDIS).

## Slide 7: From 1996
"Full disk imaging in 10 minutes is sought and so is 1 minute rapid scan modes over limited areas of say 1000 x 1000 km."
“These satellites could be first launched in 2008”
Notes: http://ac.els-cdn.com/0094576596000215/1-s2.0-0094576596000215-main.pdf?_tid=86f5529e-c98d-11e4-8a46-00000aacb35f&acdnat=1426257222_f09810532f99876bc6014fff4f4d65be
NOAA's future earth observations from advanced GOES satellites Dittberner G., Gird R., Heymann R., Howard E., Kirkner S., Uccellini L. (1996) Acta Astronautica, 38 (4-8) , pp. 467-477.

## Slide 8: Late 1990s

## Slide 9: Outline
Lockheed Martin
GOES-R series ABI
  Overview
  Spectral
  Spatial
  Temporal
ABS
Summary

## Slide 10: Mission Planning
STAR and CIMSS very involved during the early GOES-R series development. This includes: formulation studies for both ABI and Advanced Baseline Sounder (ABS), ABI band selection and modification, etc.
Originally ABI was only 8 spectral bands, now it is 16. All ABI bands were modified with input from STAR and its Cooperative Institutes.
ABI/ABS Requirements.
circa 1999/2000
Notes: Significant remaining scientific challenges for the specific science topic
Next step(s)
  Instruments (current/future), techniques, testbed, transition, …
Path into applications/operations
  Who will use it and how
  How will it get out to the real world

## Slide 11: 1 0.52 – 0.72 0.62 Visible Daytime clouds, fog 8 1.3 – 1.9 1.6 Near IR Daytime clouds/snow, water/ice clouds 2 3.8 – 4.0 3.9 Shortwave IR Nighttime low clouds, fog, fire detection 3 6.5 – 7.0 6.75 Water Vapor 1 Upper tropospheric flow, winds 6 7.0 – 7.5 7.25 Water Vapor 2 Mid tropospheric flow, winds 4 10.2 – 11.2 10.7 IR Window 3 Clouds, low-level water vapor, fog, winds 5 11.5 – 12.5 12.0 IR Window 4 Low-level water vapor, volcanic ash 7 13.2 – 13.8 13.5 Carbon Dioxide Cloud-top parameters, heights for winds
ABI - 8
# Wavelengths Description Primary Use
Range (m) Center
ABI – circa 1999
(8 total bands, most spectrally wide)
Launch was planned for 2008!
Notes: These 8 bands represent the current GOES imager “six” and 1.6 and 7.2 um bands.

## Slide 12: 0.59 – 0.69 0.64 Visible Daytime cloud, smoke, fog 0.81 ­ 0.91 0.86* Solar window Daytime cloud, NDVI, fog, aerosol, ocean studies 1.36 - 1.39 1.375* Near IR Daytime thin cirrus detection 1.58 – 1.64 1.61 Near IR Daytime clouds/snow, water/ice clouds 3.8 – 4.0 3.9 Shortwave IR Nighttime low clouds, fog, fire detection 5.7 – 6.6 6.15 Water Vapor 1 Upper tropospheric flow, winds 6.8 – 7.2 7.0 Water Vapor 2 Mid tropospheric flow, winds 8.3 – 8.7 8.5* IR Window 1 Sulfuric acid aerosols, cloud phase 10.1 – 10.6 10.35* IR Window 2 Cloud particle size, sfc properties 10.8 – 11.6 11.2 IR Window 3 Clouds, low-level water vapor, fog, winds, SST 11.8 – 12.8 12.3 IR Window 4 Low-level water vapor, volcanic ash, SST 13.0 – 13.6 13.3 Carbon Dioxide Cloud-top parameters, heights for winds
Proposed ABI (8 or 12) channels
Wavelengths Description Primary Use
Range (m) Center
* proposed additional channel to baseline of eight channels.
Notes: As originally proposed by the National Weather Service, the ABI was to have a minimum of 8 spectral channels. The selected channels were close to the five channels on the GOES-8 -10 imagers ( 0.64, 3.9, 6.15, 11.2, and 12.3 m) supplemented with a snow/cloud discriminating 1.6 m channel, a mid-tropospheric 7.0 um water vapor channel, and a cloud height determining 13.3 m channel. Two additional channels were proposed to expand the capabilities closer to meeting NWS requirements and to enhance opportunities for weather and climate research and applications; the IR windows at 8.5 m and 10.35 m offer improved moisture, cloud, aerosol, and surface sensing capabilities. In addition some of the ABI-8 spectral widths were modified to complement other satellite spectral channels and to capitalize on experience gained with the MODIS Airborne Simulator (MAS). To round out an ABI-12, another visible channel at 0.86 m was added to help with the detection of aerosols and vegetation and a near infrared channel at 1.38 m to detect very thin cirrus in the upper troposphere.
The addition of the 8.5 m enables detection of volcanic cloud with sulfuric acid aerosols and thin cirrus in conjunction with the 11.2 m channel as well as determination of cloud micro-physical properties with the 11.2 and 12.3 m channels. This includes a more accurate delineation of ice from water clouds during the day or night.
The addition of the 10.35 m improves determination of micro-physical properties of clouds with the 11.2 and 12.3 m channels; this includes a more accurate determination of cloud particle size during the day and night. Also, the observation of surface properties (such as SST) is improved using the 10.35m along with the 8.6, 11.2, and 12.3 m channels. Finally, there is more sensitivity to low level moisture with the additional split windows.
The 0.86 m channel provides synergy with the AVHRR/3, as it is similar its channel 2. This channel is used for determining vegetation amount, aerosols and ocean/land studies. Characterizing aerosols and their optical properties is essential for improving a number of satellite products, for example SST, ocean color and surface temperatures. This channel also enables very localized vegetation stress monitoring, fire danger monitoring, and albedo retrieval.
The 1.38 m channel is copied from one on MODIS. It does not see into the lower troposphere due to water vapor sensitivity and thus it provides excellent daytime sensitivity to very thin cirrus. This will aid several products relying on clear skies in the infrared windows, for example SST.

## Slide 13
IR channels on the current GOES and the proposed ABI
UW-Madison/CIMSS
The IR bands when ABI had 12 total bands
Notes: This figure, generated by Mat Gunshor, shows the spectral coverage of the current GOES Imager (in red) and that proposed in the IR region for the ABI (Advanced Baseline Imager) (in green). A sample high spectral resolution earth-emitted spectra is also plotted (in blue). It’s apparent that the ABI has advantages over the current GOES Imager. For example, a 13.3 um band for cloud heights, two water vapor bands instead of one, and a band covering at the 8.5 um region (for cloud phase).

## Slide 14
Current GOES Imagers
MSG/Sounder
MODIS/MTG/etc
ABI Bands (proposed 18)
Notes: Band pass are approximate

## Slide 15
The ABI visible and near-IR bands have many uses.
Visible and near-IR channels on the ABI
Haze
Clouds
Veg.
Cirrus
Part. size
Snow, Phase
Notes: Note how ABI bands 2 and 3 might indicate vegetation. ABI bands 2 and 5 (or 6) depict snow.
Schmit, T. J., M. M. Gunshor, W. P. Menzel, J. J. Gurka, J. Li, and A. S. Bachmeier, 2005: Introducing the next-generation Advanced Baseline Imager on GOES-R. Bull. Amer. Meteor. Soc., 86, 1079-1096.

## Slide 16
AVIRIS: Linden_haze_0.439_0.498um (simulated ABI band 1)
Smoke
The 0.47 um band was added, in part, due to a request from Fred Mosher, then of the AWC
Notes: AVIRIS (Airborne Visible/Infrared Imaging Spectrometer)
Simulated by convolving mock ABI spectral response functions with either AVIRIS data.
This band was chosen to better monitor daytime smoke, etc.

## Slide 17
Linden_0.577_0.696_um (simulated ABI band 2)
Notes: Simulated by convolving mock ABI spectral response functions with either AVIRIS data.

## Slide 18
01 September 2000-- Pre-burning
MODIS Detects Burn Scars in Louisiana
CIMSS, UW
Burn Scars
Scars (dark regions) caused by biomass burning in early September are
evident in MODIS 250 m NIR channel 2 (0.85 μm) imagery on the 17th.
MODIS Data from GSFC DAAC
17 September 2000-- Post-burning
ABI will allow for diurnal characterizations of burn areas, this has implications for re-growth patterns.
Notes: Figures from Chris Moeller, of CIMSS. The traditional visible 0.6um band does not show the burn scars (not shown).

## Slide 19
1.88 m (or 1.38 m) is helpful for contrail detection
Examples from MAS (Chs 2, 10, 16).
Contrail detection is important when estimating many surface parameters.
There is also interest in the climate change community.
Notes: MODIS Airborne Simulator. The image is 1.88 um, but that’s similar to the physics as the band chosen for the ABI.

## Slide 20
ABI (1.61 um) Example of MAS 0.66 and 1.61 um
convective cumulonimbus surrounded by lower-level water clouds
(King et al., JAOT, August 1996)

## Slide 21
Snow
MODIS 0.65 µm -- Snow is bright (but so are clouds).
Notes: Image from A. Heidnger of ASPB.

## Slide 22
Snow
MODIS 1.6 µm -- Snow is darker.
Notes: Image from A. Heidnger of ASPB.

## Slide 23
GOES-R ABI will detect SO2 plumes
Water Vapor Band Difference convolved from AIRS data
sees SO2 plume from Montserrat Island, West Indies
Current GOES Imager can not
detect SO2
Current GOES Imager
No skill in monitoring
ABI 7.34 μm – 13.3 μm
SO2 Plume
Figure courtesy of Kris Karnauskas
Notes: Current GOES can detect an ash cloud, but not the SO2 signature. The ABI can, if the plume is large and high enough.
Image on Right from:
Schmit, T. J., M. M. Gunshor, W. P. Menzel, J. J. Gurka, J. Li, and A. S. Bachmeier, 2005: Introducing the next-generation Advanced Baseline Imager on GOES-R. Bull. Amer. Meteor. Soc., 86, 1079-1096.

## Slide 24
Simulated
ABI
(11-12 μm)
One day after the Mt. Cleveland eruption
20 February 2001, 8:45 UTC
Volcanic Ash Plume: 11-12 and 8.5-11 μm images
UW/CIMSS
Simulated
ABI
(8.5-11 μm)
Notes: One of uses of the 8.5 um is better ash detection.

## Slide 25: ABI -- 8.5 m Based on MODIS used with ABI window channels to separate water from ice clouds
The 8.5 um band was added, in part, due to a request in the late 1980s from Steve Ackerman, CIMSS.
Notes: Another use of the 8.5 um band is a day and night cloud-top phase product.

## Slide 26: Ackerman memo (1989)
8 micrometer…very useful in detecting …cirrus information … microphysical properties

## Slide 27: ABI Band “Champions”
CWL | Band # | Champion
0.47 | 1 | Fred Mosher
0.64 | 2 | Vern Suomi
0.86 | 3 | Nagaraja Rao
1.38 | 4 | Bo-Cai Gao
1.61 | 5 | L. Stowe
2.25 | 6 | M. King
3.9 | 7 | Vern Suomi
6.16 | 8 | Pierre Morel
6.93 | 9 | W. L. Smith
7.34 | 10 | Gary Ellrod
8.5 | 11 | S. Ackerman
9.61 | 12 | Art Neuendorffer
10.33 | 13 | W. P. Menzel
11.2 | 14 | Vern Suomi
12.3 | 15 | Vern Suomi
13.3 | 16 | W. L. Smith

## Slide 28: ABI (10.35 m) Examples of MAS 0.66, 10.5-11.0, and 8.6-10.5 um reveal utility of new IR window for seeing through clouds to ice floes

## Slide 29
Visible
Near Infrared
Infrared
Infrared
Infrared
Infrared
Visible
Infrared
Infrared
Infrared
Infrared
Infrared
Infrared
AWG Proxy ABI Simulations of Hurricane Katrina
NOAA/NESDIS STAR and GOES-R Imagery Team
Near Infrared
Near Infrared
Near Infrared
Notes: As shown in mcidas-v

## Slide 30
0.64 m
0.86 m
1.38 m
1.61 m
2.26 m
3.9 m
6.19 m
6.95 m
7.34 m
0.47 m
8.5 m
9.61 m
10.35 m
11.2 m
12.3 m
13.3 m
AWG Proxy ABI Simulations of Hurricane Katrina
NOAA/NESDIS STAR and GOES-R Imagery Team
Notes: As shown in mcidas-v

## Slide 31
Corresponding current Imager bands of Hurricane Katrina
NOAA/NESDIS STAR

## Slide 32: Outline
Lockheed Martin
GOES-R series ABI
  Overview
  Spectral
  Spatial
  Temporal
ABS
Summary

## Slide 33: MTSAT vs AHI (Spatial)
Rinjani

## Slide 34: Outline
Lockheed Martin
GOES-R series ABI
  Overview
  Spectral
  Spatial
  Temporal
ABS
Summary

## Slide 35
Meso-scale box locations are movable
15 min
5 min
1 min
1 min
Notes: 1-km2 spatial resolution at satellite nadir. Pixel Areas are approximate. Each bin is rounded to the nearest 1km2 until we get to 9.5km2 and then all are binned into the red 10+ area. So the first, dark blue, ring covers pixel areas from 1 to 1.49km2 and is labeled “1”, above 1.5 to below 2.5km2 goes into the next ring and is called “2”, etc. GOES-West location. Proposed CONUS sector, approved by the NWS NOAT. Two meso-scale image sectors shown; these are selectable. The same central lat/lon used for these mesoscales produces a different sized and shaped area for different satellite locations.

## Slide 36
15 min
Meso-scale box locations are movable
5 min
1 min
1 min
Notes: 1-km2 spatial resolution at satellite nadir. Pixel Areas are approximate. Each bin is rounded to the nearest 1km2 until we get to 9.5km2 and then all are binned into the red 10+ area. So the first, dark blue, ring covers pixel areas from 1 to 1.49km2 and is labeled “1”, above 1.5 to below 2.5km2 goes into the next ring and is called “2”, etc. GOES-East location. Proposed CONUS sector, approved by the NWS NOAT. Two meso-scale image sectors shown; these are selectable. The same central lat/lon used for these mesoscales produces a different sized and shaped area for different satellite locations.

## Slide 37
Operational (GOES-13)
1-min mode (SRSOR from GOES-14)
1-min imagery

## Slide 38
A Glimpse into the Future
Hurricane Sandy from GOES-14 at two temporal resolutions
ABI-like

## Slide 39: Outline
Lockheed Martin
GOES-R series ABI
  Overview
  Spectral
  Spatial
  Temporal
ABS
Summary

## Slide 40: High Spectral Resolution IR
It also should be noted that the ABI was designed to have a companion high-spectral infrared sounder [Advanced Baseline Sounder]. This is why the ABI only has one CO2 band.
On GOES-R originally called ABS, later HES (with a coastal waters imager).

## Slide 41: Why do we need a high spectral resolution sounder?
GOES-12 Sounder Bands
Smooths over required absorption lines
Compared to broadband imagers and sounders, observing absorption lines is mandatory to meeting requirements for temperature and moisture structure needed to improve short-term weather forecasting
Many papers document science value of high spectral resolution sounder that support weather forecast needs. (Sieglaff et al., 2009)
Analysis courtesy of Justin Sieglaff, CIMSS.
Notes: These are calculated spectra, showing important features dealing with temperature and moisture are in the high-spectral data, but are smoothed over in the broad-band data. Figure courtesy of J. Sieglaff, CIMSS.
I’m not sure it is useful to show an entire spectrum. Rather I prefer to show the above and indicate that it is these little wiggles that make the HES so valuable and that the current GOES smears out.

## Slide 42
Improved products could be realized from combinations of ABI and HES (Hyperspectral Environmental Suite) data
ABI
HES
Surface
emissivity
Spectral
coverage
Spectral resolution
Temporal
resolution
Spatial
resolution
Cloud
clearing
circa 2004
HES cancelled in 2006

## Slide 43: Outline
Lockheed Martin
GOES-R series ABI
  Overview
  Spectral
  Spatial
  Temporal
ABS
Summary

## Slide 44: Huge, Great, Epic, Cosmic Progress!
Lockheed Martin

## Slide 45
AHI Band | AHI Approximate Central Wavelength (μm) | ABI Approximate Central Wavelength (μm) | ABI Band | Type | Nickname
1 | 0.47 | 0.47 | 1 | Visible | Blue
2 | 0.51 |  |  | Visible | Green
3 | 0.64 | 0.64 | 2 | Visible | Red
4 | 0.86 | 0.86 | 3 | Near-Infrared | Veggie
 |  | 1.4 | 4 | Near-Infrared | Cirrus
5 | 1.6 | 1.6 | 5 | Near-Infrared | Snow/Ice
6 | 2.3 | 2.2 | 6 | Near-Infrared | Cloud Particle Size
7 | 3.9 | 3.9 | 7 | Infrared | Shortwave Window
8 | 6.2 | 6.2 | 8 | Infrared | Upper-level Water Vapor
9 | 6.9 | 6.9 | 9 | Infrared | Mid-level Water Vapor
10 | 7.3 | 7.3 | 10 | Infrared | Lower-level Water Vapor
11 | 8.6 | 8.4 | 11 | Infrared | Cloud-Top Phase
12 | 9.6 | 9.6 | 12 | Infrared | Ozone
13 | 10.4 | 10.3 | 13 | Infrared | “Clean” Longwave Window
14 | 11.2 | 11.2 | 14 | Infrared | Longwave Window
15 | 12.4 | 12.3 | 15 | Infrared | “Dirty” Longwave Window
16 | 13.3 | 13.3 | 16 | Infrared | CO2 Longwave
Advanced Baseline Imager Spectral Bands
Notes: Thanks to JMA and Bill Ward and Jordan Gerth.

## Slide 46: Summary
The ABI on GOES-R will improve over the current instrument in many aspects:
  Spatial, temporal, spectral, calibration, etc.
The great amount of information from the GOES-R will offer a continuation of current products and new products.
The ABI builds on previous experience/instruments:
  The ABI has already had a long history, even before launch.
Similar imagers by Europe, Japan, Korea, etc.
  ABI-like coverage of most of the globe!
Thanks to JMA, Yasuhiko Sumida and SSEC

## Slide 47
Conclusions
The ABI on the GOES-R series continues the critical continuity of geostationary imagers and will have huge positive societal impacts, given its improved temporal, spatial, spectral and radiometric attributes.
Impact areas include, but are not limited to: weather, Numerical Weather Prediction, severe weather, hazards (volcanic ash plumes), aviation, environmental (fires), health (smoke), oceanographic, cryosphere, land, etc.
Part of a global constellation.

## Slide 48: Geostationary Imagers: Number of Spectral bands (~ resolution)
Time | Instruments | Visible/NearIR | Infrared (IR)
Late 1950s | N/A | N/A | N/A
1966+ | ATS-1/3 (Spin-Scan Cloud Camera) | 1 (0.1 μm) | N/A
1967+ | ATS-3 (Multicolor Spin-Scan Cloud Camera) | 3 (0.1 μm) | N/A
1974 | ATS-6 (Geosynchronous Very High Resolution Radiometer) | 1 (0.2 μm) | 1 (2 μm)
1974/1975 | SMS-1/2 (Visible Infrared Spin-Scan Radiometer (VISSR)) | 1 (0.15 μm) | 1 (2 μm)
1975+ | GOES-1/3 (VISSR) | 1 (0.2 μm) | 1 (1 μm)
1980+ | GOES-4/7 (VISSR + VAS) | 1 (0.2 μm) | 3 (1 μm)
1994+ | Imager-8/12 + Sounder | 1 (0.2 μm) | 4 (1 μm)
2010+ | Imager-13/15 + Sounder | 1 (0.2 μm) | 4 (1 μm)
2017+ | ABI | 6 (0.1 μm) | 10 (1 μm)
2033? |  |  | 
U.S. Meteorological Imagers
Large improvements with the ABI!
Notes: Value in parenthesis is approximate 50% width of the visible or IR window.
http://cimss.ssec.wisc.edu/goes/calibration/
Values are approximate.

## Slide 49: Geostationary Imagers: Spatial Resolution (approximate)
Time | Instruments | Visible/NearIR | Infrared (IR)
Late 1950s | N/A | N/A | N/A
1966+ | ATS-1/3 (Spin-Scan Cloud Camera) | 4 km | N/A
1967+ | ATS-3 (Multicolor Spin-Scan Cloud Camera) | 4 km | N/A
1974 | ATS-6 (Geosynchronous Very High Resolution Radiometer) | 6 km | 11 km
1974/1975 | SMS-1/2 (Visible Infrared Spin-Scan Radiometer (VISSR)) | 1 km | 8 km
1975+ | GOES-1/3 (VISSR) | 1 km | 8 km
1980+ | GOES-4/7 (VISSR + VAS) | 1 km | 7-14 km
1994+ | Imager-8/12 + Sounder | 1 km | 4-8 km
2010+ | Imager-13/15 + Sounder | 1 km | 4 km
2017+ | ABI | 0.5 – 1 km | 2 km
2033? |  |  | 
U.S. Meteorological Imagers
Large improvements with the ABI!
Notes: Values are approximate, at satellite sub-points. GOES Imager over-sampling not represented.

## Slide 50: Geostationary Imagers: Temporal Resolution
Time | Instruments | Visible/NearIR | Infrared (IR)
Late 1950s | N/A | N/A | N/A
1966+ | ATS-1/3 (Spin-Scan Cloud Camera) | 20 min | N/A
1967+ | ATS-3 (Multicolor Spin-Scan Cloud Camera) | 24 min | N/A
1974 | ATS-6 (Geosynchronous Very High Resolution Radiometer) | 25 min | 25 min
1974/1975 | SMS-1/2 (Visible Infrared Spin-Scan Radiometer (VISSR)) | 20 min | 20 min
1975+ | GOES-1/3 (VISSR) | 30 min | 30 min
1980+ | GOES-4/7 (VISSR + VAS) | 30 min | 30 min
1994+ | Imager-8/12 + Sounder | 7 – 30 min | 7 – 30 min
2010+ | Imager-13/15 + Sounder | 7 – 30 min | 7 – 30 min
2017+ | ABI | 0.5 - 5 - 15 min | 0.5 - 5 - 15 min
2033? |  |  | 
U.S. Meteorological Imagers
Large improvements with the ABI!
Notes: Values are approximate. Times are routine, not special modes.

## Slide 51: Approximate spectral and spatial resolutions of US GOES Imagers
~ Band Center (um) | GOES-1/3 | GOES-4/7 | GOES-8/11 | GOES-12/13 | GOES-13/15 | GOES-R+
0.47 |  |  |  |  |  | 
0.64 |  |  |  |  |  | 
0.86 |  |  |  |  |  | 
1.6 |  |  |  |  |  | 
1.38 |  |  |  |  |  | 
2.2 |  |  |  |  |  | 
3.9 |  |  |  |  |  | 
6.2 |  |  |  |  |  | 
~6.7 |  | 14km |  |  |  | 
7.3 |  |  |  |  |  | 
8.5 |  |  |  |  |  | 
9.7 |  |  |  |  |  | 
10.3 |  |  |  |  |  | 
11.2 |  |  |  |  |  | 
12.3 |  |  |  |  |  | 
13.3 |  |  |  |  |  | 
8
4
2
Visible
Near-IR
Infrared
Box size represents pixel size
“MSI mode”
Notes: 0.40 inches = 4km; 0.80 inches = 8km
MSI is Multi-Spectral Imaging Mode (dashed boxes)
This does not show other improvements: SNR, MTF, bit-depth, navigation, coverage rates, etc.
ATS and SMS not shown.

## Slide 52: Thanks to…
Scott Lindstrom, Paul Menzel, Steven J. Goodman, Daniel T. Lindsey, Robert M. Rabin, Kristopher M. Bedka, John L. Cintineo, Christopher S. Velden, A. Scott Bachmeier, Mat Gunshor, Chris Schmidt, Yasuhiko Sumida
Roger Heymann, Kaba Bah, Joleen Feltz, Tom Whittaker, Jordan Gerth, Margaret Mooney, Andy Heidinger, William Straka, Jun Li, Steve Ackerman, Bob Aune, Don Hillger, Tony Schreiner, Justin Sieglaff, Jim Jung, Elaine Prins, Brad Pierce, Wayne Feltz, Jean Phillips, Linda Hedges, Jim Nelson, Gary Wade, Don Hillger, Jinlong Li, Jing Zheng, Allen Huang, Bob Rabin, the SSEC data center, Mike Pavolonis, Jaime Daniels, ASPB, STAR, NESDIS, NSSL, MUG, Kevin Ludlum, GOES operators, GOES shift supervisors, CWG, PRO, PWG, AWG, PSE, Mark DeMaria, Dave Martin, Bill Ward, SSD chiefs, Joe Schmit, etc!
GOES-R Program Office, Greg Mandt, NASA, Pam Sullivan, Tim Walsh, Exelis Industries, Harris, Lockheed Martin, and other industry partners, JMA, EUMETSAT, CGMS, etc.
You.

## Slide 53: Acknowledgements
The authors would like to thank the entire GOES and GOES-R teams; both within the government, industry and academia.
The views, opinions, and findings contained in this presentation are those of the authors and should not be construed as an official National Oceanic and Atmospheric Administration or U.S. Government position, policy, or decision.

## Slide 54: Back-up

## Slide 55: Web page
www.goes-r.gov

## Slide 56: GOES-R ABI Weighting Functions
ABI has 1 CO2 band, so upper-level temperature will be affected

## Slide 57: GOES-13 Sounder WFs
The GOES-N sounder has 5 CO2 bands, more SW bands

## Slide 58
Current GOES Sounder spectral coverage and that possible from an advanced high-spectral sounder. The broad-band nature of the current GOES limits the vertical resolution.
Example spectral coverage

## Slide 59
The relative vertical number of independent pieces of information is shown. Note that the moisture content is similar between the ABI and the current GOES Sounder. The Sounder does show more temperature information than the ABI. Caveat: Even if two systems have the same number of pieces of information, they may represent different vertical levels. This information content analysis does not account for any spatial or temporal differences.

## Slide 60
Meso-scale box locations are movable
15 min
5 min
1 min
1 min
Notes: 1-km2 spatial resolution at satellite nadir. Pixel Areas are approximate. Each bin is rounded to the nearest 1km2 until we get to 9.5km2 and then all are binned into the red 10+ area. So the first, dark blue, ring covers pixel areas from 1 to 1.49km2 and is labeled “1”, above 1.5 to below 2.5km2 goes into the next ring and is called “2”, etc. GOES-Test location. PUG CONUS sector. Two meso-scale image sectors shown; these are selectable. The same central lat/lon used for these mesoscales produces a different sized and shaped area for different satellite locations.

## Slide 61: Next Generation Geo Imagers (multi-spectral (>11), on the order of 1km resolution, ~10 min FD)
2002 – SEVIRI (MSG) Europe
2014 – AHI (Himawari-8) Japan
2016 – ABI (GOES-R) USA
2016 – AGRI (FY4) China
2017 – MSU-GS (Electro-L) Russia
2017 – ABI (GOES-S) USA
2018 – AMI (KOMPSAT-2A) Korea
2019 – FCI (MTG) Europe
202? – anticipated ‘geo-like’ PCW. Canada