NOAA NESDIS

Center for Satellite Applications and Research

GOES-R Advanced Baseline Imager (ABI) Algorithm Theoretical Basis Document

For

Cloud and Moisture Imagery (CMIP)

Tim Schmit, NOAA/NESDIS/STAR

Mat Gunshor, CIMSS

Wenhui Wang, IMSG Inc.

Gang Fu, PSGS

Version 2.2

June 15, 2010

# TABLE OF CONTENTS

TABLE OF CONTENTS	2

LIST OF FIGURES	4

LIST OF TABLES	4

ACRONYMS	5

ABSTRACT	6

1	INTRODUCTION	6

1.1	Purpose of This Document	6

1.2	Who Should Use This Document	6

1.3	Inside Each Section	7

1.4	Related Documents	7

1.5	Revision History	7

2	PRODUCT OVERVIEW	9

2.1	Products Generated	9

2.2	Instrument Characteristics	9

2.3	Product Requirement Description	10

3	ALGORITHM DESCRIPTION	13

3.1	Algorithm Overview	13

3.2	Processing Outline	14

3.3	Algorithm Input	14

3.4	Theoretical Description	15

3.4.1	 Radiometric Calibration	15

3.4.1.1 Converting Scaled Reflectance to TOA Reflectance (bands 1-6)	15

3.4.1.2 Converting Scaled Radiance to Spectral Radiance (bands 7-16)	16

3.4.1.3 Converting Spectral Radiance to BT (bands 7-16)	16

3.4.2	 Mapping Reflectance and Brightness Temperature to BV	18

3.4.2.1  Bi-Linear Stretch	19

3.4.2.2  Square Root Stretch	19

3.5	Algorithm Output	20

4	TEST DATA SETS AND OUTPUTS	22

4.1	GOES-R Simulated Input Data Sets	22

4.2	Output from Simulated ABI Data Sets	28

4.2.1	 Imagery Generated from Simulated ABI Data	28

4.2.2	 Precisions and Accuracy Estimation	35

4.2.3	 Error Budget	37

5	PRACTICAL CONSIDERATIONS	37

5.1	Numerical Computation Considerations	37

5.2	Programming and Procedural Considerations	38

5.3	Quality Assessment and Diagnostics	38

5.4	Exception Handling	39

5.5	Algorithm Validation	39

6	ASSUMPTIONS AND LIMITATIONS	40

6.1	Assumed Sensor Performance	40

6.2	Pre-Planned Product Improvements	40

6.2.2 Quality Control Indicators	40

7	REFERENCES	41

ACKNOWLEDGEMENTS	42

# LIST OF FIGURES

Figure 1 High level flowchart for generating CMIP	13

Figure 2 ABI Band 2 stored as a McIDAS AREA displayed in McIDAS-X	23

Figure 3. ABI Band 14 stored as a McIDAS AREA displayed in McIDAS-X	23

Figure 4. ABI Band 1 stored as a NetCDF displayed in McIDAS-V	24

Figure 5. ABI Band 7 stored as a NetCDF displayed in McIDAS-V	25

Figure 6. ABI Bands 1-6 converted to an AWIPS-ready NetCDF and displayed in AWIPS	26

Figure 7. ABI Bands 9-16 converted to an AWIPS-ready NetCDF and displayed in AWIPS	26

Figure 8. Reflectance of ABI Band 1 at 22:00 UTC on 05 June 2005 displayed in McIDAS	27

Figure 9. Brightness Values of ABI Band 1 at 22:00 UTC on 04 June 2005 displayed in McIDAS	28

Figure 10. Radiance of ABI Band 7 at 22:00 UTC on 04 June 2005 displayed in McIDAS	29

Figure 11. Brightness Temperature of ABI Band 7 at 22:00 UTC on 04 June 2005 displayed in McIDAS	30

Figure 12. Brightness Value derived from simulated ABI Band 7 data at 22:00 UTC on 04 June 2005 displayed in McIDAS	31

Figure 13. ABI band 4 (1.38 um) simulation of hurricane Katrina at 22 UTC on September 28, 2005.	35

Figure 14. ABI band 15 (12.3 um) simulation of the Pacific at 137 West longitude at 20 UTC on June 26, 2008.	36

Figure 15. The ‘stepped-edge’ approach of the ABI FD scan	39

# LIST OF TABLES

Table 1. GOES-R ABI instrument characteristics (the spatial resolution reflects the sub-point value).	9

Table 2. CMIP Requirements	10

Table 3. Slope and intercept (TBV, the Min/Max Values are given in radiance units of mW/(m2•sr•cm-1))	13

Table 4. Table of Planck Coefficients (TBV)	15

Table 5. Table of Planck Coefficients. These values are based on the Gaussian-Hybrid version of the ABI mock SRF (ftp://ftp.ssec.wisc.edu/ABI/SRF/)	15

Table 6 Fields in CMIP single-band imagery products (the band center frequency information is the area under the curve weighted value and could be stored in a header)	19

Table 7. Fields in CMIP multi-band imagery products (the band center frequency information is the area under the curve weighted value and could be stored in a header)	19

Table 8. Comparison results of generated Imagery products and validation data serving as GOES-R ABI proxy data for the GOES-R CMIP	30

# ACRONYMS

ABI – Advanced Baseline Imager

AIT – Algorithm Integration Team

ATBD – Algorithm Theoretical Basis Document

AWG – Algorithm Working Group

AWIPS – Advanced Weather Interactive Processing System

BT – Brightness Temperature

BV – Brightness Values

CMIP – Cloud and Moisture Imagery Product

CONUS – Continental United States

DC – Digital Count

FD – Full Disk

FGF – Fixed Grid Format

GPO – GOES-R Program Office

GRB – GOES ReBroadcast

GVAR – GOES Variable

IR – InfraRed

KPP – Key Performance Parameter

McIDAS – Man computer Interactive Data Access System

MTF – Modulation Transfer Function

SI – Scaled Integer

SNR – Signal-to-Noise Ratio
SRF – Spectral Response Function

TBD – To Be Determined

TBV – To Be Verified

TOA – Top Of Atmosphere

UTC – Universal Time Coordinated

VAGL - Vendor-Allocated Ground Latency

# ABSTRACT

This document provides a theoretical description of the algorithms used by the Cloud and Moisture Imagery Product (CMIP) from the Advanced Baseline Imager (ABI) onboard the GOES-R series. The topics covered in this document include requirements for CMIP algorithms and software system, description of CMIP key algorithms, test data sets and outputs, practical considerations and assumptions and limitations.

The GOES-R ABI is designed to observe the Western hemisphere in various intervals and at 0.5, 1, 2 km spatial resolutions in visible, near-IR, and IR wavelengths, respectively. The ABI has two main scan modes, the most likely will allow full disk imagery every 15 minutes, along with the CONUS every 5 minutes and a meso-scale as often as every 30 sec. CMIP is the ABI tier 1A and key performance parameter (KPP) product, including 16 ABI single-band images for 3 coverage areas plus 3 multi-band spectral products in NetCDF and McIDAS formats, which will be used as input data by various other algorithms.

GOES-R ABI CMIP algorithms have been tested on ABI simulated data covering the CONUS and nearly Full Disk areas. The generated image files have been compared with the validation data generated by the research code, and the images are effectively identical.

# 1	INTRODUCTION

## Purpose of This Document

The primary purpose of this algorithm theoretical basis document (ATBD) is to provide a theoretical description (scientific and mathematical) of the algorithms used by the Cloud and Moisture Imagery Product (CMIP) from the Advanced Baseline Imager (ABI) onboard the GOES-R series of NOAA geostationary meteorological/environmental satellites. CMIP is the ABI tier 1A and Key Performance Parameter (KPP) product.

Cloud and Moisture Imagery algorithms produce digital maps of clouds, moisture, and atmospheric windows, through which land and water are observed, by reporting reflectance and radiance measurements for visible, near-IR and IR bands, respectively. For visible bands, the reflectance (or reflectance factor) can be converted to digital counts, ranging from 0-255 for a 8-bit system. Information will also be provided on the conversion from radiance values to reflectance factor (ABI bands 1-6) and brightness temperatures (ABI bands 7-16). These will be converted into digital counts, again ranging from 0-255 for a 8-bit system and 0-4095 for a 12-bit system. Cloud and Moisture Imagery provides input to other algorithms producing other environmental products.

## Who Should Use This Document

The intended users of this document include algorithm reviewers, who would understand the theoretical basis of CMIP, product users, who would use the product in an operational task, scientific programmers, who would develop new algorithms, and system administrator, who would maintain the software.

## Inside Each Section

This document consists of following main sections:

- Product Overview: provides relevant details of the ABI and a brief description of the products generated by the algorithm.

- Product Requirement Description: provides the detailed requirements for the CMIP key algorithms and software system.

- Algorithm Description: provides the details for CMIP processing outline, input/output parameters and key algorithms.

- Test Data Sets, and Output: provides a description of the test data sets used to characterize the performance of the algorithms and quality of the data products. It also describes the results of using test data sets.

- Practical Considerations: provides a description of the issues involving CMIP software system programming, quality assessment, diagnostics, and exception handling.

- Assumptions and Limitations: provides an overview of the current assumption and limitations of the approach and a plan for overcoming these limitations with further algorithm development.

## Related Documents

GOES-R Ground Segment (GS) Functional and Performance Specification (F&PS).

GOES-R Series Ground Segment Project Notional Transition from GVAR to GRB Operations Plan

GOES-R Mission Requirements Document

## Revision History

Version 0.1 was created by Wenhui Wang of NOAA/NESDIS/STAR and I. M. System Groups to accompany the delivery of the version 0.1 algorithm to the GOES-R AWG Algorithm Integration Team (AIT). T. Schmit added several sections.

Version 1.0 of this document was the official adaptation of Version 0.1.

Version 2.0 was developed by Gang Fu of NOAA/NESDIS/STAR and PSGS based on the GOESR Imagery CDR and TRR to meet 80% ATBD requirement. This version was reviewed by many, including T. Schmit of NOAA/NESDIS/STAR.

Version 2.0 was completed by T. Schmit (and others), leveraging the many comments from the IV&V reviewer.

# 2	PRODUCT OVERVIEW

This section describes the CMIP and the requirements it places on the system.

## 2.1	Products Generated

The CMIP is responsible for ABI clouds and moisture imagery, and will produce 54 total end-products, including:

- 16 ABI single-band products (TOA reflectance in bands 1-6 and [spectral] radiance in bands 7-16) for 3 coverage areas

- Multi-band spectral products (16 bands at 2 km resolution) for 3 coverage areas in NetCDF4 format

- Multi-band spectral products (16 bands at 2 km resolution) for 3 coverage areas in McIDAS format

Additionally, the CMIP end-products will include the information about the methods of converting TOA radiance to reflectance factor and BV (Brightness Value) for bands 1-6, and converting radiance to brightness temperature (BT) and then to BV for bands 7-16. The BV is a low-precision brightness value for a pixel on a display. It is true that the term radiance actually is a spectral radiance, e.g., radiance is only at a single frequency. Spectral radiance is radiance per unit frequency (either wavelength or wavenumber).

## 2.2	Instrument Characteristics

The ABI on GOES-R has 16 spectral bands. The selection of each covers a variety of environmental applications. ABI Infrared (IR) bands have been chosen to coincide either with spectral absorption features (including those of water vapor bands or CO2 bands) or with regions having little absorption (atmospheric windows) that permit observations of the surface. Visible and near-IR bands have been chosen in windows in order to sense lower tropospheric cloud cover (including fog) and the Earth’s surface (NOAA/NESDIS 2007).

Table 1 summarizes the instrument (nominal) central wavelength, spatial resolution (at the sub-point), and bit-depth characteristics of the ABI. The instrument has two basic modes of operation:

- Every 15 minutes, ABI will scan the full disk (FD) once, plus the continental United States (CONUS) three times (every 5 minutes). A selectable 1000 km × 1000 km mesoscale area will be scanned every 30 seconds. This has been referred to as mode 3 (or ‘flex’ mode).

- The ABI can be programmed to scan the FD iteratively. The FD image can be acquired in approximately 5 minutes (Schmit et al. 2005). The mode as been referred to as mode 4 (or the Continuous Full Disk (CFD)).

| Band Number | Nominal Central Wavelength (μm) | Spatial Resolution (km) | Bit-Depth (Expected) | Used in Cloudy and Moisture Imagery |
| --- | --- | --- | --- | --- |
| 1 | 0.47 | 1 | 12 | X |
| 2 | 0.64 | 0.5 | 12 | X |
| 3 | 0.865 | 1 | 12 | X |
| 4 | 1.378 | 2 | 12 | X |
| 5 | 1.61 | 1 | 12 | X |
| 6 | 2.25 | 2 | 12 | X |
| 7 | 3.90 | 2 | 14 | X |
| 8 | 6.19 | 2 | 12 | X |
| 9 | 6.95 | 2 | 12 | X |
| 10 | 7.34 | 2 | 12 | X |
| 11 | 8.5 | 2 | 12 | X |
| 12 | 9.61 | 2 | 12 | X |
| 13 | 10.35 | 2 | 12 | X |
| 14 | 11.2 | 2 | 12 | X |
| 15 | 12.3 | 2 | 12 | X |
| 16 | 13.3 | 2 | 12 | X |

Table 1. GOES-R ABI instrument characteristics.

The rationale for the bit-depth being 12 bits per pixel for all the bands, with the exception of 14 bits for ABI band 7 (3.9 um), is to balance the needs to minimize the transmitted data size and to ensure that the quantization step will not add noise to the system.

If we use spec noise and don't prepare for improvements in actual noise performance and loss of responsivity with time in orbit, and if we require that the noise requires 2.5 counts to be properly represented, then 10 GRB bits per pixel would be the requirement for all the ABI's solar channels.   However, if we require the noise to be represented by 3 counts, it is changed to (barely) 11 bits in all solar channels.  If you allow for an actual noise of 1/2 the spec noise, the required bit-depth increases to 12 or (barely) 13.   

In sum, we recommend a 12-bit GRB for each of the solar channels.

The following discussion on the rationale for increased bit depth to account for an actual noise level that is lower than spec, and for the likelihood that over time in orbit, the responsivities of the ABI's channels will decrease applies to all channels of the ABI, both solar and thermal IR bands. 

First, better noise levels: In the current system, ITT has built Imagers whose noise levels are almost always lower than spec, and in some cases an order of magnitude lower than spec. These means that the instrument is giving measurements with greater precision than planned, and if we don't want the GRB to lose  this precision, we need to add one bit to the GRB for every improvement of a factor of two in the noise levels.   Since the bit depth of the GRB will be fixed once and for all (and we won't be changing it for later satellites of the series), we need to include the extra bit in the original design. 

Responsivity decreases in orbit: This applies to any channel that is calibrated.  In the current GOES system, we see the instruments' responsivities falling over time, which means that as they age, the instruments can see hotter and hotter, or brighter and brighter, scenes before the detectors saturate.  But if the increase in maximum observable radiance exceeds the upper limit of what the GRB will carry, the GRB will saturate or roll over, and information from those observations will be lost.   A good example of this occurred with the 3.9-um channel of the GOES-12 Imager, whose responsivity decreased to the point where the maximum observed scene radiances exceeded 342K, which is the maximum temperature the GVAR can carry.  In this case, the GVAR count level rolled over to zero and levels slightly above, so what we got were apparent very cold pixels at the centers of the hottest scenes--such as fires or specularly reflected sunlight.  If we had established a higher maximum GVAR radiance, corresponding to, say, 350K, this would not have happened. When ITT builds an instrument to a spec for maximum observable radiance, they provide headroom in order to guarantee meeting the spec under all conditions.  This means that the actual maximum will be slightly higher than the spec.  This should also be taken into account in designing the bit-depth of the GRB.

In sum, we recommend a 12-bit GRB for each of the IR channels. That said, the 3.9 um band needs 14 bits, given it’s use both to monitor hot fires, but also cold clouds. Even with 14-bits for this band, the quantization in brightness temperature space at 200K is over 10K.

The CMIP will be produced using all 16 bands in three coverage areas: FD, CONUS, and mesoscale. Bands 1-6 are “visible bands (1 and 2)” (and include near-IR) and bands 7-16 are considered as “IR bands.” The performance of the CMIP is sensitive to any imagery artifacts or instrument noise, calibration accuracy, and geolocation accuracy.

## 2.3	Product Requirement Description

The CMIP performance requirements are derived from the GOES-R Series Ground Segment (GS) Functional and Performance Specification (F&PS) (NOAA/NASA 2008). The software system that generates routine CMIP shall meet the following requirements:

- The system should be able to convert ABI scaled radiance (SR) obtained from the GOES ReBroadcast (GRB) data stream (L1B) into reflectance factor for bands 1-6 and convert GRB scaled radiance (L1B) to spectral radiance for bands 7-16.

- The system should define the process for converting radiance to brightness temperature (BT) for IR bands.

- The system should define the process for converting TOA reflectance to BV for bands 1-6 and converting brightness temperature and to BV for bands 7-16. BV would be at least 8-bit, but it could support higher bit depths. If the maximum bit depth BV will also be provided, so that no information is lost.

- The conversion methods and the associated parameters should be embedded in CMIP end-products. Besides, users can still employ their own enhancements to the data values. For example, the users could employ a ‘square root’ function on the full bit depth BV data.

- The CMIP end-products should be produced in NetCDF (version 4) and McIDAS formats. The McIDAS convention for GOES-R is 186 for the satellite sensor. The system should ensure that these end-products could be converted into other formats, such as HDF (TBV). The NetCDF format will be Climate and Forecasts (CF) conventions compliant. More information can be found at: http://cf-pcmdi.llnl.gov

- The CMIP should contain the geolocation information with respect to the Fixed Grid Format extracted from the input data stream (TBV).

- The CMIP shall include metadata.

- The system shall implement an interface to access input data and to store the generated products.

- The GOES-R system shall produce CMIP in accordance with the requirements listed in Table 2:

|  | Threshold |
| --- | --- |
| Geographic Coverage/Conditions | CONUS | FD | Mesoscale |
| Vertical Resolution | N/A | N/A | N/A |
| Horizontal Resolution | 2 km, with finer daytime resolution |
| Mapping Accuracy | 1 km | 1 km | 1 km |
| Measurement Range | N/A | N/A | N/A |
| Refresh Rate/ Coverage Time (Mode 3—Flex Mode) | 5 min | 15 min | 30 sec |
| Refresh Rate/ Coverage Time (Mode 4—Continuous Full Disk mode) | 5 min | 5 min |  |
| VAGL | 50 sec | 50 sec | 23 sec |
| Product Measurement Precision | N/A | N/A | N/A |
| Temporal Coverage Qualifier | Day and Night |
| Product Extent Qualifier | N/A |
| Cloud Cover Conditions Qualifier | N/A | N/A | N/A |
| Product Statistics Qualifier | N/A |
| Primary Instrument | ABI |
| Prioritization | 1A |

Table 2. CMIP Requirements

# 3	ALGORITHM DESCRIPTION

This section describes the CMIP software system processing outline, input/output parameters, and key algorithms at their current level of maturity (will be improved with each revision).

## 3.1	Algorithm Overview

The CMIP algorithms consist of acquiring the radiometrically calibrated and mapped TOA radiances and BT to BV. The BV are used as indices either to customized color tables or to the red/green/blue color guns of a composite image, resulting in enhanced imagery intending to highlight environmental features of interest. The GOES-R ABI CMIP radiometric algorithms are based on GOES 8-13 algorithms (Weinreb et al. 1997; Schmit et al 1991). Algorithms for mapping TOA reflectance and BT to BV are based on examples from the literature (Acharya and Ray 2005; Russ 2002), commercial remote sensing data visualization tools (e.g., ENVI and PCI), and open source tools (e.g. McIDAS-X/V and IDV). Some display systems may be capable of displaying more that 8-bit (or 256 levels). The bit-depth of the end-products (BV) for CMIP is 12-bit for all the bands, with the exception of band 7, which is 14 bits. TBD.  Hence, the ‘square root’ function would need to be applied on the user display side and not part of converted to, say, only 8-bits..

Given the proper amount of ancillary data, the radiance data can be converted, into reflectance factor units (nominally 0-1). This is generated using what is called the ‘kappa factor’ to convert between reflectance factors to [spectral] radiances (mW/(m2 ster cm-1)). Inputs needed are the inband solar irradiance at 1 AU (Esun) for each of the first six ABI bands, a correction (e.g., ratio) for the earth-sun distance (d) correction and the value of pi. d is the ratio of the actual distance (as acquired via the GRB) to the mean earth-sun distance. The relationship is the reflectance factor () times the Esun, divided by pi and the distance correction squared.  is the solar zenith angle. It is assumed that E_sun and the distance will flow as part of GRB. Equation 3-1 is the relationship between the reflectance factor (left-hand side) and the reflectance.

(3-1)

(3-2a)

(3-2b)

Equation 3.2b shows how the radiance data can be converted into reflectance factor.  This is the equation that will be used. The values for Esun , π and d will be provided via the GRB.

CMI algorithms are responsible for:

- Converting the scaled [spectral] radiance from the input data stream to an unscaled radiance (bands 1-6)

- Converting unscaled [spectral] radiance, convert to reflectance factor to BV (bands 1-6)

- Re-sampling bands 1, 2, 3, and 5 from 1 km to 2 km for multi-band product

- Converting scaled radiance from the input data stream to an unscaled spectral radiance (bands 7-16)

- Converting the unscaled spectral radiance to equivalent BT (bands 7-16)

- Converting BT to BV (bands 7-16)

## 3.2	Processing Outline

Figure 1 High level flowchart for generating CMIP

## Algorithm Input

### 3.3.1   Primary Sensor Data

The primary input data to the CMIP algorithm is the scaled GRB radiance data (level 1b; provided as digital counts), scaling coefficients and calibration coefficients (also available from the GRB data stream).  The scaling coefficients are used to convert scaled GRB radiance data to unscaled radiance for all ABI bands. The calibration coefficients are related to the visible, near-IR radiances to a reflectance factor and using the modified Planck conversion to brightness temperatures for the IR bands.

The details regarding the actual format and data structures of the GRB will be determined by the Harris Ground System implementation and hence are not covered in detail in this document.

Table 3 shows the slope and intercept using in conversion to (and from) Scaled Radiances values similar to the work by Hillger and Schmit (2004). The slope and intercept are chosen from a trade-off of two competing interests: 1) accommodate all realistic values of scene radiance for a given band, and 2) use the full dynamic range to maximize the radiometric resolution of the data (Schmit et al 1991). In CMIP, scale coefficients (slopes and intercepts in Table 3b) are also used to convert scaled data to un-scaled quantities. Table 3a shows the version assuming scaling to reflectance factor for ABI bands 1-6, while Table 3b shows the version assuming scaling to [spectral] radiances. It is this method that was apparently decided by the GPO in earier 2010 (Clarke, personal communication).

| Band Number | Central Wavelength (μm) | Min Value | Max Value | Slope | Intercept |
| --- | --- | --- | --- | --- | --- |
| 1 | 0.47 | tbd | tbd | tbd | tbd |
| 2 | 0.64 | tbd | tbd | tbd | tbd |
| 3 | 0.86 | tbd | tbd | tbd | tbd |
| 4 | 1.38 | tbd | tbd | tbd | tbd |
| 5 | 1.61 | tbd | tbd | tbd | tbd |
| 6 | 2.26 | tbd | tbd | tbd | tbd |
| 7 | 3.9 | -0.0114 | 24.96 | 655.9884675 | 8.4782685 |
| 8 | 6.15 | -0.1692 | 28.37 | 143.4709168 | 25.2752791 |
| 9 | 7.0 | -0.2472 | 45 | 90.4853365 | 23.3679752 |
| 10 | 7.4 | -0.2871 | 79.83 | 51.0996918 | 15.6707215 |
| 11 | 8.5 | -0.3909 | 134.9 | 30.2545252 | 12.8264939 |
| 12 | 9.7 | -0.4617 | 108.4 | 37.5936052 | 18.3569675 |
| 13 | 10.35 | -0.4935 | 183.6 | 22.2359817 | 11.9734570 |
| 14 | 11.2 | -0.5154 | 198.7 | 20.5491038 | 11.5910081 |
| 15 | 12.3 | -0.5262 | 212.3 | 19.2378811 | 11.1229730 |
| 16 | 13.3 | -1.5726 | 170.2 | 23.8354319 | 38.4836002 |

Table 3a. Slope and intercept to convert from the calibrated radiance data for the generation of the SR counts in GRB (TBV, the Min/Max Values are given in terms of radiance units of mW/(m2•sr•cm-1))

| Band Number | Central Wavelength (μm) | Min Value | Max Value | Slope | Intercept |
| --- | --- | --- | --- | --- | --- |
| 1 | 0.47 | tbd | tbd | tbd | tbd |
| 2 | 0.64 | tbd | tbd | tbd | tbd |
| 3 | 0.86 | tbd | tbd | tbd | tbd |
| 4 | 1.38 | tbd | tbd | tbd | tbd |
| 5 | 1.61 | tbd | tbd | tbd | tbd |
| 6 | 2.26 | tbd | tbd | tbd | tbd |
| 7 | 3.9 | -0.0114 | 24.96 | 0.0015273 | -0.0215273 |
| 8 | 6.15 | -0.1692 | 28.37 | 0.0017306 | -0.2517306 |
| 9 | 7.0 | -0.2472 | 45 | 0.0027927 | -0.4527927 |
| 10 | 7.4 | -0.2871 | 79.83 | 0.0049261 | -0.5049261 |
| 11 | 8.5 | -0.3909 | 134.9 | 0.0083048 | -0.6583048 |
| 12 | 9.7 | -0.4617 | 108.4 | 0.0067147 | -0.8067147 |
| 13 | 10.35 | -0.4935 | 183.6 | 0.0113081 | -0.8613081 |
| 14 | 11.2 | -0.5154 | 198.7 | 0.0122604 | -0.8622604 |
| 15 | 12.3 | -0.5262 | 212.3 | 0.0130662 | -0.8630662 |
| 16 | 13.3 | -1.5726 | 170.2 | 0.0106428 | -2.6606428 |

Table 3b. Slope and intercept to convert from the GRB SR to radiance values (TBV, the Min/Max Values are given in radiance units of mW/(m2•sr•cm-1))

The values for the min/max radiance were requested in February of 2010 and are currently not available since they are stamped ITAR. This issue is being addressed.

The values in Table 3.3a would be used when one is generating GRB (at a central facility). The minimum and maximum values listed in Table 3.3a and b represent the bounds of the un-scaled radiances. These values are larger than the instrument only minimum and maximum values, to limit data being ‘clipped’ on either end. Coefficients for converting data to TOA radiance/BT are also input parameters for CMIP. They may be obtained from GRB data stream (TBV).  The values in Table 3.3b would be used to un-scale the SR by the many users. Table 3.3c is the maximum values used for the generation of the maximum radiance values in Table 3.3a and 3.3b.

| Band Number | Central Wavelength (μm) | Min Rad for Scaling | Max Rad for Scaling | Min Rad - Noise | Max Rad. + Noise |
| --- | --- | --- | --- | --- | --- |
| 1 | 0.47 | tbd | tbd | tbd | tbd |
| 2 | 0.64 | tbd | tbd | tbd | tbd |
| 3 | 0.86 | tbd | tbd | tbd | tbd |
| 4 | 1.38 | tbd | tbd | tbd | tbd |
| 5 | 1.61 | tbd | tbd | tbd | tbd |
| 6 | 2.26 | tbd | tbd | tbd | tbd |
| 7 | 3.9 | 0 | 24.95 | -0.0114 | 24.96 |
| 8 | 6.15 | 0 | 28.197 | -0.1692 | 28.37 |
| 9 | 7.0 | 0 | 44.751 | -0.2472 | 45 |
| 10 | 7.4 | 0 | 79.544 | -0.2871 | 79.83 |
| 11 | 8.5 | 0 | 134.54 | -0.3909 | 134.9 |
| 12 | 9.7 | 0 | 107.98 | -0.4617 | 108.4 |
| 13 | 10.35 | 0 | 183.13 | -0.4935 | 183.6 |
| 14 | 11.2 | 0 | 198.2 | -0.5154 | 198.7 |
| 15 | 12.3 | 0 | 211.76 | -0.5262 | 212.3 |
| 16 | 13.3 | 0 | 168.62 | -1.5726 | 170.2 |

Table 3c. Min/Max Values are given in radiance units of mW/(m2•sr•cm-1)). A factor of three was used for the IR band noise.

Instrument specifications for noise are given in degrees Kelvin for the IR bands.  The specification is for noise at a temperature of 300 K.  This is called the Noise Equivalent delta Temperature (NEdT) and NEdT is 0.1 K for all IR bands except for band 16 (the 13.3 micrometer band) which is 0.3 K.  The Noise Equivalent delta Radiance is referred to as NEdN  in mW/m2/ster/cm-1.  There is a requirement that the quantization step be no larger than 0.5 times the NEdN.  Since radiances are distributed and stored as digital counts, there can only be as many values as the bit depth allows (for instance, if data are 12-bits there are 212 = 4096 values that can be used.  The difference in radiance units between the values stored in these counts will be uniform across the range of available counts, though it is not uniform in brightness temperature.  To calculate NEdN from brightness temperature, first the radiance at 300 K, where the NEdT is defined, must be calculated.  This is done using the modified Planck function which takes into account the instrument’s spectral response, so solving equation 3-8 for radiance given a brightness temperature of 300:

(300) = fk1 / [ exp (fk2 / (bc1 + (bc2 * 300))) - 1 ]			(X-1)

NEdN = (300 + NEdT) - (300)				(X-2)

NEdN is a constant value across the entire temperature range of the instrument.  To calculate NEdT at a temperature other than 300 K, the NEdN can be used in conjunction with the modified inverse Planck Function (equation 3-7) and the modified Planck Function (equation 3-8).  For example, to calculate NEdT at 240 K, first the radiance at 240 K must be calculated the same as in equation X-1.

(240) = fk1 / [ exp (fk2 / (bc1 + (bc2 * 240))) - 1 ]			(X-3)

T+ = [ fk2 / (alog((fk1 / (+ NEdN) + 1))  -  bc1 ] / bc2			(X-4)

NEdT(240) = T+ - 240					(X-5)

Equations X-3 through X-5 can be used to obtain the NEdT at any brightness temperature.  Table X.1 lists the NEdT values at 300, 240, and 200 K for the IR bands on the ABI.

| Band | Central WL (µm) | NEdT (300) K | NEdT (240) K | NEdT (200) K | NEdN mW/m2/ster/cm-1 |
| --- | --- | --- | --- | --- | --- |
| 7 | 3.9 | 0.1 | 1.3253 | 12.2034 | 0.0038 |
| 8 | 6.19 | 0.1 | 0.4346 | 1.9664 | 0.0564 |
| 9 | 6.95 | 0.1 | 0.3576 | 1.3583 | 0.0824 |
| 10 | 7.34 | 0.1 | 0.3272 | 1.1423 | 0.0957 |
| 11 | 8.5 | 0.1 | 0.2628 | 0.7408 | 0.1303 |
| 12 | 9.61 | 0.1 | 0.2248 | 0.5421 | 0.1539 |
| 13 | 10.35 | 0.1 | 0.2062 | 0.4599 | 0.1645 |
| 14 | 11.2 | 0.1 | 0.1899 | 0.3856 | 0.1718 |
| 15 | 12.3 | 0.1 | 0.1738 | 0.3221 | 0.1754 |
| 16 | 13.3 | 0.3 | 0.4880 | 0.8421 | 0.5242 |

Table X.1.  Noise Equivalent delta Temperature (NEdT) and Radiance (NEdN) for the infrared bands on the ABI.  NEdT is given, the other values are derived from it.  Note that these values were calculated using the University of Wisconsin mock spectral response functions as a basis for spec noise; they will change when flight spectral response functions are available and these are not representative of actual noise measurements from the ABI.

The fixed grid coordinates and QC flags are also extracted from the GRB data stream. It is assumed that the upper-left of the fixed grid format corresponds to the (0,0) point. This is following the convention of the current GOES Imager and predominate scan pattern of the ABI.

### 3.3.2	Ancillary Data

Many parameters are acquired from the GRB data stream. This includes, but is not limited to: SR, un-scaling coeffiencts, conversion information to reflectance factor, modified Planck conversion coefficients, etc.

### 3.3.3     Derived Data

N/A

## 3.4	Theoretical Description

### 3.4.1		Radiometric Calibration

#### 3.4.1.1 Un-scaling Scaled Radiance (bands 1-6)

The radiance is derived from the SR (Scaled Radiance) value.  A linear conversion is required:

(3-3)

where  is radiance; is digital counts of the scaled reflectance;  and   are scaling coefficients obtained from the GRB data stream.

#### 3.4.1.2 Un-scaling Scaled Radiance to Spectral Radiance (bands 7-16)

To obtain BT, the scaled radiance from the input data stream will first be converted to spectral radiance:

(3-4)

where  is spectral radiance (mW/(m2 ster cm-1)) for an ABI band characterized by central wavenumber (, is digital counts of the scaled radiance, and  and  are calibration coefficients obtained from the GRB data stream.

#### 3.4.1.3 Converting Spectral Radiance to BT (bands 7-16)

Spectral radiance will be converted to BT using two steps (Weinreb et al. 1997). Historically the first step is to convert spectral radiance to effective temperature using inverse Planck Function:

(3-5)

where  is the effective temperature,  and are two constants ( = 1.191066 x 10-5 [mW/(m2-sr-cm-4)];  = 1.438833 (K/cm-1)), is spectral radiance, and is the central wavenumber of the channel.

The second step converts effective temperature to BT (K):

(3-6)

where  and depend on band and detector (TBV) and are summarized in Table 4.

| Band Number | Central Wavelength (μm) | Central Wavenumber |  |  |
| --- | --- | --- | --- | --- |
| 7 | 3.9 | 2564.1501 | -0.51176 | 1.000721 |
| 8 | 6.15 | 1617.15 | -2.12889 | 1.004591 |
| 9 | 7.0 | 1439.15 | -0.33248 | 1.000791 |
| 10 | 7.4 | 1362.1 | -0.07097 | 1.00018 |
| 11 | 8.5 | 1176.15 | -0.17922 | 1.00051 |
| 12 | 9.7 | 1041.15 | -0.10528 | 1.00033 |
| 13 | 10.35 | 966.1 | -0.13208 | 1.00044 |
| 14 | 11.2 | 893.15 | -0.24766 | 1.000881 |
| 15 | 12.3 | 813.15 | -0.26232 | 1.001021 |
| 16 | 13.3 | 752.15 | -0.07141 | 1.0003 |

Table 4. Table of Planck Coefficients (TBV). These values are based on the Gaussian-Hybrid version of the ABI mock SRF (ftp://ftp.ssec.wisc.edu/ABI/SRF/).

A parallel method of Planck Function constants has been used to make the conversion between radiance (mW/(m2-sr-cm-1) and BT or vice versa. To convert from radiance to temperature (Kelvins):

T  =  [ fk2 / (alog((fk1 / ) + 1))  -  bc1 ] / bc2 		(3-7)

To convert from temperature (K) back to radiance (mW/(m2-sr-cm-1):

=  fk1 / [ exp (fk2 / (bc1 + (bc2 * T))) - 1 ]	         (3-8)

The two methods are needed given they both have expansive user bases with the current GOES system. The parameters in the two methods are listed in Table 5. Note that these values will need to be updated with the flight SRF.

| Band Number | Central Wavelength (μm) | Central Wavenumber (μm-1) | fk1 | fk2 | bc1 | bc2 |
| --- | --- | --- | --- | --- | --- | --- |
| 7 | 3.9 | 2564.1501 | 2.00800E+05 | 3.68920E+03 | 0.51139 | 0.99928 |
| 8 | 6.15 | 1617.15 | 5.03710E+04 | 2.32670E+03 | 2.11916 | 0.99543 |
| 9 | 7.0 | 1439.15 | 3.55010E+04 | 2.07060E+03 | 0.33222 | 0.99921 |
| 10 | 7.4 | 1362.10 | 3.00990E+04 | 1.95980E+03 | 0.07096 | 0.99982 |
| 11 | 8.5 | 1176.15 | 1.93780E+04 | 1.69220E+03 | 0.17913 | 0.99949 |
| 12 | 9.7 | 1041.15 | 1.34420E+04 | 1.49800E+03 | 0.10525 | 0.99967 |
| 13 | 10.35 | 966.10 | 1.07400E+04 | 1.39000E+03 | 0.13202 | 0.99956 |
| 14 | 11.2 | 893.15 | 8.48600E+03 | 1.28500E+03 | 0.24744 | 0.99912 |
| 15 | 12.3 | 813.15 | 6.40380E+03 | 1.16990E+03 | 0.26205 | 0.99898 |
| 16 | 13.3 | 752.15 | 5.06800E+03 | 1.08220E+03 | 0.07139 | 0.99970 |

Table 5. Table of Planck Coefficients. (TBV). These values are based on the Gaussian-Hybrid version of the ABI mock SRF (ftp://ftp.ssec.wisc.edu/ABI/SRF/).

The relationship between the two approaches is:

fk1 = 	                                             (3-9)

fk2 =                                                      (3-10)

bc1 = -α/β		                                 (3-11)

bc2 = 1/β			                   (3-12)

Finally, an implementation of the above method uses the fk1 and fk2, along with the central wavelength to derive the bc1 and bc2 internally. It should be noted that that the central wavenumber needs to be properly computed to derive the most accurate fk1 and fk2. For example, a nominal value should not be used. The central wavenumber is calculated by the integral of the  relative response times the wavenumber divided by the integral of the relative response. It is this methodology that has been coded for the GOES-R AWG usage.

fk1 = C1 * WaveNumber ** 3		            	(3-13)

fk2 = C2 * WaveNumber			 		(3-14)

Var_Tmp1 = log(1.0 + fk1 / Radiance)			(3-15)

Var_Tmpy = fk2 / Var_Tmpy1				(3-16)

Brt_Temp = ( Var_Tmpy - bc1)   / bc2			(3-17)

Note that the Planck Conversion coefficients will need to be updated with the official flight ABI system-level SRF. C1 is 1.191066 x 10-5 [mW/(m2·sr·cm-4)] and C2 is 1.438833 (K/cm-1). Bc1 and bc2 are the intercept and slope from linear regression fits over equally spaced radiance values between a monochromatic Planck conversion and one that integrates over the instrument SRF. Again, these values would need to be updated with the flight SRF.

### 3.4.2		Mapping Reflectance and Brightness Temperature to BV

The TOA reflectance and BT calculated from spectral radiance are floating point numbers. The method for mapping TOA reflectance and BT to integer BV (8-bit or more, TBV) are described in this section.

The Square-Root stretch method is recommended to be used for converting TOA reflectance to BV for the visible bands. The advantages and disadvantages of this method are summarized as follows:

- Advantages:

  - Covers more temperature range than a 1K/1Count stretch

  - Heritage

  - Efficient

  - Algorithm is mature

- Disadvantages:

  - Not as straight forward as a linear stretch

The Bi-Linear stretch method is recommended to be used for converting brightness temperature to BV for IR bands. The advantages and disadvantages of this method are summarized as follows:

- Advantages:

  - Highlights important features that would have been too dark

  - Heritage

  - Low risks

  - Efficient

  - Algorithm is mature

- Disadvantages:

  - Not as straight forward as a linear stretch

The square-root method (for the visible and near-IR bands) and a bi-linear method (for the IR bands) are recommended, because there is a long history in both McIDAS and AWIPS of employing a bi-linear approach for the IR bands and a square-root function for the reflective bands.

Alternatively, user can employ other methods, similar to methods used in image enhancement, to convert TOA reflectance and BT to 8-bit (or other bit-depth) scaled BV.

#### 3.4.2.1  Bi-Linear Stretch

Assuming 8 bits per pixels, the linear scaling method provides a linear amplitude transformation of input reflectance or radiance/BTs to output BV.

BV08= 418 – BT (for “cold” scenes)                                               (3-18a)

BV08= 660 – (2*BT)                                                     (3-18b)

where BV08 is the new brightness value,BT is the original value BT. This allows for two slopes at either side of a break point. For example, if the BT is less then 242 K, then BV08 = 418 – T; while for value equal or great than 242 K, then BV08 = 660 – (2 * T).

Assuming the maximum bit depth (12 for most bands) is used for the IR bands, then this ‘bi-linear’ approach will not be needed, since the information would not need to be similarly ‘compressed’.

BV12 = abs(count-((2^n)-1))						(3-18c)

#### 3.4.2.2  Square Root Stretch

Power law stretch is a nonlinear algorithm that changes image brightness according to:

(3-19)

where BV08 is the new brightness value for an 8-bit system, is the original reflectance factor value, and n is the power scaling coefficient. If n > 1, high values are enhanced disproportionately with respect to low values. If n < 1, low BV are enhanced disproportionately with respect to high values.

The square root enhancement is a special case of the power law stretch (n=1/2). It compresses the upper end of spectrum and stretches the lower end. This method has been used for decades when displaying GOES visible data (and for many years for AWIPS displays).  Reflectance factors darker than 0 would be mapped to a 0 BV, while values greater than 1 will be mapped to 255 (in an 8-bit system).

(3-20)

Where NINT (or IDINT) is the “nearest integer” and SQRT is the Square-root function.

If a system can display the full bit depth (12 or 14), for bands 1-6, then this square root function could be applied locally. So, the conversion is simply:

BV12 = GRB_Count (SR)							(3-20a)

3.4.3	Down-scaling Algorithm

To produce CMIP multi-band end-products, it is necessary to re-sample the scaled radiance from 1 km to 2 km for ABIl visible and near-IR bands (1, 3 & 5), since the spatial resolution of the data in multi-band products is 2 km while the native resolution of ABI bands 1, 3 and 5 is 1 km.

There are two methods for this down-scaling. The default method is via re-sampling. The re-sampling algorithm is applied to downscale the data and it is described as follows:

,                  	                         (3-21)

where  is the re-sampled data and  is the original data. The current algorithm simply sub-samples.  For the 1 km data, the ‘upper-left’ pixels are selected. Assuming we are following the FGF for the coordinate of (0,0) being the most ‘northwest’ pixel. For example, pixels, (0,0), (0,2), (0,4), etc. This is independent of the saturation or quality flag. Those flags will be carried along from the selected pixel.

The ABI band 2 spatial resolution is 0.5 km nominally, so more ‘down-scaling’ is needed for the multi-band files. For the 0.5 km data to 2 km,  the pixel “northwest” of the 2 km pixels will be used. For example, (1,1), (1, 5), (1,9), etc.

Figure 2. Re-sampling points for the ABI FGF for the 0.5, 1 and 2 km. The cyan points represent the 0.5 km data, the yellow points the 1 km data and the black points the 2 km data.

The advantages of using this sampling algorithm include:

- Quicker

- Traceable, less “blurry”

- Doesn’t create artificial values

  - If the scene has a bi-modal distribution

- Straight forward (due to resolutions nested in one another)

In addition, uses that need the full resolution data could still access the full resolution files (e.g., not the multi-band files).

The second method is to average pixels. An advantage of spatially averaging is that it can improve the signal-to-noise ratio and it may more closely match the 2 km IR bands with respect to implicit ‘area averaging’. The final methodology may need to consider the expected instrument performance. This is also dependent on the nature of the kernel used when ABI data are remapped from detector to pixel space. The averaging method will give equal weight to the 4 pixels (for the 1 km to 2 km case) and the 16 pixels (for the 0.5 km to 2 km case). The “majority” saturation or quality flag will be transferred to the output file. This means that if say, 8 or more of the pixels were flagged, then the average pixel would be similarity flagged. Those flags will be carried along from the selected pixel.

Hence, at this time it is thought that the option a straight arithmetic average needs to be available, along with the default sampling option.

3.4.4	Radiance Unit Conversions

The spectral radiance units will be (mW/(m2 ster cm-1)), that said,  some users may be interested in switching to other units, such as (W/(m2 ster µm)). Therefore, the methodology is included here based on Cao and Heidinger, 2002.

,                  	                         (3-22)

## where Lν = Radiance in wavenumber (mW/m2/ster/cm-1) 
Lλ = Radiance in wavelength (W/m2/ster/um) 
1000 = convert W to mW 
EQWλ=Equivalent Width in wavelength (µm) space, which is the integral of the SRF in um 
EQWν=Equivalent Width in wavenumber (cm-1) space, which is the integral of the SRF in cm-1

## The table below are the EQW values for the UW mock spectral response functions. The Equivalent Width values can be computed once the flight SRF are available.

Table: University of Wisconsin simulated SRF band Eqw’s. TBV.

| UW | Band 1 | Band 2 | Band 3 | Band 4 | Band 5 | Band 6 |
| --- | --- | --- | --- | --- | --- | --- |
| Band Eqw [cm-1] | 1872.4315 | 2535.0581 | 537.7881 | 81.5463 | 238.4452 | 101.1587 |
| Band Eqw [µm] | 0.0415 | 0.1047 | 0.0403 | 0.0155 | 0.0618 | 0.0512 |

## 3.5	Algorithm Output

The primary output of this algorithm is the information to generate enhanced cloud and moisture images. In total, 54 end-products are produced: 16 ABI channels for the 3 coverage areas (CONUS, FD, and mesoscale) in NetCDF format, 1 multi-banded image (all 16 bands) at the spatial resolution of the IR bands (2 km) for each of the 3 coverage areas in NetCDF format, and 1 multi-banded image (all 16 bands) at 2 km resolution for each of the 3 coverage areas in McIDAS format. The supported formats will be in NetCDF (version 4) format and McIDAS format. Output should be able to be converted from NetCDF or McIDAS format to other formats.

Table 6 summarizes the fields in the single-band imagery products:

| Field | Name | Description | Dimension |
| --- | --- | --- | --- |
| 1 | Radiance Data | Radiance for channels 1-16 at full spatial resolution | grid (xsizeh, ysizeh) grid (xsize1, ysize1) grid (xsize2, ysize2) |
| 2 | Reflectance Factor | Bands 1-6 [0-1] | grid (xsizeh, ysizeh) grid (xsize1, ysize1) grid (xsize2, ysize2) |
| 3 | Brightness Temperature | Bands 7-16 [K] | grid (xsize2, ysize2) |
| 4 | Day | Julian Date | array (zsize) |
| 5 | Times | Nominal and swath start/end | array (zsize) |
| 6 | Fixed Grid Coordinates | Definition of earth in GRS80 | array (lsize) |
| 7 | Sub-point (nominal) | Sub point latitude and longitude nominal | array (2) |
| 8 | Sub-point (actual) | Sub point latitude and longitude actual | array (2) |
| 9 | Un-scaling coefficients | Coefficients to unscale to reflectance factor/radiance | array (2, 6) |
| 10 | Band Center wavenumbers | Band Center wavenumbers | array (10) |
| 11 | Radiance to Brightness Temperature conversion coeffs | Plank Coefficients | array (2, 10) |
| 12 | Reflectance Factor to Radiance Coefficients | Coefficients to convert from reflectance factor to radiances for reflective bands | array (jsize) |
| 13 | Quality Flags (by band) | Quality Flags by band per swath | Array (numofswaths, 16) |
| 14 | Sat. id | Satellite ID | array (1) |
| 15 | Earth-Sun Distance | Earth-Sun Distance | array (1) |
| 16 | Image Center point | Latitude/Longitude | array (2) |
| 17 | Line array | Dimension in image coordinates | array (xsizeh) array (xsize1) array (xsize2) |
| 18 | Element array | dimension in image coordinates | array (ysizeh) array (ysize1) array (ysize2) |

Table 6. Fields in CMIP single-band imagery products (the band center frequency information is the area under the curve weighted value and could be stored in a header)

For a full disk 2 km image, the xsize2 would be 5534. For a meso-scale image, xsize would be 1000.

Table 7 summarizes the fields in the multi-band imagery products:

| Field | Name | Description | Dimension |
| --- | --- | --- | --- |
| 1 | Chs. 1 – 6 scaled radiance | Band 1-6 radiance at 2 km | grid (xsize2, ysize2, 6) |
| 2 | Chs. 7 – 16 scaled radiance | Band 7-16 radiance at 2 km | grid (xsize2, ysize2, 10) |
| 3 | Reflectance Factor | Bands 1-6 [0-1] | grid (xsize2, ysize2, 6) |
| 4 | Brightness Temperature | Bands 7-16 [K] | grid (xsize2, ysize2, 10) |
| 5 | Day/Time | Nominal and swath start/end | array (zsize) |
| 6 | Fixed Grid Coordinates | Definition of earth in GRS80 | array (lsize) |
| 7 | Sub-point (nominal) | Sub point latitude and longitude nominal | array (2) |
| 8 | Sub-point (actual) | Sub point latitude and longitude actual | array (2) |
| 9 | Un-scaling coefficients | Coefficients to unscale to reflectance factor/radiance | array (2, 6) |
| 10 | Band Center wavenumbers | Band Center wavenumbers | array (10) |
| 11 | Radiance to Brightness Temperature conversion coeffs | Plank Coefficients | array (2, 10) |
| 12 | Reflectance Factor from Radiance Coefficients | Coefficients to convert from radiances to reflectance factor for reflective bands | array (jsize) |
| 13 | Quality Flags (by band) | Quality Flags by band per swath | array (numofswaths, 16) |
| 14 | Sat. id | Satellite ID | array (1) |
| 15 | Earth-Sun Distance | Earth-Sun Distance | array (1) |
| 16 | Image Center point | Latitude/Longitude | array (2) |
| 17 | Line array | dimension | array (xsizeh) array (xsize1) array (xsize2) |
| 18 | Element array | dimension | array (ysizeh) array (ysize1) array (ysize2) |
| 19 | Down-scaling method | Sampling or average | array (1) |

Table 7. Fields in CMIP multi-band imagery products (the band center frequency information is the area under the curve weighted value and could be stored in a header)

The output also includes metadata (min, max, standard deviation, processing day/time stamp, etc.) and geolocation information (TBV). Metadata examples might be the actual satellite sub-point, or the scaling methods and corresponding coefficients that are used to generate “n”-bit BV. It is assumed that “n” will be 8 at current stage. Users can use these scaling coefficients to convert BV back to TOA reflectance or BT.  Another example of needed metadata is the angles describing the earth/sun/satellite geometry.

Latitude and Longitude information for each pixel would not have to be stored if enough information is stored to describe the location of the data. For example, current AWIPS NetCDF do not store the latitude/longitude information, given the data is first remapped to a known projection/location. Once more information is known about the ABI fixed grid format details, that coordinate system could be employed.

# 4	TEST DATA SETS AND OUTPUTS

## 4.1	GOES-R Simulated Input Data Sets

Simulated GOES-R ABI data has been used in the pre-launch phase to develop, test, and validate the ABI CMIP products. The data is derived from use of a radiative transfer model, where the atmospheric and earth surface representations are provided by a high resolution numerical weather prediction forecast model. The GOES-R Algorithm Working Group Proxy Data Team is responsible for the generation of the proxy and simulated instrument data sets.

Much work has been done to generate high-quality simulated ABI images based on output from the high resolution Weather Research and Forecasting (WRF) numerical model. The forward radiative transfer models used to transform from model (environmental parameter) space to measurement (radiances and BTs) space cover from the visible, to the IR spectral regions (Otkin and Greenwald 2008). High quality forward model simulations have been made of each of the ABI 16 bands.

The GOES-R AWG Proxy Data team has created several ABI simulations. This section details the work on a CONUS simulation which mimics one of the proposed scan segments on the future ABI (Otkin et. al 2007). Two flexible scanning scenarios are currently under review for the ABI.  The first mode allows the ABI to scan the full disk (FD) every 15 minutes, 3 CONUS scenes, and scan a 1000 km x 1000 km selectable area every 30 seconds. A second mode would program the ABI to scan the FD every 5 minutes (Schmit et al. 2005).

The synthetic GOES-R ABI imagery begins as a high resolution Weather Research and Forecasting (WRF) model simulation. The CONUS simulation was performed at the National Center for Supercomputing Applications (NCSA) at the University of Illinois at Urbana-Champaign by the GOES-R AWG proxy data team. Simulated atmospheric fields were generated using version 2.2 of the WRF model (ARW core). The simulation was initialized at 23:55 UTC on 04 June 2005 with 1° GFS data and then run for 30 hours using a triple-nested domain configuration. The outermost domain covers the entire GOES-R viewing area with a 6-km horizontal resolution while the inner domains cover the CONUS and mesoscale regions with 2-km and 0.667-km horizontal resolution, respectively.

WRF model output, including the surface skin temperature, atmospheric temperature, water vapor mixing ratio, and the mixing ratio and effective particle diameters for each hydrometeor species, were ingested into the Successive Order of Interaction (SOI) forward radiative transfer model in order to generate simulated top of atmosphere (TOA) radiances. Gas optical depths were calculated for each ABI infrared band using the Community Radiative Transfer Model (CRTM). Ice cloud absorption and scattering properties were obtained from Baum et al. (2005), whereas the liquid cloud properties were based on Lorenz-Mie calculations.

Figures 3-7 show an example of simulated ABI imagery images over the CONUS. The simulated data captures the general features and locations well. Some differences can be observed in the cloud structures.

Figure 3a ABI Band 2 stored as a McIDAS AREA displayed in McIDAS-X

Figure 3b. ABI Band 14 stored as a McIDAS AREA displayed in McIDAS-X

Figure 4. ABI Band 1 stored as a NetCDF displayed in McIDAS-V

Figure 5. ABI Band 7 stored as a NetCDF displayed in McIDAS-V

Figure 6. ABI Bands 1-6 converted to an AWIPS-ready NetCDF and displayed in AWIPS

Figure 7. ABI Bands 9-16 converted to an AWIPS-ready NetCDF and displayed in AWIPS

## 4.2	Output from Simulated ABI Data Sets

### 4.2.1		Imagery Generated from Simulated ABI Data

The Imagery products have been generated from the CONUS simulated ABI data at 23:55 UTC on 04 June, 2005. Figures 9 and 10 show examples of reflectance and brightness values products generated from simulated ABI band 1 data over the CONUS. Figures 8-12 show the examples of radiance, brightness temperature and brightness values products generated from simulated ABI band 7 data over the CONUS.

Figure 8. Reflectance of ABI Band 1 at 22:00 UTC on 05 June 2005 displayed in McIDAS

Figure 9. Brightness Values of ABI Band 1 at 22:00 UTC on 04 June 2005 displayed in McIDAS

Figure 10. Radiance of ABI Band 7 at 22:00 UTC on 04 June 2005 displayed in McIDAS

Figure 11. Brightness Temperature of ABI Band 7 at 22:00 UTC on 04 June 2005 displayed in McIDAS

Figure 12. Brightness Value derived from simulated ABI Band 7 data at 22:00 UTC on 04 June 2005 displayed in McIDAS

Sample netCDF structure for the simulated ABI data is envisioned as follows for a visible and infrared bands. Note that these will be revised based on now scaling the ABI bands 1-6 with radiance and updated into the ABI fixed grid format.

netcdf GRB_scaled_1km_conus_sim_abi_band02_2005_0604_2200utc {

dimensions:

west-east = 5304 ;

south_north = 2438 ;

time = 1 ;

e_sun = 1 ;

variables:

float lat(south_north, west-east) ;

lat:long_name = "Latitude" ;

lat:units = "degrees_north" ;

lat:valid_range = -90.f, 90.f ;

lat:_FillValue = -999.f ;

float lon(south_north, west-east) ;

lon:long_name = "Longitude" ;

lon:units = "degrees_east" ;

lon:valid_range = -180.f, 180.f ;

lon:_FillValue = -999.f ;

short ABI_scaledint_02(time, south_north, west-east) ;

ABI_scaledint_02:long_name = "Reflectance band 2 (0.64um)" ;

ABI_scaledint_02:units = "None" ;

ABI_scaledint_02:add_offset = -0.0502931f ;

ABI_scaledint_02:coordinates = "lat lon" ;

ABI_scaledint_02:scale_factor = 0.0002931f ;

ABI_scaledint_02:valid_min = 1s ;

ABI_scaledint_02:_FillValue = 0s ;

ABI_scaledint_02:missing_value = 0s ;

float time(time) ;

time:long_name = "Image start time" ;

time:units = "seconds since 2005-06-04 22:00" ;

float E_sun(e_sun) ;

E_sun:long_name = "E_SUN" ;

E_sun:units = " W/(m^2 micrometer)" ;

// global attributes:

:TITLE = "NCSA-FCM 2-KM CONUS ABI VISIBLE DATA REMAPPED TO GOES-R 2-KM DOMAIN" ;

:INSTITUTE = "UNIVERSITY OF WISCONSIN-MADISON SSEC/CIMSS" ;

:HISTORY = "The model was simulated on a supercomputer at the National Center for Supercomputing  Applications. The CIMSS forward radiative transfer modeling system was then used to compute simulated radiances for each ABI band" ;

:SOURCE = "Simulated ABI scaled integer data  for this dataset  were computed using output from a high-resolution Weather Research and Forecasting model coupled with the CIMSS forward radiative transfer models" ;

:REFERENCE = "Otkin, J. A., T. J. Greenwald, J. Sieglaff, and H.-L. Huang, 2009: Validation of a large-scale simulated brightness temperature dataset using SEVIRI satellite observations. [accepted for publication in/ J. Appl. Meteor. Climatol/.]" ;

:SOLAR_CONSTANT = "2000 ASTM Standard Extraterrestrial Spectrum Reference E-490-00 for a solar constant of 1366.1 W/m**2" ;

:pi = "3.14159265" ;

:Reflectance_factor = "(ABI_scaledint* scale_factor) + add_offset" ;

:Radiance = "(Reflectance_factor * E_sun ) / pi" ;

:Conventions = "CF-1.4" ;

:REMAP_AUTHOR = "JASON OTKIN" ;

:GRB_SCALED_AUTHOR = "KABA BAH" ;

:PROCESSED_DATE = "Wed Jul  8 19:18:24 2009" ;

:FM_CVS_VERSION = "Release_Sep08_A" ;

:NWP_MODEL = "OUTPUT FROM WRF V2.2 MODEL" ;

:CEN_LAT = 37.34798f ;

:CEN_LON = -96.5871f ;

:OUTPUT_TIME = "2005-06-04_22:40:00" ;

:WRF_MAP_PROJ = "Mercator" ;

:dyKm = 2.f ;

:dxKm = 2.f ;

:rotation = 0.f ;

:xMin = -0.1179891f ;

:xMax = 0.1966484f ;

:yMin = -0.8768772f ;

:yMax = -0.5622401f ;

netcdf GRB_scaled_2km_conus_sim_abi_band14_2005_0604_2200utc {

dimensions:

west-east = 2652 ;

south_north = 1219 ;

time = 1 ;

e_sun = 1 ;

variables:

float lat(south_north, west-east) ;

lat:long_name = "Latitude" ;

lat:units = "degrees_north" ;

lat:valid_range = -90.f, 90.f ;

lat:_FillValue = -999.f ;

float lon(south_north, west-east) ;

lon:long_name = "Longitude" ;

lon:units = "degrees_east" ;

lon:valid_range = -180.f, 180.f ;

lon:_FillValue = -999.f ;

short ABI_TBB_14(time, south_north, west-east) ;

ABI_TBB_14:long_name = "ABI brightness temperatures band 14 (11.2um)" ;

ABI_TBB_14:units = "K" ;

ABI_TBB_14:add_offset = -0.8622603f ;

ABI_TBB_14:coordinates = "lat lon" ;

ABI_TBB_14:scale_factor = 0.01f ;

ABI_TBB_14:valid_min = 0s ;

ABI_TBB_14:_FillValue = -32768s ;

ABI_TBB_14:missing_value = -32768s ;

short ABI_scaledint_14(time, south_north, west-east) ;

ABI_scaledint_14:long_name = "ABI radiance band 14 (11.2um)" ;

ABI_scaledint_14:units = "milliwatts/m2/steradian/cm-1" ;

ABI_scaledint_14:add_offset = -0.8622603f ;

ABI_scaledint_14:coordinates = "lat lon" ;

ABI_scaledint_14:scale_factor = 0.0122604f ;

ABI_scaledint_14:valid_min = 1s ;

ABI_scaledint_14:_FillValue = 0s ;

ABI_scaledint_14:missing_value = 0s ;

float time(time) ;

time:long_name = "Image start time" ;

time:units = "seconds since 2005-06-04 22:00" ;

// global attributes:

:TITLE = "NCSA-FCM 2-KM CONUS ABI VISIBLE DATA REMAPPED TO GOES-R 2-KM DOMAIN" ;

:INSTITUTE = "UNIVERSITY OF WISCONSIN-MADISON SSEC/CIMSS" ;

:HISTORY = "The model was simulated on a supercomputer at the National Center for Supercomputing  Applications. The CIMSS forward radiative transfer modeling system was then used to compute  simulated radiances for each ABI band" ;

:SOURCE = "Simulated ABI scaled integer data  for this dataset  were computed using output from a high-resolution Weather Research and Forecasting model coupled with the CIMSS forward radiative transfer models" ;

:REFERENCE = "Otkin, J. A., T. J. Greenwald, J. Sieglaff, and H.-L. Huang, 2009: Validation of a large-scale simulated brightness temperature dataset using SEVIRI satellite observations. [accepted for publication in/ J. Appl. Meteor. Climatol/.]" ;

:Conventions = "CF-1.4" ;

:REMAP_AUTHOR = "JASON OTKIN" ;

:GRB_SCALED_AUTHOR = "KABA BAH" ;

:PROCESSED_DATE = "Wed Jul  8 19:25:01 2009" ;

:FM_CVS_VERSION = "Release_Sep08_A" ;

:NWP_MODEL = "OUTPUT FROM WRF V2.2 MODEL" ;

:CEN_LAT = 37.34798f ;

:CEN_LON = -96.5871f ;

:OUTPUT_TIME = "2005-06-04_22:40:00" ;

:WRF_MAP_PROJ = "Mercator" ;

:dyKm = 2.f ;

:dxKm = 2.f ;

:rotation = 0.f ;

:xMin = -0.1179891f ;

:xMax = 0.1966484f ;

:yMin = -0.8768772f ;

:yMax = -0.5622401f ;

}

Two other ABI simulated datasets are also being used as part of the imagery validations.

Figure 13. ABI band 4 (1.38 um) simulation of hurricane Katrina at 22 UTC on August 28, 2005.

Figure 14. ABI band 15 (12.3 um) simulation of the Pacific at 137 West longitude at 20 UTC on June 26, 2008.

Figure 15. ABI band Fixed Grid Format (FGF) coverage sample from 75W. The point is that latitudes and longitude would not have to be carried, given the grid format.

Using the FGF will reduce the file size (by not needing to carry a latitude/longitude value for each pixel) and should also improve the performance of any remapping functions.

### 4.2.2		Precisions and Accuracy Estimation

This section describes the predicted performance and product quality of the CMIP relative to the CMIP specifications found within the GOES-R Functional and Performance Specification Document (F&PS). To estimate the precision and accuracy of the Imagery product requires validation files generated by the research code running offline. The reference (“truth”) data files include reflectance, radiance, brightness values and geolocation information for bands 1-6, and radiance, brightness temperature, brightness values and geolocation information for bands 7-16.

The accuracy and precision estimates for the Imagery products are determined by computing the following values: mean difference, max difference and standard deviation of difference of reflectance, radiance, brightness values for bands 1-6 and radiance, brightness temperature and brightness values for bands 7-16. The comparison results are summarized in the Table 8, in which s is the value generated by the software and t is the reference (“true”) data.

|  | Reflectance | Radiance | Brightness Value |
| --- | --- | --- | --- |
|  | mean(s – t) | stdev(s – t) | max(¦s - t¦) | mean(s – t) | stdev(s – t) | max(¦s - t¦) | mean(s – t) | stdev(s – t) | max(¦s - t¦) |
| 01 | -1.80270e-09 | 8.77219e-09 | 5.96046e-08 | -8.23024e-06 | 1.14099e-05 | 9.15527e-05 | 1.93469e-05 | 0.00439843 | 1.00000 |
| 02 | 5.43765e-10 | 9.10306e-09 | 5.96046e-08 | -4.51243e-06 | 7.01644e-06 | 6.10352e-05 | 0.00000 | 0.00000 | 0.00000 |
| 03 | -3.63924e-09 | 1.04284e-08 | 5.96046e-08 | -5.55586e-06 | 6.18800e-06 | 4.57764e-05 | 0.00434283 | 1.88608e-05 | 1.00000 |
| 04 | 6.02707e-10 | 1.39890e-09 | 2.98023e-08 | 1.53219e-08 | 2.71043e-07 | 7.62939e-06 | 0.00000 | 0.00000 | 0.00000 |
| 05 | 6.95558e-09 | -8.69477e-10 | 5.96046e-08 | 1.03450e-06 | -6.73960e-07 | 1.14441e-05 | 0.00000 | 0.00000 | 0.00000 |
| 06 | -4.82609e-10 | 5.72237e-09 | 2.98023e-08 | -1.45095e-07 | 2.36706e-07 | 1.90735e-06 | 0.00000 | 0.00000 | 0.00000 |
|  | Radiance | Brightness Temperature | Brightness Value |
|  | mean(s – t) | stdev(s – t) | max(¦s - t¦) | mean(s – t) | stdev(s – t) | max(¦s - t¦) | mean(s – t) | stdev(s – t) | max(¦s - t¦) |
| 07 | 8.07578e-09 | 2.31943e-08 | 1.19209e-07 | 7.14495e-06 | 1.57137e-05 | 6.10352e-05 | 0.00000 | 0.00000 | 0.00000 |
| 08 | -3.38373e-07 | 1.27241e-07 | 5.96046e-07 | -7.39373e-07 | 1.18933e-05 | 6.10352e-05 | 0.0000 | 0.0000 | 0.0000 |
| 09 | -4.15323e-07 | 3.61135e-07 | 9.53674e-07 | 4.15826e-06 | 1.04421e-05 | 3.05176e-05 | 0.00000 | 0.00000 | 0.00000 |
| 10 | -5.85536e-09 | 7.67321e-07 | 1.90735e-06 | 6.83676e-06 | 1.29271e-05 | 6.10352e-05 | 0.00000 | 0.00000 | 0.00000 |
| 11 | -5.51336e-07 | 2.43044e-06 | 7.62939e-06 | -7.01631e-06 | 1.64498e-05 | 6.10352e-05 | 0.00000 | 0.00000 | 0.00000 |
| 12 | -2.97309e-07 | 2.42303e-06 | 3.81470e-06 | -5.58301e-06 | 1.43563e-05 | 6.10352e-05 | 0.00000 | 0.00000 | 0.00000 |
| 13 | 2.34330e-06 | 3.65624e-06 | 1.52588e-05 | 2.67977e-06 | 1.58865e-05 | 6.10352e-05 | 0.00000 | 0.00000 | 0.00000 |
| 14 | 1.27602e-06 | 2.86722e-06 | 1.52588e-05 | 4.47034e-06 | 1.55042e-05 | 6.10352e-05 | 0.00000 | 0.00000 | 0.00000 |
| 15 | -1.57553e-06 | 3.15149e-06 | 1.52588e-05 | -5.84233e-06 | 1.57901e-05 | 6.10352e-05 | 0.00000 | 0.00000 | 0.00000 |
| 16 | 5.44584e-06 | 3.28566e-06 | 7.62939e-06 | 4.06769e-06 | 1.72088e-05 | 6.10352e-05 | 0.00037225 | 0.0192876 | 1.00000 |

Table 8. Comparison results of generated Imagery products and validation data serving as GOES-R ABI proxy data for the GOES-R CMIP. This is for data from the June 2005 case.

### 4.2.3		Error Budget

This section will be removed.

# 5	PRACTICAL CONSIDERATIONS

## 5.1	Numerical Computation Considerations

Handling of the large ABI image datasets is one of the major challenges to the CMIP. There will be a 4 to 16-fold data increase for the ABI compared with the current GOES imager in individual channels. The 0.5 km visible band has a data volume larger than all ten of the IR bands combined. Moreover, for the full disk scans, the temporal resolution will be improved to 5 minutes, compared to 25 minutes for current GOES instruments.

The system shall design and implement appropriate algorithm(s) to address issues related to handling the large dimension and volume of data from the ABI. The related issues include, but are not limited to:

- Memory limitation versus large image dimension

- Fulfill the product latency requirements

The ‘stepped-edge’ approach of the ABI FD scan certainly improves the efficiency of this operation. At the same time, it complicates the image generation step, given that ‘swaths’ can be varying width. The “corners” of the stepped-earth edge image should be considered to allow for easy user amalgamation of swath data. One solution may be to ‘null fill’ the ‘corners’ to form a rectangular data array.

Figure 16. The ‘stepped-edge’ approach of the ABI FD scan

## 5.2	Programming and Procedural Considerations

Striping or banding is systematic noise in an image that results from variation in the response of the individual detectors used for a particular band. This usually happens when a detector goes out of adjustment and produces readings that are consistently much higher or lower than the other detectors for the same band.

Many methods have been developed to correct for striping, such as histogram matching, the empirical distribution function (EDF) matching (Weinreb et al. 1989), and the moment matching (Gurka and Dittberner 2001). Appropriate methods should be developed or to address the potential striping issue.

Due to the nature of the ABI data being remapped prior to distribution, any needed de-striping will need to be conducted before data distribution.

## 5.3	Quality Assessment and Diagnostics

To be completed. This section describes how the quality of the output products is assessed, documented, and any anomalies diagnosed. In general, any quality control information that is included in the GRB will be passed on. This includes information related to the calibration and navigation attributes.

## 5.4	Exception Handling

The CMIP includes checking the validity of each band before applying radiometric calibration procedures. The CMIP also expects the Level 1b processing to flag any pixels with missing geolocation information.

Exception handling is required for the development of robust and efficient numerical software. Requirements set forth by the AIT also stress the importance of exception handling. While the main modules of the CMIP program  are using the AIT-provided subroutine for error messaging, its use is limited. More extensive error checking will be added to future versions of the CMIP.

For the most part, the CMIP assumes that all necessary image and ancillary data are available through the processing framework. The only data that the algorithm explicitly checks for is the temporal brightness temperature data, which is necessary for the tracking portion of the algorithm. If the temporal data is unavailable, the algorithm outputs an error message and control is returned to the processing framework.

## 5.5	Algorithm Validation

Validation of the Imagery products requires comparing to reference (“truth”) data  for the CONUS and other scan sectors. From these validation data, comparison metrics can be calculated that characterize the agreement between the satellite-derived CMIP and the reference values.

During the pre-launch phase of the GOES-R program, the product validation activities are aimed at characterizing the performance and uncertainties of the CMIP products resulting from parameterizations and algorithmic implementation artifacts. During this phase, there is total reliance on the use of GOES-R ABI simulated dataset as described in Section 4.1. Post-launch validation will apply lessons learned to inter-comparisons of actual CMIP products generated from real ABI measurements and reference (“ground-truth”) wind observations. Validation methodologies and tools developed and tested during the pre-launch phase will be automated and applied. More specific details on CMIP product validation activities can be found in the Product Validation Document for the CMIP product.

# 6	ASSUMPTIONS AND LIMITATIONS

This section describes the current assumptions and limitations in the current version of the CMIP.

## 6.1	Assumed Sensor Performance

We assume the sensor will meet its current specifications. However, the CMIP will be dependent on the following instrumental characteristics. In addition, it is assumed that the supplied SRF will be the relative response and provided in historically consistent units (cm-1).

- Any needed information to ‘combine’ ABI swaths will be supplied.

- The quality of the CMIP will depend on the amount of striping in the data.

- The quality of the CMIP will depend on the overall quality of the data.  This includes (but is not limited to), the cross-talk, the modulation transfer function (MTF), the signal-to-noise ratio (SNR), similarity of detector responses, etc.

- GRB will include Quality indicators with respect to calibration and navigation.

- Only one SRF per band per instrument

- The minimum and maximum radiance value for the GRB scaling does not need to change from instrument to instrument.

- GRB will include various version numbers (say of the Planck coefficients, instrument number, SRF version, etc.)

- Errors in navigation from input GRB data stream will affect the quality of CMIP.

- Unknown spectral shifts in some bands will affect the quality of CMIP.

- A zero (GRB) count is a ‘missing’ value. Data counts begin with one.

- That there will be ‘space’ data around the edge of full disk sectors. Calculations imply that will be at least 70 km of the atmosphere on the edge of full disk scans.

- That ‘system-level’ tests will be conducted to test the algorithm sensitivity on any satellite transmission-induced noise.

- Negative radiances will be mapped to a 0 K brightness temperature.

## 6.2	Pre-Planned Product Improvements

### 6.2.2 Quality Control Indicators

The relevant quality control flags, obtained from the GRB signal, will be passed along.

# 7	REFERENCES

Acharya, T., and A. K. Ray. 2005. Image processing: principles and applications: Wiley-Interscience.

Baum, Bryan , P. Yang,  Yang, Ping; Heymsfield, Andrew J.; Platnick, Steven; King,

Cao and Heidinger 2002, Proceedings of SPIE (http://www.star.nesdis.noaa.gov/smcd/spb/calibration/icvs/documents/Cao_2002SPIE.pdf).

Clarke, J., 2010: GOES-R ABI LEVEL 1B SOLAR CHANNEL DATA DISTRIBUTION STUDY: Analysis of alternatives for utilization of Radiance and Reflectance Factor Instrument Data.

Michael D.; Hu, Y.-X., and Bedka, Sarah T., 2005: Bulk scattering properties for the remote sensing of ice clouds, part II: Narrowband models. Journal of Applied Meteorology, Volume 44, Issue 12, pp.1896-1911.

Gurka, J. J., and G. J. Dittberner. 2001. The next generation GOES instruments: Status and potential impact. Paper read at Fifth Symp. on Integrated Observing Systems, at Albuquerque, NM.

Hillger, D. W., and T. Schmit. 2004. Quantization noise for GOES-R ABI bands. Paper read at Proceedings of the 13th Conference on Satellite Meteorology and Oceanography, Sep., 2004, at Norfolk, VA.

NOAA/NASA. 2008. GOES-R Ground Segment (GS) Functional and Performance Specification (F&PS): GOES-R/Code 417.

NOAA/NESDIS. 2007. GOES-R Series Mission Requirements Document (MRD, version 3.1): GOES-R Program/Code 417.

Otkin, J. A., D. J. Posselt, E. R. Olson, H.-L. Huang, J. E. Davies, J. Li, and C. S. Velden, 2007:  Mesoscale numerical weather prediction models used in support of infrared hyperspectral measurements simulation and product algorithm development.  J. Atmospheric and Oceanic Tech., 24, 585-601.

Otkin, J. A., and T. J. Greenwald. 2008. Comparison of WRF model-simulated and MODIS-derived cloud data. Mon. Wea. Rev. 136:1957-1970.

Russ, J. C. 2002. The Image Processing Handbook, Fourth Edition CRC Press.

Schmit, T. J., M. M. Gunshor, W. P. Menzel, J. Li, S. Bachmeier, and J. J. Gurka. 2005. Introducing the next-generation Advanced Baseline Imager (ABI) on GOES-R. Bull. Amer. Meteor. Soc. 8:1079-1096.

Schmit, T. J., M. P. Weinreb, and W. P. Menzel. 1991. GVAR IR scale factor coefficients: NOAA.

Weinreb, M. P., M. Jamison, N. Fulton, Y. Chen, J. X. Johnson, J. Bremer, C. Smith, and J. Baucom. 1997. Operational calibration of Geostationary Operational Environmental Satellite-8 and -9 imagers and sounders. Appl. Opt. 36:6895-6904.

Weinreb, M. P., J. X. Johnson, J. H. Lienesch, and D. S. Crosby. 1989. Destriping GOES images by matching empirical distribution functions. Rem. Sens. Environ 29 (185-195).

# ACKNOWLEDGEMENTS

The entire Imagery and Visualization team is thanked for their input to these critical products. This includes: Mat Gunshor, Kaba Bah and Tom Rink of CIMSS and Walter Wolf of NOAA/NESDIS. Will Straka is thanked as well. Many members of the GOES-R Calibration Working Group (CWG) also provided much needed information, especially thanked are Mike Weinreb and Frank Padula. Also thanked for a review of the document are Steve Miller and Don Hillger. Steve Wanzong, CIMSS, is thanked for the McIDAS-X images, while Kaba Bah, CIMSS, is thanked for the McIDAS-V images.