## Slide 1
The Advanced Baseline Imager (ABI) on the GOES-R series
  Timothy J. Schmit (tim.j.schmit@noaa.gov)
NOAA/NESDIS/Satellite Applications and Research
Advanced Satellite Products Branch (ASPB)
Kaba Bah, Mathew M. Gunshor, Jun Li, Scott Bachmeier, Jason Otkin, etc.
CIMSS, Madison, WI
Steve Goodman, James J. Gurka, etc.
GOES-R Program Office
UW-Madison
National Weather Association
Birmingham, AL
20 October 2011

## Slide 2: Also Thanks to…
Renkevens, Tom; Achtor, Tom; Ackerman, Steve; Antonelli, Paolo; Aune, Bob; Baggett, Kevin; Baum, Bryan; Ellrod, Gary; Feltz, Joleen; Feltz, Wayne; Frey, Rich; Griffin, Michael K.; Gumley, Liam; Heymann, Roger; Hillger, Don; Huang, Allen; Key, Jeff; Knuteson, Bob; Mecikalski, John; Menzel, Paul; Moeller, Chris; Mosher, Fred; Nelson, James; Nasiri, Shaima; Olander, Tim; Plokhenko, Youri; Prins, Elaine; Rabin, Bob; Revercomb, Hank; Schmidt, Chris; Schreiner, Tony; Seemann-Wetzel, Suzanne; Sieglaff, Justin; Strabala, Kathy; Sun, Fengying; Will Straka, Tobin, Dave; Velden, Chris; Wade, Gary; Whittaker, Tom; Woolf, Hal, Jason Otkin, etc.
Jaime Daniels, Mitch Goldberg, AWG co-chairs, AWG Leads, Walter Wolf, GPO, Jordan Gerth, Chian-Yi Liu, Thomas Greenwald, Monica Coakley, GOES-R flight/ground, Bill Smith, ASPB, PG, SSEC data center, CWG, etc.
NASA, ITT Industries, Lockheed-Martin, other industry partners, etc.

## Slide 3: GOES-R Overview
Advanced Baseline Imager (ABI)
No dedicated Sounder
Geostationary Lightning Mapper (GLM)
Space Weather
  Space Environmental In-Situ Suite (SEISS)
  Solar Ultra Violet Imager (SUVI)
  Extreme Ultra Violet/X-Ray Irradiance Sensor (EXIS)
  Magnetometer
Communications
  GOES Rebroadcast (GRB)
  High Rate Information Transmissions (HRIT)
  Emergency Managers Weather Information Network (EMWIN)
  Search and Rescue (SAR)
  Data Collection System (DCS)
Notes:   Advanced Baseline Imager (ABI) Earth-viewing
  Geostationary Lightning Mapper (GLM) Earth-viewing
  Solar Ultra-Violet Imager (SUVI) Sun-viewing
  EUVS and XRS Irradiance Sensors (EXIS) Sun-viewing
  Space Environment In-Situ Suite (SEISS) Space-viewing
  Magnetometer (MAG) Space-viewing

## Slide 4: Overview
ABI (Advanced Baseline Imager)
  Temporal
  Spatial
  Spectral
  Imagery
Select Products
Summary
  More information
See Poster 4.18: GOES-R Sectorized Cloud and Moisture Imagery Products
GOES-R Spacecraft
Lockheed Martin

## Slide 5: The Advanced Baseline Imager:
ABI Current
Spectral Coverage
16 bands 5 bands
Spatial resolution
0.64 mm Visible 0.5 km Approx. 1 km
Other Visible/near-IR 1.0 km n/a
Bands (>2 mm) 2 km Approx. 4 km
Spatial coverage
Full disk 4 per hour Scheduled (3 hrly)
CONUS 12 per hour ~4 per hour
Mesoscale Every 30 sec n/a
Visible (reflective bands)
On-orbit calibration Yes No

## Slide 6
There are two anticipated scan modes for the ABI:
- Full disk images every 15 minutes + 5 min CONUS images + mesoscale.
or - Full disk every 5 minutes.
ABI scans about 5 times faster
than the current GOES imager

## Slide 7
ABI can offer Continental US images every 5 minutes for routine monitoring of a wide range of events (storms, dust, clouds, fires, winds, etc).
This is every 15 or 30 minutes with the current GOES in routine mode.
Notes: Approx. size of CONUS

## Slide 8
Notes: Approx. size of CONUS

## Slide 9
Mesoscale images every 30 seconds for rapidly changing phenomena
(thunderstorms, hurricanes, fires, etc). Or two regions every 60 seconds.
Notes: Approx. size of meso-scale showing “Franklin”.

## Slide 10
Current GOES Imager scan coverage within 15 minutes
GOES-R ABI scan coverage within 15 minutes
CIMSS
In 15 Minutes ABI (“Flex Mode”) will scan:
1 Full Disk Image
3 CONUS Images
30 Mesoscale Images
In 15 Minutes Current GOES Imager can scan:
3/5th of a Full Disk Image
Notes: From Jun Li and Chian-Yi Liu (CIMSS). Water vapor Image. Data from AWG Proxy Teams.

## Slide 11: GOES-14: Sample “5-min” imagery
“Water vapor” data from the GOES-14 NOAA Science Test, lead by Hillger and Schmit
GOES-12
GOES-14
Notes: Note the comma head is forming in the dry slot as a vort max swings around. This is not obvious from the 15 min.

## Slide 12: GOES-14: Sample “1-min” imagery
Visible data from the GOES-14 NOAA Science Test, lead by Hillger and Schmit
GOES-12
GOES-14
Notes: Note the number of different levels of motion you can see (the cyclonic low level circulation over the ocean through the breaks in the higher clouds)... and you can't distinguish those on the GOES-12 loop.

## Slide 13: GOES-10: Experimental 1-min data
Experimental 1-minute GOES-10 visible data provided a rapid assessment of the current state of the atmosphere over western Tennessee, and indicated that although there was some development of the cumulus clouds, the apparent TCUs did not appear to favor continued development. Hence, the odds of strong convection developing over that area would be lower during the next several hours.
Notes: ftp://satepsanone.nesdis.noaa.gov/volcano/GOES10/g10_spie_125898_0_art_1_jzbn7k_with_copyright.pdf
Schmit, T. J., R. M. Rabin, A. S. Bachmeier, J. Li, M. M. Gunshor, H. Steigerwaldt, A. J. Schreiner, R. M. Aune, and G. S. Wade, 2009: Many uses of the geostationary operational environmental satellite-10 sounder and imager during a high inclination state (2.6Mb PDF), Journal of Applied Remote Sensing, Vol. 3, 033514.

## Slide 14
“GOES” from AVHRR

## Slide 15
“ABI” from AVHRR

## Slide 16
“GOES-13 Visible Loop”

## Slide 17: ABI Visible/Near-IR Bands
Schmit et al, 2005
Notes: Schmit, T. J., M. M. Gunshor, W. P. Menzel, J. J. Gurka, J. Li, and A. S. Bachmeier, 2005: Introducing the next-generation Advanced Baseline Imager on GOES-R. Bull. Amer. Meteor. Soc., 86, 1079-1096.

## Slide 18: ABI IR Bands
Schmit et al, 2005
Notes: Schmit, T. J., M. M. Gunshor, W. P. Menzel, J. J. Gurka, J. Li, and A. S. Bachmeier, 2005: Introducing the next-generation Advanced Baseline Imager on GOES-R. Bull. Amer. Meteor. Soc., 86, 1079-1096.

## Slide 19
The ABI visible and near-IR bands have many uses.
Aerosols, Insolation
Clouds, Snow
Vegetation, Imagery
Cloud mask, Suspended matter
Cloud Particle size
Snow, Phase
Visible and near-IR channels on the ABI
Sample use only, many other uses
Notes: Schmit, T. J., M. M. Gunshor, W. P. Menzel, J. J. Gurka, J. Li, and A. S. Bachmeier, 2005: Introducing the next-generation Advanced Baseline Imager on GOES-R. Bull. Amer. Meteor. Soc., 86, 1079-1096.

## Slide 20
ABI has many more bands than the current operational GOES imagers.
The IR channels on the ABI
Clouds, Stability Indices
Rainfall, Aerosol
SST, Fires
Hurricane, Imagery
Cloud Phase, SST
Ozone, Downward Radiation
SO2, WV
Winds, WV profiling
TPW, Rainfall rate
Fires, Fog
Sample use only, many other uses
Notes: Schmit, T. J., M. M. Gunshor, W. P. Menzel, J. J. Gurka, J. Li, and A. S. Bachmeier, 2005: Introducing the next-generation Advanced Baseline Imager on GOES-R. Bull. Amer. Meteor. Soc., 86, 1079-1096.

## Slide 21
These NWP model simulations were performed on the 'cobalt' supercomputer at the National Center for Supercomputing Applications at the University of Illinois.
Band 1: Daytime “Blue” band -- aerosols

## Slide 22
Band 2: Daytime “Red” band – clouds, etc.

## Slide 23
Band 3: Daytime “Veggie” band

## Slide 24
Band 4: Daytime “Cirrus” band

## Slide 25
Band 5: Daytime “Snow” band

## Slide 26
Band 6: Daytime “Cloud-top phase” band

## Slide 27
Band 7: Shortwave IR window band - fog, fires, etc.

## Slide 28
Band 8: Upper-level tropospheric water vapor band

## Slide 29
Band 9: Upper/mid-level tropospheric water vapor band

## Slide 30
Band 10: Lower mid-level tropospheric water vapor band

## Slide 31
Band 11: “Cloud-top phase” band

## Slide 32
Band 12: “Ozone” band

## Slide 33
Band 13: “Clean” IR longwave window band

## Slide 34
Band 14: IR longwave window band

## Slide 35
Band 15: “Dirty” IR longwave window band

## Slide 36
Band 16: “CO2” longwave IR band

## Slide 37: Visualization (“true color” as a decision aid”)
“True Color” with “synthetic” green from ABI simulated data (from CIMSS); image from Don Hillger, RAMMB.

## Slide 38: Visualization (“RGB highlights cloud phase”)
“RGB Color” (VIS 0.6, VIS 0.8, and NearIR 1.6 um) with ABI simulated data (from CIMSS); image from William Straka, CIMSS and using the EUMETSAT enhancement.
P4.3 Demonstration of RGB Composite Imagery at NOAA National Centers in Preparation for GOES-R

## Slide 39: Overview
ABI (Advanced Baseline Imager)
  Temporal
  Spatial
  Spectral
  Imagery
Select Products
Summary
  More information
Photo courtesy of ITT Geospatial Systems
See Poster 4.1: ABI Flight Performance Predictions Based on PTM Test Results

## Slide 40
Algorithm Working Group (AWG)
Develop algorithms for the Level 2 products
(Both ‘Baseline’ and ‘Future Capability’ products)
Clouds and Moisture Imagery (KPP)
Clear Sky Mask
Cloud Top Pressure and Height
Cloud Top Phase
Cloud Top Temperature
Cloud Particle Size Distribution
Cloud Optical Path
Temperature and Moisture Profiles
Total Precipitable Water
Stability Parameters (Lifted Index, etc.)
Aerosol Detection
Aerosols Optical Depth
Derived Motion Winds
Hurricane Intensity
Fire/Hot Spot Characterization
Land and Sea Surface Temperature
Volcanic Ash
Rainfall Rate
Snow Cover
Downward Solar Insolation: Surface
Reflected Solar Insolation: TOA
Lightning Detection
Cloud Layer/Heights
Cloud Ice Water Path
Cloud Liquid Water
Cloud Type
Convective Initiation
Turbulence
Low Cloud and Fog
Enhanced “V”/Overshooting Top
Aircraft Icing Threat
SO2 Detections (Volcanoes)
Visibility
Upward Longwave Radiation (TOA)
Downward Longwave Radiation (SFC)
Upward Longwave Radiation (SFC)
Total Ozone
Aerosol Particle Size
Surface Emissivity
Surface Albedo
Vegetation Index
Vegetation Fraction
Flood Standing Water
Rainfall probability and potential
Snow Depth
Ice Cover
Sea & Lake Ice Concentration, Age, Extent, Motion
Ocean Currents, Currents: Offshore
Advanced Baseline Imager (ABI)
GLM

## Slide 41: Imagery
Imagery for nowcasting
  Clouds
  Input for products
  Channel differences
  RGB
  Broadcasters
  General Users
  Etc.
Radiances for NWP
  Clear-sky
  Cloudy-sky
  Validations
  Monitoring
  Etc.

## Slide 42
http://cimss.ssec.wisc.edu/goes_r/proving-ground/nssl_abi/nssl_wrf_goes.html
Simulated ABI band – NSSL WRF

## Slide 43
0.64 m
0.86 m
1.38 m
1.61 m
2.26 m
3.9 m
6.19 m
6.95 m
7.34 m
0.47 m
8.5 m
9.61 m
10.35 m
11.2 m
12.3 m
13.3 m
AWG Proxy ABI Simulations of Hurricane Katrina
NOAA/NESDIS STAR and GOES-R Imagery Team
Notes: As shown in mcidas-v

## Slide 44
Corresponding current Imager bands of Hurricane Katrina
NOAA/NESDIS STAR

## Slide 45: Cloud Phase
45
45
45
45
45
Algorithm Highlights
  An Infrared only algorithm that exploits the rich infared information (7.4, 8.5, 11.2, and 12.3 mm) provided by the ABI
  Algorithm determines the cloud top (layer that the radiometer senses) thermodynamic phase of the highest cloud layer
  Exploits recent improvements in fast clear-sky radiative transfer models and ancillary data (land cover, surface emissivity)
  Makes advanced use of spatial information
Operational Applications
  Prerequisite for other cloud property retrievals (height, temperature)
  Climate prediction
  Aviation forecasting (Aircraft icing)
Water, Supercooled Water, Mixed Phase, Ice
M. Pavolonis
Notes: 45
45
45
45
45
This ABI Cloud Phase Algorithm determines the cloud top (layer that the radiometer senses) thermodynamic phase of the highest cloud layer.
The cloud phase output is a subset of a more detailed cloud classification produced by the GOES-R Cloud Type Algorithm
A unique infrared cloud classification scheme is used to determine the cloud type
ABI channels used: 10, 11, 14, and 15
Effective absorption optical depth ratios (-ratios) are used to determine cloud type (liquid water, supercooled liquid water, mixed phase, opaque ice, semi-transparent ice, and multilayered clouds).
The cloud phase (liquid water, supercooled liquid water, mixed phase, and ice) is determined from the cloud type output (ice = opaque ice, semi-transparent ice, and multilayered clouds).

## Slide 46
IR AMVs derived from WRF model images
using simulated future GOES-R radiances
2 km resolution; 5-minute time step
IR AMVs derived from current GOES-12
4km resolution; 15-minute time step
GOES-R Atmospheric Motion Vectors
Product Example: Hurricane Katrina
Low-mid level vectors- cyan Upper-level vectors - yellow
Courtesy C. Velden: UWisc-CIMSS/NOAA-STAR
Notes: Will provide automated hurricane intensity estimates for tropical cyclone analysts over the GOES-R observation domain using infrared geostationary infrared window (IRW) imagery
Significant Heritage to draw from:
Based on Subjective Dvorak “Enhanced Infrared” (EIR) Technique (SDT) developed in the 1970’s and 1980’s by NOAA/NESDIS scientist Vern Dvorak.
Provides estimated hurricane intensity in oceanic regions where direct aircraft reconnaissance measurements of intensity are not available.
Satellite-based technique that employs image pattern recognition techniques and empirically based rules to derive an estimate of Tropical Cyclone (TC) intensity in “T numbers” which ultimately relate to surface wind speeds.
The increased higher density winds derived from the higher resolution GOES-R ABI allows forecasters to more accurately determine the extent of the eye and gale force winds (upper winds, not ground), and improve the model forecasts of track and intensity. Example compares the winds GOES-R ABI can produce with its 2-km IR spatial resolution and 5-min refresh rate as simulated using the Weather Research and Forecast (WRF) Model compared to the current GOES-R imager with 4-km IR resolution and 15 min or longer refresh rate.
GOES-R improves spatial and temporal resolution thereby increasing the accuracy of storm height assigment. GOES-R will also detect and more define eye helping to more accurately predict forward track.
The higher density winds derived from the GOES-R ABI allows forecasters to more accurately determine the extent of the eye and gale force winds, and will improve the model forecasts of track and intensity.

## Slide 47
GOES-12 and GOES-R ABI
Simulation of Grand Prix Fire/Southern California
GOES-12
GOES-12
GOES-R ABI
GOES-R ABI
J. Feltz
Notes: Here are two different fires. What we can see is a more defined peak in the higher resolution data and it is easier to pick out individual hotspots. In addition, the higher saturation tempearture of the ABI allows us to see that the fire is around 370K.

## Slide 48: Overview
ABI (Advanced Baseline Imager)
  Temporal
  Spatial
  Spectral
  Imagery
Select Products
Summary
  More information
P4.14 GOES-R Products List and Planned Availability

## Slide 49: Approximate spectral and spatial resolutions of US GOES Imagers
~ Band Center (um) | GOES-6/7 | GOES-8/11 | GOES-12/N | GOES-O/P | GOES-R+
0.47 |  |  |  |  | 
0.64 |  |  |  |  | 
0.86 |  |  |  |  | 
1.6 |  |  |  |  | 
1.38 |  |  |  |  | 
2.2 |  |  |  |  | 
3.9 |  |  |  |  | 
6.2 |  |  |  |  | 
6.5/6.7/7 | 14km |  |  |  | 
7.3 |  |  |  |  | 
8.5 |  |  |  |  | 
9.7 |  |  |  |  | 
10.35 |  |  |  |  | 
11.2 |  |  |  |  | 
12.3 |  |  |  |  | 
13.3 |  |  |  |  | 
8
4
2
Visible
Near-IR
Infrared
Box size represents pixel size
“MSI mode”
Notes: 0.40 inches = 4km; 0.80 inches = 8km
MSI is Multi-Spectral Imaging Mode (dashed boxes)
This does not show other improvements: SNR, MTF, bit-depth, navigation, coverage rates, etc.

## Slide 50: Summary
The ABI on GOES-R will improve over the current instrument in many aspects (spectral, spatial, and temporal on orders of 3, 4, and 5, respectively), plus improved image navigation and registration and radiometer performance.
These improvements will greatly assist a host of applications, especially on the regional and meso-scales.
ITT Industries

## Slide 51: Back-up Slides
Google Earth
Select links
Acknowledgements
Products vs bands
GOES-R at 137W scan strategy

## Slide 52: Google Earth
Sample ABI simulated data are available in google earth format:
  http://cimss.ssec.wisc.edu/goes/abi/loops/links.html

## Slide 53
GOES-R:
  http://www.goes-r.gov
  http://www.meted.ucar.edu/index.htm
  http://cimss.ssec.wisc.edu/goes_r/proving-ground.html
GOES and NASA:
  http://goespoes.gsfc.nasa.gov/goes/index.html
  http://goes.gsfc.nasa.gov/text/goes.databookn.html
UW/SSEC/CIMSS/ASPB:
  http://cimss.ssec.wisc.edu/goes_r/proving-ground/nssl_abi/nssl_abi_rt.html
  http://cimss.ssec.wisc.edu/goes_r/awg/proxy/nwp/
  http://cimss.ssec.wisc.edu/goes/abi/
  http://cimss.ssec.wisc.edu/goes/abi/wf
  http://cimss.ssec.wisc.edu/goes/blog/
  http://www.ssec.wisc.edu/data/geo/
More information
AMS BAMS Article on the ABI (Aug. 2005)

## Slide 54: Acknowledgements
The authors would like to thank the entire GOES-R team; within the government, industry and academia.
The views, opinions, and findings contained in this presentation are those of the authors and should not be construed as an official National Oceanic and Atmospheric Administration or U.S. Government position, policy, or decision.

## Slide 55: ABI “Baseline” Products
Wavelength Micrometers | 0.47 | 0.64 | 0.865 | 1.378 | 1.61 | 2.25 | 3.90 | 6.185 | 6.95 | 7.34 | 8.5 | 9.61 | 10.35 | 11.2 | 12.3 | 13.3
Channel ID | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
Baseline Products |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Aerosol Detection | X | X | X | X | X | X | X |  |  |  |  |  |  | X | X | 
Suspended Matter/OD | X | X | X |  | X | X |  |  |  |  |  |  |  |  |  | 
Clear Sky Masks |  | X |  | X | X |  | X |  | X | X | X |  |  | X | X | 
Cloud & Moisture Imagery | X | X | X | X | X | X | X | X | X | X | X | X | X | X | X | X
Cloud Optical Depth |  | X |  |  |  | X | X |  |  |  |  |  |  | X | X | 
Cloud Particle Size |  | X |  |  |  | X | X |  |  |  |  |  |  | X | X | 
Cloud Top Phase |  |  |  |  |  |  |  |  |  | X | X |  |  | X | X | 
Cloud Top Height |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X | X
Cloud Top Pressure |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X | X
Cloud Top Temperature |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X | X
Hurricane Intensity |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  | 
Rainfall Rate/QPE |  |  |  |  |  |  |  | X |  | X | X |  |  | X | X | 
Legacy Vertical Moisture Profile |  |  |  |  |  |  |  | X | X | X | X | X | X | X | X | X
Legacy Vertical Temp Profile |  |  |  |  |  |  |  | X | X | X | X | X | X | X | X | X
Derived Stability Indices |  |  |  |  |  |  |  | X | X | X | X | X | X | X | X | X
Total Precipitable Water |  |  |  |  |  |  |  | X | X | X | X | X | X | X | X | X
Downward Solar Insolation Surf | X | X | X |  | X | X |  |  |  |  |  |  |  |  |  | 
Reflected Solar Insolation TOA | X | X | X |  | X | X |  |  |  |  |  |  |  |  |  | 
Derived Motion Winds |  | X |  |  |  |  | X | X | X | X |  |  |  | X |  | 
Fire Hot Spot Characterization |  | X |  |  |  |  | X |  |  |  |  |  |  | X | X | 
Land Surface Temperature |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X | 
Snow Cover | X | X | X |  | X | X | X |  |  |  |  |  | X |  |  | 
Sea Surface Temps |  |  |  |  |  |  | X |  |  |  | X |  | X | X | X | 
Bands may also be used by needed “upstream” products, such as the cloud mask.

## Slide 56: ABI “Future Capabilities” Products
Wavelength Micrometers | 0.47 | 0.64 | 0.865 | 1.378 | 1.61 | 2.25 | 3.90 | 6.185 | 6.95 | 7.34 | 8.5 | 9.61 | 10.35 | 11.2 | 12.3 | 13.3
Channel ID | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
Option 2 Products |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Cloud Layer/Heights |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X | X
Cloud Ice Water Path |  |  |  |  |  |  | X |  |  |  |  |  |  | X | X | 
Cloud Liquid Water |  | X |  |  |  | X |  |  |  |  | X |  |  |  |  | 
Cloud Type |  |  |  |  |  |  |  |  |  | X | X |  |  | X | X | 
Convective Initiation |  |  |  |  |  |  |  | X | X | X | X | X |  | X | X | X
Turbulence |  |  |  |  |  |  |  | X |  |  |  |  |  |  |  | 
Low Cloud and Fog |  | X |  |  |  |  | X |  |  |  |  |  |  |  |  | 
Enhanced-V/Overshooting Top |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  | 
Aircraft Icing Threat |  | X |  |  |  | X | X |  |  | X | X |  |  | X | X | X
SO2 Detection |  |  |  |  |  |  |  | X |  | X | X |  |  | X | X | 
Visibility (no direct use of ABI bands) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Upward Longwave Radiation (TOA) |  |  |  |  |  |  |  | X |  | X | X |  | X |  |  | X
Downward Longwave Radiation (SFC) |  |  |  |  |  |  |  |  | X | X | X | X | X | X | X | X
Upward Longwave Radiation (SFC) |  |  |  |  |  |  |  |  |  |  | X |  | X | X | X | 
Total Ozone |  |  |  |  |  |  |  | X | X | X |  | X | X | X | X | X
Aerosol Particle Size | X | X | X |  | X | X |  |  |  |  |  |  |  |  |  | 
Surface Emissivity |  |  |  |  |  |  |  | X | X | X | X | X | X | X | X | X
Surface Albedo | X | X | X |  | X | X |  |  |  |  |  |  |  |  |  | 
Vegetation Index |  | X | X |  |  |  |  |  |  |  |  |  |  |  |  | 
Vegetation Green Fraction |  | X | X |  |  |  |  |  |  |  |  |  |  |  |  | 
Flood/Standing Water |  | X | X |  | X |  |  |  |  |  |  |  |  | X | X | 
Rainfall Potential (no direct use of ABI bands) |  |  |  |  |  |  |  | X |  | X | X |  |  | X | X | 
Rainfall Probability (no direct use of ABI bands) |  |  |  |  |  |  |  | X |  | X | X |  |  | X | X | 
Snow Depth (no direct use of ABI bands) | X | X | X |  | X | X | X |  |  |  |  |  | X |  |  | 
Sea & Lake Ice: Age (no direct use of ABI bands) |  | X | X |  | X |  |  |  |  |  |  |  |  | X | X | 
Sea & Lake Ice: Concentration |  | X | X |  | X |  |  |  |  |  |  |  |  | X | X | 
Sea & Lake Ice: Motion |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  | 
Ocean Currents |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  | 
Ocean Currents: Offshore |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  | 

## Slide 57
Current GOES Imager scans: PACUS and CONUS (note that PACUS is one-third larger). These regions are sub-selected for AWIPS.

## Slide 58
Proposed –Shifted “5 min PACUS”
Proposed “shifted” “PACUS” would give a 5 min scan of southern AK and western CONUS. This would mean that Hawaii could be covered with one of the meso-scales (and 15 min FD); if in ‘flex mode (3)’. Note that the positions are approximate.
“5 min PACUS”