## Slide 1
GOES-R ABI
(Advanced Baseline Imager)
  Timothy J. Schmit (tim.j.schmit@noaa.gov)
NOAA/NESDIS/Satellite Applications and Research
Advanced Satellite Products Branch (ASPB)
Madison, WI
UW-Madison
GOES-R Education Proving Ground
Telecom
February 20, 2016

## Slide 2
GOES-R ABI
  Spectral, Spatial and Temporal
  Improved, Improved and Improved
Lockheed Martin
Me!
ABI

## Slide 3
ABI

## Slide 4: 1966: ATS-1 launched
Applications Technology Satellite (ATS)-1 was the first geostationary imager, launched 6 December 1966. Imaging instrument designer and SSEC co-founder, Verner E. Suomi, proclaimed, “the clouds move, not the satellite”.
11 December 1966
Notes: http://cimss.ssec.wisc.edu/news/geo_image_anniversary.html

## Slide 5: A History of GOES “Weather” Satellites
ATS
SMS
Notes: The focus of this Short Course is to describe the advancements with the GOES-R series

## Slide 6
Why GOES-R ?
Visible & IR Imagery
Lightning Mapping
Space Weather Monitoring
Solar Imaging
The GOES-R series will provide significant improvements in the detection and observations of meteorological phenomena that directly impact public safety, protection of property, and our Nation’s economic health and prosperity.
  Improves hurricane track & intensity forecasts
  Increases thunderstorm & tornado warning lead time
  Improves aviation flight route planning
  Data for long-term climate variability studies
  Improved air quality warnings and alerts
  Improves solar flare warnings for communications and navigation disruptions
  More accurate monitoring of energetic particles responsible for radiation hazards to humans and spacecraft
  Better monitoring of Coronal Mass Ejections to improve geomagnetic storm forecasting
6
ABI
GLM
SEISS and MAG
EXIS and SUVI

## Slide 7: NOAA GOES Constellation
Operational
GOES-16 or -17
(137W)
GOES-16 or -17
(75W)
Operational
After GOES-R and -S are launched, checked out and operational!
Notes: Template footer obscured. Fixed.
Estimate during mid-2010.

## Slide 8: The Advanced Baseline Imager:
ABI Current
Spectral Coverage
16 bands 5 bands
Spatial resolution
0.64 mm Visible 0.5 km Approx. 1 km
Other Visible/near-IR 1.0 km n/a
Bands (>2 mm) 2 km Approx. 4 km
Spatial coverage
Full disk 4 per hour Scheduled (3 hrly)
CONUS 12 per hour ~4 per hour
Mesoscale Every 30 sec n/a
Visible (reflective bands)
On-orbit calibration Yes No
Notes: The ABI allows more bands, finer spatial resolution, faster refresh rates and on-orbit calibration of all bands!

## Slide 9: Advanced Baseline Imager (ABI)
5
4
3
X
Faster coverage (5-minute full disk vs. 25-minute)
X
Improved spatial resolution
(2 km IR vs. 4 km)
X
More spectral bands (16 on ABI vs. 5 on the current imager)
ABI on GOES-S
Notes: Slide from J. Gerth, CIMSS.

## Slide 10
ABI Band | Wavelength (µm) | Wavelength range (µm) | Sub-point pixel spacing (km) | Descriptive Name
1 | 0.47 | 0.45 - 0.49 | 1 | “Blue”
2 | 0.64 | 0.60 - 0.68 | 0.5 | “Red”
3 | 0.864 | 0.847 - 0.882 | 1 | “Veggie”
4 | 1.373 | 1.366 - 1.380 | 2 | “Cirrus”
5 | 1.61 | 1.59 - 1.63 | 1 | “Snow/Ice”
6 | 2.24 | 2.22 -2.27 | 2 | “Cloud Particle Size”
ABI: Bands 1-6 (Visible / NearIR)
Six visible or near visible bands on ABI, one on heritage imager
Notes: Based on Schmit et al, 2017. stars = today’s imager band.

## Slide 11
ABI Band | Wavelength (µm) | Wavelength range (µm) | Sub-point pixel spacing (km) | Descriptive Name
7 | 3.90 | 3.80 - 3.99 | 2 | “Shortwave window”
8 | 6.19 | 5.79 - 6.59 | 2 | “Upper-level Water Vapor”
9 | 6.93 | 6.72 - 7.14 | 2 | “Mid-Level Water Vapor”
10 | 7.34 | 7.24 - 7.43 | 2 | “Lower/Mid-level Water Vapor”
11 | 8.44 | 8.23 - 8.66 | 2 | “Cloud-top Phase”
12 | 9.61 | 9.42 - 9.80 | 2 | “Ozone”
13 | 10.33 | 10.18 - 10.48 | 2 | “Clean longwave window”
14 | 11.21 | 10.82 - 11.60 | 2 | “Longwave window”
15 | 12.29 | 11.83 - 12.75 | 2 | “Dirty longwave window”
16 | 13.28 | 12.99 - 13.56 | 2 | “CO2”
ABI: Bands 7-16 (IR)
10 infrared bands on the ABI, four on heritage imager
Notes: Based on Schmit et al, 2017. stars = today’s imager band.

## Slide 12: Future vs. Current Spectral Bands
The current GOES (right) has 5 spectral bands, while the GOES-R series ABI (left) will have 16 spectral bands.

## Slide 13: AHI: Spectral (20-September-2015)
Visible
Infrared
Near- infrared

## Slide 14
Current
GOES
Future
GOES

## Slide 15
GOES
Figure courtesy of K. Bedka and W. Feltz

## Slide 16
“ABI” from MODIS
Figure courtesy of K. Bedka and W. Feltz

## Slide 17
Nocturnal Fog/Stratus Over the Northern Plains
ABI image (from MODIS) shows greater detail in structure of fog.
“ABI” 4 minus 11 μm Difference
Notes: Note the ABI (from MODIS) image is better spatial resolution and better signal-to-noise ratio then the GOES-10 imager.
Schmit, T. J., M. M. Gunshor, W. P. Menzel, J. J. Gurka, J. Li, and A. S. Bachmeier, 2005: Introducing the next-generation Advanced Baseline Imager on GOES-R. Bull. Amer. Meteor. Soc., 86, 1079-1096.

## Slide 18
ABI image (from MODIS) shows greater detail in structure of fog.
GOES-10 4 minus 11 μm Difference
Nocturnal Fog/Stratus Over the Northern Plains
Notes: Schmit, T. J., M. M. Gunshor, W. P. Menzel, J. J. Gurka, J. Li, and A. S. Bachmeier, 2005: Introducing the next-generation Advanced Baseline Imager on GOES-R. Bull. Amer. Meteor. Soc., 86, 1079-1096.

## Slide 19
GOES-12 and GOES-R ABI
Simulation of Grand Prix Fire/Southern California
GOES-12
GOES-12
GOES-R ABI
GOES-R ABI
Notes: Here are two different fires from J. Feltz of CIMSS (using mcidas-v). What we can see is a more defined peak in the higher resolution data and it is easier to pick out individual hotspots. In addition, the higher saturation temperature of the ABI allows us to see that the fire is around 370K. ABI is simulated from MODIS.

## Slide 20
What’s this infrared image showing?
Rinjani
?
?
?
?
?
Clouds
Arc clouds
Plume
Hot spot
Land
?
Cooler
Improved spatial resolution of an advanced imager
MTSAT
(older generation)
AHI
(new generation)
Notes: MTSAT vs AHI (Spatial) Plume is volcanic ash from Rinjani. Data from JMA, via STAR and the SSEC Data Center.

## Slide 21: Baseline ABI Scan Modes
Scan mode (3) or ‘flex mode’ for the ABI:
- Full disk every 15 minutes + 5 min CONUS
+ 1-min mesoscales (2 locations).
[Scan mode (4) or ‘Continuous Full Disk’ (CFD) is a full disk every 5 min]
Notes: CONUS image is the shifted center point.

## Slide 22
Meso-scale box locations are movable
15 min
5 min
1 min
1 min
Notes: 1-km2 spatial resolution at satellite nadir. Pixel Areas are approximate. Each bin is rounded to the nearest 1km2 until we get to 9.5km2 and then all are binned into the red 10+ area. So the first, dark blue, ring covers pixel areas from 1 to 1.49km2 and is labeled “1”, above 1.5 to below 2.5km2 goes into the next ring and is called “2”, etc. GOES-Test location. PUG CONUS sector. Two meso-scale image sectors shown; these are selectable. The same central lat/lon used for these mesoscales produces a different sized and shaped area for different satellite locations.

## Slide 23: GOES-14 Super Rapid Scan Operations to Prepare for GOES-R (SRSOR)
SRSOR plans for 2015 include May 18-June 12, and August 10-22:
  http://cimss.ssec.wisc.edu/goes/srsor2015/GOES-14_SRSOR.html
  Data during parts of 2012 (Hurricane Sandy, convection), 2013 (CA Rim Fire, convection) and 2014 (Hurricane Marie, convection):
  http://cimss.ssec.wisc.edu/goes/srsor/GOES-14_SRSOR.html
  http://cimss.ssec.wisc.edu/goes/srsor2013/GOES-14_SRSOR.html
  http://cimss.ssec.wisc.edu/goes/srsor2014/GOES-14_SRSOR.html
GOES-14 provided very unique data and offered a glimpse into the possibilities that will be provided by the ABI on GOES-R in one minute mesoscale imagery
GOES-14 visible image showing rapid convective development
Notes: http://cimss.ssec.wisc.edu/goes/srsor2015/GOES-14_SRSOR.html

## Slide 24
Operational (GOES-13)
1-min mode (SRSOR from GOES-14)
1-min imagery

## Slide 25
A Glimpse into the Future
Hurricane Sandy from GOES-14 at two temporal resolutions
ABI-like

## Slide 26: GOES-14 Super Rapid Scan Operations to Prepare for GOES-R (SRSOR)
SRSOR in 2016 include February 1- 25, and April 18 - May 15:
  http://cimss.ssec.wisc.edu/goes/srsor2016/GOES-14_SRSOR.html
  GOES-14 provided very unique data and offered a glimpse into the possibilities that will be provided by the ABI on GOES-R in one minute mesoscale imagery (lows, fires, convection, fog, smoke, hurricanes, etc.)
Notes: http://cimss.ssec.wisc.edu/goes/srsor2015/GOES-14_SRSOR.html

## Slide 27: MTSAT (old generation) and AHI (advanced imager)
Manum (volcano)
Differences in the scanning intervals between images

## Slide 28: Summary
The ABI on GOES-R will improve over the current instrument in many aspects:
  Spatial, temporal, spectral, calibration, etc.
The great amount of information from the GOES-R will offer a continuation of current products and new products.
The ABI builds on previous experience/instruments
Similar imagers by Europe, Japan, Korea, etc.
  ABI-like coverage of most of the globe!
Thanks to JMA, Yasuhiko Sumida and SSEC

## Slide 29
Conclusions
The ABI on the GOES-R series continues the critical continuity of geostationary imagers and will have huge positive societal impacts, given its improved temporal, spatial, spectral and radiometric attributes.
Impact areas include, but are not limited to: weather, Numerical Weather Prediction, severe weather, hazards (volcanic ash plumes), aviation, environmental (fires), health (smoke), oceanographic, cryosphere, land, etc.
Part of a global constellation.

## Slide 30: GOES-R Series web site
Lockheed Martin
http://www.goes-r.gov