The GOES-14 Science Test:

Imager and Sounder Radiance and Product Validations

Editors:

Donald W. Hillger1, and Timothy J. Schmit3

Other Contributors:

Americo S. Allegrino6, A. Scott Bachmeier4, Jaime M. Daniels5, Mathew M. Gunshor4, Jay Hanna12, Andy Harris7, Michael P. Hiatt2, Seiichiro Kigawa13, John A. Knaff1, Jun Li4, Daniel T. Lindsey1, Eileen M. Maturi9, Wen Meng10, Kevin Micke2, Jon Mittaz7, James P. Nelson III4, Walt Petersen11, Dale G. Reinke2, Christopher C. Schmidt4, Anthony J. Schreiner4, Dustin Sheffler12, Dave Stettner4, Fangfang Yu???, Chris Velden4, Gary S. Wade3, Steve Wanzong4, Dave Watson2, and Xiangqian (Fred) Wu8

Affiliations:

1StAR/RAMMB (SaTellite Applications and Research/Regional and Mesoscale Meteorology Branch)

2CIRA (Cooperative Institute for Research in the Atmosphere)

Colorado State University, Fort Collins

3StAR/ASPB (SaTellite Applications and Research/Advanced Satellite Products Branch)

4CIMSS (Cooperative Institute for Meteorological Satellite Studies)

University of Wisconsin, Madison

5StAR/OPDB (SaTellite Applications and Research/Operational Products Development Branch)

6Raytheon IIS

Camp Springs MD

7CICS (Cooperative Institute for Climate Studies)

University of Maryland, College Park

8StAR/SPB (SaTellite Applications and Research/Sensor Physics Branch)

Camp Springs MD

9StAR/SOCD (SaTellite Applications and Research/Satellite Oceanography and Climatology Branch)

10Perot Systems

Camp Springs MD

11NSSTC (National Space Science and Technology Center), Lightning and Thunderstorm Group, NASA (National Aeronautics and Space Administration), MSFC (Marshall Space Flight Center), University of Alabama, Huntsville

12NOAA/NESDIS Satellite Analysis Branch (SAB)

13Meteorological Satellite Center, Japan Meteorological Agency

TABLE OF CONTENTS

Executive Summary of the GOES-13 NOAA Science Test	1

1.	Introduction	2

1.1.	Goals for the GOES-13 Science Test	3

2.	Satellite Schedules and Sectors	4

3.	Changes to the GOES Imager from GOES-8 through GOES-13	8

4.	GOES Data Quality	8

4.1.	First Images	8

4.1.1.	Visible	9

4.1.2.	Infrared (IR)	9

4.1.3.	Sounder	11

4.2.	Spectral Response Functions (SRFs)	13

4.2.1.	Imager	13

4.2.2.	Sounder	13

4.3.	Random Noise Estimates	14

4.3.1.	Imager	14

4.3.1.1.	Structure-estimated Noise	15

4.3.2.	Sounder	16

4.3.2.1.	Structure-estimated Noise	17

4.4.	Detector-to-Detector Striping	19

4.4.1.	Imager	19

4.4.2.	Sounder	20

4.5.	Imager-to-Imager Comparison	25

4.6.	Imager-to-Polar-Orbiter Comparisons	26

4.7.	Keep-Out-Zone Analysis	27

5.	Product Validation	31

5.1.	Total Precipitable Water (TPW) from Sounder	31

5.1.1.	Validation of Precipitable Water (PW) Retrievals from the GOES-13 Sounder	33

5.2.	Lifted Index (LI) from Sounder	38

5.3.	Cloud Parameters from Sounder and Imager	39

5.4.	Atmospheric Motion Vectors (AMVs) from Sounder and Imager	42

5.5.	Clear Sky Brightness Temperature (CSBT) from Imager	48

5.6.	Sea Surface Temperature (SST) from Imager	50

5.6.1.	SST Generation	50

5.6.2.	SST Validation	51

5.6.3.	SST Summary	55

5.7.	Fire Detection	55

5.8.	Volcanic Ash Detection	58

5.9.	Total Column Ozone	58

6.	Other accomplishments with GOES-13	59

6.1.	GOES-13 Imager Visible (Band-1) Spectral Response	59

6.2.	Lunar calibration	60

6.3.	Over-sampling Test	61

6.4.	The Effect of Satellite Temporal Resolution on IR Cooling Rate	62

6.4.1.	Non-severe convection over southern Mississippi	62

6.4.2.	Strong convection over central Argentina	63

6.5.	Coordination with University of Alabama/Huntsville	65

6.6.	VISITview	67

6.7.	Improved Image Registrations	67

6.7.1.	Wildfire in Upper Peninsula of Michigan	67

6.7.2.	Ice floes in Hudson Bay	68

7.	Recommendations for Future Science Tests	69

Acknowledgments	70

References	71

Appendix A:	Web Sites Related to the GOES-14 Science Test	73

Appendix B:	Acronyms Used in this Report	74

LIST OF TABLES

Table 2.1:  Summary of Test Schedules for the GOES-14 Science Test	6

Table 2.2:  Daily Implementation of GOES-14 Science Test Schedules	7

Table 3.1:  GOES Imager band nominal wavelengths (GOES-8 through 14)	11

Table 4.1:  Estimated noise for GOES-13 for 10 (0045 UTC) – 11 (1145 UTC) December compared to estimated noise values for GOES-12.	14

Table 4.2:  GOES-13 Imager noise (in 10-bit GVAR counts and temperature units) compared to GOES-12.	14

Table 4.3:  Summary of the noise (in temperature units) for GOES-8 through GOES-13 Imager bands.  The specification (SPEC) noise levels are also listed.	14

Table 4.4:  GOES-14 Sounder Noise Levels	16

Table 4.5:  Summary of the Noise for GOES-8 through GOES-14 Sounder Bands	16

Table 4.6:  GOES-13 Imager Striping.  (20 July 2007 [Julian day 201] 1800 UTC)	17

Table 4.7:  GOES-13 Sounder Detector-to-Detector Striping.  (From 48 hours of limb (earth and space) measurements on Julian days 343-345)	18

Table 4.8:  GOES-13 Sounder Detector-to-Detector Striping.  (From 48 hours of limb (space-only and earth-only) measurements on Julian days 343-345)	18

Table 4.9:  GOES-13 Sounder Detector Averages.  (From limb (space-only) measurements one-time only on Julian day 343 at ~1700 UTC)	18

Table 4.10:  GOES-13 Sounder Detector Standard Deviations (Noise).  (From limb (space-only) measurements one-time-only on Julian day 343 at ~1700 UTC)	18

Table 4.11:  Imager-to-Imager Comparison Between GOES-11 and GOES-13	19

Table 4.12:  Imager-to-Imager Comparison Between GOES-12 and GOES-13	19

Table 4.13:  Comparison of GOES-13 Imager to Atmospheric InfraRed Sounder (AIRS).  The Bias is the mean of the absolute values of the differences for n=19.	19

Table 5.1:  Verification statistics between GOES-12 and GOES-13 retrieved precipitable water, first guess (GFS) precipitable water, and radiosonde observations of precipitable water for the period 7 December 2006 to 5 January 2007.	22

Table 5.2:  Verification statistics for GOES-12 and GOES-13 AMVs vs. radiosonde winds for 18 comparison cases.	25

Table 5.3:  Verification statistics for GOES-12 and GOES-13 AMVs vs. radiosonde winds, after a fixed bias correction was applied.  Only samples that had a radiosonde match in both the GOES-12 and GOES-13 datasets were included.	25

LIST OF FIGURES

Figure 1.1:  GOES-O spacecraft decal	3

Figure 3.1:  The GOES-14 Imager instrument Spectral Response Functions (SRF). A corresponding earth-emitted high-resolution spectrum is also plotted.	12

Figure 4.1:  The first visible (0.65 μm) image from the GOES-14 Imager occurred on 27 July 2009 starting at 1730 UTC.	14

Figure 4.2:  A GOES-14 close-up view centered over central California showed marine fog and stratus hugging the Pacific coast, with cumulus clouds developing inland over the higher terrain of the Sierra Nevada.	15

Figure 4.4:  The visible (band-19) image from the GOES-13 Sounder shows the database correct on 6 July 2006.	16

Figure 4.5:  The first IR Sounder images for GOES-13 from 12 July 2006 (top) compared to GOES-12 (bottom).  Both sets of images have been remapped to a common projection.  Note the less noisy Sounder band-15 (4.6 μm).	16

Figure 4.6:  The four GOES-13 Imager IR band SRFs super-imposed over the calculated high-resolution earth-emitted U.S. Standard Atmosphere spectrum.  Absorption due to carbon dioxide (CO2), water vapor (H2O), and other gases are evident in the high-spectral resolution earth-emitted spectrum.	16

Figure 4.7:  The eighteen GOES-13 Sounder IR band SRFs super-imposed over the calculated high-resolution earth-emitted U.S. Standard Atmosphere spectrum.  The central wavenumbers (wavelengths) of the spectral bands range from 680 cm-1 (14.7 (m) to 2667 cm-1 (3.75 (m) (Menzel et al. 1998).	16

Figure 4.8:  GOES-13 Sounder noise values (NEdR) compared to those from GOES-11, GOES-12, and the specification noise values for GOES-I through M.	18

Figure 4.9:  The ratio of GOES-I through M specification noise values to the measured noise values for GOES-11, GOES-12, and GOES-13.	18

Figure 4.10: GOES-13 Sounder band 7 radiances (mW(m2(sr(cm-1)), before the de-striping (upper-left), after the de-striping (upper-right), and the differences (lower).	21

Figure 4.11: Sequences of images from 12 September 2006 comparing GOES-13 (top) to GOES-12 (bottom) through eclipse.  Rather than one long gap while the sun is either within view on each side of the earth or behind the earth, there are two shorter gaps when the sun is within view on each side of the earth.	23

Figure 4.12:  GOES-13 Imager visible (0.7 μm) band.  The bad lines were due to a noisy data ingest.	23

Figure 4.13:  GOES-13 Imager shortwave window band.	23

Figure 4.14:  GOES-13 Imager temporal difference (0525 – 0510 UTC) of the ‘water vapor’ band.  The bad lines were due to a noisy data ingest.	23

Figure 4.15:  GOES-13 Imager temporal difference (0525 – 0510 UTC) of the longwave IR window band.	23

Figure 4.16:  GOES-13 Imager temporal difference (0525 – 0510 UTC) of the CO2 band.  The bad lines were due to a noisy data ingest.	23

Figure 5.1:  GOES-13 (top panel) and GOES-12 (lower panel) retrieved to TPW (mm) from the Sounder displayed as an image.  The data are from 1146 UTC on 13 December 2006.  Measurements from radiosondes are overlaid as white text; cloudy FOVs are denoted as shades of gray.	24

Figure 5.2:  GOES-13 Sounder retrieved TPW with the original data (top panel) and after data has been de-striped (lower panel).  The data are from 1446 UTC on 3 January 2007.  The process to de-stripe the image was generated by D. Hillger; striping is removed via a process that moves each line average toward the mean.	24

Figure 5.3:  Time series of Root Mean Square Error (RMSE) between GOES-12 and GOES-13 retrieved precipitable water and radiosonde observation of precipitable water over the period 7 December 2006 to 5 January 2007.	26

Figure 5.4:  Time series of Bias (GOES-radiosonde) between GOES-12 and GOES-13 retrieved precipitable water and radiosonde observation of precipitable water over the period 7 December 2006 to 5 January 2007.	26

Figure 5.5:  Time series of correlation between GOES-12 and GOES-13 retrieved precipitable water and radiosonde observation of precipitable water over the period 7 December 2006 to 5 January 2007.	26

Figure 5.6:  Time series of the number of collocations between GOES-12 and GOES-13 retrieved precipitable water and radiosonde observation of precipitable water over the period 7 December 2006 to 5 January 2007.	26

Figure 5.7:  GOES-13 (top panel) and GOES-12 (lower panel) retrieved Lifted Index (LI)  from the Sounder displayed as an image.  The data are from 1146 UTC on 13 December 2006. Radiosonde values are over-plotted.	26

Figure 5.8:  GOES-13 (upper panel) and GOES-12 (lower panel) retrieved cloud-top pressure from the Sounder displayed as an image.  The data are from 1746 UTC on 4 January 2007 and the GOES-12 is remapped into the GOES-13 Sounder projection.	27

Figure 5.9:  GOES-13 cloud-top pressure from the Imager from 1445 UTC on 13 December 2006.	27

Figure 5.10:  GOES-13 cloud top pressure from the Sounder from 1445 UTC on 13 December 2006.	27

Figure 5.11:  GOES-11 and GOES-12 cloud-top pressure from the Sounder from the nominal 1500 UTC on 13 December 2006.  The image is reformatted to the GOES-13 Imager projection	27

Figure 5.12:  GOES-12 (left) and GOES-13 (right) AMVs for 25 December 2006 plotted over band-4 (10.7 μm) images.  The color coding differentiates the satellite bands used in AMV derivation.  Not all AMVs are shown for clarity of display.	28

Figure 5.13:  GOES-13 Imager (0.65 μm) visible AMVs from 20 December 2006 generated using 1, 5, and 15-minute interval images in upper-left, upper-right, and lower-left panels, respectively.  A broader view of the aforementioned 3 panels is shown in the lower-right panel for perspective.  Wind flag colors delineate pressure levels, except in the lower-right panel where colors delineate AMVs from different image intervals.	29

Figure 5.14:  AMVs generated using 60-minute interval 7.0 and 7.4 μm images from GOES-13 Sounder are shown in the top panel, while AMVs generated using thirty-minute interval images are shown in the bottom panel, all overlain on GOES-13 Sounder 7.4 μm images from 20 December 2006.	29

Figure 5.15:  GOES-12 (top) and GOES-13 (bottom) Imager Clear-Sky Brightness Temperature cloud mask from 1200 UTC on 22 December 2006.	30

Figure 5.16:  Radiance imagery: GOES-13 north sector band-2 (upper-left); GOES-13 north sector band-4 (upper-right); GOES-13 south sector band-2 (lower-left); GOES-13 south sector band-4 (lower-right).	30

Figure 5.17:  GOES-13 SST Imagery (Hourly SST composite with applied 98% clear sky probability (left) and hourly composite clear sky probability)	31

Figure 5.18:  GOES-12 SST retrievals vs. Buoys	31

Figure 5.19:  GOES-13 SST dual window vs. Buoy SST	31

Figure 5.20:  GOES-13 SST triple-window vs. Buoy SST.	31

Figure 5.21:  GOES-13 Day scatter plots of Satellite – Buoy SST vs. Satellite Zenith Angle for dual window (left) and triple window (right).	31

Figure 5.22:  GOES-13 Nighttime scatter plots of Satellite – Buoy SST vs. Satellite Zenith Angle for dual window (left) and triple window (right).	31

Figure 5.23:  Comparisons of GOES-12 SST Imagery with the GOES-13 SST Dual Window and Triple Window for 3 and 4 January 2007.	31

Figure 5.24:  GOES Imager 3.9 µm images from GOES-13 (top panel) and GOES-12 (lower panel).	32

Figure 5.25:  GOES Imager 3.9 µm time series from GOES-13 and GOES-12.	32

Figure 5.26:  Example of GOES-13 Imager 3.9 µm band data while GOES-13 was out of storage during July of 2007.	33

Figure 6.1:  GOES-12 (blue) and GOES-13 (red) Imager visible (0.7 μm) band SRFs, with a representative spectrum for grass over-plotted (green).	33

Figure 6.2:  Comparison of the visible (0.7 μm) imagery from GOES-12 and GOES-13 (20 July 2007) demonstrates how certain features are more evident with the GOES-13 visible data.  For example, the network of cities, towns and highways can be seen in the GOES-13 visible image, especially across northwestern Iowa and southwestern Minnesota.	33

Figure 6.3:  GOES-13 Imager visible (0.7 μm) band image of the moon from 14 July 2006 for a scan that started at 20:41 UTC.	34

Figure 6.8:  GOES-13 10.7 µm image from 2057 UTC on 12 December 2006.  The red "X" in northern Alabama denotes the location of Huntsville.	35

Figure 6.9:  Reflectivity (top) and radial velocity (bottom) from the HNT radar on 12 December 2007 at 2058 UTC.	35

Figure 6.10:  RHI scan of differential reflectivity (ZDR) from the HNT radar on 12 December 2007 at 2058 UTC.  Location of an undular bore and the radar bright band is indicated.	35

Executive Summary of the GOES-14 NOAA Science Test

The Science Test for GOES-14 produced several results and conclusions:

- GOES-14 Imager and Sounder data were collected during the 5-week NOAA Science Test that took place during December of 2009 while the satellite was stationed at 105ºW longitude.  Additional pre-Science Test data, such as the first visible and IR images, were collected during the summer and fall of 2009.

- Improved (4 km) resolution of 13.3 µm band required changes to the GVAR format. Several issues with implementing the new GVAR format were discovered, communicated, rectified, and verified. For example, the paired detectors on the higher-resolution 13.3 µm band were inadvertently swapped when the satellite was in an inverted mode.  This was quickly resolved.

- Imager and Sounder data collected for a host of schedules, including rapid scan imagery. GVAR datastream stored at several locations for future needs.

- Helped to identify a GOES Sounder calibration issue with respect to averaging calibration slopes.

- Initial IASI and AIRS inter-calibrations with both the imager and sounders verified good radiometric accuary.

- Many level 2 products generated (retrievals, atmospheric motion vectors, clouds, CSBT, SST, etc.) and validated.

- Many GOES-14 images and examples were posted on the web in near real-time.

Changes were implemented with the GOES-14 compared to previous GOES Imagers:

- The detector size of the Imager 13.3 µm band (band-6) was changed from 8 km to 4 km, by incorporating two detectors instead of just one.

- The change in the Imager 13.3 µm band (band-6) necessitated a change in the GVAR (GOES VARiable) data format, by including another block for data from the additional detector.

- Ability to operate the instruments during the eclipse periods and Keep-Out-Zone periods by utilizing batteries and partial-image frames.

- Colder patch (detector) temperatures due to the new spacecraft design. In general, Imager and Sounder data from GOES-14 (and GOES-13) are improved considerably in quality (noise level) to that from GOES-8 through GOES-12.

- In addition, the image navigation and registration with GOES-14 (and GOES-13) is much improved, especially in comparison to GOES-8 through GOES-12.

# Introduction

The latest Geostationary Operational Environmental Satellite (GOES), GOES-O, was launched on 27 June 2009, and reached geostationary orbit at 89.5°W on 8 July 2009 to become GOES-14.  It was later moved to 104.5ºW for the Science Test and eventual storage. {While the XRS is operating on GOES-14, the Imager and Sounder await operational use.}  This was the second of three GOES-N/O/P series spacecraft, with one more that was launched in March of 2010.

The National Oceanic and Atmospheric Administration (NOAA)/National Environmental Satellite, Data, and Information Service (NESDIS) conducted a 5-week GOES-14 Science Test that began 30 November 2009 and ended officially on 4 January 2010.  The first two weeks of the Science Test schedule were integrated within the NESDIS/National Aeronautics and Space Administration (NASA) GOES-14 Post-Launch Test (PLT) schedule.  An additional three weeks of the Science Test were performed under NOAA control.

GOES-14 has instruments similar to those on GOES-8/12, but GOES-14 (and GOES-13) are on a different spacecraft bus.  The new bus allows improvements both to navigation and registration, as well as the radiometrics.  By supplying data through the eclipse periods, the GOES-N/O/P system addresses one of the major limitations which are eclipse and related outages.  This is possible due to larger spacecraft batteries.  Outages due to Keep Out Zones (KOZ) are also minimized.  There are radiometric improvements, since the GOES-13/14 instruments (Imager and Sounder) are less noisy.  A colder patch (detector) temperature is the main reason.  (In addition, there is a potential reduction in detector-to-detector striping to be achieved through increasing the Imager scan-mirror dwell time on the blackbody from 0.2 sec to 2 sec).  There are improvements in both the navigation and registration on GOES-N/O/P.  The navigation was improved due to the new spacecraft bus and the use of star trackers (as opposed to the previous method of edge-of-earth sensors).  In general, the navigation accuracy (at nadir) improves from between 4-6 km with previous Imagers to less than 2 km with those on the GOES-N/O/P satellites.

Figure 1.1:  GOES-O spacecraft decal

This report describes the NOAA/NESDIS Science Test portion only. This report covers the Imager and Sounder instruments, but not the solar/space instruments. System performance and operational testing of the spacecraft and instrumentation was performed as part of the PLT.  During the Science Test, GOES-14 was operated in a special test mode, where the default schedule involved routine emulation of either GOES-east or GOES-west operations.  Numerous other scan schedules and sectors were constructed and used for both the Imager and the Sounder.  GOES-14 was then placed into storage mode on 19 January 2010.  Current plans call for GOES-14 not to become operational until after GOES-13 has become operational.  At the time of the GOES-14 Science Test, GOES-12 was operating in the GOES-east position, and GOES-11 was operating in the GOES-west position.

## Goals for the GOES-14 Science Test

First goal: To assess the quality of the GOES-14 radiance data.  This was accomplished by comparison to data from other satellites or by calculating the signal to-noise ratio compared to specifications, as well as assess the striping in the imagery due to multiple detectors.

Second goal: To generate products from the GOES-14 data stream and compare to those produced from other satellites.  These products included several Imager and Sounder products: land skin temperatures, temperature/moisture retrievals, total precipitable water, lifted index, cloud-top pressure, atmospheric motion vectors, and sea surface temperatures.  Validation of these products was accomplished by comparing these products to products generated from other satellites or by comparing them to radiosondes and ground-based instruments.

Third goal: To collect nearly-continuous rapid-scan imagery of interesting weather cases at temporal resolutions as fine as every 30 seconds, a capability of rapid-scan imagery from GOES-R that is not implemented operationally on current GOES.  The rapid-scan data may augment radar and lightning data collected at special networks, to investigate the potential for improving severe weather forecasts.

Fourth goal: To monitor the impact of any instrument changes.  This included the increased spatial resolution (from 8 km to 4 km) for the 13.3 µm band (band-6) on GOES-14.  Other improvements which began with GOES-13 include: better navigation, improved calibration and the capabilities of the GOES-N series to operate through eclipse, when the satellite is in the shadow of the earth, as well as to minimize outages due to Keep Out Zones (KOZ), when the sun can potentially contaminate imagery by being within the field of view of the instruments.

Finally, the GOES-14 Imager and Sounder data were received via direct downlink at the following sites: (1) CIRA, Colorado State University, Fort Collins CO; (2) Space Science and Engineering Center (SSEC), University of Wisconsin, Madison WI; and (3) NOAA/NESDIS, Suitland/Camp Springs MD.  Each site ingested, archived, and made the data available on its own internal network in McIDAS (Man computer Interactive Data Access System) format, as well as to other sites as needed.  The NOAA/NESIDS Regional and Mesoscale Meteorology Branch (RAMMB) at CIRA also made the GOES-14 imagery available over the internet via the RAMSDIS Online.  Image and product loops were also made available on the CIMSS Web.  See Appendix A for the appropriate URLs for these and many other GOES-14 related web sites.

This report documents results from these various activities undertaken by NOAA/NESDIS and its Cooperative Institutes during this test period.  Organizations which participated in these GOES-14 Science Test activities included the: NOAA/NESDIS SaTellite Applications and Research (StAR); NOAA/NESDIS Office of Satellite Data Processing and Distribution (OSDPD); Cooperative Institute for Meteorological Satellite Studies (CIMSS); Cooperative Institute for Research in the Atmosphere (CIRA); and NOAA/NESDIS Satellite Analysis Branch (SAB), and NASA/MSFC.

NOAA Technical Reports similar to this one were produced for both the GOES-11 (Daniels et al. 2001), GOES-12 (Hillger et al. 2003), and GOES-13 (Hillger and Schmit, 2007 and 2009) Science Tests.  The reference/bibliography section contains other articles related to GOES-14 Science Test.

# Satellite Schedules and Sectors

A total of nine schedules involving numerous predefined Imager and Sounder sectors were constructed for the GOES-14 Science Test.  The choice of Imager and Sounder sectors was a result of input from the various research and development groups participating in the Science Test.  Most of these schedules are similar to those run during the GOES-13 Science Test (Hillger and Schmit 2006).

Thanks to dedicated support provided by the NOAA/NESDIS/Satellite Operations Control Center (SOCC) and the Office of Satellite Operations (OSO), a significant amount of flexibility existed with respect to switching and activating the schedules on a daily basis.  The ease with which the schedules could be activated was important for capturing significant weather phenomena of varying scales and locations during the Science Test period.

A brief summary of the nine schedules is provided in Table 2.1.  The C5RTN or  C4RTN schedules, emulation of GOES-east or GOES-west operations respectively, were the default schedules if no other schedule was requested at the cutoff of 1 hour before the 1630 UTC daily schedule change time.  For the Sounder, the default schedules were also emulation of normal GOES-east and GOES-west operations.

The C1CON schedule was mainly for emulation of GOES-R Advanced Baseline Imager (ABI) data, where 5 minute images will be routine.  The C2SRSO and C3SRSO schedules, with images as 1-minute and 30-second intervals respectively, were prepared to provide the ability to call up Super Rapid Scan Operations (SRSO) during the test period.  The C6FD schedule was for continuous 30-minute interval full-disk imaging of the entire earth.  The C7MOON and “C8” schedules were for specialized data sets of the moon and for over-sampling of Imager data to emulate the spatial resolution of the GOES-R ABI, respectively.  And finally, the C59RTN schedule contained partial-image frames that will be available to users during Keep-Out-Zones, to avoid solar contamination radiances and the detrimental effect on image products.

The daily implementation of the various schedules during the entire Science Test is presented in Table 2.2.  The GOES-14 daily call-up began on 20 November 2009 and continued through 4 January 2010.  At that time the GOES-14 continued to collect imagery for more than two weeks, through 19 January 2010, before the GOES-14 imager and sounder instruments were turned off.

Table 2.1:  Summary of Test Schedules for the GOES-14 Science Test

| Test Schedule Name | Imager | Sounder | Purpose |
| --- | --- | --- | --- |
| C1CON | Continuous 5-minute CONUS sector | 26-minute CONUS sector every 30 minutes | Test navigation, ABI-like (temporal) CONUS scans |
| C2SRSO | Continuous 1-minute rapid-scan (with center point specified for storm analysis) | 26-minute CONUS sector every 30 minutes | Test navigation, ABI-like (temporal) mesoscale scans |
| C3SRSO | Continuous 30-second rapid-scan (with center point at one of three locations: Huntsville AL, Norman OK, or Washington DC)1 | 26-minute CONUS sector every 30 minutes | Coordination with lightning detection arrays in Huntsville AL, Norman OK, and Washington DC areas |
| C4RTN | Emulation of GOES-west routine operations | Emulation of GOES-west routine operations | Radiance and product comparisons |
| C5RTN | Emulation of GOES-east routine operations | Emulation of GOES-east routine operations | Radiance and product comparisons |
| C6FD | Continuous 30-minute Full Disk (including off-earth measurements) | Sectors on both east and west limbs every hour (including off-earth measurements)2 | Imagery for noise, striping, etc. |
| C7MOON (depends on moon availability) | Capture moon off edge of earth (when possible) for calibration purposes | Inserted into GOES-east routine operations | Test ABI lunar calibration concepts |
| "C8" (inserted into C5 GOES-east routine schedule) | Emulation of 2 km ABI resolution thru spatial over-sampling (19 minutes for a small sector per specific line-shifted scan strategy) | Emulation of GOES-east routine operations | ABI-like higher-resolution data emulation |
| C59RTN (modified C5 GOES-east routine schedule) | Partial-image frames3 testing (such frames will be available during semi-annual satellite-eclipse/keep-out-zone periods) | Emulation of GOES-east routine operations | AWIPS testing and product generation |

1 Including the Hazardous Weather Testbed in North Alabama (centered at Huntsville AL, 34.72 N -86.65 E), the Oklahoma Lightning Mapping Array (centered at Norman OK, 35.28 N -97.92 E), and the Washington DC lightning mapping array (centered over Falls Church VA, 38.89 N -77.17 E). 
2 Limb sectors similar to GOES Sounder scans during previous GOES Science Tests. 
3 Partial-image frames include the following: CONUS & CONUS replacement, Northern HEMI & Northern HEMI replacement, Southern HEMI & Southern HEMI replacement, and Northern HEMI-extended & Northern HEMI-extended replacement,

Table 2.2:  Daily Implementation of GOES-14 Science Test Schedules

(Daily starting time: 1630 UTC)

| Starting Date [Julian Day] (Day of Week) | Test Schedule Name | Imager | Sounder | Purpose |
| --- | --- | --- | --- | --- |
| Start of 5-week Science Test |
| November 30 [334] (Monday) | C5RTN | Emulation of GOES-east routine operations | Emulation of GOES-east routine operations | Some final changes in software at Satellite Operations are still being implemented |
| December 01 [335] (Tuesday) | C6FD | Continuous 30-minute Full Disk (including off-earth measurements) | Sectors on both east and west limbs every hour (including off-earth measurements) | Imagery for noise, striping, etc. |
| December 02 [336] (Wednesday) | C2SRSO | Continuous 1-minute rapid-scan (centered at 34.7 N / 85.6 W, 1 deg E of Huntsville AL) | 26-minute CONUS sector every 30 minutes | Significant weather event over SE U.S. |
| December 03 [337] (Thursday) | "C8" (inserted into C5 schedule) | Emulation of GOES-east routine operations (with special scans inserted) | Emulation of GOES-east routine operations | Radiance and product comparisons (plus ABI-like higher-resolution data emulation) |
| December 04 [338] (Friday) | C1CON | Continuous 5-minute CONUS sector | 26-minute CONUS sector every 30 minutes | ABI-like (temporal) CONUS scans |
| December 05 [339] (Saturday) | C2SRSO | Continuous 1-minute rapid-scan (centered at 28.59 N / 80.65 W, Kennedy Space Center) | 26-minute CONUS sector every 30 minutes | Coordination with lightning mapping array over KSC |
| December 06 [340] (Sunday) | C5RTN | Emulation of GOES-east routine operations | Emulation of GOES-east routine operations | Radiance and product comparisons |
| December 07 [341] (Monday) | C4RTN | Emulation of GOES-west routine operations | Emulation of GOES-west routine operations | Radiance and product comparisons |
| December 08 [342] (Tuesday) | C2SRSO | Continuous 1-minute rapid-scan (centered at 34.7 N / 86.6 W, Huntsville AL) | 26-minute CONUS sector every 30 minutes | Coordinate with lightning detection array in Huntsville AL |
| December 09 [343] (Wednesday) | C1CON | Continuous 5-minute CONUS sector | 26-minute CONUS sector every 30 minutes | ABI-like (temporal) CONUS scans |
| December 10 [344] (Thursday) | C4RTN | Emulation of GOES-west routine operations | Emulation of GOES-east routine operations | Radiance and product comparisons |
| December 11 [345] (Friday) | C1CON | Continuous 5-minute CONUS sector | 26-minute CONUS sector every 30 minutes | ABI-like (temporal) CONUS scans |
| December 12 [346] (Saturday) | C4RTN | Emulation of GOES-west routine operations | Emulation of GOES-west routine operations | Radiance and product comparisons |
| December 13 [347] (Sunday) | C4RTN | Emulation of GOES-west routine operations | Emulation of GOES-west routine operations | Radiance and product comparisons |
| December 14 [348] (Monday) | C5RTN | Emulation of GOES-east routine operations | Emulation of GOES-east routine operations | Radiance and product comparisons |
| December 15 [349] (Tuesday) | C5RTN | Emulation of GOES-east routine operations | Emulation of GOES-east routine operations | Radiance and product comparisons |
| December 16 [350] (Wednesday) | C5RTN | Emulation of GOES-east routine operations | Emulation of GOES-east routine operations | Radiance and product comparisons |
| December 17 [351] (Thursday) | C59RTN | Partial-image frames testing (modified C5 GOES-east routine schedule) | Emulation of GOES-east routine operations | AWIPS testing and product generation |
| December 18 [352] (Friday) | C2SRSO | Continuous 1-minute rapid-scan (centered at 32 N / 82 W, on the Georgia coast) | 26-minute CONUS sector every 30 minutes | Significant weather event over SE U.S. |
| December 19 [353] (Saturday) | C2SRSO | Continuous 1-minute rapid-scan (centered at 39 N / 77 W, Washington DC) | 26-minute CONUS sector every 30 minutes | Significant east coast snowstorm |
| December 20 [354] (Sunday) | C2SRSO | Continuous 1-minute rapid-scan (centered at 50 N / 123 W, Whistler BC, Canada) | 26-minute CONUS sector every 30 minutes | Mountain snow study for 2010 Olympics |
| December 21 [355] (Monday) | C4RTN | Emulation of GOES-west routine operations | Emulation of GOES-west routine operations | Radiance and product comparisons |
| December 22 [356] (Tuesday) | C4RTN | Emulation of GOES-west routine operations | Emulation of GOES-west routine operations | Radiance and product comparisons |
| December 23 [357] (Wednesday) | C4RTN | Emulation of GOES-west routine operations | Emulation of GOES-west routine operations | Radiance and product comparisons |
| December 24 [358] (Thursday) | C2SRSO | Continuous 1-minute rapid-scan (centered at 35.1 N / 89.8 W, Memphis TN) | 26-minute CONUS sector every 30 minutes | Large weather system over central U.S. |
| December 25 [359] (Friday) | C1CON | Continuous 5-minute CONUS sector | 26-minute CONUS sector every 30 minutes | ABI-like (temporal) CONUS scans |
| December 26 [360] (Saturday) | C1CON | Continuous 5-minute CONUS sector | 26-minute CONUS sector every 30 minutes | ABI-like (temporal) CONUS scans |
| December 27 [361] (Sunday) | C1CON | Continuous 5-minute CONUS sector | 26-minute CONUS sector every 30 minutes | ABI-like (temporal) CONUS scans |
| December 28 [362] (Monday) | C6FD | Continuous 30-minute Full Disk (including off-earth measurements) | Sectors on both east and west limbs every hour (including off-earth measurements) | Imagery for noise, striping, etc. |
| December 29 [363] (Tuesday) | C5RTN | Emulation of GOES-east routine operations | Emulation of GOES-east routine operations | Radiance and product comparisons |
| December 30 [364] (Wednesday) | C1CON | Continuous 5-minute CONUS sector | 26-minute CONUS sector every 30 minutes | ABI-like (temporal) CONUS scans |
| December 31 [365] (Thursday) | C4RTN | Emulation of GOES-west routine operations | Emulation of GOES-west routine operations | Radiance and product comparisons |
| January 01 [001] (Friday) | C4RTN | Emulation of GOES-west routine operations | Emulation of GOES-west routine operations | Radiance and product comparisons |
| January 02 [002] (Saturday) | C4RTN | Emulation of GOES-west routine operations | Emulation of GOES-west routine operations | Radiance and product comparisons |
| January 03 [003] (Sunday) | C4RTN | Emulation of GOES-west routine operations | Emulation of GOES-west routine operations | Radiance and product comparisons |
| January 04 [004] (Monday) | C7MOON1 | Capture moon off edge of earth (when possible) for calibration purposes | Inserted into GOES-east routine operations | Test ABI lunar calibration concepts |
| End of 5-week Science Test |
| Starting January 05 [005] thru January 19 [019] | C5RTN or C4RTN | Emulation of GOES-east or west routine operations | Emulation of GOES-east or west routine operations | GOES-14 operated in this schedule until it was put into storage mode |

1 Additional (and better) moon images were taken on 10 August 2009 [Julian Day 09222].

# Changes to the GOES Imager from GOES-8 through GOES-14

The differences in spectral bands between the two versions of the GOES Imager (Schmit et al. 2002a) are explained in Table 3.1.  Each version has five bands.  The Imager on GOES-8 through GOES-11 contains bands 1 through 5.  The Imagers on GOES-12, 13, 14, and 15 contain bands 1 through 4 and band 6.

Table 3.1:  GOES Imager band nominal wavelengths (GOES-8 through 14)

| GOES Imager Band | Wavelength Range (μm) | Central Wavelength (μm) | Meteorological Objective |
| --- | --- | --- | --- |
| 1 | 0.53 to 0.75 (0.70) | 0.65 (GOES-8/12) 0.63 (GOES-13/15) | Cloud cover and surface features during the day |
| 2 | 3.8 to 4.0 | 3.9 | Low cloud/fog and fire detection |
| 3 | 6.5 to 7.0 5.8 to 7.3 | 6.75 (GOES-8/11) 6.48 (GOES-12/14) | Upper-level water vapor |
| 4 | 10.2 to 11.2 | 10.7 | Surface or cloud top temperature |
| 5 | 11.5 to 12.5 | 12.0 (GOES-8/11) | Surface or cloud top temperature and low-level water vapor |
| 6 | 12.9 to 13.7 | 13.3 (GOES-12/14) | CO2 band: Cloud detection |

The differences in the nominal spatial resolution between the more recent GOES Imager are explained in Table 3.2.  The east-west over-sampling is not included in the table. The increased resolution of band-6 necessitated a change in the GVAR format, to include an additional block of data associated with two detectors instead of only one detector.

Table 3.2:  GOES Imager band spatial resolution (GOES-12 through 14)

| GOES Imager Band | Central Wavelength (μm) | Spatial Resolution (km) | Number of Detectors |
| --- | --- | --- | --- |
| 1 | 0.65 | 1 | 8 |
| 2 | 3.9 | 4 | 2 |
| 3 | 6.48 | 4 | 2 |
| 4 | 10.7 | 4 | 2 |
| 6 | 13.3 | 8 (GOES-12/13) 4 (GOES-14/15) | 1 (GOES-12/13) 2 (GOES-14/15) |

Figure 3.1:  The GOES-14 Imager weighting function plot.

Figure 3.2:  The GOES-14 Sounder weighting function plot.

Figures 3.1 and 3.2 show the nominal region of the atmosphere sensed by each Imager and Sounder band on GOES-14. Note these are representative of clear-skies.

# GOES Data Quality

## First Images

The first step to ensure quality products is to verify the quality of the radiances that are used as inputs to the product generation.

### Visible

Figure 4.1:  The first visible (0.65 μm) image from the GOES-14 Imager occurred on 27 July 2009 starting at 1730 UTC.

Figure 4.2:  A GOES-14 close-up view centered over central California showed marine fog and stratus adjacent to the Pacific coast, with cumulus clouds developing inland over the higher terrain of the Sierra Nevada.

### Infrared (IR)

Figure 4.3:  GOES-14 full-disk image for “water vapor” band (band-3, 6.5 (m) from 17 August 2009 starting at 1732 UTC.

Figure 4.4:  GOES-14 Imager bands (top) and the corresponding GOES-12 Imager bands (bottom).  Both sets of images are shown in their native projections.

The above images have been sub-sampled. This is necessary, in part, due to the fact that the first GOES-14 Imager full disk images were too wide.

### Sounder

The first GOES-14 Sounder images showed good qualitative agreement with GOES-12.

Figure 4.5  The visible (band-19) image from the GOES-14 Sounder shows data from 28 July 2009.

Figure 4.6  The first IR Sounder images for GOES-14 from 18 August 2009 (top) compared to GOES-12 (bottom).  Both sets of images have been remapped to a common projection.  Note the less noisy Sounder band-15 (4.6 μm).

## Spectral Response Functions (SRFs)

### Imager

The GOES spectral response functions (SRFs) for the GOES series Imagers can be found at:

http://www.oso.noaa.gov/goes/goes-calibration/goes-imager-srfs.htm and are plotted in Figure 4.7. Note that there are two versions (Revision D and E) on the GOES-14 Imager SRF. The GOES-14 Imager is spectrally similar to the GOES-12 Imager, in that it has the spectrally-wide ‘water vapor’ band.  Information about the GOES calibration can be found in Weinreb et al. 1997.

Figure 4.7  The four GOES-14 Imager IR band SRFs super-imposed over the calculated high-resolution earth-emitted U.S. Standard Atmosphere spectrum.  Absorption due to carbon dioxide (CO2), water vapor (H2O), and other gases are evident in the high-spectral resolution earth-emitted spectrum.

### Sounder

The GOES SRFs for the GOES series Sounders can be found at: http://www.oso.noaa.gov/goes/goes-calibration/goes-sounder-srfs.htm and are plotted in Figure 4.7.  The band selection is unchanged from previous GOES Sounders (Schmit et al. 2002b).  As before, the carbon dioxide (CO2), ozone (O3), and water vapor (H2O) absorption bands are indicated in the calculated high-spectral resolution earth-emitted U.S. Standard Atmosphere spectrum.

Figure 4.8:  The eighteen GOES-14 Sounder IR band SRFs super-imposed over the calculated high-resolution earth-emitted U.S. Standard Atmosphere spectrum.  The central wavenumbers (wavelengths) of the spectral bands range from 680 cm-1 (14.7 (m) to 2667 cm-1 (3.75 (m) (Menzel et al. 1998).

## Random Noise Estimates

Band noise estimates for the GOES-14 Imager and Sounder instruments were computed using two different approaches.  In the first approach, the band noise values were determined by calculating the variance of radiance values in a space look scene.  The second approach involved performing a spatial structure analysis (Hillger and Vonder Haar, 1988).  Both approaches yielded nearly identical band noise estimates and are presented below.

### Imager

Full-disk images for the Imager provided space views and allowed noise values to be determined.  Estimated noise values for the GOES-14 Imager from 10 December 2006 at 0045 UTC through 11 December 2006 at 1145 UTC were averaged over that time period from both east and west-limb space views.  The noise values were much improved from those for GOES-13 as in Table 4.1. The exception is that the band 3 noise values seem to be comparable.

<insert table>

Table 4.1:  Estimated noise for GOES-14 for 10 (0045 UTC) – 11 (1145 UTC) December compared to estimated noise values for GOES-12.

Band noise estimates for the GOES-14 Imager visible channel was also monitored at the GOES-14 IPM system with the variance of the pre-clamp and post-clamp space-look count data embedded in the GVAR B11.  Figure 4.9 shows the mean pre-clamp and post-clamp space-look count variance of GOES-14 Imager in December 2009, compared with those of GOES-13 data in February 2010, GOES-11 and 12 data in December 2009.  As shown in this figure, GOES-14 Imager has the similar visible band noise level with GOES-13, greatly improved over the other GOES satellites.  Except for the diurnal variations, there is no significant long-term change in space-look variance during the GOES-14 PLT test period (Figure 4.10).  Both the pre-clamp and post-clamp space count variance shows that the noise level reaches the peak at night around 12:00UTC.  Same with the pre-clamp space look monitoring, occasional ZERO values also observed at the pre-clamp space look variance values which are associated with at not-used 9.2sec scan clamp.  This ZERO values do not impact the operational calibration accuracy (Weinreb and Mitchell, 2010).

Figure 4.9:  Variance of pre-clamp and post-clamp space-look scan count for GOES-14, compared with those for GOES-11/12/13.

Figure 4.10.  Time-series of the variance of GOES-14 Imager pre-clamp and post-clamp space-look scan at three temporal scales.  Top: 2-day period with 8 detector data, middle: 10-day period with 8 detector data, and bottom: mean values from Nov. 30, 2009 through Jan. 19, 2010.

The noise of GOES-14 IR bands were monitored with the NEdN and NEdT at blackbody scan data with the GOES-IPM system (Figure 4.11).   GOES-14 Imager IR band noise in temperature units is compared to the rest of the GOES series (GOES-8 through GOES-13) in Table 4.2.  GOES-14 seems to have larger noise level for all the IR bands expect for Band 2.  But all the IR band noise is comparable with the other satellite IR bands which are all within the specifications.  There is slight diurnal variation in the NEdT values for each IR band, with highest values around 12:00UTC.

| Imager Band | Central wave-length (µm) | GOES-14 | GOES-13 | GOES-12 | GOES-11 | GOES-10 | GOES-9 | GOES-8 | SPEC |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | K@300K, except band-3@230K |
| 2 | 3.9 | 0.057 | 0.059 | 0.102 | 0.123 | 0.090 | 0.094 |  | 1.4 |
| 3 | 6.5/6.7 | 0.197 | 0.170 | 0.149 | 0.265 | 0.149 | 0.134 |  | 1.0 |
| 4 | 10.7 | 0.051 | 0.045 | 0.073 | 0.073 | 0.061 | 0.055 |  | 0.35 |
| 5 | 12.0 |  |  |  | 0.176 | 0.112 | 0.123 |  | 0.35 |
| 6 | 13.3 | 0.106 | 0.067 | 0.102 |  |  |  |  | 0.32 |

Table 4.2. Summary of the noise (in temperature units) for GOES-8 through GOES-14 Imager IR bands.  The specification (SPEC) noise levels are also listed.

Figure 4.11. GOES-14 Imager NEdT calculated at 300K temperature except band 3 at 230K, compared to the specifications.

#### Structure-estimated Noise

Noise was also estimated using spatial structure analysis on a 150-line by 150-element (22,500 pixel) space-view portion of the GOES images.  Structure analysis compares adjacent Fields-Of-View (FOVs) to determine the random component of the signal in the images.

Results for GOES-13 are presented in Table 4.2, in both 10-bit GVAR counts and temperature units, with equivalent values for GOES-12 given for comparison (from both the first Science Test images and from images taken at the same time as the preliminary GOES-13 analysis).  Variations between preliminary and 5th-year noise levels for all bands of GOES-12, typically values within a factor of two, are as expected.

Table 4.2:  GOES-14 Imager noise (in 10-bit GVAR counts and temperature units) compared to GOES-12.

GOES-14 noise in temperature units is compared to the rest of the GOES series (GOES-8 through GOES-12) in Table 4.3.  GOES-13 noise levels in all bands except band-3 appear to be much improved over those from the other GOES satellites.

Table 4.3:  Summary of the noise (in temperature units) for GOES-8 through GOES-14 Imager bands.  The specification (SPEC) noise levels are also listed.

### Sounder

Special GOES-14 limb-view Sounder sectors allow noise values to be determined by the scatter of radiance values looking at uniform space.  Indications from 10 December 2006 at 0045 UTC through 11 December 2006 at 1145 UTC show that GOES-13 appears to be within specification for all bands.  Noise values were taken from both west-limb and east-limb and averaged over that time period.  The bar plot in Figure 4.8 comparing GOES-11, GOES-12, and GOES-13 to the GOES-I through M specifications illustrates the improvement in most bands GOES-13 represents.  The GOES-13 signal to noise values (in radiance units) compare well to those from other satellites.  The bar plot in Figure 4.9 shows the ratio of GOES-I through M spec noise to noise measurements comparing GOES-11, GOES-12, and GOES-13.

Figure 4.8:  GOES-13 Sounder noise values (NEdR) compared to those from GOES-11, GOES-12, and the specification noise values for GOES-I through M.

Figure 4.9:  The ratio of GOES-I through M specification noise values to the measured noise values for GOES-11, GOES-12, and GOES-13.

The Sounder visible band noise was measured with space look variance.  It is monitored at GOES-14 IPM system.  Summary of GOES-14 are presented in Figure 4.12.  It seems that the visible band noise was much improved from those for GOES-11, 12 and 13.

GOES-14 Sounder noise is monitored with NEdN and NEdT at blackbody scan with measured blackbody temperature and the results also available at the GOES-14 IPM webpage.  Table 3 and 4 summarized that noise levels for GOES-8 through GOES-14.  It seems that GOES-14 sounder noise levels were all improved compared to other GOES.

Figure 4.12. GOES-14 Sounder noise values (space-look count variance) compared to those from GOES-11/12/13.

Table 4-????. GOES-14 NEdN compared to those from GOES-8 through GOES-13, and the specification noise values.

| Sounder Band | Central Wave-length (µm) | GOES-14 | GOES-13 | GOES-12 | GOES-11 | GOES-10 | GOES-9 | GOES-8 | SPEC |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | (mW/m2Srcm-1) |
| 1 | 14.71 | 0.268 | 0.288 | 0.326 | 0.300 | 0.645 | 0.563 | 0.998 | 0.66 |
| 2 | 14.37 | 0.221 | 0.230 | 0.282 | 0.247 | 0.441 | 0.455 | 0.755 | 0.58 |
| 3 | 14.06 | 0.188 | 0.211 | 0.221 | 0.186 | 0.347 | 0.344 | 0.685 | 0.54 |
| 4 | 13.64 | 0.142 | 0.167 | 0.200 | 0.179 | 0.360 | 0.294 | 0.512 | 0.45 |
| 5 | 13.37 | 0.141 | 0.169 | 0.185 | 0.175 | 0.338 | 0.275 | 0.495 | 0.44 |
| 6 | 12.66 | 0.064 | 0.080 | 0.076 | 0.092 | 0.147 | 0.127 | 0.223 | 0.25 |
| 7 | 12.02 | 0.042 | 0.054 | 0.056 | 0.058 | 0.079 | 0.080 | 0.144 | 0.16 |
| 8 | 11.03 | 0.044 | 0.097 | 0.127 | 0.137 | 0.096 | 0.079 | 0.129 | 0.16 |
| 9 | 9.71 | 0.054 | 0.127 | 0.184 | 0.132 | 0.120 | 0.113 | 0.161 | 0.33 |
| 10 | 7.43 | 0.033 | 0.096 | 0.129 | 0.107 | 0.077 | 0.716 | 0.082 | 0.16 |
| 11 | 7.02 | 0.020 | 0.054 | 0.075 | 0.070 | 0.048 | 0.044 | 0.071 | 0.12 |
| 12 | 6.51 | 0.027 | 0.076 | 0.138 | 0.134 | 0.091 | 0.079 | 0.111 | 0.15 |
| 13 | 4.57 | 0.0028 | 0.0046 | 0.024 | 0.0045 | 0.006 | 0.006 | 0.008 | 0.013 |
| 14 | 4.52 | 0.0029 | 0.0049 | 0.023 | 0.0056 | 0.004 | 0.005 | 0.008 | 0.013 |
| 15 | 4.46 | 0.0025 | 0.0042 | 0.025 | 0.0044 | 0.004 | 0.005 | 0.008 | 0.013 |
| 16 | 4.13 | 0.0016 | 0.0023 | 0.009 | 0.0023 | 0.002 | 0.002 | 0.003 | 0.008 |
| 17 | 3.98 | 0.0013 | 0.0020 | 0.008 | 0.0021 | 0.002 | 0.002 | 0.002 | 0.008 |
| 18 | 3.74 | <0.0001 | <0.0001 | 0.0033 | 0.0010 | <0.0001 | 0.001 |  | 0.004 |

Table 4-???. GOES-14 Sounder NEdT compared to those from GOES-8 through GOES-13.

| Sounder Band | Central Wave-length (µm) | GOES-14 | GOES-13 | GOES-12 | GOES-11 | GOES-10 | GOES-9 | GOES-8 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | K @ blackbody temperature |
| 1 | 14.71 | 0.158 | 0.170 | 0.193 | 0.178 | 0.383 | 0.333 | 0.591 |
| 2 | 14.37 | 0.129 | 0.135 | 0.165 | 0.147 | 0.259 | 0.267 | 0.443 |
| 3 | 14.06 | 0.109 | 0.123 | 0.128 | 0.108 | 0.201 | 0.199 | 0.398 |
| 4 | 13.64 | 0.082 | 0.096 | 0.115 | 0.103 | 0.208 | 0.169 | 0.295 |
| 5 | 13.37 | 0.081 | 0.097 | 0.106 | 0.100 | 0.194 | 0.158 | 0.283 |
| 6 | 12.66 | 0.036 | 0.046 | 0.043 | 0.053 | 0.084 | 0.072 | 0.127 |
| 7 | 12.02 | 0.024 | 0.031 | 0.032 | 0.033 | 0.045 | 0.046 | 0.082 |
| 8 | 11.03 | 0.026 | 0.057 | 0.074 | 0.081 | 0.056 | 0.047 | 0.076 |
| 9 | 9.71 | 0.035 | 0.082 | 0.118 | 0.104 | 0.077 | 0.072 | 0.103 |
| 10 | 7.43 | 0.034 | 0.097 | 0.130 | 0.108 | 0.078 | 0.071 | 0.082 |
| 11 | 7.02 | 0.023 | 0.063 | 0.088 | 0.083 | 0.056 | 0.052 | 0.084 |
| 12 | 6.51 | 0.039 | 0.112 | 0.206 | 0.201 | 0.135 | 0.116 | 0.165 |
| 13 | 4.57 | 0.023 | 0.038 | 0.195 | 0.038 | 0.047 | 0.045 | 0.084 |
| 14 | 4.52 | 0.026 | 0.043 | 0.205 | 0.050 | 0.035 | 0.046 | 0.067 |
| 15 | 4.46 | 0.025 | 0.042 | 0.248 | 0.043 | 0.037 | 0.046 | 0.075 |
| 16 | 4.13 | 0.027 | 0.038 | 0.147 | 0.040 | 0.038 | 0.039 | 0.056 |
| 17 | 3.98 | 0.028 | 0.045 | 0.186 | 0.047 | 0.042 | 0.054 | 0.085 |
| 18 | 3.74 | <0.001 | <0.001 | 0.119 | 0.037 | <0.001 | 0.038 | 0.064 |

#### Structure-estimated Noise

Structure analysis was performed on half-hourly space-view measurements acquired over a 24-h period: 1 December 2009 [Julian day 335] at 1646 UTC through 2 December 2009 [Julian day 336] at 1546 UTC.  East-limb, west-limb, and limb-average values are presented and compared to CIMSS analysis values in Table 4.4.  The noise estimates from RAMMB/CIRA are very similar to those calculated independently by ASPB/CIMSS.

Table 4.4:  GOES-14 Sounder Noise Levels

(In radiance units, from 24 hours of limb/space views on Julian days 335-336).

In Table 4.5 GOES-14 Sounder noise appears to be lower than previous GOES in the longwave IR bands in particular.  Other bands have noise similar to GOES-12 and 13.  Noise in all bands is much lower than instrument specifications.

Table 4.5:  Summary of the Noise for GOES-8 through GOES-14 Sounder Bands

(The Specification (SPEC) values are also listed).

## Striping Due to Multiple Detectors

### Imager

Full-disk images from the Imager provide off-earth space views, allowing both noise levels and detector-to-detector striping to be determined in an otherwise constant signal situation.  Striping estimates for the first calibrated infrared (IR) images from the GOES-13 Imager taken on 20 July 2006 at 1800 UTC were determined to be similar to those for GOES-12 Imager.  Table 4.6 gives estimates of GOES-13 Imager detector-to-detector striping (from both-detector mean*) and noise compared to GOES-12.  Calculated on ~300,000 earth-view pixels.  Comparison is made to striping determined for both the GOES-12 Science Test images and to images from GOES-12 taken at the same time as the preliminary GOES-13 analysis, the 5th year into the life of GOES-12.

Table 4.6:  GOES-13 Imager Striping.  (20 July 2007 [Julian day 201] 1800 UTC)

Striping is defined as the difference between the average value for each detector from the average value in both detectors.  Therefore striping between the two detectors is actually twice the value listed, and is often more noticeable than noise. In general, the GOES-13 Imager striping is less than that on GOES-12, possibly due to the longer black-body look.

Striping is also compared to random noise in Table 4.6, to recognize that increased striping may contribute to increased noise.  (For example, the increased noise in GOES-13 band-3 compared to the other GOES-13 bands may be the reason the noise in GOES-13 band-3 is higher than the other GOES-13 bands.  For GOES-12, noise appears to be equal to or much greater than striping in all bands.)

### Sounder

Detector-to-detector striping for the Sounder is documented in Table 4.7 from both earth and space measurements taken from the same limb-view sectors used for the noise analysis for the Sounder.  In this case however, the analysis included measurements from the entire Sounder sector, including both the earth and space views.  Of significance was the fact that the results from the east-limb and west-limb were significantly different.  The last column gives the west-to-east ratio for the striping, indicating that there is significantly more striping in data from the west-limb than from the east-limb.

Table 4.7:  GOES-13 Sounder Detector-to-Detector Striping.  (From 48 hours of limb (earth and space) measurements on Julian days 343-345)

To determine the source of this difference between the limbs seen in Table 4.7, the limb-view data were split into space-only and earth-only measurements for further analysis.  From the results in Table 4.8, the increased west-limb striping is mainly manifested in the earth-only measurements, and to a much lesser extent in the space-only measurements.  This implies that the striping is related to the larger signal of the earth-only measurements compared to the low signal of the space-view measurements.  Current thought is that this difference might also be related to the east-west correction applied to the measurements due to angular-related emissivity variations of the scan mirror.

Table 4.8:  GOES-13 Sounder Detector-to-Detector Striping.  (From 48 hours of limb (space-only and earth-only) measurements on Julian days 343-345)

Finally, Tables 4.9 and 4.10 give the averages and standard deviations, respectively, for each detector for a sample of the space-only measurements in the tables above.  These numbers indicate that the signal and noise are similar on both limbs, and the limb effect is probably not due to the scan mirror emissivity correction as first assumed above.

Table 4.9:  GOES-13 Sounder Detector Averages.  (From limb (space-only) measurements one-time only on Julian day 343 at ~1700 UTC)

Table 4.10:  GOES-13 Sounder Detector Standard Deviations (Noise).  (From limb (space-only) measurements one-time-only on Julian day 343 at ~1700 UTC)

The GOES-14 (G-14) Sounder exhibits discontinuous calibration slopes across many of the daily Housekeeping (HK) times.  Outside of the discontinuity itself (which occurs between the pre- and post-Housekeeping blackbody/calibration events), the slopes usually display typical diurnal behavior throughout the rest of the day.  Because of these discontinuous slopes, calibration M-mode=1 (‘instantaneous’ slopes) is used instead of M-mode=3 (diurnal averaging of slopes over multiple days) in SPS for processing the G-14 Sounder frames.

However, on Jan. 14, 2010 following the slope discontinuity at HK (at ~18:34), the G-14 Sounder continued to display rapid slope changes lasting for a few hours.  Other occurrences of rapid slope changes following G-14 HK have also been observed, although relatively rarely.   Evidence of striping/banding in the G-14 Sounder earth-frames after the Jan. 14th HK is attributable to these post-HK rapid slope changes.

Modified calibration proceducres are being investigated to mitigate this rapid slope changes affects on the radiances.

Figure 4.11: GOES-13 Sounder band 7 radiances (mW(m2(sr(cm-1)), before the de-striping (upper-left), after the de-striping (upper-right), and the differences (lower).

## Imager-to-Imager Comparison

GOES-14 data was evaluated by comparing pixel temperatures of a 10 x 10 pixel box in a Mercator projection centered at 40˚N/90˚W for bands 2, 3, 4 and 6 to a similar domain on the operational GOES-East satellite (GOES-12).  Comparisons were also performed with the operational GOES-West satellite (GOES-11) by comparing pixel temperatures of a 10 x 10 pixel box in a Mercator projection centered at 40˚N/120˚W for bands 2, 3 and 4.  All results were plotted in a two-dimensional smoothed histogram approach which allows for a better representation of data in dense areas (Eilers and Goeman 2004).  Additionally, numerous statistics were calculated in order to determine the performance of the GOES-14 imager bands compared to the respective imager bands on GOES-11 and GOES-12.  

GOES-East emulation testing began in SAB on November 25, 2009 and was completed on January 19, 2010.  This testing period resulted in sample sizes of at least nearly 100,000 pixels for all bands tested.  Figs. 4.10 show two-dimensional smoothed histograms of GOES-12 vs. GOES-14 pixel temperatures taken from a 10 x 10 domain centered at 40˚N/90˚W for bands 2, 3, 4 and 6.  Figs. 4.10 feature a dashed line representing the perfect fit line with numerous performance statistics included on the graphs.  A nearly perfect degree of correlation (r > 0.98) was observed between GOES-12 and GOES-14 pixel temperatures for all tested bands.  On bands 2, 3 and 4 (see Figs. 4.10, a-c) no significant biases were detected in the data.  Mean Absolute Errors (MAE) were less than or equal to roughly 1 K for bands 3 and 4 and was around 1.7 K for band 2.  For band 6 (see Fig. 4.10d), SAB did note a modest bias of roughly 1.2 K where GOES-14 pixel temperatures were warmer than corresponding GOES-12 pixel temperatures.  MAE's for those pixels was around 1.5 K.  It's believed that the increased spatial resolution of band 6 data on GOES-14 could be the primary reason for the observed differences.  Root Mean Square Errors (RMSE) compared favorably to their respective MAE’s on bands 3 and 6 while differences of over 0.8K were noted on bands 2 and 4.  RMSE’s place more emphasis on large errors (Jolliffe and Stephenson, 2003) and this suggests there were several cases of large differences between band 2 and 4 pixels on GOES-12 and GOES-14.  These cases were manually investigated and most were determined to be a function of slight navigational errors near cloud edges.

GOES-West emulation testing began in SAB on December 22, 2009 and was completed on January 14, 2010.  The shorter testing period resulted in much smaller sample sizes (~40,000 pixels) for bands 2 and 4.  Additionally, scripting errors for band 3 data retrieval further limited the sample size (~12,000 pixels).  Figs. 4.11 show two-dimensional smoothed histograms of GOES-11 vs. GOES-14 pixel temperatures taken from a 10 x 10 domain centered at 40˚N/120˚W for bands 2, 3 and 4.  Similar to Figs. 4.10, Figs. 4.11 feature a dashed line representing the perfect fit line with numerous performance statistics included on the graphs.  A high degree of correlation (r > 0.88) was also observed between GOES-11 and GOES-14 data but it is noted that the correlation coefficients were much lower than what was observed between GOES-12 and GOES-14.  For bands 2 and 4 no significant biases (~ < 1.0 K) were detected with the data while band 3 did feature a rather large bias of ~2.6 K where GOES-14 pixels were warmer than the corresponding GOES-11 pixels.  This rather large bias may be a result of the very limited sample size of band 3 data.  MAE’s were around 3.0 K for bands 2 and 3 and a very large 6 K for band 4. RMSE compared favorably to it’s respective MAE on band 3 data while the RMSE’s for bands 2 and 4 data was nearly double their respective MAE’s.  This suggests numerous very large differences were observed between pixel temperatures of GOES-11 and GOES-14.

Since the performance statistics between GOES-11 and GOES-14 data featured much larger errors than what was observed between GOES-12 and GOES-14 data, a manual investigation was conducted to determine the source of the errors.  It was determined that many, if not all, of the large errors were due to rather significant navigational differences between GOES-11 and GOES-14 data.  An examination of land features surprisingly showed that GOES-11 data featured the superior navigation during these test time period.

Quantitative testing of GOES-14 while in GOES-East emulation yielded a nearly perfect correlation between pixel temperatures of GOES-12 and GOES-14.  Mean errors were generally within 1-2 K with little bias noted with the exception of band 6 data. Since the horizontal resolution of band 6 data is finer on GOES-14 Imager, it is believed that this may be explain part of the observed differences. Also, others have compared this band to high-spectral resolution co-located IASI and AIRS measurements and have shown a smaller bias than from GOES-12.

Quantitative testing of GOES-14 while in GOES-East emulation yielded a high degree of correlation between pixel temperatures of GOES-11 and GOES-14.  Despite the high degree of correlation, correlation coefficients were not nearly as high as what was observed between pixels of GOES-12 and GOES-14.  Mean errors were much higher than differences between GOES-12 and GOES-14, and were generally between 3-6 K.  Manual investigation of the data indicated that rather large navigational differences between GOES-11 and GOES-14 was the main contributor for the poor performance scores.

Figure 4.10a. Two-Dimensional smoothed histogram of GOES-12 Band 2 pixel temperatures (K) vs. GOES-14 Band 2 pixel temperatures

Figure 4.10b. Two-Dimensional smoothed histogram of GOES-12 Band 3 pixel temperatures (K) vs. GOES-14 Band 3 pixel temperatures (K)

Figure 4.10c. Two-Dimensional smoothed histogram of GOES-12 Band 4 pixel temperatures (K) vs. GOES-14 Band 4 pixel temperatures (K).

Figure 4.10d. Two-Dimensional smoothed histogram of GOES-12 Band 6 pixel temperatures (K) vs. GOES-14 Band 6 pixel temperatures (K)

Figure 4.11a. Two-Dimensional smoothed histogram of GOES-11 Band 2 pixel temperatures (K) vs. GOES-14 Band 2 pixel temperatures (K).

Figure 4.11b. Two-Dimensional smoothed histogram of GOES-11 Band 3 pixel temperatures (K) vs. GOES-14 Band 3 pixel temperatures (K).

Figure 4.11c. Two-Dimensional smoothed histogram of GOES-11 Band 4 pixel temperatures (K) vs. GOES-14 Band 4 pixel temperatures (K).

On 19 December 2006 GOES-13 was switched to the GOES-11 (GOES-west) schedule.  A comparison between the GOES-11 and GOES-13 Imagers at 0600 UTC that day revealed good agreement in brightness temperatures at the mid-point between the two satellites (0(N, 120(W) as shown in Table 4.11.  Comparisons were done for a 31 by 31 FOV box, where an average radiance is computed.  The band-3 difference of 3.3 K was due mostly to the differing SRFs; the brightness temperatures more closely agree when this is taken into account (to within approximately 0.7 K)

Table 4.11:  Imager-to-Imager Comparison Between GOES-11 and GOES-13

On 18 December 2006 GOES-13 was switched to the GOES-12 schedule.  A comparison between the GOES-12 and GOES-13 Imagers at 0545 UTC that day revealed mixed results in terms of agreement in brightness temperatures at the mid-point between the two satellites (0(N, 90(W) as shown in Table 4.12.  A night-time case was chosen so that the band-2 measurements would not be affected by differing solar reflections. Comparisons were done for a 31 by 31 FOV box, where an average radiance is computed.  The most unexpected result is the band-4 (10.7 (m) difference of 1.1 K.  It is possible that one of the satellites was not operating optimally during this comparison.  The next section discusses comparisons to a polar-orbiting instrument, which will provide another set of measurements to analyze the GOES-13 Imager radiance performance.

Table 4.12:  Imager-to-Imager Comparison Between GOES-12 and GOES-13

## Imager-to-Polar-Orbiter Comparisons

Data were collected during the checkout period near the GOES-14 sub-satellite point from the high spectral resolution Atmospheric InfraRed Sounder (AIRS), polar-orbiting on NASA’s Aqua satellite.  GOES-14 Imager data were collected within 30 minutes of polar-orbiter overpass time.  During the checkout period there were approximately 20 comparisons between GOES-14 and AIRS.  The methodology used was identical to that outlined in prior conference reports (Gunshor et al. 2006).  The results are presented in Table 4.13.  The mean brightness temperature difference for these comparisons show that GOES-14 is well calibrated based on the accuracy of AIRS measurements and that it compares favorably with similar results to operational GOES-12 and GOES-11.  Recall that the GOES-13 Imager initially had a very large bias in the 13.3 (m band.  This is not the case with GOES-14. The large Imager band-6 bias on GOES-13 was subsequently reduced when the SRF was updated.

Table 4.13:  Comparison of GOES-13 Imager to Atmospheric InfraRed Sounder (AIRS).  The Bias is the mean of the absolute values of the differences.

| Imager Band | Mean temperature differences (K) | Standard Deviations (K) | Number of cases |
| --- | --- | --- | --- |
| 2 | 0.14 | 0.31 | Shortwave Window band (9 night cases) |
| 3 | 0.81 | 0.22 | Water Vapor band (20 cases) |
| 4 | 0.31 | 0.37 | Longwave IR Window band (22 cases) |
| 6 | -0.53 | 0.33 | CO2 Absorption band (23 cases) |

The GOES-14 Imager/Sounder IR radiometric calibration accuracy was evaluated with the GSICS GEO-LEO baseline algorithm (Wu, 2009).  During the GOES-14 PLT test, GOES-14 IR channel data were inter-calibrated with two hyperspectral instruments on Low Earth Orbit (LEO), Atmospheric Infrared Sounder (AIRS) and Infrared Atmospheric Sounding Interferometer (IASI).  The broad-band GOES simulated radiance is spectrally convoluted with the AIRS/IASI spectral radiances over the GOES spectral response function:

(4)

where RLEO is the simulated GOES measurement from AIRS/IASI radiances, R( is AIRS/IASI radiance at wavenumber (, and Φ( is GOES spectral response at wavenumber (.  As shown in Figure 4.12, AIRS has the problem with missing spectral gap and unstable or dead detectors. JMA’s gap-filling method is applied to compensate the missing radiance (Tahara and Kato, 2009).  The brightness temperature difference between the instruments were monitored over the homogeneous collocated GEO-LEO pixels during the test period and available at http://www.star.nesdis.noaa.gov/smcd/spb/fwu/homepage/GSICS_GOES14_ AIRS_IASI.php.

Figure 4.12. Spectral response function of GOES-14 Imager(left) and Sounder(right), together with the AIRS/IASI spectra.

Two sets of GEO-LEO inter-calibration data, based on the daytime and nighttime collocation pixels, are used to evaluate the Imager IR radiometric calibration accuracy.  Both inter-calibrations yielded very similar results in Table 4.14.  Note that during the GOES-14 PLT test, the Imager SRFs were updated on November 24, 2009 with Revision E version and the new SRFs have been operated even since.   These mean brightness temperature (Tb) difference listed in Table 5 are calculated with the homogeneous collocation pixels after Nov. 24, 2009.  Unlike GOES-12 which has very small GEO-LEO Tb difference at the water vapor channel (6.5(m), both the GOES-AIRS and GOES-IASI inter-calibration results indicated large and consistent bias (~1K) for the GOES-14 water vapor channel.  Compared to the large Tb bias at the GOES-13 PLT test, GOES-14 has a smaller Tb difference (-0.5K) for 13.3(m channel (Gushor et al. 2009, Wu et al. 2009).  The shortwave channel (3.8(m) had large Tb difference at daytime.  This may be due to the bi-directional reflectance distribution function (BRDF) effect of solar reflectance.  As shown in Figure 4.15 and 4.15, the Tb difference is consistent over the study period.

Table 4.14.  Brightness temperature (Tb) biases between GOES-14 Imager and AIRS/IASI for the daytime collocated pixels and the double difference between AIRS and IASI through GOES-14 Imager daytime collocation data.  The Tb biases between GOES-14 and IASI over the night time (9:30pm) collocated pixels are also compared.   The Tb biases were based on the collocated pixels acquired after Nov. 24, 2009.

| Band # | Central wavelength (μm) | day-time (K) | night-time (K) |
| --- | --- | --- | --- |
|  |  | GOES-AIRS | GOES-IASI | (GOES-AIRS) – (GOES-IASI) | GOES-IASI (9:30pm) |
| 2 | 3.9 | -1.31(±2.13) | -1.24(±1.09) | -0.094(±2.58) | -0.01(±0.04) |
| 3 | 6.5 | 0.99(±0.12) | 0.97(±0.08) | -0.096(±0.11) | 0.77(±0.11) |
| 4 | 10.7 | 0.28(±0.20) | 0.02(±0.18) | -0.31(±0.34) | 0.07(±0.11) |
| 6 | 13.3 | -0.48(±0.13) | -0.55(±0.12) | -0.1(±0.18) | -0.59(±0.20) |

Figure 4.13. GOES-14 Imager and AIRS/IASI inter-calibration for the daytime.

The effect of the change in SRF was evaluated with GOES-IASI inter-calibration at the night-time (9:30pm) collocation pixels.  As shown in Figure 4.14, update changed brightness temperature (Tb) by -18mK, -64mK, +96mK, and +130mK for the 3.9μm, 6.5μm, 10.7μm, and 13.3μm channels, respectively. The update changed the sign, but not much of the magnitude, of bias for the window channels, and slightly reduced the Tb bias.

Figure 4.14. The Tb bias between GOES-14 and IASI Tb bias over the night-time (9:30pm) collocated pixels.

The GOES-14 Sounder radiometric calibration accuracy was also evaluated with the GSICS GEO-LEO baseline inter-calibration algorithm.  Results presented in Table 4.15 and Figure 4.15 indicate that GOES-14 Sounder is well calibrated, with bias less than 0.2K for most channels (all less than 0.3K) when compared with AIRS and IASI. This is remarkable in view that GOES-11/12 Sounders have large bias, up to 8K, for some of its shortwave channels (e.g., Channel 15). Also noted is that the standard deviation for Channel 1 is less than 0.2K. This value is an indirect estimate of this channel’s noise, which has been 1-2K for current and earlier GOES.

Table 4.15. GOES-14 Sounder IR vs. IASI brightness temperature difference at night-time, compared to those of GOES-11/12 Sounder.  The data in the parenthesis is the standard deviation of the Tb difference at the collocation pixels.

| Ch# | Central wavelength | GOES-14 Mean (±stdv) K | GOES-12 Mean (±stdv) K | GOES-11 Mean (±stdv) (K) |
| --- | --- | --- | --- | --- |
| 1 | 14.71µm | 0.274(±0.195) | -0.006(±0.233) | -0.023±0.230 |
| 2 | 14.37µm | 0.127(±0.245) | 0.078(±0.197) | 0.140±0.207 |
| 3 | 14.06µm | 0.103(±0.610) | 0.180(±0.739) | 0.318(±0.966) |
| 4 | 13.64µm | 0.208(±0.917) | -0.258(±1.373) | 0.151(±1.148) |
| 5 | 13.37µm | 0.041(±1.159) | 0.313(±1.837) | -1.765(±1.399) |
| 6 | 12.66µm | 0.106(±1.601) | -0.160(±2.094) | -0.081(±1.968) |
| 7 | 12.02µm | -0.041(±1.575) | -0.086(±2.068) | 0.178(±2.200) |
| 8 | 11.03µm | -0.067(±1.363) | -0.109(±1.906) | -0.034(±1.576) |
| 9 | 9.71µm | 0.076(±0.838) | -0.055(±1.366) | 0.009(±1.551) |
| 10 | 7.43µm | -0.040(±0.747) | -0.328(±1.088) | 0.235(±0.676) |
| 11 | 7.02µm | -0.121(±0.574) | -0.119(±0.994) | 0.178(±0.510) |
| 12 | 6.51µm | -0.178(±0.438) | -0.236(±0.680) | -0.056(±0.535) |
| 13 | 4.57µm | 0.263(±0.506) | -0.883(±1.052) | -0.031(±0.808) |
| 14 | 4.52µm | -0.049(±0.341) | -0.499(±0.936) | 0.232(±1.124) |
| 15 | 4.45µm | 0.144(±0.506) | -5.076(±2.766) | -4.578(±1.568) |
| 16 | 4.13µm | 0.076(±0.517) | 0.304(±1.283) | 0.258(±0.874) |
| 17 | 3.98µm | -0.116(±0.648) | 0.106(±1.529) | 0.153(±0.842) |

Figure 4.15.  Mean and standard deviation of GOES-11/12/14 Sounder brightness temperature difference from nighttime IASI data in December, 2009.

## Stray Light Analysis

By supplying data through the eclipse periods, the GOES-N/O/P system addresses one of the major current limitations which are eclipse and related outages.  This is possible due to larger spacecraft batteries.  Outages due to Keep Out Zones (KOZ) will be minimized.  See Figure 4.16 for images from 1 October 2009 comparing GOES-14 to GOES-12 through an eclipse time.

With the new capability of data during previous outages, comes the risk of allowing images contaminated with energy of the sun to be produced.  Of course an image with artificial brightness temperature excursions up to 75 K (e.g. band 2) may affect products. To determine how much good data can be acquired, at the same time minimizing the amount of bad data, many scans were conducted during the eclipse period during 2009.

All the Imager bands can be affected.  Of course the visible and shortwave bands (2) are affected the most.  There are investigations to possibility correcting these images with stray light.

Figure 4.16.  GOES-12 and GOES-14 Imager (top panel) and GOES-14 band 2 (lower panel) from 21 September 2009. Note the large stray radiation from the sun.

In general, the GOES Sounder can be affected even more during the KOZ periods, due to the relatively slow sounder scanning (not shown).

## Instrument Performance Monitoring

During the GOES-14 post-launch test (PLT) period, a new version of GOES Instrument Performance Monitoring (IPM) system was implemented to track the stability and noise of the sensor parameters that affect the instrument calibration, The GOES IPM system uses the near real-time GOES Variable Format (GVAR) Block 11 (B11) data routinely downloaded from NOAA Comprehensive Large Array-data Stewardship System data source.  Four types of calibrated related parameters are ingested from the GVAR B11 data, including the instrument telemetry data, infrared (IR) calibration coefficients, statistics of space look and blackbody scan data.  Instrument noise, such as noise equivalent radiance difference (NEdN) and noise equivalent temperature difference (NEdT) are also monitored for each detector.  To detect any potential calibration anomaly, all these monitored parameters are displayed at various temporal scales for diurnal to long-term variations.  Note that although the GOES-PLT test period started from November 30, 2009 through January 4, 2010, GOES-14 continued to transmit the data until January 19; when it was placed into storage.  The GOES-14 data analyzed in this study therefore ranges from the beginning of the PLT period to January 19 2010.  During this period, the monitoring results were daily updated at the GOES-14 IPM webpages at:

- http://www.star.nesdis.noaa.gov/smcd/spb/fwu/homepage/GOES14_Imager_IPM.php

- http://www.star.nesdis.noaa.gov/smcd/spb/fwu/homepage/GOES14_Sounder_IPM.php

4.8.1 Telemetry monitoring

About 14 Imager telemetry variables and 16 Sounder telemetry variables were under monitoring at the GOES-14 IPM system.  Table 4-16 lists the name of the telemetry variables and the number of its detectors.  Most of the telemetry detectors have apparent diurnal variations.  But no significant change with telemetry data was observed during the GOES-14 PLT test period.  Figure 4.17 displays the 8 PRT temperature data embedded at GOES-14 the Imager and Sounder blackbodies (BBs).  The BB temperature, together with the other telemetry temperature data, clearly displays the heating of the instrument surface around the midnight when the Sun is above the equator (John and Weinreb, 1996).   However, due to the inhomogeneous heating attributes within the satellite, the detectors are not simultaneously warming up or cooling down.  While the lowest BB temperature is relatively consistent every day, there are some variations with the daily peak temperature, which may be the resulted from the sun-earth-satellite position changes.   Similar patterns are also observed at the GOES-11/12/13 IPM system.

Table 4-16. Telemetry variables.

|  | Telemetry variables | #Detector (Imager) | #Detector (Sounder) |
| --- | --- | --- | --- |
| 1 | Electronics Temperature | 2 | 2 |
| 2 | Sensor Assy Baseplate temperature | 6 | 6 |
| 3 | BB Target Temperature | 8 | 8 |
| 4 | Scan mirror temperature | 1 | 1 |
| 5 | Telescope Primary Temperature | 1 | 1 |
| 6 | Telescope Secondary Temperature | 2 | 2 |
| 7 | Telescope Baffle Temperature | 2 | 2 |
| 8 | Aft Optics Temperature | 1 | 1 |
| 9 | Cooler Radiator Temperature | 1 | 1 |
| 10 | Wide Range IR Detector Temperature | 1 | 1 |
| 11 | Narrow Range IR Detector Temperature | 1 | 1 |
| 12 | Filter Wheel Housing Temperature | X | 1 |
| 13 | Filter Wheel Control Heater Voltage | X | 1 |
| 14 | Patch Control Voltage | 1 | 1 |
| 15 | Instrument Current | 1 | 1 |
| 16 | Cooler-Housing Temperature | 1 | 1 |

Figure 4.17. Monitoring of GOES-14 Imager and Sounder PRT temperature data.  The top panels are 2 consecutive day observation data, the middle ones are for 10-day data, and the bottom one is the mean of the 8 detectors over the PLT period, from Nov. 30, 2009 through Jan. 19, 2010.

4.8.2 IR Calibration coefficients monitoring

The GOES IPM system monitors the calibration slope (first-order gain) and bias values at 30m and 20m time interval for the Imager and Sounder instruments, respectively, according to its calibration procedure (Weinreb et al., 1997).   The second-order parameters are not under monitoring because the fixed pre-launch second-order calibration coefficients are used for non-linear correction for all the IR channels.  Similar to the GOES-11/12, the calibration slopes and biases have the diurnal variations with some difference in between the detectors at each IR channel.  This is due to the difference in the detector characteristics and the inhomogenous instrument heating patterns (Figure 4-18).  However,  during the GOES-14 PLT period,  discontinuity in the both time-series of calibration slope and bias for the GOES-14 Sounder mid-wave and short-wave IR channels are observed around the around 1800Z, the telemetry house-keeping time everyday (Figure 4-18).

Figure 4-18. Monitoring of the first-order gain and the bias values for GOES-14 Imager GOES-14 Sounder Channel 8 (11.03µm).  A sudden disruption of the slope values can be observed around 1800Z at the two-day observation panel for the GOES-14 Sounder data.

4.8.3 Monitoring of space look (SPLK) statistics

The Imager space-look monitoring includes mean of filtered space-look data and its variance at pre-clamp and post-clamp for each detector at each channel.  The Sounder space-look statistics include the mean filtered space look and the variance.

The issue with GOES-14 Imager SPLK monitoring is the frequent ZERO data for the mean filtered pre-clamp space-look data at the GVAR B11 files (Figure 4-19).  This ZERO GVAR data are not observed at GOES-11/12 Imager SPLK data, but appear at GOES-13 Imager pre-clamp space-look data too.  Communications with the scientist at NOAA Satellite Operation Control Center (SOCC) pointed out that these ZERO mean filtered pre-clamp SPLK data is caused with the “idle” space-looks at 9.2-sec intervals and does not affect the calibration accuracy (Weinreb and Mitchell, 2010).

The issue with the GOES-14 Sounder SPLK data is that The GOES-14 Sounder SPLK has the sudden change around the 18:00Z, the telemetry house-keeping time for the short-wave and long-wave IR channels (Figure 4-20).  The concurrence with the sudden changes in the Sounder IR calibration coefficients are later found to relate with the GOES-14 Sounder loose-len problem.

Figure 4-19.  Monitoring of mean filtered pre-clamp space-look data for GOES-14 Imager channel 3 (6.5µm).  The zero values happen periodically for the two detectors at the same time period everyday.

Figure 4-20. Monitoring of GOES-14 Sounder space look data for Channel 14 (4.57µm).

4.8.4 Monitoring of blackbody (BB) scan statistics

The Imager/Sounder blackbody data are monitored with the mean filtered blackbody values and the corresponding variance for each detector of each IR channel.  No significant trending of the blackbody data is found during the GOES-14 PLT test.  The diurnal variations of the BB data are comparable with those of GOES-11/12/13.  The GOES-11/12/13 IPM are available at the following web-pages.

- http://www.star.nesdis.noaa.gov/smcd/spb/fwu/homepage/GOES11_Imager_IPM.php

- http://www.star.nesdis.noaa.gov/smcd/spb/fwu/homepage/GOES12_Imager_IPM.php

- http://www.star.nesdis.noaa.gov/smcd/spb/fwu/homepage/GOES13_Imager_IPM.php

- http://www.star.nesdis.noaa.gov/smcd/spb/fwu/homepage/GOES11_Sounder_IPM.php

- http://www.star.nesdis.noaa.gov/smcd/spb/fwu/homepage/GOES12_Sounder_IPM.php

- http://www.star.nesdis.noaa.gov/smcd/spb/fwu/homepage/GOES13_Sounder_IPM.php

Figure 4-21.  GOES-14 Sounder Channel 15 (4.45μm) mean filtered BB data.  The discontinuity in the BB data is also observed at GOES-11/12 Imager BB data monitoring systems, which is related to scan angle effect of scan mirror emissivity at changes in eastern/western clamp position.

4.8.5 Initial post-launch calibration for the Imager visible channel

The visible channels of GOES-14 Imager experience continuous degradation once commissioned in orbit.   A post-launch calibration method has been developed to correct for such degradation using the collocated cloud pixels of GOES-14 and Terra Moderate Resolution Imaging Spectroradiometer (MODIS) Band 1 data (Wu and Sun 2004).

Rpost = Rpre * C1

Where Rpost is the post-launch calibration reflectance/radiance for GOES-14 Imager visible channel; Rpre is the pre-launch calibration reflectance/radiance; and C1 is the correction factor, C1 = 1.0695.  This result was derived based on the collocated GOES-14 and Terra MODIS pixels acquired on Y09D357.

## Finer GOES-14 Imager band 6 (13.3 µm)

The improved (4 km) spatial resolution of 13.3 µm band required changes to GVAR format. Several issues with implementing the new GVAR format were discovered, communicated, rectified, and verified. The image below demonstrated the improved spatial resolution of this band on the GOES-14 imager. This is also the case with the GOES-15 imager.

Figure 4-22.  Improved Imager spatial resolution at 13.3 µm for GOES-14 (right panel) compared to GOES-12 (left panel) from 26 August 2009.

# Product Validation

A number of products were generated with data from the GOES-13 instruments and then compared to products generated from other satellites or ground-based measurements.  Products derived from the Sounder and described below are Total Precipitable Water (TPW), Lifted Index (LI), Clouds products, and Atmospheric Motion Vectors.  The products derived from the Imager are Clouds, Atmospheric Motion Vectors, Clear Sky Brightness Temperature (CSBT), Sea Surface Temperature (SST), and Fire Detection.

## Total Precipitable Water (TPW) from Sounder

### Validation of Precipitable Water (PW) Retrievals from the GOES-14 Sounder

GOES-14 retrievals of precipitable water were validated against radiosonde observations of precipitable water for the period 30 November 2009 to 4 January 2010.  To achieve this, GOES-14 retrievals were collocated in space (within 11 km) and time (within 30 minutes) to daily radiosonde observations at 0000 UTC and 1200 UTC.  At the same time, these GOES-14 retrievals were collocated in space (within 11 km) and time (within 60 minutes) to GOES-12 retrievals.  The relative performance of the GOES-14 PW retrievals, GOES-12 PW retrievals, and first guess PW supplied to the retrieval algorithm could then be compared since all of these PW values were collocated to the same radiosonde observation.  Table 5.1 provides a summary of these statistics for the Total Precipitable Water (TPW) and the PW at three layers (Sfc-900 hPa; 900-700 hPa, and 700-300 hPa).  The statistics indicate that the quality of the GOES-14 Sounder PW retrievals compare very well to the quality of the operational GOES-12 PW retrievals.  It should be remembered that the GOES-14 retrievals used a GOES-12 dataset for the radiance bias adjustment for initial processing.

Table 5.1:  Verification statistics between GOES-12 and GOES-14 retrieved precipitable water, first guess (GFS) precipitable water, and radiosonde observations of precipitable water for the period 30 November 2009 to 4 January 2010.

| Statistic | GOES-12/RAOB | GOES-14/RAOB | GUESS/RAOB | RAOB |
| --- | --- | --- | --- | --- |
| Total Precipitable Water |
| RMS (mm) | 2.31 | 2.46 | 2.64 |  |
| Bias (mm) | -0.18 | -0.10 | -0.06 |  |
| Correlation | 0.98 | 0.97 | 0.97 |  |
| Mean (mm) | 11.24 | 11.32 | 11.36 | 11.42 |
| Sample | 3677 | 3677 | 3677 | 3677 |
| Layer Precipitable Water (surface to 900 hPa) |
| RMS (mm) | 1.04 | 1.01 | 1.03 |  |
| Bias (mm) | -0.45 | -0.42 | -0.43 |  |
| Correlation | 0.98 | 0.98 | 0.98 |  |
| Mean (mm) | 4.03 | 4.07 | 4.06 | 4.49 |
| Layer Precipitable Water (900 hPa to 700 hPa) |
| RMS (mm) | 1.27 | 1.37 | 1.39 |  |
| Bias (mm) | -0.12 | -0.06 | -0.02 |  |
| Correlation | 0.96 | 0.96 | 0.96 |  |
| Mean (mm) | 4.85 | 4.91 | 4.95 | 4.97 |
| Layer Precipitable Water (700 hPa to 300 hPa) |
| RMS (mm) | 1.27 | 1.26 | 1.36 |  |
| Bias (mm) | 0.37 | 0.35 | 0.36 |  |
| Correlation | 0.83 | 0.82 | 0.81 |  |
| Mean (mm) | 2.30 | 2.28 | 2.28 | 1.93 |

Figures 5.1 through Figure 5.4 present time series of various comparison statistics (GOES retrieved TPW vs. radiosonde observed TPW) for GOES-14 (in green with open circles) and GOES-12 (in red with filled circles) for the same time period (30 November 2009 to 4 January 2010) as in Table 5.1.  Each tick mark represents a data point (2 points per day) with the calendar day label centered at 0000 UTC of that day.  A majority of the GOES-14 data points are very close to, if not on top of, the GOES-12 data points.

Figure 5.1:  Time series of Root Mean Square Error (RMSE) between GOES-12 and GOES-14 retrieved precipitable water and radiosonde observation of precipitable water over the period 30 November 2006 to 4 January 2010.

Figure 5.2:  Time series of Bias (GOES-radiosonde) between GOES-12 and GOES-14 retrieved precipitable water and radiosonde observation of precipitable water over the period 30 November 2009 to 4 January 2010.

Figure 5.3:  Time series of correlation between GOES-12 and GOES-14 retrieved precipitable water and radiosonde observation of precipitable water over the period 30 November 2009 to 4 January 2010.

Figure 5.4:  Time series of the number of collocations between GOES-12 and GOES-14 retrieved precipitable water and radiosonde observation of precipitable water over the period 30 November 2009 to 4 January 2010.

--------------------------------------------------------------

Total precipitable water retrievals (displayed in the form of an image) for GOES-12 and GOES-13 are presented in Figure 5.5 over the same area at approximately the same time (4 December 2009).  These retrievals are generated for each clear radiance Field-Of-View (FOV).  Radiosonde measurements of TPW are plotted on top of the images.  Qualitatively, there is good agreement between the GOES-12 and GOES-14 TPW retrievals that, in turn, compare reasonably well with the reported radiosonde measurements of TPW.  When comparing measurements from two satellites, one must consider the different satellite orbital locations; even precisely co-located fields-of-view are seen through different atmospheric paths.

Figure 5.5:  GOES-14 (top panel) and GOES-11/12 (lower panel) retrieved to TPW (mm) from the Sounder displayed as an image.  The data are from 00 UTC on 4 December 2009.  Measurements from radiosondes are overlaid as white text; cloudy FOVs are denoted as shades of gray.

???????????

Figure 5.6:  GOES-14 Sounder retrieved TPW with the via two retrieval algorithms.

## Lifted Index (LI) from Sounder

The lifted index (LI) product is generated from the retrieved temperature and water vapor profiles (Ma et al. 1999) that are generated from clear radiances for each FOV.  Figure 5.7 shows lifted index retrievals (displayed in the form of an image) for GOES-12 and GOES-14 over the same area at approximately the same time, showing no discernable bias in the LI values.  Of course the overall large (stable) LI values also illustrates that ideally satellite post-launch check-outs should be conducted in seasons with more atmospheric moisture/instability.

<insert figure>

Figure 5.7:  GOES-13 (top panel) and GOES-12 (lower panel) retrieved Lifted Index (LI)  from the Sounder displayed as an image.  The data are from 1146 UTC on 13 December 2006. Radiosonde values are over-plotted.

## Cloud Parameters from Sounder and Imager

The presence of the 13 µm band on the GOES-14 Imager, similar to the GOES-12 Imager, makes near full-disk cloud products possible.  This product complements that from the GOES Sounders.

Figures 5.8 and 5.9 shows a comparison of GOES-14 Imager (and Sounder) cloud-top pressure derived product images from late 2009. Note the improved coverage of the Imager-based product. Another comparison between GOES-14 and GOES-12 Sounders showed generally good correlations.

Figure 5.8:  GOES-14 Imager cloud-top pressure from 11 November 2009 starting at 17:45 UTC.

Figure 5.9:  GOES-14 Sounder cloud-top pressure from 11 November 2009 starting at 17:45 UTC. The sounder data has been remapped into the GOES-14 Imager projection.

Figure 5.10:  GOES-12 cloud top pressure from the Sounder from 1746 UTC on 10 September 2009.

Figure 5.11:  GOES-14 cloud-top pressure from the Sounder from the nominal 1746 UTC on 10 September 2009.

Figure 5.12:  GOES-14 Sounder visible image from the nominal 1746 UTC on 10 September 2009.

## Atmospheric Motion Vectors (AMVs) from the Imager

Atmospheric Motion Vectors (AMVs) from GOES are derived using a sequence of three images. Features targeted in the middle image (cirrus cloud edges, gradients in water vapor, small cumulus clouds, etc.) are tracked from the middle image back to the first image, and forward to the third image, thereby yielding two displacement vectors. These vectors are averaged to give the final wind vector, or AMV. This report summarizes the quality of AMVs from GOES-14 as part of the Post Launch Science Test (PLST) in late 2009.

The varied imaging schedules activated during the GOES-14 Science Test provided an opportunity to run AMV assessments for what are currently considered operational as well as special case scenarios. Thinned (for display clarity) samples of AMVs from GOES-14 on 1/7/2010 at 10:45Z are shown for Cloud-Drift (Figure 5.13) and Water Vapor (Figure 5.14) AMVs.

Figure 5.13:  GOES-14 NHEM Cloud Drift AMV 1/7/2010, 10:45UTC

Figure 5.14:  GOES-14 NHEM Water Vapor AMV 1/7/2010, 10:45UTC

During the PLST objective statistical comparisons were made using collocated radiosonde (RAOB) data matched to the various GOES-14 AMVs. Table 5.2 shows the results of these GOES vs. RAOB match statistics.

Table 5.2:  Verification statistics for GOES-14 vs. RAOB Match Verification Statistics

NHEM winds (in m/s): 11/30/2009 – 1/16/2010

| NHEM | RMS | MVD | Std Dev | Speed Bias | Mean Speed (Sat) | Mean Speed (RAOB) | Sample Size |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Cloud-Drift | 6.61 | 5.27 | 3.98 | -0.92 | 23.06 | 23.99 | 6897 |
| Water Vapor | 7.19 | 5.89 | 4.12 | -0.37 | 27.11 | 27.48 | 14203 |
| Short Wave IR | 4.71 | 3.98 | 2.52 | -1.32 | 8.77 | 10.10 | 4338 |
| VIS | 6.29 | 5.52 | 3.01 | 1.75 | 10.23 | 8.48 | 214* |

*Note: Visible AMV sample sizes were limited due to limited daylight hours at RAOB valid times

Comparison statistics were also generated for collocated GOES-12 and GOES-14 AMV data sets with RAOB observations. To be considered in the statistical evaluation, the respective GOES AMVs had to be within 1/10 degree horizontal and 25 hPa vertical. The small differences confirm that the AMV products from GOES-14 are at least comparable in quality with the existing GOES-12 operational AMVs.

Table 5.3:  Verification statistics for GOES-12 and GOES-14, collocated (0.1 deg, 25 hPa) RAOB

Match Verification Statistics for NHEM winds (in m/s): 11/30/2009 – 1/16/2010

| NHEM | RMS | MVD | Std Dev | Speed Bias | Mean Speed (Sat) | Mean Speed (RAOB) | Sample Size |
| --- | --- | --- | --- | --- | --- | --- | --- |
| GOES-12 Cloud-Drift | 5.53 | 4.45 | 3.29 | -0.85 | 19.92 | 20.75 | 337 |
| GOES-14 Cloud- Drift | 5.69 | 4.48 | 3.51 | -1.03 | 19.77 | 20.82 | 337 |
| GOES-12 Water Vapor | 6.57 | 5.51 | 3.59 | -0.21 | 29.21 | 29.41 | 791 |
| GOES-14 Water Vapor | 6.60 | 5.47 | 3.68 | -0.50 | 28.93 | 29.42 | 791 |
| GOES-12 Short Wave IR | 3.98 | 3.55 | 1.81 | 1.07 | 8.26 | 7.17 | 40 |
| GOES-14 Short Wave IR | 4.13 | 3.64 | 1.95 | 1.14 | 8.43 | 7.26 | 40 |
| GOES-12 Visible | 6.61 | 5.52 | 3.64 | 0.85 | 10.19 | 9.36 | 24* |
| GOES-14 Visible | 5.95 | 5.11 | 3.05 | 0.98 | 10.32 | 9.35 | 24* |

*Note: Visible AMV sample sizes were limited due to limited daylight hours at RAOB valid times

-------------------------------------------------

In addition, normally an image navigation correction is attempted before the wind generation.  Basically, the second and third images are corrected to the first image.  As a test, this was needed for GOES-12 in 3 of the 18 cases, yet it was not needed in any of the GOES-14 cases.  This is an indication that GOES-14 image registration is improved.

## Clear Sky Brightness Temperature (CSBT) from Imager

The GOES-14 Imager Clear Sky Brightness Temperatures (CSBT) product was generated.  This product spatially averages the clear fields of view for use in global numerical weather prediction (NWP) applications.  In general, there is fair agreement between the GOES-11, GOES-12 and GOES-14.  The CSBT can be used to initialize global numerical models.

A sample GOES-12 Imager Clear Sky Brightness Temperature cloud mask image was generated and is shown in Figure 5.15.

Figure 5.15:  GOES-11 (top panel), GOES-14 (middle panel) and GOES-14 (lower panel) Imager Clear-Sky Brightness Temperature cloud mask from 1400 UTC on 06 January 2010. Each image is shown in the GOES-14 satellite projection.

## Sea Surface Temperature (SST) from Imager

GOES-13 Imager data were collected for both the north and south hemispheric sectors every half hour from 8 December 2006 to 5 January 2007 for use as input for Sea Surface Temperature (SST) retrievals.  The north hemispheric sector is centered at latitude 14°19′53″ N, longitude 96°40′17″ W; the south hemispheric sector is centered at latitude 31°55′10″ S, longitude 96°06′36″ W.  Pre-processed visible and IR imagery data were used to create multi-spectral imagery files as input of SST retrieval.  Examples of the radiance imagery are shown in Figure 5.16.

Figure 5.16:  Radiance imagery: GOES-13 north sector band-2 (upper-left); GOES-13 north sector band-4 (upper-right); GOES-13 south sector band-2 (lower-left); GOES-13 south sector band-4 (lower-right).

### SST Generation

GOES-13 SST coefficients were generated for all possible locations of the GOES-13 satellite (75°W, 105°W, and 135°W).  The GOES-13 Community Radiative Transfer Model (CRTM) spectral and transmittance coefficients were acquired.  Radiative-transfer-based SST retrieval algorithms are used to generate the GOES-13 SST retrievals.  The form of the current GOES operational SST equation is:

where i is GOES-Imager band number (2, 4, 6), S = sec (satellite zenith angle) – 1

Ti is band brightness temperature (K).

SST retrievals were generated for dual and triple window.  The Radiative Transfer Model (RTM) coefficients for dual window (3.9 µm and 11 µm) and triple window (3.9 µm, 11 µm and 13 µm) were applied.  The GOES-13 SST coefficients for 105°W was used for the algorithm generation.  Then a Bayesian Cloud Mask was applied to obtain clear sky pixels.  Bayes’ theorem applied to estimate the probability of a particular pixel being clear of cloud given the satellite-observed brightness temperatures, a measure of local texture and band brightness temperatures calculated for the given location and view angle using NCEP GFS surface and upper air data and the CRTM fast radiative transfer model.  The method is described in detail in a paper by Merchant et al. (2005).

Hourly SST is created by compositing three half hour SST McIDAS Area files with an applied threshold of ≥98% clear sky probability.  Satellite retrieval SST was matched with Buoy and NCEP GDAS data to create match-up dataset for validation.  Example of the GOES-13 SST imagery is shown in Figure 5.17.

Figure 5.17:  GOES-13 SST Imagery (Hourly SST composite with applied 98% clear sky probability (left) and hourly composite clear sky probability)

### SST Validation

The comparison of GOES-13 SST with operational GOES-12 SST was performed.  Figure 5.18 shows the operational GOES-12 SST validation.  Figure 5.19 shows the GOES-13 SST dual-window validation.  Figure 5.20 shows the GOES-SST triple-window validation.  There are a warm cluster of points where Buoy SST is ~24°C and Satellite SST is ~29°C.  Figure 5.21 shows daytime scatter plots.  The angular dependence is reduced with triple-window algorithm, also change in Y-scale for RH plot.  Figure 5.22 shows nighttime scatter plots.  Since the 13.3 µm band is a lower-tropospheric sounding band, its use at angles above 65° – 70° is inevitably going to be compromised (as shown in the right panel).  This increase in warm bias is responsible for the cluster of points noted previously.

Figure 5.18:  GOES-12 SST retrievals vs. Buoys

Figure 5.19:  GOES-13 SST dual window vs. Buoy SST

Figure 5.20:  GOES-13 SST triple-window vs. Buoy SST.

Figure 5.21:  GOES-13 Day scatter plots of Satellite – Buoy SST vs. Satellite Zenith Angle for dual window (left) and triple window (right).

Figure 5.22:  GOES-13 Nighttime scatter plots of Satellite – Buoy SST vs. Satellite Zenith Angle for dual window (left) and triple window (right).

Figure 5.23:  Comparisons of GOES-12 SST Imagery with the GOES-13 SST Dual Window and Triple Window for 3 and 4 January 2007.

### SST Summary

The GOES-13 SST appears noisier than the GOES-12 SSTs.  This may be partially due to the unfavorable view angle conditions for the validation data.  The GOES-13 nighttime SST results suggest that 3.9 µm and 11 µm radiances are unbiased compared to the model used to generate the retrieval coefficients.  The daytime solar correction appears to be over compensating the 3.9 μm band effects, especially at high satellite angles (colder SSTs).  There may be a radiance bias issue in the 13 µm, which happens to compensate for the over-correction of solar contamination – the daytime triple probably looks good because of two opposing biases that occur at high satellite zenith angles.  Comparison of the dual window and triple night time plots also suggests that there is some residual cloud that affects the 13 µm band severely but not the 3.9 µm or 11 µm – e.g., thin cirrus.  This means that the night-time triple retrieval should not be introduced at night time until the 13 µm is also incorporated into the cloud screening information vector.

In light of the above results, the triple window should be applied in the day.  Thin cirrus clouds are more likely to be caught when the visible (band-1) is available.

## Fire Detection

Basic fire detection relies primarily on shortwave window (3.9 µm, band-2) data from the GOES Imager.  This band, along with the IR window (11 µm, band-4), provides the basis for locating the fire and other information aids in estimating the sub-pixel fire size and temperature.  The number of fires that can be successfully detected and characterized is related to the saturation temperature, or upper limit of the observed brightness temperatures, in the 3.9 µm band.  A higher saturation temperature is preferable as it affords a greater opportunity to identify and estimate sub-pixel fire size and temperature. That said, the maximum saturation temperature should still be low enough to the transmitted via the GVAR data stream. Low saturation temperatures can result in the inability to distinguish fires from a hot background in places where the observed brightness temperature meets or exceeds the saturation temperature.

A comparison of GOES-11 (GOES West), GOES-14, and GOES-12 (GOES East) 3.9 µm shortwave IR images (above)  indicated that there were a number of fires burning across parts of southern British Columbia, Canada on 01 December 2009, as confirmed by the NOAA Hazard Mapping System. The 3 sets of images are displayed in the native projection of their respective satellites. The fire “hotspots” showed up as warmer (darker black enhancement) pixels.

The plot below shows that the warmest 3.9 µm IR brightness temperature on the GOES-14 imagery was 325.8º K at 22:15 UTC, compared to 317.7º K on GOES-11 at 20:15 and 304.9º K on GOES-12 at 19:45 UTC. This difference in maximum fire pixel brightness temperature and time was due to such factors as different satellite viewing angles (compounded by the steep slopes of the mountainous terrain) and possible brief obscuration by clouds and/or smoke. More information on this case can be found at: http://cimss.ssec.wisc.edu/goes/blog/archives/4053

Figure 5.24:  GOES Imager 3.9 µm images from GOES-11 (left panel), GOES-14 (center panel) and GOES-12 (right panel). Each satellite is shown in its native perspective.

Figure 5.25:  GOES Imager 3.9 µm time series from GOES-11, GOES-12 and GOES-14.

The GOES-14 Imager 3.9 µm band has a saturation temperature of approximately 338.5 K.  For reference, the GOES-12 Imager 3.9 µm band has a saturation temperature of approximately 336 K, although this value has changed over time, peaking at approximately 342K.

Preliminary indications are that GOES-14 is performing comparably to GOES-11 and GOES-12.

The Biomass Burning team at CIMSS currently produces fire products for GOES-11/12 covering North and South America.  These data can be viewed at the Wildfire Automated Biomass Burning Algorithm (http://cimss.ssec.wisc.edu/goes/burn/wfabba.html).

## Volcanic Ash Detection

There were several times that volcanic ash was able to be seen by both GOES-12 and GOES-14; for example, on December 15 and again on December 30. On both occasions the ash signature in visible and multispectral imagery showed up better in GOES-14 imagery than in GOES-12 imagery. For the multispectral imagery, there seems to be a better alignment between the channels used to produce the imagery using GOES-14 than when using GOES-12. With GOES-12, there was a distinct "venetian blind" or striping effect to the imagery making it harder to detect the ash. In GOES-14 multispectral imagery there was much less striping resulting in an improvement for ash detection.

Another case is from the Galeras volcano in Colombia (located in the Andes Mountains near Colombia’s border with Ecuador) which experienced an explosive eruption around 00:43 UTC on 03 January 2010 (Figure 5.27).

Volcanic ash detection from GOES-14 should be comparable or slightly improved (due to the improved SNR) compared to GOES-12.  With operations through the eclipse periods, there is the potential for capturing additional events.

Figure 5.27:  GOES-11, GOES-14, and GOES-12 10.7 µm IR and 6.7/6.5 µm water vapor images.

## Total Column Ozone

Total Column Ozone (TCO) is an experimental product produced from the GOES Sounder.  The GOES-14 Sounder TCO is expected to be of similar, or higher, quality as derived from earlier GOES.

Figure 5.28:  Example of GOES-11/12 Imager Total Colum Ozone on 14 January 2010 at 1200 UTC

.

Figure 5.29:  Example of GOES-14 Imager Total Colum Ozone on 14 January 2010 at 1200 UTC

# Other accomplishments with GOES-13

## GOES-13 Imager Visible (Band-1) Spectral Response

A comparison of enhanced visible channel images from GOES-12 and GOES-14 at 13:15 UTC on 01 September 2009 is shown below — both images have been remapped to a Mercator projection over the state of Wisconsin. The obvious “meteorological” phenomenon is the early morning fog in the Mississippi, Wisconsin, and Kickapoo River basins, in addition to numerous other valleys and river basins feeding into the Mississippi River.

There are a couple of significant differences to note between the 2 visible images. First of all, the fog is a bit brighter and a little more extensive in the GOES-14 image compared to the GOES-12 image. This is primarily due to the relative age of the visible sensors (which noticeably degrades with time). The second major difference is the relative contrast of lakes, rivers, vegetation, and land usage. GOES-12 has slightly more contrast between land and lakes (and/or other bodies of water) than GOES-14.

On the other hand, GOES-14 is able to discern urban centers more readily than GOES-12, as well as variations in vegetation type. Examples of this are around the large metropolitan region of southeastern Wisconsin and northeastern Illinois (i.e. Milwaukee to Chicago). Also, both the Baraboo Range (located just to the northwest of Madison) and the “Military Ridge” (which runs east to west from Madison to Prairie du Chien) stand out more boldly in the GOES-14 image compared to the GOES-12 image. This difference is primarily due to the slight variation in the spectral width of the two visible bands on the GOES-12 and GOES-14 Imager instruments. A comparison of the visible channel spectral response function for GOES-12 and GOES-14 shows that the sharper cutoff for wavelengths beyond 0.7µm on the GOES-14 visible channel makes it less sensitive to the signal from the mature corn crops, allowing greater contrast between the thick vegetation of the agricultural fields and the more sparsely vegetated cities, towns, and highway corridors.

Figure 6.1:  GOES-12 (blue) and GOES-14 (red) Imager visible (approximately 0.65 or 0.63 μm) band SRFs, with a representative spectrum for grass over-plotted (green).

Figure 6.2:  Comparison of the visible (0.65 μm) imagery from GOES-12 and GOES-14 (0.63 μm) on 1 September 2009 demonstrates how certain features are more evident with the GOES-14 visible data.  For example, surface vegetation.

More information on this case can be found at: http://cimss.ssec.wisc.edu/goes/blog/archives/3355

## Lunar calibration

Several GOES-14 Imager datasets were acquired during the PLT. The main objective of these tests was to observe the lunar images as soon as possible in order to establish a baseline for future study of instrument degradation. While not intended, lunar images may allow an attempt on absolute calibration, although this has not been researched.

Figure 6.3:  GOES-13 Imager visible (0.65 μm) band image of the moon from 9 August 2010 for a scan that started at 20:53 UTC.

## Over-sampling Test

One of the Science Tests was intended to simulate GOES-R ABI-like (2 km) spatial resolution data.  Data for this test were gathered from four different sectors at different times during the day.  For each sector thee successive images were taken in rapid succession, in order to minimize any changes between the images, but with the scan lines offset by a half of the normal (4 km) distance between image lines.  It was then hoped that this over-sampled data could be de-convolved to produce imagery at 2 km resolution similar to that to be available from ABI.

Unfortunately, the data collector for this test failed to be line shifted between successive images, a fact that was not discovered until the Science Test had concluded and there was not time for redoing the test.  The result was no usable data for simulating ABI spatial resolution at 2 km spatial resolution.  A similar test was undertaken with GOES-12, but failed for other reasons.  Therefore, this test will hopefully be repeated during the Science Test for either GOES-O or GOES-P or both.

## Coordination with University of Alabama/Huntsville

Throughout the GOES-13 Science Test in December 2006, NOAA Science Team members coordinated with researchers from the NASA-MSFC SPoRT Center and the University of Alabama/Huntsville (UAH) THOR Center/Hazardous Weather Testbed.  The goal was to capture high resolution satellite imagery (30-seconds) to compare with ground-based polarimetric radar and VHF total lightning data from Huntsville.  Since the Science Test occurred in December 2006, widespread convection was barely observed in the U.S., but on 12 December 2006, there was a threat for some weak convection in the Southeast associated with an approaching cold front.  After speaking with UAH/NASA researchers, we decided to call for 30-second imagery centered over Huntsville, in hopes that thunderstorms would indeed develop over the area.

Figure 6.8 shows a 10.7 µm satellite image from 2057 UTC on 12 December 2006.  There was active convection, but most of it was confined to the southern half of Alabama.  No lightning was observed within the coverage area of the 3-D VHF Lightning Mapping Array.

Figure 6.8:  GOES-13 10.7 µm image from 2057 UTC on 12 December 2006.  The red "X" in northern Alabama denotes the location of Huntsville.

However, coincident with the rapid scanning, another very interesting feature was captured by the UAH ARMOR polarimetric radar.  Figure 6.9 shows the radar reflectivity (top) and radial velocity (bottom) at 2058 UTC.  It is believed that the northeast/southwest oriented line of enhanced reflectivity and with large gradients in radial velocity was caused by an undular bore.  Figure 6.10 shows a radar cross-section of differential reflectivity (ZDR).  The radar bright band (melting level) shows up as a zone of increased positive ZDR value, and is located at approximately the same height, except for an abrupt change in elevation at the location of the bore.  Close examination of the 30-second satellite data did not reveal any indication of the bore or its attendant influence on the precipitation bands.  There appeared to be two decks of clouds, the topmost layer possibly obscuring a cloud-top bore signature in the lower deck.

Figure 6.9:  Reflectivity (top) and radial velocity (bottom) from the HNT radar on 12 December 2007 at 2058 UTC.

Figure 6.10:  RHI scan of differential reflectivity (ZDR) from the HNT radar on 12 December 2007 at 2058 UTC.  Location of an undular bore and the radar bright band is indicated.

## Improved INR with GOES-14

McIDAS images of GOES-12 and GOES-14 visible channel data showed that large chunks of ice (known as “ice fields”) were drifting north-northeastward across the western portion of Lake Erie on 14 January 2010. The improved INR is clearly evident with GOES-14, as opposed to GOES-12. Southerly to southwesterly winds were beginning to increase on that day, helping to move the ice features across the surface of the lake. The animate can be found at:

http://cimss.ssec.wisc.edu/goes/blog/archives/category/goes-14

## Special 1-minute scans

On 19 December, a comparison of 15-minute interval GOES-12 and 1-minute interval GOES-14 visible images centered off the east coast of the Delmarva Peninsula offers a compelling demonstration of the value of more frequent imaging for monitoring the development and evolution of cloud features. During this 18:15 – 19:04 UTC time period, there were only 3 images available from GOES-12, compared to 44 images using GOES-14. This animation can be seen at: http://cimss.ssec.wisc.edu/goes/blog/wp-content/uploads/2009/12/ecb_g12g14_vis_anim.gif

# Recommendations for Future Science Tests

The following conclusions and recommendations were drawn during the GOES-15 Science Test:

- Science Tests should continue as a vital aspect of the checkout of each GOES satellite, as this was found that real-time data is an effective way to detect problems both in the data stream and in ground systems.

- Science Test duration should be at least 5 weeks for ‘mature’ systems (and ideally should be in times of the year with active convention over the continental U.S.). Much longer times will be needed for brand new systems such as GOES-R. It is expected on the order of a year will be needed for the many steps of engineering, science, products, validation and user readiness.

- An additional aspect to the Science Test could involve yearly checkout of GOES data when individual spacecraft are taken out of storage and turned on.

- While the GOES-14 GVAR data stream are captured and saved by a number of research groups, these unique and important pre-operational data should be part of the official GOES archive and be made available.

Acknowledgments

A large number of people played important roles in the success of the GOES-14 Science Test.  The contributors listed on the front cover of this report provided analysis of GOES-14 radiance data and Imager and Sounder products.  Dan Lindsey and John Knaff (StAR/RAMMB), Gary Wade (StAR/ASPB), and Scott Bachmeier (UW/CIMSS) are specially thanked for their participation in the daily coordination where decisions were made to determine which test schedules should be implemented in order to either capture interesting weather event(s), and to meet the requirements for the various data tests and generation of products.  In addition, thanks to Kevin Ludlum (GOES Scheduling Lead) and the rest of the GOES-14 Team at NOAA/NESDIS/OSO (Office of Satellite Operations), for coordinating and establishing the numerous schedules and sectors used during the Science Test. Tom Renkevens and Brian Hughes of the Satellite Services Division User Services are also thanked. Hyre Bysal, Chris Wheeler, Ken Mitchell and Mike Weinreb are thanked for their GOES engineering expertise.

This project was funded by the NOAA/NESDIS Office of Systems Development (OSD).

The views, opinions, and findings contained in this article are those of the authors and should not be construed as an official National Oceanic and Atmospheric Administration or U.S. Government position, policy, or decision.

References/Bibliography

Daniels, J.M., T.J. Schmit, and D.W. Hillger, 2001: Imager and Sounder Radiance and Product Validations for the GOES-11 Science Test, NOAA Technical Report NESDIS 103, (August), 49 pp.

Eilers, P.H.C. and Goeman, JJ, 2004:  Enhancing scatterplots with smoothed densities, Bioinformatics 20(5):623-628.

Gunshor, M., T. Schmit, W. Menzel and D. Tobin, 2009. Inter-calibration of broadband Geostationary Imagers using AIRS, Journal of Atmospheric and Oceanic Technology, Vol. 26, 746-758.

Johnsom, R. and M. Weinreb, 1996, GOES-8 Imager mid-night effects and slope correction. Proc. SPIE, Vol. 2812,, 596(1996), dio:10.1117/12.254104.

Jolliffe, I.T., and D.B. Stephenson, 2003:  Forecast Verification.  A Practioner’s Guide in Atmospheric Science.  Wiley and Sons Ltd, 240 pp.

Hillger, D.W., and T.J. Schmit, 2007: Imager and Sounder Radiance and Product Validation for the GOES-13 Science Test. NOAA Technical Report, NESDIS 125, (September), 75 pp.

Hillger, D.W., and T.J. Schmit, 2009: The GOES-13 Science Test: A Synopsis. Bull. Amer. Meteor. Soc., 90(5), (May), 6-11.

Hillger, D.W., T.J. Schmit, and J.M. Daniels, 2003: Imager and Sounder Radiance and Product Validation for the GOES-12 Science Test. NOAA Technical Report, NESDIS 115, (September), 70 pp.

Hillger, D.W., and T.H. Vonder Haar, 1988: Estimating Noise Levels of Remotely Sensed Measurements from Satellites Using Spatial Structure Analysis. J. Atmos. Oceanic Technol., 5, 206-214.

Ma, X. L., T. Schmit, and W.L. Smith, 1999: A non-linear physical retrieval algorithm - its application to the GOES-8/9 sounder. J. Appl. Meteor., 38, 501-513.

Menzel, W.P., F.C. Holt, T.J. Schmit, R.M. Aune, G.S. Wade, D.G. Gray, and A.J. Schreiner, 1998: Application of GOES-8/9 Soundings to weather forecasting and nowcasting. Bull. Amer. Meteor. Soc., 79, 2059-2078.

Merchant, C.J., A.R. Harris, E. Maturi, and S. MacCallum, 2005, Probabilistic physically-based cloud-screening of satellite infrared imagery for operational sea surface temperature retrieval. Quart. J. Roy. Meteorol. Soc., 131(611), 2735-2755.

Schmit, T.J., E.M. Prins, A.J. Schreiner, and J.J. Gurka, 2002a: Introducing the GOES-M imager. Nat. Wea. Assoc. Digest, 25, 2-10.

Schmit, T.J., W.F. Feltz, W.P. Menzel, J. Jung, A.P. Noel, J.N. Heil, J.P. Nelson III, G.S. Wade, 2002b: Validation and Use of GOES Sounder Moisture Information. Wea. Forecasting, 17, 139-154.

Tahara, Y. and K. Kato, 2009. New spectral compensation method for inter-calibration using high spectral resolution sounder, Met. Sat. Center Technical Note, No. 52, 1-37.

X. Wu and S. Sun, 2004. Post-launch calibration of GOES Imager visible channel using MODIS, Proc. SPIE, Vol. 5882, doi:10.1117/12.615401.

X. Wu, T. Schmit, R. Galvin, M. Gunshor, T. Hewison, M. Koening, Y. Tahara, D. Blumstein, Y, Li, S. Sohn, and M. Goldberg, 2009.  Investigation of GOES Imager 13µm channel cold bias. NOAA Technical Memo.

Weinreb, M.P., M. Jamison, N. Fulton, Y. Chen, J.X. Johnson, J. Bremer, C. Smith, and

J. Baucom, 1997: Operational calibration of Geostationary Operational Environmental

Satellite-8 and -9 Imagers and Sounders. Appl. Opt., 36, 6895-6904.

Weinreb, M. and K. Mitchell, 2010.  Personal communication on the issues with GOES-14 Imager space-look count.

Appendix A:	Web Sites Related to the GOES-14 Science Test

GOES-14 NOAA/Science Post Launch Test: http://rammb.cira.colostate.edu/projects/goes-o

GOES-14 RAMSDIS Online: http://rammb.cira.colostate.edu/ramsdis/online/goes-14.asp (contained real-time GOES-14 imagery and product during the Science Test)

CIMSS Satellite Blog: Archive for the 'GOES-14' Category: http://cimss.ssec.wisc.edu/goes/blog/archives/category/goes-14

NESDIS/StAR: GOES-14 News:  http://www.star.nesdis.noaa.gov/star/GOES-14FirstImage.php

NOAA: GOES-14: http://www.noaa.gov/features/monitoring/goes-14/

CIMSS GOES Calibration:

http://cimss.ssec.wisc.edu/goes/calibration

NOAA: GOES Imager SRF:

http://www.oso.noaa.gov/goes/goes-calibration/goes-imager-srfs.htm

NOAA: GOES Sounder SRF:

http://www.oso.noaa.gov/goes/goes-calibration/goes-sounder-srfs.htm

STAR Calibration:

http://www.star.nesdis.noaa.gov/smcd/spb/fwu/homepage/GOES_Imager.php

NOAA, Office of Systems Development: The GOES-O Spacecraft: http://www.osd.noaa.gov/GOES/goes_o.htm (including GOES-O Data Book)

United Launch Alliance: GOES-O: http://rammb.cira.colostate.edu/projects/goes-o/GOES-O_msnBk_j.pdf

NASA GSFC: GOES-O Mission Overview video: http://svs.gsfc.nasa.gov/vis/a010000/a010400/a010422/

NASA GSFC: GOES-O Project: GOES-O Spacecraft: http://goespoes.gsfc.nasa.gov/goes/spacecraft/goes_o_spacecraft.html

NASA-HQ: GOES-O Mission: http://www.nasa.gov/mission_pages/GOES-O/main/index.html

Boeing: GOES-N/P: http://www.boeing.com/defense-space/space/bss/factsheets/601/goes_nopq/goes_nopq.html

CLASS: http://www.class.ngdc.noaa.gov/saa/ products/welcome

Appendix B:	Acronyms Used in this Report

ABI		Advanced Baseline Imager (GOES-R)

AIRS		Atmospheric InfraRed Sounder

AMV		Atmospheric Motion Vector

ASPB		Advanced Satellite Products Branch

CICS		Cooperative Institute for Climate Studies

CIMSS	Cooperative Institute for Meteorological Satellite Studies

CIRA		Cooperative Institute for Research in the Atmosphere

CONUS	Continental United States

CRTM		Community Radiative Transfer Model

CSBT		Clear Sky Brightness Temperature

CSU		Colorado State University

DPI		Derived Product Image

FOV		Field Of View

GOES		Geostationary Operational Environmental Satellite

GOES-R	Next generation GOES, starting with GOES-R

GVAR		GOES Variable (data format)

hPa		Hectopascals (equivalent to millibars in non-SI terminology)

INR		Image Navigation and Registration

IR		InfraRed

KOZ		Keep Out Zone

LI		Lifted Index

LW		Longwave

LWIR		LongWave InfraRed

McIDAS	Man-Computer Interactive Data Access System

MSFC		Marshall Space Flight Center

NASA		National Aeronautics and Space Administration

NEdR		Noise Equivalent delta Radiance

NESDIS	National Environmental Satellite, Data, and Information Service

NSSTC	National Space Science and Technology Center

NOAA		National Oceanic and Atmospheric Administration

OPDB		Operational Products Development Branch

ORA		Office of Research and Applications (now StAR)

OSDPD	Office of Satellite Data Processing and Distribution

OSO		Office of Satellite Operations

PLT		Post Launch Test

PW		Precipitable Water

RAMMB	Regional and Mesoscale Meteorology Branch

RAMSDIS	RAMM Advanced Meteorological Satellite Demonstration and Interpretation System

RAOB	Radiosonde Observation

RMS		Root Mean Square

RSO		Rapid Scan Operations

RT		Real Time

RTM		Radiative Transfer Model

SAB		Satellite Analysis Branch

SPB		Sensor Physics Branch

SOCC		Satellite Operations Control Center

SPEC		Specifications

SPoRT		Short-term Predication Research and Transition center

SRF		Spectral Response Function

SRSO		Super Rapid Scan Operations

SSEC		Space Science and Engineering Center

SST		Sea Surface Temperature

StAR		SaTellite Applications and Research (formerly ORA)

SW		Shortwave

SWIR		Split-Window InfraRed

THOR		Tornado and Hazardous weather Observations Research center

TPW		Total Precipitable Water

UAH		University of Alabama, Huntsville

UTC		Coordinated Universal Time

μm		Micrometers (micron was officially declared obsolete in 1968)

UW		University of Wisconsin (Madison)

WV		Water Vapor

XRS		X-Ray Sensor