## Slide 1: ABI “Baseline” Products
Wavelength Micrometers | 0.47 | 0.64 | 0.865 | 1.378 | 1.61 | 2.25 | 3.90 | 6.185 | 6.95 | 7.34 | 8.5 | 9.61 | 10.35 | 11.2 | 12.3 | 13.3
Channel ID | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
Baseline Products |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Aerosol Detection | X | X | X | X | X | X | X |  |  |  |  |  |  | X | X | 
Suspended Matter/OD | X | X | X |  | X | X |  |  |  |  |  |  |  |  |  | 
Clear Sky Masks |  | X |  | X | X |  | X |  | X | X | X |  |  | X | X | 
Cloud & Moisture Imagery | X | X | X | X | X | X | X | X | X | X | X | X | X | X | X | X
Cloud Optical Depth |  | X |  |  |  | X | X |  |  |  |  |  |  | X | X | 
Cloud Particle Size |  | X |  |  |  | X | X |  |  |  |  |  |  | X | X | 
Cloud Top Phase |  |  |  |  |  |  |  |  |  | X | X |  |  | X | X | 
Cloud Top Height |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X | X
Cloud Top Pressure |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X | X
Cloud Top Temperature |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X | X
Hurricane Intensity |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  | 
Rainfall Rate/QPE |  |  |  |  |  |  |  | X |  | X | X |  |  | X | X | 
Legacy Vertical Moisture Profile |  |  |  |  |  |  |  | X | X | X | X | X | X | X | X | X
Legacy Vertical Temp Profile |  |  |  |  |  |  |  | X | X | X | X | X | X | X | X | X
Derived Stability Indices |  |  |  |  |  |  |  | X | X | X | X | X | X | X | X | X
Total Precipitable Water |  |  |  |  |  |  |  | X | X | X | X | X | X | X | X | X
Downward Solar Insolation Surf | X | X | X |  | X | X |  |  |  |  |  |  |  |  |  | 
Reflected Solar Insolation TOA | X | X | X |  | X | X |  |  |  |  |  |  |  |  |  | 
Derived Motion Winds |  | X |  |  |  |  | X | X | X | X |  |  |  | X |  | 
Fire Hot Spot Characterization |  | X |  |  |  |  | X |  |  |  |  |  |  | X | X | 
Land Surface Temperature |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X | 
Snow Cover | X | X | X |  | X | X | X |  |  |  |  |  | X |  |  | 
Sea Surface Temps |  |  |  |  |  |  | X |  |  |  | X |  | X | X | X | 
Bands may also be used by needed “upstream” products, such as the cloud mask.

## Slide 2: ABI “Option 2” Products
Wavelength Micrometers | 0.47 | 0.64 | 0.865 | 1.378 | 1.61 | 2.25 | 3.90 | 6.185 | 6.95 | 7.34 | 8.5 | 9.61 | 10.35 | 11.2 | 12.3 | 13.3
Channel ID | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
Option 2 Products |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Cloud Layer/Heights |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X | X
Cloud Ice Water Path |  |  |  |  |  |  | X |  |  |  |  |  |  | X | X | 
Cloud Liquid Water |  | X |  |  |  | X |  |  |  |  | X |  |  |  |  | 
Cloud Type |  |  |  |  |  |  |  |  |  | X | X |  |  | X | X | 
Convective Initiation |  |  |  |  |  |  |  | X | X | X | X | X |  | X | X | X
Turbulence |  |  |  |  |  |  |  | X |  |  |  |  |  |  |  | 
Low Cloud and Fog |  | X |  |  |  |  | X |  |  |  |  |  |  |  |  | 
Enhanced-V/Overshooting Top |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  | 
Aircraft Icing Threat |  | X |  |  |  | X | X |  |  | X | X |  |  | X | X | X
SO2 Detection |  |  |  |  |  |  |  | X |  | X | X |  |  | X | X | 
Visibility (no direct use of ABI bands) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Upward Longwave Radiation (TOA) |  |  |  |  |  |  |  | X |  | X | X |  | X |  |  | X
Downward Longwave Radiation (SFC) |  |  |  |  |  |  |  |  | X | X | X | X | X | X | X | X
Upward Longwave Radiation (SFC) |  |  |  |  |  |  |  |  |  |  | X |  | X | X | X | 
Total Ozone |  |  |  |  |  |  |  | X | X | X |  | X | X | X | X | X
Aerosol Particle Size | X | X | X |  | X | X |  |  |  |  |  |  |  |  |  | 
Surface Emissivity |  |  |  |  |  |  |  | X | X | X | X | X | X | X | X | X
Surface Albedo | X | X | X |  | X | X |  |  |  |  |  |  |  |  |  | 
Vegetation Index |  | X | X |  |  |  |  |  |  |  |  |  |  |  |  | 
Vegetation Green Fraction |  | X | X |  |  |  |  |  |  |  |  |  |  |  |  | 
Flood/Standing Water |  | X | X |  | X |  |  |  |  |  |  |  |  | X | X | 
Rainfall Potential (no direct use of ABI bands) |  |  |  |  |  |  |  | X |  | X | X |  |  | X | X | 
Rainfall Probability (no direct use of ABI bands) |  |  |  |  |  |  |  | X |  | X | X |  |  | X | X | 
Snow Depth (no direct use of ABI bands) | X | X | X |  | X | X | X |  |  |  |  |  | X |  |  | 
Sea & Lake Ice: Age (no direct use of ABI bands) |  | X | X |  | X |  |  |  |  |  |  |  |  | X | X | 
Sea & Lake Ice: Concentration |  | X | X |  | X |  |  |  |  |  |  |  |  | X | X | 
Sea & Lake Ice: Motion |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  | 
Ocean Currents |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  | 
Ocean Currents: Offshore |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  |