## Slide 1
High-Spectral Resolution IR Observations for Weather-related Applications
  Timothy J. Schmit (tim.j.schmit@noaa.gov)
NOAA/NESDIS/Satellite Applications and Research
Advanced Satellite Products Branch (ASPB)
Jun Li, etc., CIMSS
UW-Madison
16th Atmospheric Science from Space using Fourier Transform Spectrometry
Pyle Center, University of Wisconsin-Madison
Madison, WI
23-May-2012

## Slide 2: Overview
GOES-R Overview
  No dedicated Sounder
  Synergy with ABI
Current GOES Sounder
Select products
Sample applications
Summary
  More information
  References
Lockheed Martin

## Slide 3: GOES-R main instruments
Images courtesy of SOHO EIT, a joint NASA/ESA program
Space Weather/Solar
ABI covers the earth approximately five times faster than the current Imager.
ABI – Advanced Baseline Imager
Geostationary Lightning Mapper

## Slide 4: GOES Fly-out Schedule
http://www.goes-r.gov/

## Slide 5: GOES-R Series Overview
No dedicated Sounder
Advanced Baseline Imager (ABI)
Geostationary Lightning Mapper (GLM)
Space Weather
  Space Environmental In-Situ Suite (SEISS)
  Solar Ultra Violet Imager (SUVI)
  Extreme Ultra Violet/X-Ray Irradiance Sensor (EXIS)
  Magnetometer
Communications
  GOES Rebroadcast (GRB)
  Low Rate Information Transmissions (LRIT)
  Emergency Managers Weather Information Network (EMWIN)
  Search and Rescue (SAR)
  Data Collection System (DCS)
Notes:   Advanced Baseline Imager (ABI) Earth-viewing
  Geostationary Lightning Mapper (GLM) Earth-viewing
  Solar Ultra-Violet Imager (SUVI) Sun-viewing
  EUVS and XRS Irradiance Sensors (EXIS) Sun-viewing
  Space Environment In-Situ Suite (SEISS) Space-viewing
  Magnetometer (MAG) Space-viewing

## Slide 6
Advanced Sounders
Timothy J. Schmit
NOAA/NESDIS/ORA
Advanced Satellite Products Team (ASPT)
in collaboration with
Cooperative Institute for Meteorological Satellite Studies
(CIMSS)
UW-Madison
Madison, Wisconsin
[2001]

## Slide 7
More than 5 years of high spectral measurements from polar orbits:
- AIRS (Atmospheric InfraRed Sounder)
- IASI (Infrared Atmospheric Sounding Interferometer)
- CrIS (Crosstrack Infrared Sounder)
Approximately 5 years of high spectral, spatial and temporal measurements from geostationary orbit:
- GIFTS (Geostationary Imaging Fourier Transform Spectrometer)
30 years of filter wheel technology in geostationary orbit:
- VAS and GOES Sounder
40 years since the first interferometer flown in space to study the weather: IRIS (Infrared Radiation Interferometer Spectrometer)
Sounders, circa 2010
The time is right to update the GOES sounder! The technology is mature. The need is documented.
Forecast from 2001… with 67% accuracy!

## Slide 8
Improved products could be realized from combinations of ABI and HES (Hyperspectral Environmental Suite) data
ABI
HES
Surface
emissivity
Spectral
coverage
Spectral resolution
Temporal
resolution
Spatial
resolution
Cloud
clearing
cira 2004

## Slide 9: Geo advanced sounder – a history
Low-earth demonstration -- IRIS (1970)
Successful aircraft demonstrations (1980s and 1990s, etc.)
G-HIS was (briefly) slated to be on GOES-L (eg, GOES-11)
GOES-N/O/P were to be advanced instruments
  they turned out to be continuation instruments
The Advanced Baseline Sounder (ABS) was slated to be on GOES-Q, then -R
The ABI was designed assuming a companion high-spectral resolution sounder
Successful low-earth spectral resolution IR sounders demonstrated
  IMG, AIRS, IASI, etc.
HES was removed from GOES-R/S series (2006)
Strong support from the NRC Decadal study and others.
Plans for operational geo sounders by EUMETSAT and China
ABI is not an advanced sounder, and hence cannot meet the original sounding or derived requirements
CrIS launched on Suomi NPP
Notes: The need for geo high-spectral resolution data have been demonstrated with aircraft and leo data.

## Slide 10
Current GOES Sounder spectral coverage and that possible from an advanced high-spectral sounder. The broad-band nature of the current GOES limits the vertical resolution.
Example spectral coverage

## Slide 11: Why do we need a high spectral resolution sounder?
GOES-12 Sounder Bands
Smooth over required absorption lines
Compared to broadband sounders, observing absorption lines is mandatory to meeting requirements for temperature and moisture structure needed to improve weather forecasting
Many papers document science value of high spectral resolution sounder that support weather forecast needs. (Sieglaff et al.)
Analysis courtesy of Justin Sieglaff, CIMSS.
Notes: These are calculated spectra, showing important features dealing with temperature and moisture are in the high-spectral data, but are smoothed over in the broad-band data. Figure courtesy of J. Sieglaff, CIMSS.
I’m not sure it is useful to show an entire spectrum. Rather I prefer to show the above and indicate that it is these little wiggles that make the HES so valuable and that the current GOES smears out.

## Slide 12: High-Spectral, combined with High-Temporal Resolution is the key
Water Vapor and Carbon Dioxide absorption lines within the infrared window are sensitive to changes in the lower tropospheric thermodynamic state
Current GOES sounders are spectrally too broad to resolve these lines
High-time information obtained from a high spectral resolution IR GEO sounder would be very useful for monitoring pre-convective clear sky regions

## Slide 13: Need to monitor rapidly evolving situations

## Slide 14
Longwave window region
Allen Huang, CIMSS
On-line/off-line “signal”

## Slide 15
Longwave window region
Allen Huang, CIMSS
“AIRS or IASI-like”

## Slide 16
Longwave window region
Allen Huang, CIMSS

## Slide 17
Longwave window region
Allen Huang, CIMSS

## Slide 18
Longwave window region
Allen Huang, CIMSS

## Slide 19
Longwave window region
Allen Huang, CIMSS

## Slide 20
Longwave window region
Allen Huang, CIMSS
“Current GOES-like”

## Slide 21
The relative vertical number of independent pieces of information is shown. Note that the moisture content is similar between the ABI and the current GOES Sounder. The Sounder does show more temperature information than the ABI. Caveat: Even if two systems have the same number of pieces of information, they may represent different vertical levels. This information content analysis does not account for any spatial or temporal differences.

## Slide 22: GOES-R ABI Weighting Functions
ABI has only 1 CO2 band, so upper-level temperature will be degraded compared to the current sounder. Hence short-term NWP temperature information will be needed.

## Slide 23: GOES-13 Sounder Weighting Functions
The current GOES sounders have 5 CO2 bands, and more SW bands than ABI

## Slide 24: Overview
GOES-R Overview
  No dedicated Sounder
  Synergy with ABI
Current GOES Sounder
Select products
Sample applications
Summary
  More information
  References
http://cimss.ssec.wisc.edu/goes/rt/sounder-dpi.php

## Slide 25: Current Sounder Operational Uses
GOES Sounder Product | Operational Use within the NWS
Clear-sky Radiances | Assimilation into NCEP operational regional & global NWP models over water
Layer & Total Precipitable Water | Assimilation into NCEP operational regional & global NWP models; display and animation within NWS AWIPS for use by forecasters at NWS WFOs & National Centers in forecasting precipitation and severe weather
Cloud-top retrievals (pressure, temperature, cloud amount) | Assimilation into NCEP operational regional NWP models; display and animation within NWS AWIPS for use by forecasters at NWS WFOs; supplement to NWS/ASOS cloud measurements for generation of total cloud cover product at NWS/ASOS sites
Surface skin temperature | Image display and animation within NWS AWIPS for use by forecasters at NWS WFOs
Profiles of temperature & moisture | Display (SKEW-Ts) within NWS AWIPS for use by forecasters at NWS WFOs in forecasting precipitation and severe weather
Atmospheric stability indices | Image display and animation within NWS AWIPS for use by forecasters at NWS WFOs in forecasting precipitation and severe weather
Water Vapor Winds | Image display and animation within NWS AWIPS for use by forecasters at NWS WFOs
While there are limitations, the current GOES sounder is used today!
Courtesy of J. Daniels, STAR
Notes: Note the many operational uses of today’s sounder, even with its limited spatial and spectral attributes.

## Slide 26
Total Precipitable Water
Cloud-Top Height
Surface Skin Temperature
Lifted Index
AWIPS Display
Courtesy of J. Daniels, STAR

## Slide 27
Hourly Precipitation Forecasts in Early Stage
2012/5/10 01 Z ~ 2012/5/10 12 Z
Forecast with Conventional data
OBS
Forecast with GOES Sounder
Hourly precipitation forecast from 00 Z – 12 Z 05-10-2010 over CONUS with WRF/3DVAR, model resolution is 12 km, GOES Sounder 300 – 700 hPa precipitable water (PW) is used every 3 hours (preliminary results).
Notes: convert -delay 60 *png match_GCIP_prep1.gif
H:\CIMSS\NCEP_GCIP_prep_4km\match_GCIP_wrf_prep1

## Slide 28
Cumulative precipitation forecast from 00Z to 06 Z 05-10-2010 over CONUS with WRF/3DVAR, model resolution is 12 km, GOES Sounder 300 – 700 hPa moisture profile is used every 3 hours.
Observation
Forecast with
GOES Sounder
Forecast with
Conventional

## Slide 29: Forecasters value the current sounder
NWS Forecaster responses (Summer of 1999) to: "Rate the usefulness of LI, CAPE & CINH (changes in time/axes/gradients in the hourly product) for location/timing of thunderstorms."
There were 248 valid weather cases.
- Significant Positive Impact (30%)
- Slight Positive Impact (49%)
- No Discernible Impact (19%)
- Slight Negative Impact (2%)
- Significant Negative Impact (0)
National Weather Service, Office of Services
Notes: This 1999 NWS survey was written up as part of a Schmit et al paper.
Note that almost 80% of the responses were positive in terms of forecasters support for satellite derived images from the existing GOES sounder.
Current NWS training programs (e.g. SHyMet) will hopefully increase the use and appreciation of new satellite data.
Main Objective of SHyMet (Satellite Hydrology and Meteorology) training program
To prepare National Oceanic and Atmospheric Administration (NOAA) and National Weather Service (NWS) users for the latest polar orbiting and geostationary satellite data and products in the warning and forecast programs with direct links to Government Performance Results Act (GPRA) goals.
Completes end-to-end program cycle for space-based remote sensing as part of NOAA's Strategic Plan for an Integrated Global Environmental Observation and Data Management System and Global Earth Observation System of Systems (GEOSS).

## Slide 30: Forecasters need a better GEO sounder
Forecasters value the current GOES sounder products; however, the same forecasters also noted several limitations of the current sounder:
  retrievals limited to clear skies;
  the scanning rate is relatively slow, which limits coverage;
  the vertical resolution from the current generation GOES radiometers is limited.
Each of these limitations can be mitigated with an advanced sounder in the geostationary perspective.
Notes: This is related to the pie chart of previous slide

## Slide 31: What are NearCasts? Can GOES sounder data improve short-range forecasts of Convection? How can NearCasts be used to improve forecaster awareness and reduce false alarms?
Ralph Petersen1, Robert M Aune2 and Bill Line1
1 Cooperative Institute for Meteorological Satellite Studies (CIMSS), University of Wisconsin – Madison, Madison, Wisconsin ( Ralph.Petersen@ssec.wisc.edu and Bill.Line@ssec.wisc.edu )
2 NOAA/NESDIS/ORA, Advanced Satellite Products Team, Madison, Wisconsin (Robert.Aune@noaa.gov )
Improving the utility of GOES products
in operational forecasting

## Slide 32: What are we trying to improve?
Short-range forecasts of timing and locations of severe thunderstorms
- especially hard-to-forecast, isolated summer-time convection
NearCasts are 1-9 hour forecasts specifically designed to monitor conditions where hazardous weather will (or will not) form.
NearCasts are designed:
to be available within minutes of observation times,
to be frequently updated (hourly or sub-hourly), and
to rely on observations more than traditional NWP products
GOES NearCasts use high-density observations of moisture and humidity made over land from the GOES sounder. These data are not included in any operational NWP system
What are NearCasts?

## Slide 33: What are we trying to improve?
Short-range forecasts of timing and locations of severe thunderstorms
- especially hard-to-forecast, isolated summer-time convection
What are we trying to correct?
Poor precipitation forecast accuracy in short-range NWP (esp. in summer)
Underutilization of satellite moisture information over land in NWP
Time delay in getting NWP guidance to forecasters
Excessive smoothing of mesoscale moisture patterns
in NWP data assimilation
- Loss of Infra-Red (IR) satellite information about the convective environment after convection has begun
Lack of objective, observation-based tools for use by forecasters in detecting and monitoring the pre-convective environments 1-9 hours in advance

## Slide 34
Basic premises - NearCasting Models Should:
Update/Enhance NWP guidance:
Be Fast (valid 1-9 hrs in advance)
Be run frequently
Use all available data quickly:
“Draw closely” to good data
Preserve observed gradients and
data extremes (maxima/minima)
Be used to anticipate rapidly developing weather events:
“Perishable” guidance products – need rapid delivery
Focus on the “pre-storm environment”
- Short-range forecasts of timing and locations of convective storms- especially hard-to-forecast, isolated summer-time convection
Goals: - Increase the ability of forecasters to use frequent, quality GOES sounder observations to supplement NWP guidance in the next 1-9 hours
- Provide objective tools to help them do this
0 1 8 9 hours
Filling the Gap
Between
<Nowcasts & NWP>

## Slide 35
35
Example from 24 May 2011
Generally good forecasts, but

## Slide 36
36
Example from 24 May 2011
No storms in Chicago-NYC flight corridor
Few storms in
center of Outlook
Major sustained
storms near Dallas
Low-top supercells
In Colorado/Kansas
Generally good forecasts, but

## Slide 37
37
Example from 24 May 2011
No storms in Chicago-NYC flight corridor
Early storms in
center of Outlook
Major sustained
storms later near Dallas
Low-top supercells
In Colorado/Kansas
Generally good forecasts, but
Initial storms in
Nebraska died as they approached the Mississippi

## Slide 38
Mid-Level
Theta-E
Lower-Level
Theta-E
CONVECTIVE INSTABILITY .
Mid to Lower-level Theta-E DiffERENCE
Multiple-Parameter Displays that
explain the physical processes producing
Convective Instability
are more useful than
sets of single parameter images
Choice of color bars for display is critical
0 hours NearCasts from 1800 UTC 24 May 2011

## Slide 39
Mid-Level
Theta-E
Lower-Level
Theta-E
CONVECTIVE INSTABILITY .
Mid to Lower-level Theta-E DiffERENCE
0-9 hours NearCasts from 1800 UTC 24 May 2011
Note:
- Instability moves first to central Oklahoma
- Instability increases, reaching Dallas later
- Instability intensifies over western Kansas near low-top super-cells
- Stable air remains over Great Lake, covers most of Pennsylvania by end of end of period

## Slide 40: Overview
GOES-R Overview
  No dedicated Sounder
  Synergy with ABI
Current GOES Sounder
Select products
Sample applications
Summary
  More information
  References

## Slide 41: Product Impacts and Requirements
With data from an advanced high-spectral sounder in the geostationary orbit, the following NOAA validated product requirements can be reinstated, improving now, short and long term forecasts :
Advanced Atmospheric vertical moisture profile;
Advanced Atmospheric vertical temperature profile;
Capping inversion information (height & strength);
Moisture flux;
Surface emissivity;
Cloud Base altitude;
Carbon monoxide concentration.
Plus, high spectral resolution IR data will help at least 17 other products.
Notes: There are 6 products that will not meet requirements without a GEO high-spectral resolution sounder. This presentation focuses on T, Q vertical profiles, capping inversion and moisture flux.
Without an advanced high-spectral sounder on GOES, the following validated product requirements will either not be produced or will provide limited value added over numerical model guidance in the 2020 time frame

## Slide 43: Atmospheric Motion Vectors from Sounder data
Iliana Genkova, Chris Velden, Steve Wanzong, Paul Menzel, CIMSS
Much improved height-resolved winds from tracking features in retrieval fields from high spectral/temporal resolution rather than spectral images using broad band sounder
  Imager WV cloud tracked AMVs (yellow), Imager WV clear sky AMVs (red) and clear sky GOES Sounder AMVs (blue)
Notes: 43
MM5 - Pennsylvania State University - National Center for Atmospheric Research Mesoscale Model.
GIFTS forward model retrievals from GIFTS water vapor channels. CIMSS retrievals of MM5 model run. Raw vectors. No winds beneath the clouds because of the cloud mask.
30 minute time steps at 50mb intervals. 1000mb – 350 mb. NASTI example compared well with LIDAR.
GIFTS - Geostationary Imaging Fourier Transform Spectrometer.

## Slide 44: High spectral (HS) resolution IR data will help at least 17 other ABI-based products
GOES-R Observational Requirements:
Surface Emissivity *
Surface Albedo
Vegetation Fraction: Green
Vegetation Index
Sea & Lake Ice / Age
Sea & Lake Ice / Concentration
Currents
Sea & Lake Ice / Extent & Edge
Sea & Lake Ice / Motion
Ice Cover / Landlocked
Snow Cover
Snow Depth
Sea Surface Temps
Energetic Heavy Ions
Solar & Galactic Protons
Solar Flux: EUV
Mag Electrons & Protons: Low Energy
Solar Flux: X-Ray
Mag Electrons & Protons: Med & High Energy
Solar Imagery: extreme UV/X-Ray
Rainfall Potential
Probability of Rainfall
Rainfall Rate/QPE
Aerosol Detection (including Smoke and Dust)
Aerosol Particle Size
Suspended Matter / Optical Depth
Volcanic Ash *
Aircraft Icing Threat
Cloud & Moisture Imagery
Cloud Imagery: Coastal
Cloud Particle Size Distribution
Cloud Ice Water Path *
Cloud Liquid Water
Cloud Optical Depth
Cloud Top Phase
Cloud Top Height *
Cloud Top Pressure *
Cloud Type
Enhanced "V"/Overshooting Top Detection
Hurricane Intensity
Convection Initiation
Lightning Detection
Low Cloud & Fog
Turbulence
Visibility
* = Products degraded from original GOES-R (e.g.; now no HES)
Cloud Layers / Heights & Thickness *
Cloud Top Temperature *
Total Water Content *
Downward Solar Insolation: Surface
Upward Longwave Radiation *: Surface & TOA
Ozone Total *
Downward Longwave Radiation: Surface
Radiances *
Absorbed Shortwave Radiation: Surface
Reflected Solar Insolation: TOA
Fire / Hot Spot Characterization
Flood / Standing Water
SO2 Detection *
Clear Sky Masks
Derived Stability Indices *
Total Precipitable Water *
Land Surface (Skin) Temperature *
Derived Motion Winds *
Legacy Atm. Vertical Temperature Profile *
Legacy Atm. Vertical Moisture Profile *
ABI – Advanced Baseline Imager
Continuity of GOES Legacy Sounder Products from ABI
SEISS – Space Env. In-Situ Suite
EXIS – EUV and X-Ray Irradiance Sensors
GLM – Geostationary Lightning Mapper
Magnetometer
SUVI – Solar extreme UltraViolet Imager
Geomagnetic Field
Improved with HS

## Slide 45: Better Observation of Cloud Properties
High spectral data allow a more accurate determination of high, thin clouds.
Notes: Simulations. GOES-8 vs CrIS-type. 75 CONUS raob profiels. J. Li. 2001

## Slide 46: Overview
GOES-R Overview
  No dedicated Sounder
  Synergy with ABI
Current GOES Sounder
Select products
Sample applications
Summary
  More information
  References

## Slide 47
Root Mean Square Error
Forecast: 0.40
ABI like + fcst: 0.35
GOES 12 + fcst: 0.34
HES + fcst: 0.16
Experiments show that retrievals of Total Precipitable Water (TPW) from high-spectral (HES) data are much improved over current broadband (GOES-12+forecast).
Benefits of high-spectral over broad-band measurements!
Notes: For TPW, the error is half from high-spectral data, compared to broad-band measurements.
Raob data are used for truth.
The ABI-like data are select sounder bands.
The GOES-12 case is GOES-12 sounder bands.
The HES (high-spectral) data are simulated.
The region is over CONUS.

## Slide 48
Root Mean Square Error
Forecast: 2.27
ABI like + fcst: 2.20
GOES 12 + fcst: 2.18
HES + fcst: 1.79
Experiments show that retrievals of atmospheric instability from high-spectral (HES) data are much improved over current broadband (GOES-12+forecast).
Benefits of high-spectral resolution over narrowband measurements!
Notes: For LI, the error much less from high-spectral data, compared to broad-band measurements.
Raob data are used for truth.
The ABI-like data are select sounder bands.
The GOES-12 case is GOES-12 sounder bands.
The HES (high-spectral) data are simulated.
The region is over CONUS.

## Slide 49
Derived Product Images of Lifted Index: GOES and AIRS
Current GOES Sounder showed a stable atmosphere.
No profiling via thin clouds.
Sample of AIRS (high-spectral IR) showed un-stable regions.
Retrievals generated through thin clouds.
Analysis courtesy of Jun Li, CIMSS.

## Slide 50: Sample AIRS (LI) in AWIPS
Might a polar Proving Ground reformat AIRS products in near realtime for AWIPS?

## Slide 51
Animation
(GOES Sounder and AIRS)
See poster on Nearcast
Nearcast (using Sounder)
Sounder (Lifted Index)
AIRS (Lifted Index)
Loop from J. Feltz

## Slide 52: Assimilation of AIRS SFOV Retrieval Profiles in the Rapid Refresh Model System Haidao Lin1,2, Steve Weygandt1, Ming Hu1,3, Stan Benjamin1, Curtis Alexander1,3, Patrick Hofmann1,3, Tim Schmit4, Jinlong Li5, Jun Li5 1NOAA/ESRL/GSD Assimilation and Modeling Branch 2Cooperative Institute for Research in the Atmosphere, Colorado State University 3Cooperative Institute for Research in Environmental Sciences, University of Colorado at Boulder 4NOAA/NESDIS/STAR Advanced Satellite Products Branch 5Cooperative Institute for Meteorological Satellite Studies, University of Wisconsin-Madison From Poster at NOAA Science Week: http://www.goes-r.gov/users/past-2012-science-week-abstracts.html
SFOV water vapor mixing ratio (g/kg) at 750 hPa
Analysis 850-500 hPa mean relative humidity (%) from RAP AIRS SFOV run on 10 May 2010
Analysis 850-500 hPa mean relative humidity (%) from RAP control run on 10 May 2010

## Slide 53: Assimilation of AIRS SFOV Retrieval Profiles in the Rapid Refresh Model System Haidao Lin1,2, Steve Weygandt1, Ming Hu1,3, Stan Benjamin1, Curtis Alexander1,3, Patrick Hofmann1,3, Tim Schmit4, Jinlong Li5, Jun Li5 1NOAA/ESRL/GSD Assimilation and Modeling Branch 2Cooperative Institute for Research in the Atmosphere, Colorado State University 3Cooperative Institute for Research in Environmental Sciences, University of Colorado at Boulder 4NOAA/NESDIS/STAR Advanced Satellite Products Branch 5Cooperative Institute for Meteorological Satellite Studies, University of Wisconsin-Madison From Poster at NOAA Science Week: http://www.goes-r.gov/users/past-2012-science-week-abstracts.html
Observed radar composite reflectivity
HRRR forecast composite reflectivity initialized from AIRS SFOV RAP run
HRRR forecast composite reflectivity initialized from control RAP run

## Slide 54
AIRS and CrIS has similar sounding accuracy
(Matchup comparisons, ECMWF analysis as reference)

## Slide 55
AIRS LI at 06:35 UTC on 07 August 2010 (rainfall started at 10 UTC on 07 August 2010)
Lifted Index (LI)
  0< LI  Stable
  -3< LI <0  Moderate instable
  -6< LI <-3  Instable
  -9< LI <-6  Very instable
  LI <-9  Extremely instable
Lat=34.19; Lon=104.41
This storm caused 1456 deaths and left another 309 people missing due to a massive mudslide in the urban area of Zhou Qu.

## Slide 56: Evolution of the Vertical Moisture is the Key! Simulated Relative humidity cross-section at 20 UTC 12 June 2002
“Truth”
“GEO advanced IR sounder ”
“ABI”
“RUC”
Li et. al.
Notes: Warning information in pre-convection environment from geostationary advanced infrared sounding system – a simulation study using the IHOP case
Jun Li, Jinlong Li, Jason Otkin, Timothy J. Schmit, Chian-Yi, LiuJournal of Applied Meteorology and Climatology

## Slide 57
True
IRS/FY4
RUC forecast
Simulated Radar
Jun Li, Jinlong Li, Jason Otkin, and Tim Schmit
Red = extreme instability
IRS/FY4 provides needed monitoring of pre-convective environment hours earlier than regional forecast (+3-4 hrs) and Radar (+8 hrs)
RUC forecasts
Notes: LI>0 stable, -3 to 0 moderately stable, -6 to -3 moderately unstable, -6 to -9 very unstable, -6 to -9 extreme instability

## Slide 58: Hurricane eye sounding provides good intensity estimate (hurricane Isabel as example)
Eye Sounding
Environment
Sounding
Eye - Environment
Temperature
Integrate Hydrostatic Equation Downward from 100 hPa to Surface
Environment Sounding: Ps = 1012 hPa
Eye Sounding: Ps = 936 hPa
Aircraft Recon: Ps = 933 hPa
Courtesy: Mark DeMaria, NOAA

## Slide 60: Hyperspectral IR soundings improve tropical cyclone track forecasts (hurricane Ike as exmple), using WRF/3DVAR
Notes: AIRS single FOV soundings in clear skies are used. WRF/3DVAR forecasting and assimilation system is used. Assimilation is done every 6 hours. 0-h is from analysis, others are forecasts.

## Slide 61
Central sea level pressure (SLP) forecast RMSE (hPa)
（Hurricane Irene as example, 23 – 25 August 2011), using WRF/DART

## Slide 62
Lifecycle Hurricane Ike (2008) track RMSE for 0-h (analysis), 6-h to 48-h forecasts. The radiance assimilation of AIRS and AMSU are used in the experiments. GTS contains all the conventional data. WRF/GSI are used in the experiments.
Future work will include assimilation of radiances and/or soundings.

## Slide 63: Overview
GOES-R Overview
  No dedicated Sounder
  Synergy with ABI
Current GOES Sounder
Select products
Sample applications
Summary
  More information
  References

## Slide 64
Current GOES Sounder
Current Sounder Data Volume
Horizontal
Notes: Define current GOES sounder information volume to be 1 x 1 x 1 for the attributes.

## Slide 65
Advanced High-Spectral IR Sounder
(GIFTS example)
Horizontal

## Slide 66: Nearcasting Severe Weather using a Hyperspectral Environmental Sounder (HES) [Aune, Lindstrom, Petersen]
A WRF model simulation of the June 12, 2002 IHOP case was used to generate simulated radiances from an Advanced Baseline Imager (ABI), a geostationary Hyper-spectral Environmental Sounder (HES), and simulated radar reflectivity.
Temperature and moisture profiles were retrieved from the radiance datasets and assimilated by the CIMSS Nearcasting Model and compared. Detailed Theta-E gradients were resolved by HES.
5-hour NearCast for 2000 UTC
Low level Theta-E
5-hour NearCast for 2000 UTC
Low to Mid level Theta-E Differences
Rapid Development of Convection over Texas and Nebraska between 2000 and 2100 UTC 12 June 2002
Strong low-level Theta-E gradients are indicated by HES which has the ability to detect low-level moisture.
5-hour NearCast for 2000 UTC
Low to Mid level Theta-E Differences
5-hour NearCast for 2000 UTC
Low level Theta-E
Weak gradients of low-level Theta-E are indicated by ABI which has only two water vapor channels.
Simulated composite reflectivity from nature run indication the formation of convection.
Simulated ABI
Simulated ABI
Simulated HES
Simulated HES
Notes: Specific NOAA requirement(s) being addressed
  Associated Science Question(s) being worked (objective(s) of the specific research effort)
  (Traceability)
Who cares (recipients/beneficiaries of the work; societal benefit)?

## Slide 67: Summary
An advanced geostationary sounder would overcome existing instrument limitations.
High-spectral infrared observations needed for trace gas monitoring could also be used for a number of weather-related applications.
High-spectral resolution IR observations will resolve high temporal and vertical fluctuations of moisture that are not resolved by current in-situ or satellite measurements. High temporal resolution is unique aspect of GEO measurements.
Critical meteorological parameters (temperature, moisture, clouds, winds) with necessary temporal, spatial and vertical resolutions will improve monitoring of atmospheric conditions.
An advanced high-spectral sounder in GEO will fulfill requirements of several validated products.
Studies have estimated the economic and societal benefits of a high-spectral resolution sounder to be at least $4.2 B (Centrec study).

## Slide 68: Conclusions on the need for advanced geostationary IR observations wrt weather applications
As stated in 2001…
  Technology is mature
  Meteorological need is documented.
  Time is right to update geostationary sounding instruments to provide required high spectral resolution measurements with high temporal refresh rates.

## Slide 69: Select References
Schmit, T. J., J. Li, S. A. Ackerman, and J. J. Gurka, 2009: High spectral and temporal resolution infrared measurements from geostationary orbit, Journal of Atmospheric and Oceanic Technology, 26, 2273 - 2292. (a.k.a., why we need an advanced geo-sounder)
Sieglaff, J., M., T. J. Schmit, W. P. Menzel, S. A. Ackerman, 2009: Inferring Convective Weather Characteristics with Geostationary High Spectral Resolution IR Window Measurements: A Look into the Future. J. Atmos. Oceanic Technol., 26, 1527–1541. (a.k.a., potential now-casting applications)
Schmit, T. J., J. Li, J. J. Gurka, M. D. Goldberg, K. Schrab, J. Li, W. Feltz, 2008: The GOES-R ABI (Advanced Baseline Imager) and the continuation of current sounder products. J. of Appl. Meteor., 47, 2696–2711. (a.k.a., the ABI isn’t an advanced sounder)

## Slide 70
Li, Jun, Chian-Yi Liu, Peng Zhang, Timothy J. Schmit, 2012: Applications of Full Spatial Resolution Space-Based Advanced Infrared Soundings in the Preconvection Environment. Wea. Forecasting, 27, 515–524. doi: http://dx.doi.org/10.1175/WAF-D-10-05057.1
Select References
Hyperspectral Earth Observation from IASI:
Five Years of Accomplishments
Fiona Hilton, Raymond Armante, Thomas August, Chris Barnet, Aurelie Bouchard, Claude Camy-Peyret, Virginie Capelle, Lieven Clarisse, Cathy Clerbaux, Pierre-Francois Coheur, Andrew Collard, Cyril Crevoisier, Gaelle Dufour, David Edwards, Francois Faijan, Nadia Fourrié, Antonia Gambacorta, Mitchell Goldberg, Vincent Guidard, Daniel Hurtmans, Samuel Illingworth, Nicole Jacquinet-Husson, Tobias Kerzenmacher, Dieter Klaes, Lydie Lavanant, Guido Masiello, Marco Matricardi, Anthony McNally, Stuart Newman, Edward Pavelin, Sebastien Payan, Eric Péquignot, Sophie Peyridieu, Thierry Phulpin, John Remedios, Peter Schlüssel, Carmine Serio, Larrabee Strow, Claudia Stubenrauch, Jonathan Taylor, David Tobin, Walter Wolf, Daniel Zhou
Bulletin of the American Meteorological Society
Volume 93, Issue 3 (March 2012) pp. 347-370
doi: http://dx.doi.org/10.1175/BAMS-D-11-00027.1