## Slide 1
Operational uses of the ABI (Advanced Baseline Imager) on the GOES-R series
  Timothy J. Schmit (tim.j.schmit@noaa.gov)
NOAA/NESDIS/Satellite Applications and Research
Advanced Satellite Products Branch (ASPB)
Madison, WI
Mathew M. Gunshor, Kaba Bah, James J. Gurka, Jason Otkin
UW-Madison
National Weather Association 37th Annual Meeting Monona Terrace Convention Center, Madison, Wisconsin October 8, 2012

## Slide 2: Thanks to…
Scott Lindstrom, Scott Bachmeier, Joleen Feltz, William Straka, Jun Li, Scott Bachmeier, Steve Ackerman, Bob Aune, Don Hillger, Paul Menzel, Steve Ackerman, Tony Schreiner, Justin Sieglaff, Jim Jung, Elaine Prins, Brad Pierce, Wayne Feltz, Jean Phillips, Gary Wade, Don Hillger, Jinlong Li, Jing Zheng, Allen Huang, Bob Rabin, the SSEC data center, Mike Pavolonis, Jaime Daniels, ASPB, STAR, NESDIS, NSSL, MUG, Kevin Ludlum, GOES operators, GOES shift supervisors, Mark DeMaria, and many others!
GOES-R Program Office (Steve Goodman, etc.), NASA, ITT Industries, other industry partners, etc.
You.

## Slide 3: Outline
ABI (Advanced Baseline Imager)
  Temporal
  Spatial
  Spectral
Products
Summary
  More information
  Questions

## Slide 4: GOES-R series is 5th Generation!
GOES-13/14/15
Launched
2005
2009
2010
Better navigation and calibration.
No eclipse outages.
Better spatial resolutions for the 6.5 um on GOES-12+ and the 13.3 um band on GOES-14/15.
Operational Sounder
GOES-8/12
Launched
1994
1995
1997
2000
2001
3-axis stabilized.
Imager Bands: 4 IR; 1 visible.
Operational Sounder
(18 IR bands)
GOES-R/S+
Planned Launch
2015
2017
2020
2025
Faster coverage.
16 Imager Bands.
Improved spatial.
No sounder.
GLM
GOES-4/7
Launched
1980
1981
1983
1987
VISSR–VAS visible, 12 IR. MSI (visible, IRW, and 2 additional IR channels)
GOES-1/3
Launched
1975
1977 1978
One visible and one infrared .
Operational.
Notes: The circles represent an estimate of the impact of GOES on regional scale numerical models.

## Slide 5: GOES-R main instruments
Images courtesy of SOHO EIT, a joint NASA/ESA program
Space Weather/Solar
ABI covers the earth approximately five times faster than the current Imager.
ABI – Advanced Baseline Imager
Geostationary Lightning Mapper

## Slide 6: GOES-R Overview
Advanced Baseline Imager (ABI)
Geostationary Lightning Mapper (GLM)
Space Weather
  Space Environmental In-Situ Suite (SEISS)
  Solar Ultra Violet Imager (SUVI)
  Extreme Ultra Violet/X-Ray Irradiance Sensor (EXIS)
  Magnetometer
No dedicated Sounder
Communications
  GOES Rebroadcast (GRB)
  Low Rate Information Transmissions (LRIT)
  Emergency Managers Weather Information Network (EMWIN)
  Search and Rescue (SAR)
  Data Collection System (DCS)
Notes:   Advanced Baseline Imager (ABI) Earth-viewing
  Geostationary Lightning Mapper (GLM) Earth-viewing
  Solar Ultra-Violet Imager (SUVI) Sun-viewing
  EUVS and XRS Irradiance Sensors (EXIS) Sun-viewing
  Space Environment In-Situ Suite (SEISS) Space-viewing
  Magnetometer (MAG) Space-viewing

## Slide 7: GOES Fly-out Schedule

## Slide 8: Outline
ABI (Advanced Baseline Imager)
  Temporal
  Spatial
  Spectral
Products
Summary
  More information
  Questions
Lockheed Martin

## Slide 9: The Advanced Baseline Imager:
ABI Current
Spectral Coverage
16 bands 5 bands
Spatial resolution
0.64 mm Visible 0.5 km Approx. 1 km
Other Visible/near-IR 1.0 km n/a
Bands (>2 mm) 2 km Approx. 4 km
Spatial coverage
Full disk 4 per hour Scheduled (3 hrly)
CONUS 12 per hour ~4 per hour
Mesoscale Every 30 sec n/a
Visible (reflective bands)
On-orbit calibration Yes No

## Slide 10
Anticipated scan mode for the ABI:
- Full disk images every 15 minutes + 5 min CONUS images + mesoscale.
ABI scans about 5 times faster
than the current GOES imager

## Slide 11
ABI can offer Continental US images every 5 minutes for routine monitoring of a wide range of events (storms, dust, clouds, fires, winds, etc).
This is every 15 or 30 minutes with the current GOES in routine mode.
Notes: Approx. size of CONUS

## Slide 12
Notes: Approx. size of CONUS

## Slide 13
Mesoscale images every 30 seconds for rapidly changing phenomena
(thunderstorms, hurricanes, fires, etc). Or two regions every 60 seconds.
Notes: Approx. size of meso-scale showing “Franklin”.

## Slide 14
1-min imagery
Operational (GOES-13)
1-min mode (SRSOR from GOES-14)

## Slide 15: ABI Visible/Near-IR Bands
Schmit et al, 2005
Notes: Schmit, T. J., M. M. Gunshor, W. P. Menzel, J. J. Gurka, J. Li, and A. S. Bachmeier, 2005: Introducing the next-generation Advanced Baseline Imager on GOES-R. Bull. Amer. Meteor. Soc., 86, 1079-1096.

## Slide 16: ABI IR Bands
Schmit et al, 2005
Notes: Schmit, T. J., M. M. Gunshor, W. P. Menzel, J. J. Gurka, J. Li, and A. S. Bachmeier, 2005: Introducing the next-generation Advanced Baseline Imager on GOES-R. Bull. Amer. Meteor. Soc., 86, 1079-1096.

## Slide 17
The ABI visible and near-IR bands have many uses.
Aerosols, Insolation
Clouds, Snow
Vegetation, Imagery
Cloud mask, Suspended matter
Cloud Particle size
Snow, Phase
Visible and near-IR channels on the ABI
Sample use only, many other uses
Notes: Schmit, T. J., M. M. Gunshor, W. P. Menzel, J. J. Gurka, J. Li, and A. S. Bachmeier, 2005: Introducing the next-generation Advanced Baseline Imager on GOES-R. Bull. Amer. Meteor. Soc., 86, 1079-1096.

## Slide 18
ABI has many more bands than the current operational GOES imagers.
The IR channels on the ABI
Clouds, Stability Indices
Rainfall, Aerosol
SST, Fires, Radiances
Hurricane, Imagery
Cloud Phase, SST
Ozone, Downward Radiation
SO2, Radiances
Winds, WV profiling
TPW, Rainfall rate
Fires, Fog
Sample use only, many other uses
Notes: Schmit, T. J., M. M. Gunshor, W. P. Menzel, J. J. Gurka, J. Li, and A. S. Bachmeier, 2005: Introducing the next-generation Advanced Baseline Imager on GOES-R. Bull. Amer. Meteor. Soc., 86, 1079-1096.

## Slide 19
  http://cimss.ssec.wisc.edu/goes/srsor/GOES-14_SRSOR.html

## Slide 20
Daytime “Blue” band – aerosols, solar insolation, snow cover

## Slide 21
Daytime “Red” band – clouds, cloud-mask, optical depth, winds, etc.

## Slide 22
Daytime “Veggie” band – NDVI, solar insolation, snow cover

## Slide 23
1 Daytime “Cirrus” band – cloud mask, aerosol detection

## Slide 24
Daytime “Snow” band – snow cover, cloud mask, etc.

## Slide 25
Daytime “Cloud-top phase” band – cloud particle size, snow cover

## Slide 26
Shortwave IR window band - fog, fires, winds, SST, etc.

## Slide 27
Upper-level tropospheric water vapor band – moisture, flow, winds

## Slide 28
Upper/mid-level tropospheric water vapor band – moisture, flow, winds

## Slide 29
Lower mid-level tropospheric water vapor band– moisture, flow, winds

## Slide 30
“Cloud-top phase” band – SO2, dust, SST, stability indices, etc.

## Slide 31
“Ozone” band

## Slide 32
“Clean” IR longwave window band – imagery, TPW, etc.

## Slide 33
IR longwave window band – many cloud parameters, SST, snow cover

## Slide 34
“Dirty” IR longwave window band – many cloud parameters, TPW

## Slide 35
“CO2” longwave IR band – cloud height/pressure, stability indices

## Slide 36: Outline
ABI (Advanced Baseline Imager)
  Temporal
  Spatial
  Spectral
Products
Summary
  More information
  Questions

## Slide 37: GOES-R ABI Products
Advanced Baseline Imager (ABI)
Aerosol Detection (Including Smoke and Dust) Aerosol Optical Depth (AOD) Clear Sky Masks Cloud and Moisture Imagery Cloud Optical Depth Cloud Particle Size Distribution Cloud Top Height Cloud Top Phase Cloud Top Pressure Cloud Top Temperature Derived Motion Winds Derived Stability Indices Downward Shortwave Radiation: Surface Fire/Hot Spot Characterization Hurricane Intensity Estimation Land Surface Temperature (Skin) Legacy Vertical Moisture Profile Legacy Vertical Temperature Profile Radiances Rainfall Rate/QPE Reflected Shortwave Radiation: TOA Sea Surface Temperature (Skin) Snow Cover Total Precipitable Water Volcanic Ash: Detection and Height
Baseline Products
Advanced Baseline Imager (ABI)
Absorbed Shortwave Radiation: Surface Aerosol Particle Size Aircraft Icing Threat Cloud Ice Water Path Cloud Layers/Heights Cloud Liquid Water Cloud Type Convective Initiation Currents Currents: Offshore Downward Longwave Radiation: Surface Enhanced “V”/Overshooting Top Detection Flood/Standing Water Ice Cover Low Cloud and Fog Ozone Total Probability of Rainfall Rainfall Potential Sea and Lake Ice: Age Sea and Lake Ice: Concentration Sea and Lake Ice: Motion Snow Depth (Over Plains) SO2 Detection Surface Albedo Surface Emissivity Tropopause Folding Turbulence Prediction Upward Longwave Radiation: Surface Upward Longwave Radiation: TOA Vegetation Fraction: Green Vegetation Index Visibility
Future Capabilities

## Slide 38: Three Groups of Users
Direct use of radiances/imagery
  Numerical models
  Forecasters
  Broadcasters
  General public/private sector/Internet
Direct use of satellite products
  Numerical models
  Forecasters
  Blended products, etc.
  General public/private sector/Internet
Use of services which use data/products
  Basically everyone!

## Slide 39: Pseudo-Natural Color

## Slide 40: Outline
ABI (Advanced Baseline Imager)
  Temporal
  Spatial
  Spectral
Products
Summary
  More information
  Questions

## Slide 41: Approximate spectral and spatial resolutions of US GOES Imagers
~ Band Center (um) | GOES-6/7 | GOES-8/11 | GOES-12/N | GOES-O/P | GOES-R+
0.47 |  |  |  |  | 
0.64 |  |  |  |  | 
0.86 |  |  |  |  | 
1.6 |  |  |  |  | 
1.38 |  |  |  |  | 
2.2 |  |  |  |  | 
3.9 |  |  |  |  | 
6.2 |  |  |  |  | 
6.5/6.7/7 | 14km |  |  |  | 
7.3 |  |  |  |  | 
8.5 |  |  |  |  | 
9.7 |  |  |  |  | 
10.35 |  |  |  |  | 
11.2 |  |  |  |  | 
12.3 |  |  |  |  | 
13.3 |  |  |  |  | 
8
4
2
Visible
Near-IR
Infrared
Box size represents pixel size
“MSI mode”
Notes: 0.40 inches = 4km; 0.80 inches = 8km
MSI is Multi-Spectral Imaging Mode (dashed boxes)
This does not show other improvements: SNR, MTF, bit-depth, navigation, coverage rates, etc.

## Slide 42: Summary
1. The GOES-R ABI provides mission continuity
2. Two times the image navigation quality
3. Three times the number of imaging bands
4. Four times the spatial resolutions
5. Five times the coverage rate

## Slide 44
GOES-R:
  http://www.goes-r.gov
  http://www.meted.ucar.edu/index.htm
  http://cimss.ssec.wisc.edu/goes_r/proving-ground.html
GOES and NASA:
  http://goespoes.gsfc.nasa.gov/goes/index.html
  http://goes.gsfc.nasa.gov/text/goes.databookn.html
UW/SSEC/CIMSS/ASPB:
  http://cimss.ssec.wisc.edu/goes_r/proving-ground/nssl_abi/nssl_abi_rt.html
  http://cimss.ssec.wisc.edu/goes/abi/
  http://cimss.ssec.wisc.edu/goes/blog/
  http://www.ssec.wisc.edu/data/geo/
  http://cimss.ssec.wisc.edu/goes/srsor/GOES-14_SRSOR.html
More information
AMS BAMS Article on the ABI (Aug. 2005)