## Slide 1: NWA Talk
Background
Spectral
Temporal
  ABI CONUS locations
  Baseline scan modes
  Exploratory scan modes
Spatial
Misc
  AHI
  NSC?

## Slide 2: Continuity of GOES Operational Satellite Program
2
GOES-R Launch Readiness 2Q FY 2016
Notes: GOES-R moved from October 2015 Launch Commitment Date to 2Q FY2016 and GOES-S shifted to 3Q FY17. GOES-T and U LCD remain unchanged.

## Slide 3: GOES-R main instruments
Images courtesy of SOHO EIT, a joint NASA/ESA program
Space Weather/Solar
ABI covers the earth 5X faster than current Imager
ABI – Advanced Baseline Imager
Geostationary Lightning Mapper
Unique Payload Services
No Sounder
SEISS
SUVI
EXIS
Magnetometer

## Slide 4
GOES- R Flight Segment
4
Atlas V 541 ELV
GOES-R ABI
GLM vibration testing complete
SUVI and EXIS (solar/space instruments
Solar Array Wing deployment
Notes: Credit: GOES-R web page and G. Mandt presentation

## Slide 5: 16 (ABI) versus only 5 (GOES Imager) bands
Notes: http://cimss.ssec.wisc.edu/goes/goes-r/

## Slide 6: Baseline ABI Scan Modes
‘Flex mode’ for the ABI:
Full disk every 15 minutes + 5 min CONUS
+ 1-min mesoscale sectors (2 locations)
‘Continuous Full Disk’ (CFD) is a full disk every 5 min
MESO
CONUS
FD
Notes: CONUS image is the shifted center point.

## Slide 7
GOES-14: Special Rapid Scanning offers glimpse of the ABI
GOES-14 provided very unique information and offers a glimpse into the possibilities that will be provided by the ABI on GOES-R. Data used by the NWS.
GOES-14 Image from CIMMSE blog
http://cimmse.wordpress.com/2014/08/24/an-example-of-how-goes-14-super-rapid-scan-operations-for-goes-r-helped-during-warning-operations-at-nws-wfo-raleigh-nc-on-18-august-2014/
SRSOR (Super Rapid Scan Operations for GOES-R) from GOES-14 imager
More SRSOR data in both May 8-24 and August 14-28 of 2014.
http://cimss.ssec.wisc.edu/goes/srsor2014/GOES-14_SRSOR.html
Many phenomena were observed: convection, hurricanes, fires, smoke, ...
Data was provided to many groups: WPC, OPC, AWC, SPC, SAB, several WFO, who used the data for discussions and forecasts.
NWS Forecaster: SRSOR “….certainly increased our confidence in our warning decisions and ultimately made the process more efficient … having the Super Rapid Scan data very valuable and very worthwhile, … should be able to be built into everyday operations at NWS weather forecast offices around the country.”
Notes: mp4

## Slide 8
GOES-14: Special Rapid Scanning offers glimpse of the ABI
GOES-14 provided very unique information and offers a glimpse into the possibilities that will be provided by the ABI on GOES-R. Data used by the NWS.
GOES-14 SRSOR posts from the CIMSS blog
http://cimss.ssec.wisc.edu/goes/blog/archives/category/goes-14
SRSOR (Super Rapid Scan Operations for GOES-R) from GOES-14 imager
More SRSOR data in both May 8-24 and August 14-28 of 2014.
http://cimss.ssec.wisc.edu/goes/srsor2014/GOES-14_SRSOR.html
Many phenomena were observed: convection, hurricanes, fires, smoke, ...
Data was provided to many groups: WPC, OPC, AWC, SPC, SAB, several WFO, who used the data for discussions and forecasts.
Animation of 1-min GOES-14 Imager data on May 16, 2014
http://cimss.ssec.wisc.edu/goes/goes-r/
http://cimss.ssec.wisc.edu/goes/goes-r/600x800_GOES_B1_CLDS_SLC_animated_2014136_130000_182_2014136_230000_182_EB_TSTORM.mp4
Notes: http://cimss.ssec.wisc.edu/goes/goes-r/

## Slide 9: ABI CONUS Sector Locations
Worked with the GOES-R Program Office and the NWS on moving the ABI CONUS center points for both the GOES-East and -West positions to better address operational needs
Current (PUG) sectors for GOES-East and -West
Proposed (NOAT and GORWG-approved)

## Slide 10
Exploratory ABI Scan Mode
At some point, other ABI scan mode could be possible. Although, this requires an upgrade to the ground system.
One option is to use the idle time of when the ABI instrument is not scanning in mode 3 (‘flex’). For example, increase to an ‘extended CONUS’ image. There are other optimized scan options as well.
The ABI instrument is capable of supporting other scan modes.

## Slide 11: Mode 3 (‘flex’) “Time-Time” chart
Approximate times
This chart represents what the ABI scans when (over 15 minutes), i.e., FD, CONUS, Meso-scale sectors or star views (for navigation) and calibration events.
Notes: Copy and pasted from excel. Pasted as a picture. Resized to 44% by 44% of original. Arrange -> Align -> Align Center & Align Middle

## Slide 12: Proposed Mode ”3a” with Extended CONUS
Note larger (taller and wider) CONUS scans, while keeping full disk and meso-scale scans
The ‘special’ sector could be over American Samoa, volcanoes, or other areas (TC).
Approximate times
Notes: Copy and pasted from excel. Pasted as a picture. Resized to 44% by 44% of original. Arrange -> Align -> Align Center & Align Middle

## Slide 13: Baseline Time-Time Mode 4
This is the Continuous Full Disk (every 5 min) mode ‘time-time’ chart.
This is the highest data rate.

## Slide 14: Exploratory ABI Scan Strategies
Every 15 minutes
Every 15 minutes
Every 3 minutes
(with 6 min gap)
One extended “CONUS” sector every 5 minutes
One mesoscale sector
every 30 seconds (or 1 minute at two locations)
Option
A
Option
B
&
&
There are some alternative ABI scan strategies to baseline modes (3 and 4)
One mesoscale sector
every 30 seconds (or 1 minute at two locations)
&
One wider “CONUS” sector in 6 minute gaps
CONUS covered every 3 minute!
&
Notes: Scan areas and timing are approximate. Option B has special southern hemisphere scans.

## Slide 15: ABI CONUS Sector Size
Working on extending the ABI CONUS size to better address operational needs (and use time when the ABI instrument would be idle)
This would need a ground system upgrade
Other scan modes are being explored
Current CONUS Sector for ABI
Proposed CONUS Sector for ABI

## Slide 16
CONUS from 137W

## Slide 17
Proposed Extended ‘CONUS’ from 137W
Great
Plains
Alaska
Canada
Gulf of Alaska
Volcanoes
Notes: The northern region, including Alaska, was not covered in this simulation, but would be covered by this extended ‘CONUS’.

## Slide 18
CONUS from 75W

## Slide 19
Proposed Extended ‘CONUS’ from 75W
Atlantic
Canada
Volcanoes
Atlantic
Notes: The northern region, including Canada, was not covered in this simulation, but would be covered by this extended ‘CONUS’.

## Slide 20: Himawari launched!
Himawari-8 launched!
7 October 2014
16-band Advanced Himawari Imager (AHI)
10-min Full Disk
ABI-like
  15 of the 16 bands
AHI built by Exelis
Visible/near Infrared
Infrared
Notes: http://www.data.jma.go.jp/mscweb/en/himawari89/

## Slide 21: From MSG-SEVIRI to MTG-FCI
MTG FCI outbids MSG SEVIRI observations on cloud, aerosol, moisture and fire:
by adding new channels
by improving temporal-,
spatial-, and radiometric
resolution
High-Resolution Fast Imagery
a Full-Disk High-Spectral-resolution
Imagery (FDHSI)
Coverage Repeat cycle FDHSI mission 18ox18o 10 min
HRFI mission 1/4 FD 2.5 min
Notes: Flexible Combined Imager

## Slide 22: AHI Sectored Observations in 10 minutes
Region 1
N-E JAPAN
Region 2
S-W JAPAN
Region 3
Typhoon
Region 4
Land mark
Region 5
Land mark
Full disk
Interval : 10 minutes (6 times per hour)
23 swath
Region 1 JAPAN (North-East)
Interval : 2.5 minutes (4 times in 10minutes)
Dimension : EW x NS: 2000 x 1000 km
2 swath
Region 2 JAPAN (South-West)
Interval : 2.5 minutes (4 times in 10minutes)
Dimension : EW x NS: 2000 x 1000 km
2 swath
Region 3 Typhoon
Interval : 2.5 minutes (4 times in 10minutes)
Dimension : EW x NS: 1000 x 1000 km
2 swath
Region 4 Land mark
Interval : 0.5 minutes (20 times in 10minutes)
Dimension : EW x NS: 1000 x 500 km
1 swath
Region 5 Land mark
Interval : 0.5 minutes (20 times in 10minutes) Dimension : EW x NS: 1000 x 500 km
1 swath

## Slide 23: 4.3 COMS & GEO-KOMPSAT-2A
resolution 4times upgrade
COMS
VIS 1km
IR 4km
Geo-KOMPSAT-2A
VIS 0.5~1km
IR 2km
Observation frequency 4 times
COMS
1
(Black and white)
O
4
5 channel
Geo-KOMPSAT-2A
4
(color image)
2
10
16 channel
VIS
SW IR
IR
channel 3times increase
products 3.5 times increase
COMS
Total : 16
Cloud/pre. : 5
Aerosol : 5
AMV : 3
Land sfc. : 3
Geo-KOMPSAT-2A
Total : 52
Cloud/pre. :19
Aerosol : 16
AMV : 6
Land sfc. : 11
Full disk : 1
NH : 2
KP : every 15min
Full disk : 4
NH : 10
…....
KP : every 2min
1hr

## Slide 24
Beyond GOES-R Series
Discussions have began investigating options related to GOES-V and –W
NWS, NESDIS and the GPO, along with others are involved
Some have suggested evolving the ABI capabilities and adding back instruments cancelled on GOES-R
  high spectral sounder
  coastal water imager
GOES-V (currently) slated for operational use beginning in 2033