## Slide 1
GOES-R ABI INR:
A Users Perspective
  Timothy J. Schmit (tim.j.schmit@noaa.gov)
NOAA/NESDIS/Satellite Applications and Research
Advanced Satellite Products Branch (ASPB)
Madison, WI
Jaime Daniels, STAR
Mat Gunshor, Scott Bachmeier, CIMSS
UW-Madison
GOES-R POSST Meeting
March, 2014

## Slide 2: Outline
Current GOES
AWG (Algorithm Working Group)
INR assessment via image loops
System testing with simulated INR values?
Summary
  More information
  Questions

## Slide 3: GOES-14 Science Test December 2009
Don Hillger, Deb Molenar, Dan Lindsey, John Knaff
NOAA/NESDIS/Satellite Applications and Research
Regional And Mesoscale Meteorology Branch (RAMMB)
Dave Watson, Mike Hiatt, Dale Reinke, etc.
CIRA, Colorado State University
Fort Collins CO
Don Hillger and Tim Schmit co-lead the NOAA Science Test

## Slide 4: GOES-14 Science Test – December 2009
Hillger, D.W., and T.J. Schmit, 2010: The GOES-14 Science Test: Imager and Sounder Radiance and Product Validations. NOAA Technical Report NESDIS 131, 1-119.
http://rammb.cira.colostate.edu/projects/goes-o/NOAA_Tech_Report_NESDIS_131_GOES-14_Science_Test_with_Corrigendum.pdf

## Slide 5: GOES Science Test Goals
For all GOES check-outs, the goals of the Science Test include:
To assess the quality of the GOES radiance data. This is accomplished by comparison to other satellite measurements or by calculating the signal-to-noise ratio compared to specifications, as well as assess the striping in the imagery due to multiple detectors.
To generate products from the GOES data stream and compare to those produced from other satellites. These included several Imager and Sounder products currently used in operations.
Rapid-scan imagery of interesting weather cases are collected with temporal resolutions as fine as every 30 seconds, a capability of rapid-scan imagery from GOES-R that is not implemented operationally on current GOES.

## Slide 6: GOES-14 NOAA/Science Test Website
http://rammb.cira.colostate.edu/projects/goes-o/

## Slide 7: GOES-O Test Schedules
Test Schedule | Imager | Sounder | Purpose
C5RTN | Emulation of GOES-East routine operations | Emulation of GOES-East routine operations | Radiance and product comparisons
C4RTN | Emulation of GOES-West routine operations | Emulation of GOES-West routine operations | Radiance and product comparisons
C1CON | Continuous 5-minute CONUS sector | 26-minute CONUS sector every 30 minutes | Test navigation, ABI-like (temporal) CONUS scans
C2SRSO | Continuous 1-minute rapid-scan (with center point specified for storm analysis) | 26-minute sector every 30 minutes (with center point same as Imager) | Test navigation, ABI-like (temporal) mesoscale scans
C3SRSO | Continuous 30-second rapid-scan (with center point over either Huntsville AL, Normal OK, or Washington DC areas) three locations only | 26-minute sector every 30 minutes (with center same as Imager) | To coordinate with lightning mapping arrays in Huntsville AL, Norman OK, or Washington DC
C6FD | Continuous 30-minute Full Disk (including off-earth limb/space view measurements) | Alternating east and west limb/space views every hour | Noise, detector-to-detector striping, fires, etc.
C7MOON | Capture moon off edge of earth (when possible) | Emulation of GOES-East routine operations | Test ABI lunar calibration concepts
C8 | Emulation of 2 km ABI through spatial over-sampling (continuous 19 minutes for same sector per specific line-shifted scan strategy) | Emulation of GOES-East routine operations | ABI-like higher-resolution product development

## Slide 8
http://www.oso.noaa.gov/goes/inrstat/index.htm

## Slide 9
http://mscweb.kishou.go.jp/monitoring/navigation.htm

## Slide 10: Outline
Current GOES
AWG (Algorithm Working Group)
INR assessment via image loops
System testing with simulated INR values?
Summary
  More information
  Questions

## Slide 11: Algorithm Working Group
Mission:
  To select, develop, test, validate, and demonstrate Level-2+ algorithms that meet the GOES-R F&PS requirements and provide them to the GOES-R Ground Segment.
  Provide sustained life cycle validation and Level-2 product enhancements
End-to-End Capabilities
  Instrument Trade Studies
  Proxy Dataset Development
  Algorithm Development and Testing
  Product Demonstration Systems
  Development of Cal/Val Tools
  Integrated Cal/Val Enterprise System
  Radiance and Product Validation
  Algorithm and application improvements
  User Readiness and Education

## Slide 12: AWG Teams
AWG Product Application Teams | Team Lead
Imagery | Tim Schmit
Soundings | Tim Schmit
Winds | Jaime Daniels
Clouds | Andrew Heidinger
Aviation | Ken Pryor, Wayne Feltz
Hydrology | Robert Kuligowski
Land | Bob Yu
Cryosphere | Jeff Key
Radiation Budget | Istvan Lazslo
Lightning | Steve Goodman
SST | Alexander Ignatov
Ocean Dynamics | Eileen Maturi
Aerosols/Air Quality/Atmos. Chemistry | Shobha Kondragunta
AWG Specialty Teams | Team Lead
Proxy Data | Fuzhong Weng
Cal/Val (Sensor) | Changyong Cao
Algorithm Integration | Walter Wolf
GOES-R Products are Mapped to AWG Product Application Teams

## Slide 13
Anticipated scan mode for the ABI:
- Full disk images every 15 minutes + 5 min CONUS images + mesoscale.
ABI scans about 5 times faster
than the current GOES imager

## Slide 14
ABI can offer Continental US images every 5 minutes for routine monitoring of a wide range of events (storms, dust, clouds, fires, winds, etc).
This is every 15 or 30 minutes with the current GOES in routine mode.
Notes: Approx. size of CONUS

## Slide 15
Notes: Approx. size of CONUS

## Slide 16
Mesoscale images every 30 seconds for rapidly changing phenomena
(thunderstorms, hurricanes, fires, etc). Or two regions every 60 seconds.
Notes: Approx. size of meso-scale showing “Franklin”.

## Slide 17: GOES-R POSST Path Forward
POSST Task in Coordination with
MOST Activity
DOST Activity
Internal
POSST Activity Only
  Continue pre-launch instrument cal test assessment and reporting
  Finalize the GOES-R System-level Cal/Val CONOPS/OPSCON, and process it through Program configuration management
  Cal/INR/Product Science (CIPS) PLT Planning
  Define CIPS-related data operations validation objectives to be carried out during Data Operations Tests (DOTs)
  Support SIR and MOR reviews
  Complete CIPS tool development planning and begin implementation
  Ground Segment Training for relevant personnel
  Clarify CIPS validation schedules and milestones
  Identify CIPS resource needs and risks
GOES-R Series Pre-launch POSST Activities
Cal/INR/Product Science (CIPS) Val Tool Development
120 Days
90 Days
12 months
Mission Operations Review (MOR) and System Integration Review (SIR)
6 Months
CIPS Val Tool Testing
60 Days
Post-Launch Test (PLT) Planning/ Preparation & System-Level Test Planning/Implementation
Cal&INR PLT Long Form Definition & Development
ETE I-V Testing
DOT I & II
Cal&INR PLT Short Form Definition & Development
Data Operations Tests (DOT) Planning & Ground Segment Training
CIPS Val Definitions & CIPS CONOPS/OPSCON Development
Launch
*Post-Launch Product Test (PLPT) Definition and Development &
CIPS OPSCON Rehearsals
Sep13
Apr14
Apr15
Pre-Launch Instrument Cal Testing Assessment (Ends After All Instruments Delivered)
CIPS OPSCON Rehearsals
Flight Operations Review (FOR)
POSST Kick-Off
Adding new Operational OPSCON section.
Another look at POSST scope. Defining high-level test objectives, test deliverables, and schedules.
A glimpse at PLPT Validation Maturity Stages
Notes: To-Do: Finalize CONOPS/OPSCON and send it off for CM. Under PLT Planning – need to create PLPT test plan that includes the types of tests and their associated data acquisitions and priorities.

## Slide 18: AWG Imagery Team
What: select full resolution time animations
Why: monitor animations as users will
When: during the full Post Launch Test
How well: while qualitative, full resolution animations can depict sub-pixel INR jumps
Similar to: Previous (GOES-8 to -15) PLT
  http://rammb.cira.colostate.edu/projects/goes-p
  http://rammb.cira.colostate.edu/projects/goes-o

## Slide 19
Overview
GOES-8/12 vs GOES-13/15 vs GOES-R ABI:
GOES-N/O/P bus change
- better navigation than previous generation
- earth sensor -> star tracker
GOES-R ABI
- even better (by a factor of ~2) expected INR
GOES-8/12
GOES-13/15

## Slide 20: Better “navigation” on GOES-13
GOES-13:
GOES-12:
Notes: animation

## Slide 21
GOES-12:
GOES-13:
Visible
Shortwave Window
http://cimss.ssec.wisc.edu/goes/blog/archives/450
MI Fires - 3-Aug-2007
Notes: http://cimss.ssec.wisc.edu/goes/blog/2007/08/03/wildfire-in-the-upper-peninsula-of-michigan/

## Slide 22
GOES-12:
GOES-13:
River Fog - 31-July-2007

## Slide 23
GOES-12:
GOES-13:
Ice Floes - 30-July-2007
http://cimss.ssec.wisc.edu/goes/blog/archives/440

## Slide 24: Improved Navigation & Registration GOES-15 provides a hint of ABI’s INR quality…
GOES-11
GOES-15
http://cimss.ssec.wisc.edu/goes/blog/archives/9270
Notes: We also expect improved navigation/registration performance from the ABI which products will also benefit from, especially those that use and rely heavily on temporal information (ie, satellite winds)

## Slide 25
GOES-14: Special Rapid Scanning offers glimpse of the ABI
GOES-14 provided very unique information and offers a glimpse into the possibilities that will be provided by the ABI on GOES-R.
Animation from GOES-14 Imager visible image at 1-min time resolution.
SRSOR (Super Rapid Scan Operations for GOES-R) from GOES-14 imager
Daily scanning between mid-August and September 24th and late October 2012.
Posted many animations
http://cimss.ssec.wisc.edu/goes/srsor/GOES-14_SRSOR.html
Many phenomena were observed: convection, hurricanes, fires, smoke, etc.,
Data to many groups HPC, OPC, AWC, SPC, several regions, etc.
All data archived

## Slide 26
  GOES-14: SRSOR – Super Rapid Scan Operations for GOES-R

## Slide 27: Outline
Current GOES
AWG (Algorithm Working Group)
INR assessment via image loops
System testing with simulated INR values
Summary
  More information
  Questions
Lockheed Martin

## Slide 28: System testing with simulated INR values?
Under ‘things others should think about’…
Are there plans (pre-launch) to perturb realistic simulations with varying levels of INR performance?
  run through validation programs
  monitor effect on products

## Slide 29
ABI band 14 (11m) simulation from NWP model
From M. Gunshor – CIMSS Proxy ABI Lead
Differences
Navigation Error Introduced
Notes: 8 km

## Slide 30
Impact of navigation error (1 pixel) on ABI/SEVIRI single FOV total column ozone (TCO) product (Jin et al. 2007). SEVIRI TCO product is composite of 2 time steps, and the temporal resolution of the product is 30 minutes.
From J. Li – AWG Sounding Team Member

## Slide 31: Summary
Image loops, especially fast, full (space and time) resolution animations can be quite useful for quality assessments.
  Can share any animations built during the PLT
  Similar to previous GOES PLT.
2. ABI is expected to have two times the image navigation quality
3. Special GOES-14 1-min data available
Leveraging ABI with GLM wrt INR
What other tools exist or will exist wrt INR?

## Slide 32
GOES-R:
  http://www.goes-r.gov
  http://www.meted.ucar.edu/index.htm
  http://cimss.ssec.wisc.edu/goes_r/proving-ground.html
  (ABI WES guide with simulated images)
GOES and NASA:
  http://goespoes.gsfc.nasa.gov/goes/index.html
  http://goes.gsfc.nasa.gov/text/goes.databookn.html
UW/SSEC/CIMSS/ASPB:
  http://cimss.ssec.wisc.edu/goes_r/proving-ground/nssl_abi/nssl_abi_rt.html
  http://cimss.ssec.wisc.edu/goes/abi/
  http://cimss.ssec.wisc.edu/goes/blog/
  http://cimss.ssec.wisc.edu/goes/srsor/GOES-14_SRSOR.html
More information
AMS BAMS Article on the ABI