## Slide 1
GOES-R Overview
SOO training
Kansas City
Fall 2016 / Spring 2017

## Slide 2: Thanks to…
Tim Schmit
Bill Line
Jordan Gerth
Scott Lindstrom
Mat Gunshor
Steve Goodman
Kathryn Mozer
Matt Seybold
Kathleen Strabala
Dan Nietfeld
SSEC data center
Kaba Bah
Steve Miller and Dan Lindsey
JMA
ITT / Harris and the Entire GOES-R team!

## Slide 3: Outline
Lockheed Martin
Introduction
GLM
GOES-R ABI
  Spectral
  Spatial
  Temporal
Data
Summary

## Slide 4: GOES-R
  Geostationary Lightning Mapper (GLM)
  Advanced Baseline Imager (ABI)
    3x more spectral bands
    4x spatial resolution
    5x temporal coverage
Space weather and solar imaging instruments
  Space Environment in-Situ Sensor Suite (SEISS)
  Magnetometer
  Solar Ultra-Violet Imager (SUVI)
  Extreme Ultraviolet and X-ray Irradiance Sensors (EXIS)
Next generation of NOAA/NASA geo weather satellites
  R-Series includes 4 satellites (R, S, T, U)
  First to launch in 04 Nov 2016
  Represents first major upgrade in over 20 years
Earth-pointing instruments

## Slide 5: GOES-R
Notes: Graphic from LM

## Slide 6: A History of GOES “Weather” Satellites
ATS
SMS
Notes: The focus of this Short Course is to describe the advancements with the GOES-R series

## Slide 7
Why GOES-R ?
Visible & IR Imagery
Lightning Mapping
Space Weather Monitoring
Solar Imaging
The GOES-R series will provide significant improvements in the detection and observations of meteorological phenomena that directly impact public safety, protection of property, and our Nation’s economic health and prosperity.
  Improves hurricane track & intensity forecasts
  Increases thunderstorm & tornado warning lead time
  Improves aviation flight route planning
  Data for long-term climate variability studies
  Improved air quality warnings and alerts
  Improves solar flare warnings for communications and navigation disruptions
  More accurate monitoring of energetic particles responsible for radiation hazards to humans and spacecraft
  Better monitoring of Coronal Mass Ejections to improve geomagnetic storm forecasting
7
ABI
GLM
SEISS and MAG
EXIS and SUVI

## Slide 8: GOES-R main instruments
Images courtesy of SOHO EIT, a joint NASA/ESA program
Space Weather/Solar
ABI covers the earth 5X faster than current Imager
ABI – Advanced Baseline Imager
Geostationary Lightning Mapper
Unique Payload Services
No Sounder
SEISS
SUVI
EXIS
Magnetometer

## Slide 9: Geostationary Lightning Mapper(GLM)
East/West GLM FOV
~ 10 km across field of view with 8 km CONUS, 14 km at edge of field of view
Detects extent of total lightning activity
Day/night coverage with 70-90% flash detection (better at night)
Near-uniform detection efficiency spatially across the domain
Continuous coverage (2 ms frame rate)
<20 sec latency
Figures courtesy of Steve Goodman

## Slide 10: Geostationary Lightning Mapper(GLM)
Mission Benefits
  Potential to improve warning decision-making when combined with radar and imaging
  Cover data sparse regions
  Diagnosing convective storm structure and evolution
  Aviation and marine convective weather hazards
  Tropical cyclone intensity change
  Decadal changes of extreme weather – thunderstorms/ lightning intensity and distribution
Figures courtesy of Steve Goodman
Hurricane Katrina
PGLM Total Lightning - Denver

## Slide 11: Benefits of Total Lightning
Cloud-to-ground AND intra-cloud flashes
Stronger, deeper updrafts lead to more lightning, with most lightning in-cloud
  Total Lightning is driven by updraft in mixed phase region (above 10C)
Increase in total lightning signifies strengthening updraft
  Rapid increase often precedes occurrence of severe weather by 10s of minutes.
Figures courtesy of NASA/SPoRT

## Slide 12: Total Lightning for DSS
Total Lightning- in –cloud and cloud-to-ground lightning extent information valuable for support of outdoor events
Figures courtesy of NASA/SPoRT

## Slide 13: Current GOES Spectral Bands (5)
VIS
NIR
WV
IRW
CO2
Figures courtesy of Tim Schmit
1 VIS
0 NIR
4 IR

## Slide 14: ABI Spectral Bands (16)
0.64 m
0.86 m
1.38 m
1.61 m
2.26 m
3.9 m
6.19 m
6.95 m
7.34 m
0.47 m
8.5 m
9.61 m
10.35 m
11.2 m
12.3 m
13.3 m
Figures courtesy of Tim Schmit
2 VIS
4 NIR
10 IR

## Slide 15: Future vs. Current Spectral Bands
The current GOES (right) has 5 spectral bands, while the GOES-R series ABI (left) will have 16 spectral bands.

## Slide 16: ABI: Temporal
Figures courtesy of Tim Schmit
GOES-West in Flex Mode
GOES-East in Flex Mode
GOES-R: Current:
Flex Mode Routine
Full Disk: 15 min 3-hr
CONUS: 5 min 15-min
Mesoscale: 30-sec n/a
or, 2 x 1-min

## Slide 17
Meso-scale box locations are movable
15 min
5 min
1 min
1 min
West
Notes: 1-km2 spatial resolution at satellite nadir. Pixel Areas are approximate. Each bin is rounded to the nearest 1km2 until we get to 9.5km2 and then all are binned into the red 10+ area. So the first, dark blue, ring covers pixel areas from 1 to 1.49km2 and is labeled “1”, above 1.5 to below 2.5km2 goes into the next ring and is called “2”, etc. GOES-West location. Proposed CONUS sector, approved by the NWS NOAT. Two meso-scale image sectors shown; these are selectable. The same central lat/lon used for these mesoscales produces a different sized and shaped area for different satellite locations.

## Slide 18
Meso-scale box locations are movable
15 min
5 min
1 min
1 min
Central
Notes: 1-km2 spatial resolution at satellite nadir. Pixel Areas are approximate. Each bin is rounded to the nearest 1km2 until we get to 9.5km2 and then all are binned into the red 10+ area. So the first, dark blue, ring covers pixel areas from 1 to 1.49km2 and is labeled “1”, above 1.5 to below 2.5km2 goes into the next ring and is called “2”, etc. GOES-Test location. PUG CONUS sector. Two meso-scale image sectors shown; these are selectable. The same central lat/lon used for these mesoscales produces a different sized and shaped area for different satellite locations.

## Slide 19
15 min
Meso-scale box locations are movable
5 min
1 min
1 min
East
Notes: 1-km2 spatial resolution at satellite nadir. Pixel Areas are approximate. Each bin is rounded to the nearest 1km2 until we get to 9.5km2 and then all are binned into the red 10+ area. So the first, dark blue, ring covers pixel areas from 1 to 1.49km2 and is labeled “1”, above 1.5 to below 2.5km2 goes into the next ring and is called “2”, etc. GOES-East location. Proposed CONUS sector, approved by the NWS NOAT. Two meso-scale image sectors shown; these are selectable. The same central lat/lon used for these mesoscales produces a different sized and shaped area for different satellite locations.

## Slide 20
ABI IR Pixel size from West and East
(proposed ABI CONUS West and East)
East Optimal
West Optimal

## Slide 21: GOES-R as GOES West GOES-13 as GOES East Infrared Resolution color coded
GOES-R resolution is better than GOES-13 far to the east of the midpoint
(106 W) between the two sub-satellite points (all the way to ~92 W!)
Similarly, if GOES-R were GOES-East, there would be better pixel resolution
Compared to GOES-15 all the way to 120 W!
106 W
Notes: So, If GOES-R is GOES-West at 137 W, and GOES-13 remains GOES-East at 75 W, the midpoint longitudinally is 106 W. But that's not where satellite resolution would be the same from each satellite; rather, GOES-R would have better spatial Resolution than GOES-13 all the way to 92 W, the approximate longitude of Duluth Minnesota at the western tip of Lake Superior. If GOES-R were GOES-East, superior spatial resolution from that GOES-East (relative to the resolution of GOES-14 or GOES-15 as GOES-West at 135W) would extend west all the way to 120 W, the longitude of Reno NV and Santa Barbara CA.
When GOES-R and GOES-S both are operational as GOES-East and GOES-West, the poorest spatial resolution will be along the 106W longitude line. Glasgow MT, and thereabouts, will have dubious distinction of the worst horizontal spatial resolution in CONUS – because it's halfway between the two satellites and farthest north.

## Slide 22: GOES-R as GOES East GOES-15 as GOES West Infrared Resolution color coded
GOES-R resolution is better than GOES-15 far to the west of the midpoint
(106 W) between the two sub-satellite points (all the way to ~120 W!)
106 W
Notes: So, If GOES-R is GOES-West at 137 W, and GOES-13 remains GOES-East at 75 W, the midpoint longitudinally is 106 W. But that's not where satellite resolution would be the same from each satellite; rather, GOES-R would have better spatial Resolution than GOES-13 all the way to 92 W, the approximate longitude of Duluth Minnesota at the western tip of Lake Superior. If GOES-R were GOES-East, superior spatial resolution from that GOES-East (relative to the resolution of GOES-14 or GOES-15 as GOES-West at 135W) would extend west all the way to 120 W, the longitude of Reno NV and Santa Barbara CA.
When GOES-R and GOES-S both are operational as GOES-East and GOES-West, the poorest spatial resolution will be along the 106W longitude line. Glasgow MT, and thereabouts, will have dubious distinction of the worst horizontal spatial resolution in CONUS – because it's halfway between the two satellites and farthest north.

## Slide 23
~90W
Notes: Data from SSEC Data Center

## Slide 24: GOES-14 Super Rapid Scan Operations for GOES-R (SRSOR)
Aug, Sep, Oct 2012: 38 days
Jun, Aug 2013: 14 days
May and Aug 2014: 30 days
May, Jun, Aug 2015: 36 days
Feb, April/May, Aug 2016: 69 days
Daily changing, ~1500 km x 2000 km sector;
Prepares users for GOES-R capability
http://cimss.ssec.wisc.edu/goes/srsor2016/GOES-14_SRSOR.html
GOES (SRSOR)
~1 per minute (26 every 30)
Experimental
No other imagery
GOES-R ABI (Meso)
1 per minute for 2 locations
Operational
With FD + CONUS
+ higher spatial/spectral resolutions
Figure courtesy of T. Schmit, CIMSS

## Slide 25: Baseline ABI Scan Modes
Scan mode (3) or ‘flex mode’ for the ABI:
- Full disk every 15 minutes + 5 min CONUS
+ 1-min mesoscales (2 locations).
[Scan mode (4) or ‘Continuous Full Disk’ (CFD) is a full disk every 5 min]
Notes: CONUS image is the shifted center point.

## Slide 26: Scan Mode 3 Timeline (Flex Mode) Delivers Storm Watch Every 30 Seconds
Meso: one every 30 seconds or two at 1 minute intervals each
Scene locations can be changed on the fly (no interruption of timeline)
30 seconds
MISTiC
Full
Disk
Meso
CONUS
Nadir
Vis Star
Spacelook
Blackbody
IR Star
Note: Autonomous spacelook collected with each Full Disk swath

## Slide 27: ABI Scan Strategy
Concept of the ABI “flex mode” diagram
(image fades with time)
Full
Disk
Meso
CONUS
Meso
Time->

## Slide 28: Flex Mode Concept

## Slide 29
Default Meso Locations
Two meso from GOES-West and two from GOES-East

## Slide 32
DOE-4 Simulated ABI: Full Disk sector
Central location

## Slide 33
DOE-4 Simulated ABI: CONUS sector
Central location

## Slide 34
DOE-4 Simulated ABI: 2 meso-scale sectors
Central location

## Slide 35
DOE-4 Simulated ABI: meso-scale sectors (default)
Central location

## Slide 36
DOE-4 Simulated ABI: CONUS sector
Central location

## Slide 37
0.64 mm
3.9 mm
6.2 mm
13.3 mm
10.3 mm
11.2 mm
12.3 mm
6.9 mm
7.3 mm
8.4 mm
9.6 mm
0.47 mm
0.86 mm
1.37 mm
1.6 mm
2.2 mm
DOE-4 Simulated ABI Spectral bands
GOES-R ABI Imagery simulated at UW via AWG Proxy, processed via the Ground System, acquired via NOAAPort, shown in AWIPS-II (default enhancements)

## Slide 38
ABI CONUS from East and West
Redo with AWIPS combined image (default color map?)
Notes: Different days simulated.

## Slide 39
ABI CONUS from West and East
Redo with AWIPS combined image (default color map?)
Notes: Different days simulated.

## Slide 40
GOES-12 and GOES-R ABI
Simulation of Grand Prix Fire/Southern California
GOES-12
GOES-12
GOES-R ABI
GOES-R ABI
Notes: Here are two different fires from J. Feltz of CIMSS (using mcidas-v). What we can see is a more defined peak in the higher resolution data and it is easier to pick out individual hotspots. In addition, the higher saturation temperature of the ABI allows us to see that the fire is around 370K. ABI is simulated from MODIS.

## Slide 41
GOES
Figure courtesy of K. Bedka and W. Feltz

## Slide 42
“ABI” from MODIS
Figure courtesy of K. Bedka and W. Feltz

## Slide 43
GOES Spatial Resolution

## Slide 44
MODIS Spatial Resolution
Note that this is finer than what the ABI IR bands will be.

## Slide 45: ABI
Figure from J. Key, ASPB
In general, even at 50 degrees view angles, the spatial resolution of the ABI is comparable to today’s imager at the satellite sub-point.
Pixels size by latitude, along the longitude line of satellite nadir.

## Slide 46
A Glimpse into the Future
Hurricane Sandy from GOES-14 at two temporal resolutions
ABI-like

## Slide 47
NEdT = Noise Equivalent delta Temperature
Units: K
An estimate of noise used for IR bands
Valid at a reference temperature
Lower number is better
Recall the ABI has a much improved field-of-view size
  so the same NEdT is really an improvement
What is NEdT?

## Slide 48: ABI (and GOES) NEdT (K)
ABI |  |  |  | GOES |  |  | -12 | -15
Number | Nominal Central Freq. (µm) | Spec | Worst Case Estimate | Number | Nominal Central Freq. (µm) | Spec | Measured (PLT) | Measured (PLT)
7 | 3.9 | 0.1 | 0.064 | 2 | 3.9 | 1.4 | 0.130 | 0.063
8 | 6.2 | 0.1 | 0.016 |  |  |  |  | 
9 | 6.9 | 0.1 | 0.015 | 3 | 6.7/6.5 | 1.0 | 0.15 | 0.17
10 | 7.3 | 0.1 | 0.023 |  |  |  |  | 
11 | 8.4 | 0.1 | 0.022 |  |  |  |  | 
12 | 9.6 | 0.1 | 0.021 |  |  |  |  | 
13 | 10.3 | 0.1 | 0.032 |  |  |  |  | 
14 | 11.2 | 0.1 | 0.022 | 4 | 10.7 | 0.35 | 0.11 | 0.06
15 | 12.3 | 0.1 | 0.031 | 5 | 12.0 | 0.35 |  | 
16 | 13.3 | 0.3 | 0.068 | 6 | 13.3 | 0.32 | 0.19 | 0.13

## Slide 49
http://www.goes-r.gov
Notes: The subjects of this GOES-R Baseline products training are the aerosol products boxed in yellow.

## Slide 50
Cloud Top Phase

## Slide 51
Cloud Top Height + TPW

## Slide 52
Aerosol Optical Depth
Rain Rate
LST
Total Totals
Lifted Index
Showalter
SST
TPW
CAPE
K-index
Aerosol Detection
Cloud Mask
Cloud Top Height
Cloud Top Phase
Cloud Top Pressure
Snow
DOE-4 Simulated ABI (select) Derived Products
Using GOES-R ABI Imagery simulated at UW via AWG Proxy, processed via the Ground System, acquired via NOAAPort, in AWIPS-II (default enhancements)

## Slide 53: GOES-R Launch
16 Nov 2016 (TBR)
Cape Canaveral Air Force Station, Florida
Atlas V 541, United Launch Alliance

## Slide 54: Post Launch Plans

## Slide 55: Post Launch Plans
ABI imagery to AWIPS via NOAAPORT or GRB:
  L + 101 (TBC)
GLM data to AWIPS via NOAAPORT or GRB:
  L + 165 (TBC)
ABI Level2 products to AWIPS via NOAAPORT or GRB:
  validated in a rolling fashion once the L1b data is declared beta

## Slide 56: Advanced Baseline Imager (ABI)
5
4
3
X
Faster coverage (5-minute full disk vs. 25-minute)
X
Improved spatial resolution
(2 km IR vs. 4 km)
X
More spectral bands (16 on ABI vs. 5 on the current imager)
ABI on GOES-S
Notes: Slide from J. Gerth, CIMSS.

## Slide 57
GOES-R ABI
  Spectral, Spatial and Temporal
  Improved, Improved and Improved
Lockheed Martin
ABI

## Slide 58: Summary
1. The GOES-R ABI provides mission continuity
2. Two times the image navigation quality
3. Three times the number of imaging bands
4. Four times the spatial resolutions
5. Five times the coverage rate
- Special GOES-14 1-min data pathfinder
http://www.goes-r.gov

## Slide 59: GOES-R Series web site
Lockheed Martin
http://www.goes-r.gov