## Slide 1
GOES-R Overview
Tim Schmit
NOAA NESDIS STAR
Madison, WI
Fall 2016

## Slide 2: GOES-R
  Geostationary Lightning Mapper (GLM)
  Advanced Baseline Imager (ABI)
    3x more spectral bands
    4x spatial resolution
    5x temporal coverage
Space weather and solar imaging instruments
  Space Environment in-Situ Sensor Suite (SEISS)
  Magnetometer
  Solar Ultra-Violet Imager (SUVI)
  Extreme Ultraviolet and X-ray Irradiance Sensors (EXIS)
Next generation of NOAA/NASA geo weather satellites
  R-Series includes 4 satellites (R, S, T, U)
  First to launch in 04 Nov 2016
  Represents first major upgrade in over 20 years
Earth-pointing instruments

## Slide 3: GOES-R
Notes: Graphic from LM

## Slide 4: GOES-R main instruments
Images courtesy of SOHO EIT, a joint NASA/ESA program
Space Weather/Solar
ABI covers the earth 5X faster than current Imager
ABI – Advanced Baseline Imager
Geostationary Lightning Mapper
Unique Payload Services
No Sounder
SEISS
SUVI
EXIS
Magnetometer

## Slide 5: Geostationary Lightning Mapper(GLM)
East/West GLM FOV
~ 10 km across field of view with 8 km CONUS, 14 km at edge of field of view
Detects extent of total lightning activity
Day/night coverage with 70-90% flash detection (better at night)
Near-uniform detection efficiency spatially across the domain
Continuous coverage (2 ms frame rate)
<20 sec latency
Figures courtesy of Steve Goodman

## Slide 6: Current GOES Spectral Bands (5)
VIS
NIR
WV
IRW
CO2
Figures courtesy of Tim Schmit
1 VIS
0 NIR
4 IR

## Slide 7: ABI Spectral Bands (16)
0.64 m
0.86 m
1.38 m
1.61 m
2.26 m
3.9 m
6.19 m
6.95 m
7.34 m
0.47 m
8.5 m
9.61 m
10.35 m
11.2 m
12.3 m
13.3 m
Figures courtesy of Tim Schmit
2 VIS
4 NIR
10 IR

## Slide 8: Future vs. Current Spectral Bands
The current GOES (right) has 5 spectral bands, while the GOES-R series ABI (left) will have 16 spectral bands.

## Slide 9: Baseline ABI Scan Modes
Scan mode (3) or ‘flex mode’ for the ABI:
- Full disk every 15 minutes + 5 min CONUS
+ 1-min mesoscales (2 locations).
[Scan mode (4) or ‘Continuous Full Disk’ (CFD) is a full disk every 5 min]
Notes: CONUS image is the shifted center point.

## Slide 10
GOES-12 and GOES-R ABI
Simulation of Grand Prix Fire/Southern California
GOES-12
GOES-12
GOES-R ABI
GOES-R ABI
Notes: Here are two different fires from J. Feltz of CIMSS (using mcidas-v). What we can see is a more defined peak in the higher resolution data and it is easier to pick out individual hotspots. In addition, the higher saturation temperature of the ABI allows us to see that the fire is around 370K. ABI is simulated from MODIS.

## Slide 11
GOES
Figure courtesy of K. Bedka and W. Feltz

## Slide 12
“ABI” from MODIS
Figure courtesy of K. Bedka and W. Feltz

## Slide 13
A Glimpse into the Future
Hurricane Sandy from GOES-14 at two temporal resolutions
ABI-like

## Slide 14: Advanced Baseline Imager (ABI)
5
4
3
X
Faster coverage (5-minute full disk vs. 25-minute)
X
Improved spatial resolution
(2 km IR vs. 4 km)
X
More spectral bands (16 on ABI vs. 5 on the current imager)
ABI on GOES-S
Notes: Slide from J. Gerth, CIMSS.

## Slide 15
0.64 mm
3.9 mm
6.2 mm
13.3 mm
10.3 mm
11.2 mm
12.3 mm
6.9 mm
7.3 mm
8.4 mm
9.6 mm
0.47 mm
0.86 mm
1.37 mm
1.6 mm
2.2 mm
DOE-4 Simulated ABI Spectral bands
GOES-R ABI Imagery simulated at UW via AWG Proxy, processed via the Ground System, acquired via NOAAPort, shown in AWIPS-II (default enhancements)

## Slide 16
Aerosol Optical Depth
Rain Rate
LST
Total Totals
Lifted Index
Showalter
SST
TPW
CAPE
K-index
Aerosol Detection
Cloud Mask
Cloud Top Height
Cloud Top Phase
Cloud Top Pressure
Snow
DOE-4 Simulated ABI (select) Derived Products
Using GOES-R ABI Imagery simulated at UW via AWG Proxy, processed via the Ground System, acquired via NOAAPort, in AWIPS-II (default enhancements)

## Slide 17
http://www.goes-r.gov
Notes: The subjects of this GOES-R Baseline products training are the aerosol products boxed in yellow.

## Slide 18
GOES-R ABI
  Spectral, Spatial and Temporal
  Improved, Improved and Improved
Lockheed Martin
Me!
ABI

## Slide 19: Mission Planning
STAR very involved during the early GOES-R series development. This includes: formulation studies for both ABI and advanced geostationary sounder, ABI band selection and modification, Technical Requirement Documents, Performance and Operational Requirements Document, etc.
Originally ABI was only 8 spectral bands, now it is 16. All ABI bands were modified with input from STAR and it’s Cooperative Institutes.
ABI/ABS Requirements.
circa 1999/2000
Notes: Significant remaining scientific challenges for the specific science topic
Next step(s)
  Instruments (current/future), techniques, testbed, transition, …
Path into applications/operations
  Who will use it and how
  How will it get out to the real world

## Slide 20
Advanced Himawari Imager Spectral Bands

## Slide 21: AHI: Spectral (20-September-2015)
Visible
Infrared
Near- infrared

## Slide 22
Mount Pavlof volcano in Alaska
animation

## Slide 23
Tropical Cyclones (Meranti)

## Slide 24
Solar Eclipse

## Slide 25: AHI with Simulated Green Band