## Slide 1
GOES-R ABI “Flex” Mode (3) “CONUS” Coverage:
Increase separation between CONUS views from West and East
  Timothy J. Schmit (tim.j.schmit@noaa.gov)
NOAA/NESDIS
Satellite Applications and Research
Advanced Satellite Products Branch (ASPB)
Madison, WI
Jordan Gerth, Mat Gunshor, Kaba Bah, Will Straka and several others
CIMSS
March 28, 2014

## Slide 2: Outline
Background
Concerns/Solution
Proposal
Exploratory Scan Modes
Conclusions
Back-up material
current
proposed

## Slide 3: Background
Current plans for the center point of the GOES-R CONUS sectors from both the East and West satellites are centered over CONUS.
This implies a ‘one-satellite’ system and not the planned ‘two-satellite’ system. And hence a change should be considered to be more consistent with today’s GOES operations.
Instrument and ground system can support a shift of these center points. A ground system change would be needed to change the shape or timing of a CONUS sector.

## Slide 4
Scan mode (3) for the ABI:
- Full disk images every 15 minutes + 5 min CONUS images + mesoscale.
ABI scans about 5 times faster
than the current GOES imager

## Slide 5
ABI can offer Continental US images every 5 minutes for routine monitoring of a wide range of events (storms, dust, clouds, fires, winds, etc).
This is every 15 or 30 minutes with the current GOES in routine mode.
Notes: Approx. size of CONUS

## Slide 6
Notes: Approx. size of CONUS

## Slide 7
Mesoscale images every 30 seconds for rapidly changing phenomena
(thunderstorms, hurricanes, fires, etc). Or two regions every 60 seconds.
Notes: Approx. size of meso-scale showing “Franklin”.

## Slide 8
Volume 4 of the PUG (version C)
http://www.goes-r.gov/users/docs/PUG-GRB-vol4-verC.pdf

## Slide 9: Concerns/Solutions
Current plans for the ABI on GOES-R call for all of the CONUS to be scanned by both the GOES-West and –East (most likely at the same time), while not scanning important parts of the Pacific (as we scan today)
Consider optimizing the planned ABI CONUS sector
  (e.g., moving the GOES-West ‘CONUS’ sector towards the west and GOES-East ‘CONUS’ sector slightly east)
Time is of the essence if these schedules are to modified (requirement documents, test data, data flow, etc.)

## Slide 10
Current GOES CONUS from East
Note coverage east of Puerto Rico

## Slide 11
Current GOES PACUS from West
Note coverage both east and west of Hawaii

## Slide 12
space
space
space
Current Plans for ABI CONUS sectors
Note lack on coverage of Hawaii and much of the eastern Pacific

## Slide 13
Current view of Northeast US from 135W
Note very poor view angle from a Western GOES

## Slide 14
Option for moving ABI from GOES-West to the West (and East sector to the East)
PROPOSED

## Slide 15
Option for moving ABI from GOES-West to the West (and East sector to the East) with potential/re-locatable Alaska one-minute mesoscale sector (approximate coverage)
PROPOSED

## Slide 16
Option for moving ABI from GOES-West to the West (and East sector to the East) with potential/re-locatable Alaska one-minute mesoscale sector (approximate coverage) and additional sector for Hawaii or American Samoa from West and two locations via the Eastern satellite
PROPOSED
Notes: Of course there would also be 2 meso possible from the ABI at GOES-East

## Slide 17
space
space
space
Current Plans for ABI CONUS sectors

## Slide 18: Proposal
Move the GOES-West ‘CONUS’ sector to the west, to get less overlap over CONUS and extend coverage over the North Pacific (including Hawaii)
Move the GOES-East CONUS sector to the east, to get less overlap and more coverage to the east of Puerto Rico and for tropical waves/TC

## Slide 19: ABI CONUS Center Points
Satellite | Current | Current | Proposed | Proposed
 | Latitude | Longitude | Latitude | Longitude
GOES-West | 29.5004 | -103.1168 (PUG via lat/long) | 30.0 | -137.0
GOES-East | 29.8360 | -90.5385 | 30.0 | -87.0

## Slide 20
Simulated ABI band 9 (7 micrometer) brightness temperature at 21:45 UTC
CONUS from West (current plan)
Notes: Imagery shown in McIDAS-V

## Slide 21
Simulated ABI band 9 (7 micrometer) brightness temperature at 21:45 UTC
CONUS from West (proposed)
Notes: Imagery shown in McIDAS-V

## Slide 22
Simulated ABI band 9 (7 micrometer) brightness temperature at 21:45 UTC
CONUS from East (current plan)
Notes: Imagery shown in McIDAS-V

## Slide 23
Simulated ABI band 9 (7 micrometer) brightness temperature at 21:45 UTC
CONUS from East (proposed)
Notes: Should this be moved to the east yet to cover Montserrat? (16N 62W).

## Slide 24
CONUS from East and West (current)
Notes: Different days simulated.

## Slide 25
CONUS from East and West (proposed)
Notes: Different days simulated.

## Slide 26: Exploratory Scan Modes
In the future, when possible, consider to reshape ‘PACUS’ and/or the ‘mesoscale’ to be a more efficient system (e.g. the size aspect ratio of the CONUS scan or a “half-height” mesoscale, double wide).
These would take a ground system change.
At a minimum, data in mode 3 and 4 can be collected during the Post Launch Testing phase.

## Slide 27: Exploratory ABI Scan Strategies
Every 6 minutes
Every 10 minutes
Every 15 minutes
Every 3.75 minutes
One “CONUS” sector every 2 minutes
One mesoscale sector
every 30 seconds (one or two locations)
One mesoscale sector
every 30 seconds (one or two locations)
Option
A
Option
B
Option
C
&
&
&
There are some alternative ABI scan strategies to Mode 3 and Mode 4.
Notes: Scan areas and timing are approximate.

## Slide 28
Ground System FPS, Appendix E
Outside of CONUS, Hawaii, Alaska and Puerto Rico, imagery will be 6 km in AWIPS.
At some point, the GS FPS file will be posted on the GOES-R web page.
(File available upon request)

## Slide 29
Notes: ABI band 2 (0.6 micrometers) will be finer resolution than the imagery shown and the 6km may be worse since this is 6km in a Mercator.

## Slide 30
Notes: ABI band 2 (0.6 micrometers) will be finer resolution than the imagery shown.

## Slide 31: Conclusions
Current plans call for the GOES-West CONUS to be over CONUS (and not to the west, as the current PACUS), this means that more ‘up stream’ imagery on AWIPS will be at the 6km spatial resolutions. (Hence there will be less ‘6 km’ data if the CONUS sectors are more separated.)
Hence, it’s a good plan for the national centers, etc. to get their data via a GOES-R GRB, and hence can acquire full resolution imagery, outside of the certain sectors.
The ‘West’ CONUS should be moved much farther to the West and the ‘East’ CONUS should be slightly shifted to the East.
  Time is of the essence for requesting these changes

## Slide 32: Back-up Material
Consider sending the full GRB data to AWIPS once in the ABI Fixed Grid Format (FGF) and have AWIPS do any local remapping.
This could streamline the process of making different resolution images for various projections

## Slide 33
Current plans call for GOES-R to have a 6 month check-out and then replace GOES-15 as the Western GOES. GOES-S is slated to replace GOES-14 in 2020 as the eastern GOES.
Notes: http://www.nesdis.noaa.gov/pdf/flyout_pdf/GOES_Flyout_Chart_10_01_13.pdf

## Slide 34
Launch & Orbit Raising
Operations
Post-launch Testing (PLT) - 180 Days
Activation & Characterization Test (ACT)
System Performance Operational Test (SPOT)
14 Days
40 Days
84 Days
1 Year
Initial Checkout
14 Days
Contingency Operations Readiness Review (CORR)
Operational Acceptance Review (OAR) – Handover to OSPO
42 Days
Cal/INR Checkout
*Post-Launch Product Testing (PLPT)
Post-Handover Product Validation
ABI (L1b)
ABI (KPP)
ABI (Other L2+)@
<=5yrs Storage + >=8.4 Yrs Ops
Unvalidated Product
Beta
Provisional
Comprehensive
1 Year
GOES-R Post-Launch Product Validation Stages (Nominal Timeline)
* NOAA Science Test
Provisional values are only drafts.
@ Maturity level may vary for each product, as product availability is driven by maturity of
algorithm implementation, as well as the existence of science phenomena and associated ground-truth data.
Notes: Last updated: 9/9/2013

## Slide 35
Combined AWIPS image
The seam in AWIPS for combined imagery over CONUS is at approximately 115W.
This means that the data on the far edge isn’t used in the composites for AWIPS.

## Slide 36
seam

## Slide 37
seam

## Slide 38: ABI CONUS Center Points
Satellite | Current | Current | Proposed | Proposed
 | Latitude | Longitude | Latitude | Longitude
GOES-West | 29.5004 | -103.1168 (PUG via lat/long) | 30.0 | -137.0
 |  | -102.8004 (PUG via x,y) |  | 
 |  | -102.5111 (ITT doc) |  | 
GOES-East | 29.8360 | -90.5385 | 30.0 | -87.0