## Slide 1: Monitoring Vegetation and Land Features
Steve Ackerman
Director CIMSS
Prof. AOS

## Slide 2: Objectives
Describe the capabilities, benefits, and limitations of land remote sensing
Define NDVI and NDSI
Describe applications that benefit from vegetation indices
Interpret features in NDVI and NSDI imagery

## Slide 3
Satellite Observation (radiance, reflectance, brightness temperature)
Atmosphere Reflectance, Transmittance and Emission
Atmosphere Temperature and gas distribution
Cloud aerosol optical depth (how much), single scattering albedo (absorption) and phase function (where does scattered energy go)
Particle sizes, shapes and chemistry
Underlying surface
Particle size is relative to the wavelength

## Slide 4: Reflectance properties of surfaces

## Slide 6: Vegetation Indices
Global vegetation indices are designed to provide consistent spatial and temporal comparisons of vegetation conditions. Blue, red, and near-infrared reflectances, centered at 469-nanometers, 645-nanometers, and 858-nanometers, respectively, are used to determine the daily vegetation indices.

## Slide 7: MODIS
The Moderate Resolution Imaging Spectroradiometer (MODIS) measures radiances at 36 wavelengths including infrared and visible bands with spatial resolution of 250 m , 500m and 1 km.
It is a scanning instrument that yields ‘images’ at the different wavelengths.

## Slide 8: MODIS Bands
Reflective Bands
1,2 0.645, 0.865 land/cld boundaries
3,4 0.470, 0.555 land/cld properties
5-7 1.24, 1.64, 2.13 “
8-10 0.415, 0.443, 0.490 ocean color/chlorophyll
11-13 0.531, 0.565, 0.653 “
14-16 0.681, 0.75, 0.865 “
17-19 0.905, 0.936, 0.940 atm water vapor
26 1.375 cirrus clouds

## Slide 9: MODIS Bands
Emissive Bands
20-23 3.750(2), 3.959, 4.050 sfc/cld temp
24,25 4.465, 4.515 atm temperature
27,28 6.715, 7.325 water vapor
29 8.55 sfc/cld temp
30 9.73 ozone
31,32 11.03, 12.02 sfc/cld temp
33-34 13.335, 13.635 cld top properties
35-36 13.935, 14.235 cld top properties

## Slide 11: Vegetation Index
Vegetation indices are optical measures of vegetation canopy “greenness,” a composite property of leaf chlorophyll, leaf area, canopy cover, and structure. VIs are not “intrinsic physical quantities” but are widely used as proxies to assess canopy biophysical/biochemical variables have improved in recent years, they still have limitations.

## Slide 12: NDVI
The NOAA Advanced Very High Resolution Radiometer (AVHRR)-derived consistent global normalized difference vegetation index (NDVI) land record exists, which has contributed significantly to global biome, ecosystem, and agricultural studies.

## Slide 13: NDVI
An advantage of the NDVI as a ratio, is its ability to normalize and produce stable values across large variations in incoming direct/diffuse irradiances. However, this also results in some disadvantages including the nonlinear nature of ratios, sensitivity to soil background, and saturation at moderate-to-high vegetation densities.
Should atmosphere correct the radiances.

## Slide 14: NDVI
2004 – January - December
Notes: MODIS Vegetation Indices
Alfredo Huete, Kamel Didan, Willem van Leeuwen, Tomoaki Miura, and Ed Glenn

## Slide 15: Global NDVI

## Slide 16: NDVI – long term
Notes: http://publiclab.org/notes/cfastie/3-24-2012/grassroots-ndvi-time-series

## Slide 17: NDVI
Negative values of NDVI (values approaching -1) correspond to water. Values close to zero (-0.1 to 0.1) generally correspond to barren areas of rock, sand, or snow. Lastly, low, positive values represent shrub and grassland (approximately 0.2 to 0.4), while high values indicate temperate and tropical rainforests (values approaching 1)

## Slide 18: Enhanced Vegetation Index (EVI)
The blue band in the EVI is primarily used to stabilize aerosol influences in the
red band resulting from residual and aerosol miscorrection.
The EVI better depict biophysical canopy structural variations, and is less prone to saturate in high biomass areas.

## Slide 19: Recap
Vegetation indices are good to monitor the variations of vegetation. Need to remove clouds and correct for scattering by the atmosphere and aerosols.
NDVI and EVI are two popular indices..

## Slide 20: Snow Index?

## Slide 21: Reflectance properties of surfaces
Choose two wavelengths