## Slide 1
Why is “Lower-level water vapor” band imagery important?
The 7.3 µm “Lower-level water vapor” band is one of three water vapor bands on the ABI. It typically senses farthest down into the mid-troposphere in cloud-free regions, to around 500-750 hPa. It is used to track lower-tropospheric winds, identify jet streaks, monitor severe weather potential, estimate lower-level moisture (for legacy vertical moisture profiles), identify regions where the potential for turbulence exists, highlight volcanic plumes that are rich in sulphur dioxide (SO2) and track Lake-Effect snow bands.
  Input into Baseline Products: The 7.3 µm imagery is used in the creation of Derived Motion Winds, the Cloud Mask, Stability Indices, Total Precipitable Water, Rain Rate, and Volcanic Ash products.
  Application: Identification of volcanic plumes that have a high concentration of SO2.
  Primary Application Atmospheric feature identification (jet streaks, dry slots, signatures of potential turbulence, contrails, downslope winds., Lake Effect)
Impact on Operations
  Interpretation of water vapor imagery: The “water vapor” bands are technically infrared bands which sense the mean temperature of a layer of moisture — a layer whose altitude and depth can vary, depending on both the temperature/moisture profile of the atmospheric column and the satellite viewing angle. Water vapor weighting function plots may help you correctly interpret the three-dimensional aspects of patterns displayed on water vapor imagery. Band 8 and Band 9 Quick Guides contain simple plots.
  Regions of dense cloudiness: The presence of optically-dense clouds obstructs the view of lower altitude moisture features.
Limitations
Contributors: Scott Bachmeier, Tim Schmit, Jordan Gerth (UW-Madison CIMSS/NOAA) September 2017
Comparison of ABI Water Vapor Bands
Left: U.S. Standard Atmosphere Earth-emitted temperatures and spectral responses for ABI and GOES-13 Water Vapor Channels. The Legacy channel (6.5 mm) covers much of the 6.2 mm and 6.9 mm and 7.3 mm bands on ABI (Figure: Mat Gunshor, CIMSS)
6.5 mm
6.2 mm
6.9 mm
ABI Band 10 (7.3 mm)
7.3 mm
Quick Guide

## Slide 2
Horizontal convective rolls
Dryline
  To the east of the dryline oriented N-S along the Texas / New Mexico border, strong southerly winds caused blowing dust; plumes of lofted dust were organized into horizontal convective rolls aligned parallel to the wind flow
Image Interpretation
Resources
BAMS Article Schmit et al., 2017
GOES-R.gov ABI Band 10 Fact Sheet
VISIT Satellite Chat GOES-16 Water Vapor Band Ororgraphic Applications
Hyperlinks do not work in AWIPS but they do in VLab
1
2
Visible (0.64 µm) and Lower-Level Water Vapor (7.3 µm) images, 21:52 UTC on 23 March 2017
Quick Guide
ABI Band 1 (0.47 mm)
The 7.3 µm band can detect lower-level clouds when the middle/upper atmosphere is relatively dry— this example shows marine boundary layer stratocumulus over the Atlantic Ocean. (Credit: CIMSS)
1
    Low-Level Water Vapor
ABI Band 10 (7.3 mm)
2
2
0.64 µm
Texas
Texas
1
7.3 µm
6.9 µm
1
1
23 March 2017 2152 UTC
23 March 2017 2152 UTC
GOES-16 ABI
GOES-16 ABI
Visible Band 2
Water Vapor Band 10