## Slide 1
The ABI on GOES-R Series
  Timothy J. Schmit (tim.j.schmit@noaa.gov)
NOAA/NESDIS/Satellite Applications and Research
Advanced Satellite Products Branch (ASPB)
  Jordan Gerth (jordan.gerth@noaa.gov)
CIMSS
Madison, WI
Plus many, many more…
UW-Madison
GOES-R User Readiness
Kansas City
June 16, 2015

## Slide 2: Thanks to…
Paul Menzel, Steven J. Goodman, Daniel T. Lindsey, Robert M. Rabin, Kristopher M. Bedka, John L. Cintineo, Christopher S. Velden, A. Scott Bachmeier, Scott Lindstrom, Mat Gunshor, Chris Schmidt
Kaba Bah, Joleen Feltz, Tom Whittaker, Margaret Mooney, Andy Heidinger, William Straka, Jun Li, Steve Ackerman, Bob Aune, Don Hillger, Tony Schreiner, Justin Sieglaff, Jim Jung, Elaine Prins, Brad Pierce, Wayne Feltz, Jean Phillips, Linda Hedges, Jim Nelson, Gary Wade, Don Hillger, Jinlong Li, Jing Zheng, Allen Huang, Bob Rabin, the SSEC data center, Mike Pavolonis, Jaime Daniels, ASPB, STAR, NESDIS, NSSL, MUG, Kevin Ludlum, GOES operators, GOES shift supervisors, Mark DeMaria, Dave Martin, Joe Schmit and many others!
GOES-R Program Office, Greg Mandt, NASA, Exelis Industries, Lockheed Martin, and other industry partners, etc.
You.

## Slide 3: Outline
Overview
ABI
  Spectral
  Temporal
  Spatial
Other
Summary
More information
Lockheed Martin

## Slide 4
GOES Flyout Chart w/
Fuel-Limited Lifetime Phase Added

## Slide 5: Validation and Availability for GOES-R Baseline Products
GOES-R Launch
to 89.5° West
Milestone:
Program Phase:
Pre-Launch | PLT (6 months) | Post-Handover
Operations Handover
(includes Products)
On-Orbit East/West
Operations
Extended Validation
L1b Product Activities
L1b Validation - Products recertified against pre-launch instrument performance
‘First Light’ Data captures shared from Instruments
Insertion of L1b products into GRB service is controlled by ground system and will occur as products are certified
(Figure from Matt Seybold from NOAA Satellite Conference)
Notes: More precisely: L1b Validation – On-orbit product performance recertified against pre-launch analytically-predicted product performance.

## Slide 6
~90W (Approximate location of GOES-R during check-out)
Notes: Data from SSEC Data Center

## Slide 7: The Advanced Baseline Imager:
ABI Current
Spectral Coverage
16 bands 5 bands
Spatial resolution
0.64 mm Visible 0.5 km Approx. 1 km
Other Visible/near-IR 1.0 km n/a
Bands (>2 mm) 2 km Approx. 4 km
Spatial coverage
Full disk Every 15 min Scheduled (3 hrly)
CONUS Every 5 min ~4 per hour
Mesoscale Every 30 sec n/a
Visible (reflective bands)
On-orbit calibration Yes No
Notes: The ABI allows more bands, finer spatial resolution, faster refresh rates and on-orbit calibration of all bands!

## Slide 8
seam

## Slide 9: Advanced Baseline Imager
5
4
3
X
Faster coverage (5-minute full disk vs. 25-minute)
X
Improved spatial resolution
(2 km IR vs. 4 km)
X
More spectral bands (16 on ABI vs. 5 on the current imager)
Notes: Slide from J. Gerth, CIMSS.

## Slide 10
0.64 m
0.86 m
1.38 m
1.61 m
2.26 m
3.9 m
6.19 m
6.95 m
7.34 m
0.47 m
8.5 m
9.61 m
10.35 m
11.2 m
12.3 m
13.3 m
Simulated ABI bands (as shown in AWIPS)

## Slide 11
Current GOES Imager band selection

## Slide 12: Outline
Overview
ABI
  Spectral
  Temporal
  Spatial
Other
Summary
More information

## Slide 13: ABI bands 1-6
2 visible bands and 4 near infrared bands on the ABI, compared to only one on today’s imager
Approximate:
Notes: Final column added: heritage. The ABI band 1 was suggested by Dr. Fred Mosher at a GOES Users' Conference.
The ABI band 3 was suggested by the late Dr. C. Rao (of the then ORA).
Some of these bands have been shifted to more closely match those on the VIIRS.

## Slide 14
The ABI visible and near-IR bands have many uses.
Aerosols, Insolation
Clouds, Snow
Vegetation, Imagery
Cloud mask, Suspended matter
Cloud Particle size
Snow, Phase
Visible and near-IR channels on the ABI
Sample use only, many other uses
Notes: Schmit, T. J., M. M. Gunshor, W. P. Menzel, J. J. Gurka, J. Li, and A. S. Bachmeier, 2005: Introducing the next-generation Advanced Baseline Imager on GOES-R. Bull. Amer. Meteor. Soc., 86, 1079-1096.

## Slide 15: ABI bands 7-16
10 infrared bands on the ABI, compared to four on today’s imager
Approximate:
Notes: The ABI band 10 was modified to better depict upper-level SO2. (G. Ellrod and others)
The ABI band 11 was suggested by Steve Ackerman (CIMSS), based on HIRS experience.
The ABI band 13 was suggested by W. P. Menzel (then NOAA NESDIS).

## Slide 16
ABI has many more bands than the current operational GOES imagers.
The IR channels on the ABI
Clouds, Stability Indices
Rainfall, Aerosol
Fires, Radiances
Hurricane, Imagery
Cloud Phase, SO2, dust
Ozone, Downward Radiation
SO2, Radiances
Winds, WV profiling
TPW, Rainfall rate
Fires, Fog
Sample use only, many other uses
Notes: Schmit, T. J., M. M. Gunshor, W. P. Menzel, J. J. Gurka, J. Li, and A. S. Bachmeier, 2005: Introducing the next-generation Advanced Baseline Imager on GOES-R. Bull. Amer. Meteor. Soc., 86, 1079-1096.

## Slide 17: Future vs. Current Spectral Bands
The current GOES (right) has 5 spectral bands, while the GOES-R series ABI (left) will have 16 spectral bands.

## Slide 18
ABI Band 01 Generated by DOE-0, Visualized by McIDAS-V Script
Notes: This date & time is a processing time, not the time the data represent.

## Slide 19
ABI Band 02 Generated by DOE-0, Visualized by McIDAS-V Script

## Slide 20
ABI Band 03 Generated by DOE-0, Visualized by McIDAS-V Script

## Slide 21
ABI Band 04 Generated by DOE-0, Visualized by McIDAS-V Script

## Slide 22
ABI Band 05 Generated by DOE-0, Visualized by McIDAS-V Script

## Slide 23
ABI Band 06 Generated by DOE-0, Visualized by McIDAS-V Script

## Slide 24
ABI Band 07 Generated by DOE-0, Visualized by McIDAS-V Script

## Slide 25
ABI Band 08 Generated by DOE-0, Visualized by McIDAS-V Script

## Slide 26
ABI Band 09 Generated by DOE-0, Visualized by McIDAS-V Script

## Slide 27
ABI Band 10 Generated by DOE-0, Visualized by McIDAS-V Script

## Slide 28
ABI Band 11 Generated by DOE-0, Visualized by McIDAS-V Script

## Slide 29
ABI Band 12 Generated by DOE-0, Visualized by McIDAS-V Script

## Slide 30
ABI Band 13 Generated by DOE-0, Visualized by McIDAS-V Script

## Slide 31
ABI Band 14 Generated by DOE-0, Visualized by McIDAS-V Script

## Slide 32
ABI Band 15 Generated by DOE-0, Visualized by McIDAS-V Script

## Slide 33
ABI Band 16 Generated by DOE-0, Visualized by McIDAS-V Script

## Slide 34
0.47 um

## Slide 35
0.64 um

## Slide 36
0.86 um

## Slide 37
1.37 um

## Slide 38
1.6 um

## Slide 39
2.24 um

## Slide 40
3.9 um

## Slide 41
6.2 um

## Slide 42
6.9 um

## Slide 43
7.3 um

## Slide 44
8.4 um

## Slide 45
9.6 um

## Slide 46
10.3 um

## Slide 47
11.2 um

## Slide 48
12.2 um

## Slide 49
13.3 um

## Slide 50
Visible and Near-IR bands on the ABI ….

## Slide 51
NASA’s VIIRS M7 band (0.865 μm) is shown for two times. On the left is before (August 13, 2013) and on the right is after (August 30, 2013) the California Rim Fire. Note the smoke plume and pyrocumulus along the periphery of the dark burn scar near the center of the image on the right, and the large burn scar just to the west of the smoke plume.
0.865 m is helpful for burn scar detection

## Slide 52
1.88 m (or 1.38 m) is helpful for contrail detection
Aircraft case -- Clear?

## Slide 53
Using the 1.6 um ABI band for cloud phase….and elevated dust

## Slide 54
Why we can see hot fires in the 2.2 um (and 1.6 um) ABI bands
AHI images over Australia on March 23, 2015 of bands 3.9 μm (left) 1.6 μm (right) showing a fire. The AHI 1.6 μm is nominally 2 km spatial resolution, while on the ABI the band will be 1 km.
Radiance versus wavelength

## Slide 55
AHI Band | AHI Approximate Central Wavelength [μm] | ABI Approximate Central Wavelength [μm] | ABI Band | Type | Nickname | Information
1 | 0.47 | 0.47 | 1 | Vis | Blue | Blue
2 | 0.51 |  |  | Vis | Green | Green
3 | 0.64 | 0.64 | 2 | Vis | Red | Red
4 | 0.86 | 0.86 | 3 | NIR | Veggie | Vegetation
 |  | 1.37 | 4 | NIR |  | 
5 | 1.6 | 1.6 | 5 | NIR | Phase/Snow | Snow/Ice
6 | 2.3 | 2.24 | 6 | NIR | Particle size | Cloud particle size
7 | 3.9 | 3.9 | 7 | IR | Shortwave | Shortwave IR window
8 | 6.2 | 6.2 | 8 | WV | Upper-level | Upper-level tropospheric water vapor
9 | 6.9 | 6.9 | 9 | WV | Mid-level | Upper/mid-level tropospheric water
10 | 7.3 | 7.3 | 10 | WV | Lower-level | Lower mid-level water vapor
11 | 8.6 | 8.4 | 11 | IR | Phase | Cloud-top phase
12 | 9.6 | 9.6 | 12 | IR | Ozone | Ozone (total)
13 | 10.4 | 10.3 | 13 | IR | Clean window | Clean IR longwave window
14 | 11.2 | 11.2 | 14 | IR | Window | Traditional IR longwave window
15 | 12.4 | 12.3 | 15 | IR | “Dirty” window | “Dirty” longwave window
16 | 13.3 | 13.3 | 16 | IR | CO2 | CO2 longwave
AHI and ABI
Notes: Thanks to JMA for the format and some of the info on this slide.

## Slide 56
AHI Band | Central Wavelength [μm] | Type | Nickname | Information
1 | 0.47 | Vis | Blue | Blue
2 | 0.51 | Vis | Green | Green
3 | 0.64 | Vis | Red | Red
4 | 0.86 | NIR | Veggie | Vegetation
5 | 1.6 | NIR | Phase/Snow | Snow/Ice
6 | 2.3 | NIR | Particle size | Cloud particle size
7 | 3.9 | IR | Shortwave | Shortwave IR window
8 | 6.2 | WV | Upper-level | Upper-level tropospheric water vapor
9 | 6.9 | WV | Mid-level | Upper/mid-level tropospheric water
10 | 7.3 | WV | Lower-level | Lower mid-level water vapor
11 | 8.6 | IR | Phase | Cloud-top phase
12 | 9.6 | IR | Ozone | Ozone (total)
13 | 10.4 | IR | Clean window | Clean IR longwave window
14 | 11.2 | IR | Window | Traditional IR longwave window
15 | 12.4 | IR | “Dirty” window | “Dirty” longwave window
16 | 13.3 | IR | CO2 | CO2 longwave
AHI
Notes: Thanks to JMA for the format and some of the info on this slide.

## Slide 57
ABI Band | Central Wavelength [μm] | Type | Nickname | Information
1 | 0.47 | Vis | Blue | Blue
2 | 0.64 | Vis | Red | Red
3 | 0.86 | NIR | Veggie | Vegetation
4 | 1.37 | NIR | Cirrus | Upper level Cirrus/elevated dust
5 | 1.6 | NIR | Snow/phase | Snow/Ice
6 | 2.24 | NIR | Particle size | Cloud particle size
7 | 3.9 | IR | Shortwave | Shortwave IR window
8 | 6.2 | WV | Upper-level | Upper-level tropospheric water vapor
9 | 6.9 | WV | Mid-level | Upper/mid-level tropospheric water
10 | 7.3 | WV | Lower-level | Lower mid-level water vapor
11 | 8.4 | IR | Phase | Cloud-top phase
12 | 9.6 | IR | Ozone | Ozone (total)
13 | 10.3 | IR | Clean window | Clean IR longwave window
14 | 11.2 | IR | Window | Traditional IR longwave window
15 | 12.3 | IR | “Dirty” window | “Dirty” longwave window
16 | 13.3 | IR | CO2 | CO2 longwave
ABI

## Slide 74: Educational Webapps Developed
NOAA NESDIS ASPB teamed up with CIMSS researchers to develop three educational WebApps to explore space, time and spectral resolutions of satellite imagery.
Part of the GOES-R Educational Proving Ground at CIMSS:
http://cimss.ssec.wisc.edu/education/goesr
Teacher feedback: “…. Wow!! This is awesome!! This is impressive. Thank you for sharing. This is great. Thanks for all your hard work and help!!!! We are honored and will use it next week … Earth SySTEM Teacher Academy”
Sample interactive “Bandapp” educational webapp using simulated ABI images:
http://cimss.ssec.wisc.edu/goes/webapps/bandapp/
T. Schmit
Notes: Tim Schmit, ASPB
https://ams.confex.com/ams/95Annual/webprogram/Paper265203.html ABI = Advanced Baseline Imager
Other new webapps: one to change both the spatial and temporal sampling and the other only the pixel sampling

## Slide 75
There are also several case studies using current GOES imagery (5 spectral bands)
with the option to add descriptive annotations,
or add map outlines.

## Slide 76
Mouse over anywhere in the image to get an interactive pop-up chart that provides data (reflectance
& temperature)
for each band at that location.

## Slide 77: Hands-on…Spectral
Step through the ABI spectral bands (and turn on the interactive chart)
  One of the simulated cases
  http://cimss.ssec.wisc.edu/education/apps/bandapp/overview_goes-r.html
  or
  http://cimss.ssec.wisc.edu/goes/webapps/bandapp/
Or step through the AHI spectral bands (and turn on the interactive chart)
  One of the observed cases
  http://cimss.ssec.wisc.edu/education/apps/bandapp/overview_ahi_first_images.html
  or
  http://cimss.ssec.wisc.edu/goes/webapps/bandapp/overview_ahi_first_images.html

## Slide 78: Three ABI water vapor bands
Current GOES
Future GOES
Images from J. Feltz
Notes: Note the 3 layers of information possible from the ABI (right panel).
http://www.ssec.wisc.edu/mcidas/software/v/

## Slide 79: Weighting Functions
How the transmittance varies with height
The layer of the atmosphere observed by a given spectral band
Depends on the band, input temperature, moisture, ozone profiles, skin temperature, surface emissivity, plus the view (zenith) angle.
Clear-sky fast forward calculations
A surface emissivity value of 1 is used for each band.

## Slide 80
Rsfc R1 R2
top of the atmosphere
τ2 = transmittance of upper layer of atm
τ1= transmittance of lower layer of atm
blackbody earth surface.
Robs =
Rsfc τ1 τ2 + R1 (1-τ1) τ2 + R2 (1- τ2)
From W. P. Menzel
Notes: From W. P. Menzel

## Slide 81: ABI Clear-sky Weighting Functions

## Slide 82: http://cimss.ssec.wisc.edu/goes/wf/ABI/

## Slide 83: ABI Weighting Functions
As a function of….
  View angle

## Slide 84: Hands-on….Weighting Functions
How many mid-level water vapor bands?
How many window bands?
Which band peaks the highest in the atmosphere?
What’s the cleanest IR window?
  Select an atmosphere and view angle:
  http://cimss.ssec.wisc.edu/goes/wf/ABI/
  Look at realtime GOES WF
  http://cimss.ssec.wisc.edu/goes/wf/

## Slide 85: RGB Web App

## Slide 86: Sat RGB
Select an input for each band
Click “Combine Channels”

## Slide 87: Hands-on….Red-Green-Blue
Combine the bands to bring out a feature of interest
  http://cimss.ssec.wisc.edu/goes/webapps/satrgb/overview.html
  One of the simulated ABI cases
  http://cimss.ssec.wisc.edu/education/apps/bandapp/overview_goes-r.html
  One of the observed AHI cases
  http://cimss.ssec.wisc.edu/goes/webapps/satrgb/overview_ahi.html

## Slide 88: Outline
Overview
ABI
  Spectral
  Temporal
  Spatial
Other
Summary
More information

## Slide 89: Baseline ABI Scan Modes
Scan mode (3) or ‘flex mode’ for the ABI:
- Full disk every 15 minutes + 5 min CONUS
+ 1-min mesoscales (2 locations).
[Scan mode (4) or ‘Continuous Full Disk’ (CFD) is a full disk every 5 min]
Notes: CONUS image is the shifted center point.

## Slide 90: Recent Mode 3 (Flex mode) “Time-Time” chart
Draft
Note the ‘white’ space is instrument idle time.
Notes: Copy and pasted from excel. Pasted as a picture. Resized to 44% by 44% of original. Arrange -> Align -> Align Center & Align Middle

## Slide 91: Baseline Time-Time Mode 4 (Continuous Full Disk)
This is the Continuous Full Disk (every 5 min) mode
This is the highest data rate.

## Slide 92
Concept of flex mode scanning animation
Figure courtesy of J. Li, CIMSS

## Slide 93: Loop over Peoria

## Slide 94: GOES-15 Science Test
Unique GOES-15 Imager Visible data from the NOAA Science Test
30-min
1-min
The Science Test part of Post Launch Testing for GOES-15 occurred in the summer of 2010.
Co-led by Hillger and Schmit.
Unique 1-minute rapid scan imagery acquired
GOES-15 data analysis will continue. All the GVAR data archived.
Many products generated in near real-time.
A NOAA Technical Report was generated.
Notes: Igor

## Slide 95: Sample “1-min” visible imagery
See “what is happening”, not “what has happened”.
GOES-12
GOES-14
Notes: Note the number of different levels of motion you can see (the cyclonic low level circulation over the ocean through the breaks in the higher clouds)... and you can't distinguish those on the GOES-12 loop.

## Slide 96
Flex Mode (3) would offer a total of 4 meso-scale sectors, from the combined 2 satellite constellation.
PROPOSED
Notes: Of course there would also be 2 meso possible from the ABI at GOES-East

## Slide 97
ABI CONUS sector scan coverage from East and West (NOAT/GORWG-approved)
Notes: Different days simulated.

## Slide 98: Outline
Overview
ABI
  Spectral
  Temporal
  Spatial
Other
Summary
More information
Lockheed Martin

## Slide 99
ABI IR Pixel size from West and East
(proposed ABI CONUS West and East)
East Optimal
West Optimal

## Slide 100: ABI
Figure from J. Key, ASPB
In general, even at 50 degrees view angles, the spatial resolution of the ABI is comparable to today’s imager at the satellite sub-point.

## Slide 101
Current GOES-East Sample LZA’s
<30
<40
<50
<60

## Slide 102
Current GOES-West Sample LZA’s
<30
<40
<50
<60

## Slide 103
GOES-12 and GOES-R ABI
Simulation of Grand Prix Fire/Southern California
GOES-12
GOES-12
GOES-R ABI
GOES-R ABI
Notes: Here are two different fires from J. Feltz of CIMSS (using mcidas-v). What we can see is a more defined peak in the higher resolution data and it is easier to pick out individual hotspots. In addition, the higher saturation temperature of the ABI allows us to see that the fire is around 370K. ABI is simulated from MODIS.

## Slide 104
GOES
Figure courtesy of K. Bedka and W. Feltz

## Slide 105
“ABI” from MODIS
Figure courtesy of K. Bedka and W. Feltz

## Slide 106
Nocturnal Fog/Stratus Over the Northern Plains
ABI image (from MODIS) shows greater detail in structure of fog.
“ABI” 4 minus 11 μm Difference
Notes: Note the ABI (from MODIS) image is better spatial resolution and better signal-to-noise ratio then the GOES-10 imager.
Schmit, T. J., M. M. Gunshor, W. P. Menzel, J. J. Gurka, J. Li, and A. S. Bachmeier, 2005: Introducing the next-generation Advanced Baseline Imager on GOES-R. Bull. Amer. Meteor. Soc., 86, 1079-1096.

## Slide 107
ABI image (from MODIS) shows greater detail in structure of fog.
GOES-10 4 minus 11 μm Difference
Nocturnal Fog/Stratus Over the Northern Plains
Notes: Schmit, T. J., M. M. Gunshor, W. P. Menzel, J. J. Gurka, J. Li, and A. S. Bachmeier, 2005: Introducing the next-generation Advanced Baseline Imager on GOES-R. Bull. Amer. Meteor. Soc., 86, 1079-1096.

## Slide 108: GOES-14 Super Rapid Scan Operations to Prepare for GOES-R (SRSOR)
SRSOR for 2015 include May 18-June 12, and August 10-22:
  http://cimss.ssec.wisc.edu/goes/srsor2015/GOES-14_SRSOR.html
  Data during parts of 2012 (Hurricane Sandy, convection), 2013 (CA Rim Fire, convection) and 2014 (Hurricane Marie, convection):
  http://cimss.ssec.wisc.edu/goes/srsor/GOES-14_SRSOR.html
  http://cimss.ssec.wisc.edu/goes/srsor2013/GOES-14_SRSOR.html
  http://cimss.ssec.wisc.edu/goes/srsor2014/GOES-14_SRSOR.html
GOES-14 provided very unique data and offered a glimpse into the possibilities that will be provided by the ABI on GOES-R in one minute mesoscale imagery
GOES-14 visible image showing rapid convective
(loops over just half an hour)
Notes: http://cimss.ssec.wisc.edu/goes/srsor2015/GOES-14_SRSOR.html

## Slide 109: SRSOR vs Meso
GOES (SRSOR)
~1 per minute
Experimental
(no other imagery)
GOES-R ABI (Meso)
1 per minute for 2 locations
Operational
(with FD + CONUS)

## Slide 110
http://cimss.ssec.wisc.edu/goes/applets/overview.html

## Slide 113: Hands-on….Temporal/Spatial
Choose a case to example the temporal and/or spatial resolutions:
  http://cimss.ssec.wisc.edu/goes/applets/overview.html
  or
  http://cimss.ssec.wisc.edu/education/apps/abi/
Via temporal sampling, can you get Hurricane Sandy to appear to rotate backwards?
Can you observe an enhanced v signature in the IR case over MN?

## Slide 114: Outline
Overview
ABI
  Spectral
  Temporal
  Spatial
Other
Summary
More information

## Slide 115
http://www.goes-r.gov

## Slide 116: GOES-R ABI Products
Advanced Baseline Imager (ABI)
Aerosol Detection (Including Smoke and Dust) Aerosol Optical Depth (AOD) Clear Sky Masks Cloud and Moisture Imagery Cloud Optical Depth Cloud Particle Size Distribution Cloud Top Height Cloud Top Phase Cloud Top Pressure Cloud Top Temperature Derived Motion Winds Derived Stability Indices Downward Shortwave Radiation: Surface Fire/Hot Spot Characterization Hurricane Intensity Estimation Land Surface Temperature (Skin) Legacy Vertical Moisture Profile Legacy Vertical Temperature Profile Radiances Rainfall Rate/QPE Reflected Shortwave Radiation: TOA Sea Surface Temperature (Skin) Snow Cover Total Precipitable Water Volcanic Ash: Detection and Height
Baseline Products
Advanced Baseline Imager (ABI)
Absorbed Shortwave Radiation: Surface Aerosol Particle Size Aircraft Icing Threat Cloud Ice Water Path Cloud Layers/Heights Cloud Liquid Water Cloud Type Convective Initiation Currents Currents: Offshore Downward Longwave Radiation: Surface Enhanced “V”/Overshooting Top Detection Flood/Standing Water Ice Cover Low Cloud and Fog Ozone Total Probability of Rainfall Rainfall Potential Sea and Lake Ice: Age Sea and Lake Ice: Concentration Sea and Lake Ice: Motion Snow Depth (Over Plains) SO2 Detection Surface Albedo Surface Emissivity Tropopause Folding Turbulence Prediction Upward Longwave Radiation: Surface Upward Longwave Radiation: TOA Vegetation Fraction: Green Vegetation Index Visibility
Future Capabilities
+ others

## Slide 117: Bridging the gap between imagery and products
Qualitative
Quantitative
Both
Notes: Right now most views are either qualitative images OR quantitative derived products. How best to combine the strengths?

## Slide 118: http://cimss.ssec.wisc.edu/goesr/proving-ground/geocat_ash
Cordon Caulle
Grimsvotn
Using contours to highlight quantitative product (over RGB)
Pavolonis
Notes: Using contours is one method to “combine” a quantitative product with an RGB.
-June 4
-May 21

## Slide 119
The quantitative assessment of cloud ceiling can be overlaid on top of imagery to make the product more appealing to forecasters.
The ability to contour the IFR and MVFR probabilities will soon be available in AWIPS.
Using contours to highlight quantitative product (over RGB)
Pavolonis
Notes: Using contours is one method to “combine” a quantitative product with an RGB. This case for cloud ceilings.

## Slide 120
Mike Pavolonis

## Slide 121
Klyuchevskoy ash plume
The ash plume is clearly discernable in the Himawari-8 AHI imagery constructed using similar spectral channels
Mike Pavolonis
Notes: The AHI resolution at a viewing angle of 65+ degrees is actually better than MTSAT or GOES at nadir.

## Slide 122
Klyuchevskoy ash plume
The ash plume is not discernable in MTSAT false color imagery
Mike Pavolonis
Notes: https://volcano.ssec.wisc.edu/

## Slide 123: Himawari-8 Imagery – Real Earth http://re.ssec.wisc.edu - All 16 Bands
http://realearth.ssec.wisc.edu/s/32VeT
Notes: View of the Web UI showing the Himawari-8 Full Disk Vis and IR (Bands 2 and 14). This can be found in the “Presets” portion of the Layers control. Just click on the “Himawari” category to get a listing of predefined Himawari Channel selections for various geographic sectors. These images can be animated as a time series or as individual channels at a specific time.

## Slide 124: http://realearth.ssec.wisc.edu/s/U2Vhb
Real Earth “Features” can be easily shared via Facebook, Twitter or Embedded Email
Notes: The Share feature of the UI allows users to capture the contents of a RE display (either static or animation) suitable for FaceBook, Twitter or embedded email. Here is an example of the Himawari-8 Australia sector.

## Slide 125
Exploratory ABI Scan Mode (draft)
At some point, other ABI scan modes could be possible.
  requires an upgrade to the ground system.
  ABI instrument is capable of supporting other scan modes.
One option is to use the ‘white space’ of when the ABI instrument is not scanning in mode 3 (‘flex’). For example, increase to an ‘extended CONUS’ image.
There are other optimized scan options as well, such as investigating a FD scan every 10 min to sync with global constellation (EUMETSAT, AHI, AGRI, etc.).

## Slide 126: Draft Scan Mode ”6” with 10-min FD
DRAFT!
In 10-min:
  1 Full Disk +
  2 CONUS +
  20 Meso-scale
The 10-min Full Disk would offer synergy with other geos and improved AMVs outside of CONUS, plus still allow for meso-scale observations.
This draft mode 6 ideally could be tested during PLPT (Post Launch Products Test).
This mode should be easier to implement at the Ground System, sense the scan sectors are the same size/locations as in mode 3.

## Slide 127: Draft Scan Mode ”6” with 10-min FD
Time-time diagram from Exelis
Note less ‘white space’ than scan mode 3 (flex mode)
Notes: Copy and pasted from excel. Pasted as a picture. Resized to 44% by 44% of original. Arrange -> Align -> Align Center & Align Middle

## Slide 128: AHI Observation Modes: Areas and Temporal resolution
Full disk
Interval : 10 minutes (6 times per hour)
Region 3 Target Area
Interval : 2.5 minutes (4 times in 10 min)
Dimension : EW x NS: 1000 x 1000 km
Region 2
SW-JAPAN
Region 2 JAPAN (South-West)
Interval : 2.5 minutes (4 times in 10 min)
Dimension : EW x NS: 2000 x 1000 km
Region 1
NE-JAPAN
Region 1 JAPAN (North-East)
Interval : 2.5 minutes (4 times in 10 min)
Dimension : EW x NS: 2000 x 1000 km
Region 4 Landmark Area
Interval : 30 seconds (20 times in 10 min)
Dimension : EW x NS: 1000 x 500 km
Region 4
Landmark Area
Region 5
Landmark Area
Region 3
Target Area
Region 5 Landmark Area
Interval : 30 seconds (20 times in 10 min)
Dimension : EW x NS: 1000 x 500 km
Notes: 128

## Slide 129: JMA’s AHI
S. Miller (CIRA) on behalf of the GOES-R AWG Imagery Team
25-January-2015
02:30 UTC

## Slide 130: Pseudo-Natural Color

## Slide 131: Realtime WRF Chem and GFS ABI runs
http://cimss.ssec.wisc.edu/goes_r/proving-ground/wrf_chem_abi/wrf_chem_abi.html
Realtime simulated ABI Data used for GOES-R ground system testing

## Slide 132: Near Realtime GFS ABI runs
RaFTR-CIMSS-SIM data
Screenshot of Simulated ABI data at 140E from the National Headquarters Development system (NHDA) - AWIPS-II GOES-R test (January 23, 2015) Image from Joe Zajic.

## Slide 133: Outline
Overview
ABI
  Spectral
  Temporal
  Spatial
Other
Summary
More information

## Slide 134: Approximate spectral and spatial resolutions of US GOES Imagers
~ Band Center (um) | GOES-1/3 | GOES-4/7 | GOES-8/11 | GOES-12/13 | GOES-13/15 | GOES-R+
0.47 |  |  |  |  |  | 
0.64 |  |  |  |  |  | 
0.86 |  |  |  |  |  | 
1.6 |  |  |  |  |  | 
1.38 |  |  |  |  |  | 
2.2 |  |  |  |  |  | 
3.9 |  |  |  |  |  | 
6.2 |  |  |  |  |  | 
~6.7 |  | 14km |  |  |  | 
7.3 |  |  |  |  |  | 
8.5 |  |  |  |  |  | 
9.7 |  |  |  |  |  | 
10.3 |  |  |  |  |  | 
11.2 |  |  |  |  |  | 
12.3 |  |  |  |  |  | 
13.3 |  |  |  |  |  | 
8
4
2
Visible
Near-IR
Infrared
Box size represents pixel size
“MSI mode”
Notes: 0.40 inches = 4km; 0.80 inches = 8km
MSI is Multi-Spectral Imaging Mode (dashed boxes)
This does not show other improvements: SNR, MTF, bit-depth, navigation, coverage rates, etc.
ATS and SMS not shown.

## Slide 136: Geostationary Imagers: Number of Spectral bands (~ width)
Time | Instruments | Visible/NearIR | Infrared (IR)
Late 1950s | N/A | N/A | N/A
1966+ | ATS-1/3 (Spin-Scan Cloud Camera) | 1 (0.1 μm) | N/A
1967+ | ATS-3 (Multicolor Spin-Scan Cloud Camera) | 3 (0.1 μm) | N/A
1974 | ATS-6 (Geosynchronous Very High Resolution Radiometer) | 1 (0.2 μm) | 1 (2 μm)
1974/1975 | SMS-1/2 (Visible Infrared Spin-Scan Radiometer (VISSR)) | 1 (0.15 μm) | 1 (2 μm)
1975+ | GOES-1/3 (VISSR) | 1 (0.2 μm) | 1 (1 μm)
1980+ | GOES-4/7 (VISSR + VAS) | 1 (0.2 μm) | 3 (1 μm)
1994+ | Imager-8/12 + Sounder | 1 (0.2 μm) | 4 (1 μm)
2010+ | Imager-13/15 + Sounder | 1 (0.2 μm) | 4 (1 μm)
2017+ | ABI | 6 (0.1 μm) | 10 (1 μm)
2033? |  |  | 
U.S. Meteorological Imagers
Large improvements with the ABI!
Notes: Value in parenthesis is approximate 50% width of the visible or IR window.
http://cimss.ssec.wisc.edu/goes/calibration/
Values are approximate.

## Slide 137: Geostationary Imagers: Spatial Resolution (approximate)
Time | Instruments | Visible/NearIR | Infrared (IR)
Late 1950s | N/A | N/A | N/A
1966+ | ATS-1/3 (Spin-Scan Cloud Camera) | 4 km | N/A
1967+ | ATS-3 (Multicolor Spin-Scan Cloud Camera) | 4 km | N/A
1974 | ATS-6 (Geosynchronous Very High Resolution Radiometer) | 6 km | 11 km
1974/1975 | SMS-1/2 (Visible Infrared Spin-Scan Radiometer (VISSR)) | 1 km | 8 km
1975+ | GOES-1/3 (VISSR) | 1 km | 8 km
1980+ | GOES-4/7 (VISSR + VAS) | 1 km | 7-14 km
1994+ | Imager-8/12 + Sounder | 1 km | 4-8 km
2010+ | Imager-13/15 + Sounder | 1 km | 4 km
2017+ | ABI | 0.5 – 1 km | 2 km
2033? |  |  | 
U.S. Meteorological Imagers
Large improvements with the ABI!
Notes: Values are approximate, at satellite sub-points. GOES Imager over-sampling not represented.

## Slide 138: Geostationary Imagers: Temporal Resolution
Time | Instruments | Visible/NearIR | Infrared (IR)
Late 1950s | N/A | N/A | N/A
1966+ | ATS-1/3 (Spin-Scan Cloud Camera) | 20 min | N/A
1967+ | ATS-3 (Multicolor Spin-Scan Cloud Camera) | 20 min | N/A
1974 | ATS-6 (Geosynchronous Very High Resolution Radiometer) | 25 min | 25 min
1974/1975 | SMS-1/2 (Visible Infrared Spin-Scan Radiometer (VISSR)) | 20 min | 20 min
1975+ | GOES-1/3 (VISSR) | 30 min | 30 min
1980+ | GOES-4/7 (VISSR + VAS) | 30 min | 30 min
1994+ | Imager-8/12 + Sounder | 7 – 30 min | 7 – 30 min
2010+ | Imager-13/15 + Sounder | 7 – 30 min | 7 – 30 min
2017+ | ABI | 0.5 - 5 - 15 min | 0.5 - 5 - 15 min
2033? |  |  | 
U.S. Meteorological Imagers
Large improvements with the ABI!
Notes: Values are approximate. Times are routine, not special modes.

## Slide 139: Summary
1. The GOES-R ABI provides mission continuity
2. Two times the image navigation quality
3. Three times the number of imaging bands
4. Four times the spatial resolutions
5. Five times the coverage rate
- Special GOES-14 1-min data pathfinder

## Slide 140: Outline
Overview
ABI
  Spectral
  Temporal
  Spatial
Other
Summary
More information

## Slide 141: ABI Bands Quick Information Guides
http://www.goes-r.gov/education/ABI-bands-quick-info.html

## Slide 142: Select Links
  http://www.goes-r.gov
  http://cimss.ssec.wisc.edu/education/goesr
  http://cimss.ssec.wisc.edu/goes_r/proving-ground.html
  http://satelliteconferences.noaa.gov/2015/
  http://cimss.ssec.wisc.edu/goes/abi/
  http://cimss.ssec.wisc.edu/goes/blog/
  http://cimss.ssec.wisc.edu/goes_r/proving-ground/wrf_chem_abi/wrf_chem_abi.html
  http://cimss.ssec.wisc.edu/goes/srsor2015/GOES-14_SRSOR.html
  http://www.meted.ucar.edu/index.htm
Contact information: Tim.J.Schmit@noaa.gov

## Slide 143: Back-up

## Slide 144: Data Flow
Current plans call for several data delivery methods, for real-time, these are:
  GOES-R ReBroadcast (RGB) (National Centers)
  SBN (“NOAA Port”).
  Other (pull)
Hence, what GOES-R data you have may depend on your access method. For example, courser data outside of CONUS and certain sectors. Note that this plan is not ‘set in stone’.
GOES-R
GRB
AWIPS
Image from Matt Seybold

## Slide 145
Ground System (GS) FPS, Appendix E
Outside of CONUS, Hawaii, Alaska and Puerto Rico regional, imagery will be 6 km in AWIPS (for the data via the SBN).
http://www.goes-r.gov/resources/docs/GOES-R_GS_FPS.pdf

## Slide 146
Approximate Puerto Rico regional coverage
(from GS FPS)
Shown in satellite projection

## Slide 147
~1 km
~6 km
Notes: ABI band 2 (0.6 micrometers) will be finer resolution than the imagery shown and the 6km may be worse since this is 6km in a Mercator.

## Slide 148
~1 km
~6 km
Notes: ABI band 2 (0.6 micrometers) will be finer resolution than the imagery shown and the 6km may be worse since this is 6km in a Mercator.