## Slide 1: S-HIS: The Dual Regression Profile Retrieval Algorithm Used For HS3
Bill Smith Sr., Elisabeth Weisz, Hank Revercomb, Joe Taylor, Ray Garcia, Dave Hoese, Dan DeSlover
University of Wisconsin Space Science and Engineering Center
Suomi
NPP/JPSS
CrIS
Satellite & Ground-based
AERI (1990)
ASSIST (2008)
Airborne
S-HIS on Global Hawk (2012)
Metop IASI (A-2006, B-2012)
S-NPP CrIS (2011)
NAST-I & SHIS (1999 & 2000)
University
of
Wisconsin
Satellite, Airborne, and Ground-based FTS Remote Sensing Techniques W. L. Smith Sr., A. Larar, H. Revercomb, N. Smith, J. Taylor, D. Tobin, E. Weisz, M. Yesalusky
INTERNATIONAL SYMPOSIUM ATMOSPHERIC RADIATION and DYNAMICS" (ISARD - 2015) 23 - 26 June 2015, Saint-Petersburg-Petrodvorets, 1 Ulyanovskaya

## Slide 2: Topics
FTS Atmospheric Profile Retrieval Approach
Combined Model, Satellite, Radiosonde, & GB-FTS Atmospheric Structure Measurements
  Sensor Profile Sensitivity
  Model + Satellite + Radiosonde + GB FTS Amalgamation
S-NPP CAL/VAL Campaign (May, 2013)
  Ground-site Validation of Satellite Measurements
  Moore Tornado Satellite & Aircraft Observations
NASA HS3 Global Hawk Campaign (2014)
  SHIS Retrieval Validation Results
  Hurricane Edouard Satellite Validation Results
Conclusions

## Slide 3: Down/Up Looking FTS Dual Regression Retrieval Algorithm
Water Vapor Mixing Ratio( Uncorrected)
NAST-I/SHIS-I infrared Michelson interferometer
  (9000/4500 spectral channels)
  3.5 – 16 microns @ 0.25 /0.5cm-1
Aircraft Accommodation
  NAST-I: ER-2 Super pod
  SHIS: ER-2 Underbelly pod
Temperature (K)
SHIS
(Underbelly pod)
* Smith, W. L., E. Weisz, S. Kirev, D. K. Zhou, Z. Li, and E. E. Borbas (2012), Dual-Regression Retrieval Algorithm for Real-Time Processing of Satellite Ultraspectral Radiances. J. Appl. Meteor. Clim., 51, Issue 8, 1455-1476.
Cloud Top/Base Altitude
Level where Tcloudy>/<Tclear for p >/< Pcld
Final Profile
Clear-trained above/below
Cloud-trained below/above

## Slide 4: Physical Correction Using Forecast Model Profile
Problem: DR method uses a statistical training data set. Imperfect skill, due to lack of vertical resolution in radiances, leads to statistical bias.
Solution: Calculate radiances from forecast profile (FP) and perform DR retrieval using simulated “Truth” radiances. Retrieval Error = Statistical Bias.
Statistical Bias = FP – FP radiance Retrieval

## Slide 5: Error Statistics Slide

## Slide 6: Topics
FTS Atmospheric Profile Retrieval Approach
Combined Model, Satellite, Radiosonde, & GB-FTS Atmospheric Structure Measurements
  Sensor Profile Sensitivity
  Model + Satellite + Radiosonde + GB FTS Amalgamation
S-NPP CAL/VAL Campaign (May, 2013)
  Ground-site Validation of Satellite Measurements
  Moore Tornado Satellite & Aircraft Observations
NASA HS3 Global Hawk Campaign (2014)
  SHIS Retrieval Validation Results
  Hurricane Edouard Satellite Validation Results
Conclusions

## Slide 7
Satellite Vs. Ground-based Profile Sensitivity
CrIS/IASI
Water vapor
AERI/ASSIST
Water vapor
AERI/ASSIST
Temperature
CrIS/IASI
Temperature

## Slide 8
Satellite
Typical Hyperspectral Satellite Orbits X 4 (Aqua, Metop-A, S-NPP, Metop-B) = 8 per/day
Typical Ground-based FTS Coverage With Fixed and Mobile Sites
Summit

## Slide 9: Combined Model + Satellite + Raob + GB-FTS Product
Objectives:
Provide time continuous atmospheric profiles at climate benchmark stations (e.g., DOE ARM-sites) from the combination of model, satellite, radiosonde, and ground-based spectrometer (i.e., AERI/ASSIST) observations.
    Climate data record
    Satellite profile retrieval validation
    Atmospheric process studies

## Slide 10
Model + Satellite + Radiosonde + AERI/ASSIST
Relative Humidity at the Darwin AU ARM-site

## Slide 11: Topics
FTS Atmospheric Profile Retrieval Approach
Combined Model, Satellite, Radiosonde, & GB-FTS Atmospheric Structure Measurements
  Sensor Profile Sensitivity
  Model + Satellite + Radiosonde + GB FTS Amalgamation
S-NPP CAL/VAL Campaign (May, 2013)
  Ground-site Validation of Satellite Measurements
  Moore Tornado Satellite & Aircraft Observations
NASA HS3 Global Hawk Campaign (2014)
  SHIS Retrieval Validation Results
  Hurricane Edouard Satellite Validation Results
Conclusions

## Slide 12: Suomi-NPP Cal/Val Flight Tracks
ARM-Cart-site
Yuma AZ
10 SNPP science flights
3 HyspIRI ‘piggy-back’ flights
NAST-I & M
S-HIS
AVIRIS
May 2013

## Slide 13: SNPP Cal/Val Validation Sites
Yuma Arizona
32.6 N, 114.5 W
Lamont Ok
36.6 N, 97.5 W
ASSIST & Radiosondes
AERI & Radiosondes

## Slide 14
Yuma AZ Example (May 20, 2013)
Combined Product
Separation=4 Km
Separation=4 Km
Combined Product
Pressure (mb)
Combined (20.8 UTC)

## Slide 15: Suomi-NPP Cal/Val Flight Tracks
ARM-Cart-site
Yuma AZ
10 SNPP science flights
3 HyspIRI ‘piggy-back’ flights
May 20 Flight Track

## Slide 16
The 2013 Moore tornado was an EF5 Tornado that struck Moore, Oklahoma, and adjacent areas on the afternoon of May 20, 2013, with peak winds estimated at 210 miles per hour (340 km/h), killing 23 people (+2 indirectly) and injuring 377 others. The tornado touched down west of Moore at 2:56 PM CDT (19:56 UTC), staying on the ground for 39 minutes over a 17-mile (27 km) path, crossing through a heavily populated section of Moore. The tornado was 1.3 miles (2.1 km) wide at its peak.
Flight planned on Friday May 17
Based on this forecast
Forecast was verified with numerous tornadoes including the
Moore OK Tornado.

## Slide 17: Aircraft Track and Satellite Orbits
SNPP
1908 UTC
Aqua
1935UTC
Metop A
1556 UTC
Metop B
1653 UTC
Moore OK
SGP ARM-site
20 UTC)

## Slide 18: Profile Validation at ARM-site (5/20/2013)
IASI-A
(16 UTC)
IASI-B
(17 UTC)
CrIS
(19 UTC)
AIRS
(19.5 UTC)

## Slide 19: Lifted Index Stability Parameter
The lifted index (LI) is the temperature difference between an air parcel lifted adiabatically Tp(p) and the temperature of the environment Te(p) at a pressure height in the troposphere of 500 hPa (mb). When the value is positive, the atmosphere (at the respective height) is stable and when the value is negative, the atmosphere is unstable.
Thunderstorm Potential:
< -5 Very Unstable: Strong Thunderstorm Potential
-3 to -5 Unstable: Thunderstorm Probable
0 to -2 Marginally Unstable: Thunderstorms Possible
>0: Stable: Thunderstorms Unlikely

## Slide 21
CrIS LI (19:08 UTC)

## Slide 22: Topics
FTS Atmospheric Profile Retrieval Approach
Combined Model, Satellite, Radiosonde, & GB-FTS Atmospheric Structure Measurements
  Sensor Profile Sensitivity
  Model + Satellite + Radiosonde + GB FTS Amalgamation
S-NPP CAL/VAL Campaign (May, 2013)
  Ground-site Validation of Satellite Measurements
  Moore Tornado Satellite & Aircraft Observations
NASA HS3 Global Hawk Campaign (2014)
  SHIS Retrieval Validation Results
  Hurricane Edouard Satellite Validation Results
Conclusions

## Slide 23
The “Environmental” GH
Airborne Vertical Atmospheric Profiling System (AVAPS)
89 Dropsondes / flight
Temperature, Pressure, wind, humidity vertical profiles
Scanning High Resolution Infrared Sounder (S-HIS)
Upwelling thermal radiation at high spectral resolution between 3.3 and 18 microns.
Temperature, water vapor vertical profiles
Cloud Physics Lidar (CPL)
532/1064 nm Lidar Reflection
Cloud structure and depth
NOAA, NCAR
U of Wisc, SSEC
NASA GSFC
23

## Slide 24: NASA Venture HS3: Hurricanes
Flight tracks: 2012-2014
Global Hawk
Study of what storm and environmental properties
influence intensity changes
Joe Taylor, UW PM
24

## Slide 25: Real-time Data Collection, Downlink, and Processing
Real-Time Products
Real time data processing software
< 1 minute from data acquisition to delivery (MTS, website quick-looks)
Final Products
Full data processing pipeline
Quality control, archived at SSEC, Delivered to NASA post-mission
Preliminary (no QC) available within 8 hours post-flight
Near-Line Products
Full data processing pipeline
< 30 minutes from data acquisition to delivery (MTS, website quick-looks)

## Slide 26: S-HIS Vs Dropsonde Statistics
N= 655 comparisons
All Cases
GDAS – Drop
Differences
> 1.5 sigma

## Slide 27
HS4 Global Hawk Flight Track (9/16/2014)
Dropsonds Locations

## Slide 28
Scanning HIS over Edouard 16 September 2014
28

## Slide 29: S-HIS Sounds in the eye of Edouard
RH cross section
Example S-HIS real-time retrieval display of the eye of Hurricane Edouard:
Edouard photo from ISS
Soundings to the surface!
29

## Slide 30: Conclusions
Satellite, Ground based and Airborne FTS measurement profile retrievals are playing an important role in:
Validation of satellite measurements
Creating continuous measurements of the atmospheric state for process studies and climate change monitoring
Understanding, analysis, and prediction of weather systems including intense weather such as tornados and Hurricanes
Spasibo za vnimaniye