## Slide 1: Weather and Climate Applications of Ultraspectral IR Radiance Measurements
William Smith 1,2, Elisabeth Weisz1,
Stanislav Kireev2, Allen Larar3, and Henry Revercomb1
University of Wisconsin-Madison, (2) Hampton University, (3) NASA Langley Research Center
International Radiation Symposium
06-10 August 2012, Dahlem Cube, Berlin Germany
The Infrared Spectrum
Detailed Atmospheric Structure
Observed Radiance Spectrum
4-d Water Vapor Imaging With Geo-Imaging FTS

## Slide 2: Satellite Ultraspectral Sounders
Grating Spectrometer with resolution of 0.5 –2 cm-1 (resolving power of ~1200)
Spectral range: 650 – 2700, cm-1 PV and PC HdCdTe focal plane mechanically cooled to 60K
Focal plane has 4756 detectors, 2378 channels
310 K Blackbody and space view provides radiometric calibration
NEDT ranges from .05K to 0.5K
AIRS (2002)
Michelson Interferometer with resolution of 0.5 cm-1, Gaussian Apodized (resolving power of 2400-12000)
Spectral range:660 – 2700 cm-1
PV and PC HdCdTe focal planes radiatively cooled to 90K
Focal plane 12 detectors, 8461 spectral channels
310 K Blackbody and space view provides radiometric calibration
NEDT: 0.1 – 0.75 K
IASI (2006)
Michelson Interferometer with resolution of 0.625 cm-1 (LW), 1.25 cm-1 (MW) and 2.5 cm-1((SW) (resolving power of ~1000)
Spectral range:660 – 2700 cm-1
PV HdCdTe focal planes passively cooled to 81K( LW) and 98 K (MW and SW).
Focal plane 27 detectors, 1305 spectral channels
310 K BB and space view provides radiometric calibration
NEDT: 0.05 – 0.5 K
CrIS (2011)

## Slide 3
AIRS: 2002-
IASI: 2006-
Spectral Coverage and Resolution Comparison
CrIS: 2011-
CrIS: 2011- Full Resolution
±0.8 cm OPD unapodized 9 FOV/50 km square
±0.8, 0.4, 0.2 cm OPD unapodized 9 FOV/50km square
L1C:±2 cm OPD Gausian apodized
4 FOV/50km square
L1B: > 1200 Resolving Power 9 FOV/50km square

## Slide 4
4
Noise Comparison CrIS, AIRS, IASI
CrIS NEN 4x smaller in 15m CO2
CrIS SW is excellent

## Slide 5: Direct Broadcast “Dual-Regression” Retrieval Algorithm1
1Smith, W. L., E. Weisz, S. Kirev, D. K. Zhou, Z. Li, and E. E. Borbas, 2012: Dual-Regression Retrieval Algorithm for Real-Time Processing of Satellite Ultraspectral Radiances. J. Appl. Meteor. Clim. http://dx.doi.org/10.1175/JAMC-D-11-0173.1.

## Slide 6
DR Cloud Altitude Validation Using Lidar

## Slide 7
DR Sounding Example (Cloud)
Cloud Level

## Slide 8
DR Sounding Example (Clear)

## Slide 9
First CrIS Results Produced with the DR Retrieval Algorithm (Feb 1, 2012)

## Slide 10
Observations of Atmospheric Dynamics From
Consecutive CrIS and AIRS Measurements
Suomi NPP/JPSS
CrIS

## Slide 12
Aqua and NPP orbits over North America on Feb. 29, 2012
AIRS granules
Start times: 06:41, 06:47,
08:17, 08:23 UTC
AIRS granule size: 90x135
(12150 FOVs)
4 granules in total
CrIS granules
eastern/western orbit start times: 07:05/08:44 UTC
CrIS granule size: 90x12
(1080 FOVs)
47 granules in total

## Slide 13
Water Vapor Motion

## Slide 14
Water Vapor Motion

## Slide 15: GRASP Validation Campaign (April 20, 2012)
IASI-01:30 UT
CrIS-06:10
AIRS-07:11
IASI-15:30
CrIS-17:30
AIRS-18:17 UT
ASSIST Relative Humidity
37 N
76 W
37 N
76 W
37 N
76 W
37 N
76 W
37 N
76 W
37 N
76 W
18:48 UT
AIRS-CrIS
Moisture Change Verified
by Raob &
ASSIST
17:30 UT
Radiosonde Relative Humidity

## Slide 16
Desirable Features of Climate Retrieval Algorithm
  Linear dependence on radiance spectra
    Variation depends only on radiance
      (i.e., no other input variables)
  All sky
    clear and cloudy (0 - 100%)
  Independent of Field-of-View (FOV) size
    Can be applied to different instruments
  Retrieval Variables
    Surface : temperature & spectral emissivity
    Atmosphere : T, H2O, and O3 profiles & CO2 ppm
    Cloud : height and optical thickness
The Dual Regression Retrieval Algorithm is Optimal for Climate Trend Determination

## Slide 17: AIRS Vs GDAS Global Statistics (N=32,400)
February 2003
February 2009
August 2003
August 2009
Std
Bias

## Slide 18: 500-hPa (5-km) Temperature AIRS Vs GDAS 7-yr (2003-2009) Mean & Annual Trend (Feb+Aug)

## Slide 19: 850-hPa (2-km) Temperature AIRS Vs GDAS 7-yr (2003-2009) Mean & Annual Trend (Feb+Aug)

## Slide 20: AIRS Vs GDAS 2003 – 2009 Climate Statistics

## Slide 21: Global Mean Temperature and Humidity
 | Global Mean Temperature (K) |  |  |  | Annual Trend (K/yr) |  | 
P(hPa) | AIRS | GDAS | Difference |  | AIRS | GDAS | Difference
10 | 225.22 | 225.29 | -0.07 |  | -0.23 | -0.27 | 0.04
30 | 215.50 | 214.19 | 1.31 |  | -0.10 | 0.06 | -0.16
50 | 210.94 | 210.29 | 0.65 |  | -0.07 | 0.15 | -0.22
70 | 208.26 | 208.28 | -0.02 |  | -0.03 | 0.08 | -0.11
85 | 207.26 | 207.70 | -0.44 |  | -0.02 | 0.05 | -0.07
100 | 207.03 | 207.35 | -0.32 |  | -0.01 | 0.01 | -0.02
200 | 216.54 | 217.31 | -0.77 |  | -0.03 | 0.11 | -0.13
300 | 230.34 | 230.46 | -0.13 |  | -0.03 | -0.02 | -0.01
500 | 255.86 | 255.50 | 0.36 |  | 0.01 | -0.02 | 0.03
700 | 271.93 | 270.80 | 1.13 |  | 0.02 | 0.08 | -0.06
850 | 279.89 | 278.09 | 1.80 |  | 0.01 | 0.10 | -0.09
920 | 283.25 | 281.84 | 1.42 |  | 0.01 | 0.08 | -0.07
1000 | 285.02 | 284.77 | 0.24 |  | 0.00 | 0.05 | -0.05
 | Global Mean Relative Humidity (%) |  |  |  | Annual Trend (%/yr) |  | 
P(hPa) | AIRS | GDAS | Difference |  | AIRS | GDAS | Difference
100 | 25.75 | 13.69 | 12.05 |  | -0.32 | -2.41 | 2.09
200 | 34.92 | 44.64 | -9.72 |  | 0.05 | 0.11 | -0.05
300 | 42.40 | 53.99 | -11.59 |  | 0.09 | -0.32 | 0.41
500 | 40.01 | 47.81 | -7.80 |  | 0.07 | 0.01 | 0.06
700 | 51.42 | 58.62 | -7.20 |  | 0.03 | -0.24 | 0.27
850 | 73.49 | 71.04 | 2.45 |  | 0.28 | 0.11 | 0.17
920 | 77.60 | 75.43 | 2.17 |  | 0.32 | 0.28 | 0.04
1000 | 77.43 | 73.54 | 3.89 |  | 0.29 | 0.37 | -0.08

## Slide 22
Summary
22
Suomi NPP CrIS instrument performance is exceptional
  Very low noise
  Very stable and accurate
  Can be used with Aqua AIRS for time
  variation information (e.g., H2O winds)
Ultraspectral satellite retrievals (AIRS, IASI, and CrIS) provide accurate trends of atmospheric variables
  AIRS data is now available for an entire decade (2002-2012)
  AIRS, IASI, and CrIS will provide important input to climate analysis models
900 cm-1
18 March 2012
1250 UTC

## Slide 23
AIRS/IASI/CrIS
Water vapor
AIRS/IASI/CrIS
Temperature
GB-FTS (ASSIST)
Water vapor
GB-FTS (ASSIST)
Temperature
Satellite Vs Ground-based Profile Sensitivity

## Slide 24: Greenhouse Gas Physical Regression (PR) Retrieval Methodology
Qret = qo + (rm-ro)C
C = (R’TR’ + λETE)-1R’TQ’
q = atmospheric profiles (temperature, water vapor, etc.)
C = statistical covariance about the initial profile qo
ro = radiance calculated from the initial profile qo
Q & R = climatological ensemble of profiles & radiance spectra
( )’ = deviation from the initial conditions qo and ro
ETE = statistical covariance of spectral radiance noise
λ = scaler determined as that value which minimizes the
RMS difference between the retrieval calculated radiance
spectrum and observed radiance spectrum

## Slide 25
Statistical Data For C-Matrix
Year 2010 Global Product
3,110,400 Space/Time Samples
1-deg Resolution
Monthly Day 15, 0, 6 12, 18 GMT
T, H2O, O3, CO, CH4, N2O Profiles
Aerosol Extinction Profiles
CO2 uniformly mixed, randomly varied
Cloud Altitude/Optical Depth Profiles
Separated Into Seasonal/Regional Sets

## Slide 26: BIAS Corrections Using Forecast Model Profile
Problem: PR method uses a statistical training data set. Imperfect skill, due to lack of vertical resolution in radiances, leads to local bias in PR retrievals.
Solution: Calculate radiances from forecast model profile (FP) and perform PR retrieval using model radiances.
Statistical bias correction = FP – FP radiance retrieved FP
Bias
Corrected
Bias Correction removes statistical bias with respect to the model FP
RTVL
Corrected RTVL

## Slide 27
Ground-based Profile Sensitivity
GB-FTS measurements are very sensitive to temperature, water vapor, and GHG variations in the lower atmosphere (i.e., 0 – 4-km)
GB-FTS
O3
GB-FTS
CO2
GB-FTS
Temperature
GB-FTS
H2O

## Slide 28: ASSIST Profile Results April 19 17 UTC – April 21, 00 UTC
Temperature ( 0 – 4 km)
Relative Humidity ( 0 – 4 km)
ASSIST - only
RAQMS
ASSIST w BIAS Correction

## Slide 29: ASSIST Profile Results April 19, 17 UTC – April 21, 00 UTC
Ozone ( 0 – 4 km)
ASSIST - only
RAQMS
Carbon Monoxide( 0 – 4 km)
ASSIST w BIAS Correction

## Slide 30: ASSIST Profile Results April 19, 17 UTC – April 21, 00 UTC
Methane ( 0 – 4 km)
ASSIST - only
ASSIST w BIAS Correction
RAQMS
Nitrous Oxide( 0 – 4 km)

## Slide 31
Summary
31
CrIS instrument performance is exceptional
  Very low noise
  Very stable and accurate
  Can be used with Aqua AIRS for time
  variation information (e.g., H2O winds)
Ground-based FTS Provides excellent measurements of the Planetary Boundary Layer (PBL)
  Diurnal variation of temperature and moisture
  Trace gas profiles of O3 ,CO, CH4, and N2O
Combined Satellite and Ground-based Ultraspectral Measurements can Provide Climate Quality Profile Information
900 cm-1
18 March 2012
1250 UTC