## Slide 1
Jordan J. Gerth
Assistant Researcher, Liaison to NWS Pacific Region
Cooperative Institute for Meteorological Satellite Studies
University of Wisconsin at Madison
Timothy J. Schmit
Research Meteorologist
National Environmental Satellite, Data, and Information Service
Bill D. Ward
Environmental and Scientific Services Division Chief National Weather Service Pacific Region Headquarters
Includes contributions from the community
GOES-R: The New Generation Begins with Himawari-8

## Slide 2: GOES-R spacecraft and solar panel

## Slide 3: An update on GOES-R/S launch
GOES-R is tentatively scheduled to launch on October 14, 2016, in Cape Canaveral, Florida
GOES-S will launch approximately one year after the GOES-R launch
Post-launch testing will occur at 89.5 W and GOES-R will be positioned there for approximately one year
Operational location of GOES-R will depend on NWS priorities and the health of the existing GOES satellites

## Slide 4
Launch & Orbit Raising
Operations -
Post-launch Testing (PLT) - 180 Days
Outgas
System Performance Operational Test (SPOT)
12 Days
30 Days
60 Days
6 Mo
30 Days
PLPT
Ex-tended Val
<=5yrs Storage + >=8.4yrs Ops
PLT Cal/INR
32 Days
28 Days
09 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36
GOES West
On-orbit spare
GOES East
Fiscal Year
On-orbit storage
Operational
GOES-13
GOES-14
GOES-15
GOES-R
GOES-S
GOES-T
GOES-U
Test & Checkout
Fuel-Limited Lifetime
Post-launch Calibration, Instrument Navigation and Registration
Post-launch Product Testing
Continuity of GOES through 2036
Lockheed Martin

## Slide 5: Future GOES-R/S constellation

## Slide 6: Advanced Baseline Imager (ABI)
5
4
3
X
Faster scanning (5-minute full disk vs. 25-minute)
X
Improved spatial resolution (2 km IR vs. 4 km)
X
More spectral bands (16 on ABI vs. 5)

## Slide 7
AHI Band | AHI Approximate Central Wavelength (μm) | ABI Approximate Central Wavelength (μm) | ABI Band | Type | Nickname
1 | 0.47 | 0.47 | 1 | Visible | Blue
2 | 0.51 |  |  | Visible | Green
3 | 0.64 | 0.64 | 2 | Visible | Red
4 | 0.86 | 0.86 | 3 | Near-Infrared | Veggie
 |  | 1.4 | 4 | Near-Infrared | Cirrus
5 | 1.6 | 1.6 | 5 | Near-Infrared | Snow/Ice
6 | 2.3 | 2.2 | 6 | Near-Infrared | Cloud Particle Size
7 | 3.9 | 3.9 | 7 | Infrared | Shortwave Window
8 | 6.2 | 6.2 | 8 | Infrared | Upper-level Water Vapor
9 | 6.9 | 6.9 | 9 | Infrared | Mid-level Water Vapor
10 | 7.3 | 7.3 | 10 | Infrared | Lower-level Water Vapor
11 | 8.6 | 8.4 | 11 | Infrared | Cloud-Top Phase
12 | 9.6 | 9.6 | 12 | Infrared | Ozone
13 | 10.4 | 10.3 | 13 | Infrared | “Clean” Longwave Window
14 | 11.2 | 11.2 | 14 | Infrared | Longwave Window
15 | 12.4 | 12.3 | 15 | Infrared | “Dirty” Longwave Window
16 | 13.3 | 13.3 | 16 | Infrared | CO2 Longwave
Advanced Baseline Imager Spectral Bands

## Slide 8: Improved temporal resolution
Current GOES imager:
  CONUS covered once every fifteen minutes, except during rapid scan operations
  One full disk every three hours
GOES-R/S ABI:
  In one hour:
    4 full disk images, 12 CONUS sectors, and 120 mesoscale sectors
      OR
    Twelve full disk images

## Slide 9: ABI Visible Bands
Current GOES imager: one band at 1 km resolution
GOES-R ABI: one band at 0.5 km resolution, one band at 1 km resolution
Benefits to the operational meteorologist:
  Better resolution of cloud features and cloud-enhanced boundaries
  Easier monitoring of smoke and aerosols
  Ability to produce pseudo-true color imagery

## Slide 11: ABI Band 2 (0.64 μm) Example from the Advanced Himawari Imager
Kuchinoerabu-jima

## Slide 12: ABI Near-Infrared Bands
Current GOES imager: No near-infrared bands
GOES-R ABI: Four near-infrared bands, two at 1 km resolution, two at 2 km resolution
Benefits to the operational meteorologist:
  Depiction of vegetation health/coverage
  Sharper coastlines and easier detection of inland river flooding
  Easier cirrus cloud and cloud-phase discrimination
  Nocturnal fire detection

## Slide 13: ABI Band 4 (1.4 μm) Example from the Visible Infrared Imaging Radiometer Suite (VIIRS)
In dry environments, the ABI Band 4 is useful for identifying areas of dust, compared to traditional visible imagery.

## Slide 14: ABI Band 5 (1.6 μm) Example from the Advanced Himawari Imager
Water clouds
Ice clouds

## Slide 15: ABI Infrared Bands
Current GOES imager: four bands at 4 km resolution
GOES-R ABI: ten bands at 2 km resolution
Benefits to the operational meteorologist:
  Fire detection with better thermal signal
  Resolution of middle and upper tropospheric water vapor features
  Detection of sulfur dioxide and upper-atmosphere ozone
  Several window channels for discerning low-level water vapor gradients

## Slide 16: Extratropical Transition
Typhoon Atsani
AHI Band 8 (6.2 μm)
24 August 2015

## Slide 17: ABI quick reference guides
The University of Wisconsin and NOAA are developing a quick reference guide for each one of the ABI bands with forecaster-pertinent information.
More training on GOES-R is available from COMET
http://www.goes-r.gov/

## Slide 19: Atmospheric Motion Vectors (AMVs)
19
AMVs from 15-minute images (routine GOES imager sampling) AMVs from 1-minute images (mesoscale GOES-R ABI sampling)
C. Velden (CIMSS)
Hurricane Sandy case from GOES-14 – 18:00 UTC 26 October 2012
Low-Level (700-950 hPa) Vectors from Visible Imagery

## Slide 20: Find Himawari-8 imagery online
Japan Meteorological Agency
  http://www.data.jma.go.jp/mscweb/data/himawari/
University of Wisconsin
  http://www.ssec.wisc.edu/data/geo/
  http://realearth.ssec.wisc.edu/
Colorado State University
  http://rammb.cira.colostate.edu/ramsdis/online/himawari-8.asp

## Slide 21
Thank you!
For more information, visit www.goes-r.gov
or e-mail
Jordan.Gerth@noaa.gov
www.facebook.com/GOESRsatellite
www.youtube.com/user/
NOAASatellites
twitter.com/NOAASatellites
www.flickr.com/photos/
noaasatellites