## Slide 1
Using VIIRS DNB
and
OMI NO2 retrievals
for
constraining NOx Emissions
Brad Pierce
NOAA/NESDIS
UW-Madison AOS Senior Capstone Seminar Monday March 9, 2015, Madison WI

## Slide 2
Solar absorption Spectra
Solar Spectrum
Spectral
Fitting
Ozone Monitoring Instrument (OMI)
Visible/Infrared Imager/Radiometer
Suite (VIIRS), Day/Night Band (DNB)
Low light
Imaging
Nano-watts/cm2sr
Nitrogen Oxide (NOx)
Emissions
1 billion times fainter than sunlight
This Talk

## Slide 3
Tropospheric ozone (O3) is formed when certain precursor trace
gases are oxidized in the atmosphere by the hydroxyl radical (OH).
The two most important precursor trace gases are carbon monoxide (CO)
and a class of gases known as Volatile organic compounds (VOCs).
However, the amount of O3 that forms is most critically dependent on
the available concentration of nitrogen oxides (NOx), which are primarily
the sum of NO and NO2
There are two potential pathways:
VOC (or CO) + OH + sunlight -> H2O + CO2 (no NOx)
or
VOC (or CO) + OH + sunlight -> O3 + H2O + CO2 (with NOx)
From satellites, we can measure Formaldehyde (HCHO, a surrogate for VOC), CO, O3, and NO2 (one of the two primary components of NOx)
Fishman, J. et al., Remote Sensing of Tropospheric Pollution from Space, Bull. Amer. Meteor. Soc., 89, 805–821. doi: http://dx.doi.org/10.1175/2008BAMS2526.1

## Slide 4
Background: National Trends in Ozone (O3) Levels
http://www.epa.gov/airtrends/ozone.html
Nationally, average ozone levels declined in the 1980's, leveled off in the 1990's, and showed a notable decline after 2002.
O3 standard is currently 75ppbv based on annual fourth-highest daily maximum 8-hr concentration, averaged over 3 years

## Slide 5
Background: National Trends in Ozone (O3) Levels
http://www.epa.gov/airtrends/ozone.html
Nationally, average ozone levels declined in the 1980's, leveled off in the 1990's, and showed a notable decline after 2002.
O3 standard is currently 75ppbv based on annual fourth-highest daily maximum 8-hr concentration, averaged over 3 years

## Slide 6
Background: National Trends in Ozone (O3) Levels
http://www.epa.gov/airtrends/ozone.html
Nationally, average ozone levels declined in the 1980's, leveled off in the 1990's, and showed a notable decline after 2002.
O3 standard is currently 75ppbv based on annual fourth-highest daily maximum 8-hr concentration, averaged over 3 years

## Slide 7
Background: National Trends in Ozone (O3) Levels
http://www.epa.gov/airtrends/ozone.html
Nationally, average ozone levels declined in the 1980's, leveled off in the 1990's, and showed a notable decline after 2002.
O3 standard is currently 75ppbv based on annual fourth-highest daily maximum 8-hr concentration, averaged over 3 years

## Slide 8
Background: National Trends in Ozone (O3) Levels
http://www.epa.gov/airtrends/ozone.html
Nationally, average ozone levels declined in the 1980's, leveled off in the 1990's, and showed a notable decline after 2002.
O3 standard is currently 75ppbv based on annual fourth-highest daily maximum 8-hr concentration, averaged over 3 years

## Slide 9
Background: National Trends in Nitrogen Dioxide (NO2) Levels
Russell et al., ACP 12, 12197-12209, doi:10.5194/acp-12-12197-2012, 2012.
Overall, surface and column NO2 amounts are declining over the US due to regulations from the Clean Air Act
OMI Berkeley High-Resolution (BEHR) NO2 Column Retrievals
EPA NO2 trends from ground monitoring
http://www.epa.gov/airtrends/nitrogen.html
32±7% reduction 2005-2011

## Slide 10
Background: The US EPA 2011 National Emissions Inventory (NEI)
http://www.epa.gov/ttn/chief/net/2011inventory.html
The National Emissions Inventory (NEI) is a comprehensive and detailed estimate of emissions of air pollutants from all air emissions sources.
NEI is used to constrain Air Quality modeling in support of State Implementation Planning (SIP) required by the EPA

## Slide 11
On-road Cars and Trucks are the major source of NO2 emissions
Background: The US EPA 2011 National Emissions Inventory (NEI)

## Slide 12
Power Plants are another major source of NO2 emissions
Background: The US EPA 2011 National Emissions Inventory (NEI)

## Slide 13
Background: The US EPA 2011 National Emissions Inventory
Oil and Gas Production is another major source of NO2 emissions

## Slide 14
U.S Energy Information Administration (http://www.eia.gov/)
Background: National Trends in Oil and Gas Production
Oil and Gas Production has risen significantly since 2011

## Slide 15
Oil and Gas Production activities can be monitored with the Visible Infrared Imaging Radiometer Suite (VIIRS) Day-Night-Band (DNB) imagery
VIIRS DNB Composite Imagery from NOAA National Geophysical data Center
Can we use VIIRS DNB and OMI NO2 retrievals for constraining NOx Emissions?

## Slide 16
Approach
Evaluate the spatial correlation between NEI 2011 NOx emissions and VIIRS DNB on an urban scale
Evaluate the spatial correlation between NEI 2011 NOx emissions and OMI NO2 columns on a urban scale
Use VIIRS DNB radiances to generate a spatially enhanced OMI NO2 column retrieval appropriate for constraining Air Quality model emissions through Data Assimilation

## Slide 17
NEI 2011 total NO emissions inventory
(4km all area+point sources)
Provided by Stu McKeen (NOAA/ESRL)

## Slide 18
NEI 2011 total NO emissions inventory
(4km all area+point sources)
Provided by Stu McKeen (NOAA/ESRL)
Salt Lake City
Phoenix
Denver
Background
Background
Background
Background
Background
Minneapolis
St. Louis
Atlanta

## Slide 19
NEI 2011 Oil&Gas NO emissions inventory
(4km all area+point sources)
Provided by Stu McKeen (NOAA/ESRL)
Permian
Barnett
Haynesville-Bossier
Woodford
Eagle Ford
New Albany
Floyd-Neal
Marcellus
Antrim
Uinta Basin
San Juan Basin
Denver-Julesburg Basin
Powder River Basin
Green River Basin
Piceance Basin
Williston Basin

## Slide 20
Investigate relationship NEI 2011 emissions and SNPP VIIRS Day Night Band (DNB) radiances (2012 cloud free composite, 15 arc second resolution) for specific urban and oil and gas regions
VIIRS DNB
SNPP VIIRS cloud-free composite (2012/4/18-26 and 2012/10/11-23) DNB data on 15 arc sec grid from Earth Observation Group, NOAA National Geophysical Data Center in GEOTIFF format
http://www.ngdc.noaa.gov/eog/viirs/download_viirs_ntl.html

## Slide 21
SNPP VIIRS 2012 cloud-free composite
(15 arc sec grid)
Earth Observation Group, NOAA National Geophysical Data Center

## Slide 22
Aggregated VIIRS DNB radiances vs NEI 2011 modeled/gridded NO emissions
Region Z: Atlanta

## Slide 23
NEI 2011 modeled/gridded NO emissions
Region Z: Atlanta

## Slide 24
Aggregated VIIRS DNB radiances
Region Z: Atlanta

## Slide 25
Aggregated VIIRS DNB radiances vs NEI 2011 modeled/gridded NO emissions
Region O: Permian

## Slide 26
NEI 2011 modeled/gridded Total NO emissions
Region O: Permian
Lubbock, TX
Midland, TX
Odessa, TX

## Slide 27
NEI 2011 modeled/gridded Oil & Gas NO emissions
Region O: Permian
Lubbock, TX
Midland, TX
Odessa, TX

## Slide 28
Aggregated VIIRS DNB radiances
Region O: Permian
Lubbock, TX
Midland, TX
Odessa, TX

## Slide 29
Aggregated VIIRS DNB radiances
Region O: Permian

## Slide 30
Aggregated VIIRS DNB radiances
Region O: Permian

## Slide 31
Aggregated VIIRS DNB radiances vs NEI 2011 modeled/gridded NO emissions
Region V1: Southern Marcellus

## Slide 32
NEI 2011 modeled/gridded Total NO emissions
Region V1: Southern Marcellus
Pikeville KY

## Slide 33
NEI 2011 modeled/gridded Total NO emissions
Region V1: Southern Marcellus
Pikeville KY

## Slide 34
Aggregated VIIRS DNB radiances
Region V1: Southern Marcellus
Pikeville KY

## Slide 35
Aggregated VIIRS DNB radiances
Region V1: Southern Marcellus
Mountain Top Removal
Pikeville KY

## Slide 36
Aggregated VIIRS DNB radiances
Region V1: Southern Marcellus
McDowell FCI
1,692 Inmates

## Slide 37
Aggregated VIIRS DNB radiances vs NEI 2011 modeled/gridded NO emissions
Region N: Williston Basin

## Slide 38
NEI 2011 modeled/gridded Total NO emissions
Region N: Williston Basin
Minot
Sidney
Williston

## Slide 39
NEI 2011 modeled/gridded Total NO emissions
Region N: Williston Basin
Minot
Sidney
Williston

## Slide 40
2012 VIIRS DNB Radiances
Region N: Williston Basin
Minot
Sidney
Williston

## Slide 41
2012 VIIRS DNB Radiances
Region N: Williston Basin (103W 48N 0.1o Zoom)

## Slide 42
Google Earth
Region N: Williston Basin (103W 48N 0.1o Zoom)

## Slide 43
1km
Google Earth Zoom
Region N: Williston Basin
2.5km

## Slide 44
Google Earth Zoom
Region N: Williston Basin

## Slide 45
Chart: 2011 NEI NO emissions and 2012 VIIRS DNB correlation
 | 0.611 | 0.638 | 0.122 | 0.459 | 0.466 | 0.281 | 0.198 | 0.548 | 0.631 | 0.159 | 0.003 | 0.129 | 0.096 | 0.039 | 0.308 | 0.506 | 0.297 | 0.2 | 0.715 | 0.234 | 0.379 | 0.166 | 0.186 | 0.265 | 0.209 | 0.178 | 0.25 | 0.509 | 0.407 | 0.392
Summary of Regional Correlations 2011
A B C D E F G H I J K L M N O P Q1 Q2 Q3 R S T U V1 V2 V3 W X Y Z
Region
A= Salt Lake City
B=Phoenix
C=Uinta Basin
D=Green River Basin
E=Piceance Basin
F=San Juan Basin
G=Powder River Basin
H=Denver/Denver-Julesburg Basin
I=NW Background
J=SW Background
K=Northern Background
L=SW Background
M=Eastern Background
N=Williston Basin
O=Permian
P=Barnett
Q1=Haynesville-Bossie S
Q2=Haynesville-Bossie C
Q3=Haynesville-Bossie N
R=Woodford
S=Eagle Ford
T=New Albany
U=Floyd-Neal
V1=Marcellus S
V2=Marcellus C
V3=Marcellus N
W=Antrim
X=Minneapolis
Y=St. Louis
Z=Atlanta
VIIRS DNB shows reasonable (0.3-0.7) correlations with aggregated 2011 NEI NO emissions for urban areas (Salt Lake City, Phoenix, Denver/ Denver-Julesburg Basin, Minneapolis, St. Louis, Atlanta) and some O&G regions (Green River, Piceance, Permian, Barnett, Haynesville-Bossie North, Eagle Ford)

## Slide 46
Chart: 2011 NEI NO emissions and OMI BEHR NO2 correlation
 | 0.375 | 0.343 | 0.169 | 0.038 | 0.194 | 0.249 | 0.138 | 0.316 | 0.04 | 0.06 | -0.01 | 0.02 | 0.02 | 0.01 | 0.11 | 0.236 | 0.06 | 0.11 | 0.04 | 0.11 | 0.07 | 0.13 | 0.17 | 0 | 0.15 | 0.22 | 0.07 | 0.2 | 0.16 | 0.21
Summary of Regional Correlations 2011
A= Salt Lake City
B=Phoenix
C=Uinta Basin
D=Green River Basin
E=Piceance Basin
F=San Juan Basin
G=Powder River Basin
H=Denver/Denver-Julesburg Basin
I=NW Background
J=SW Background
K=Northern Background
L=SW Background
M=Eastern Background
N=Williston Basin
O=Permian
P=Barnett
Q1=Haynesville-Bossie S
Q2=Haynesville-Bossie C
Q3=Haynesville-Bossie N
R=Woodford
S=Eagle Ford
T=New Albany
U=Floyd-Neal
V1=Marcellus S
V2=Marcellus C
V3=Marcellus N
W=Antrim
X=Minneapolis
Y=St. Louis
Z=Atlanta
OMI BEHR NO2 shows lower (0.3-0.4) correlations with aggregated 2011 NEI NO emissions for Western urban areas (Salt Lake City, Phoenix, Denver/ Denver-Julesburg Basin) only
A B C D E F G H I J K L M N O P Q1 Q2 Q3 R S T U V1 V2 V3 W X Y Z
Region

## Slide 47
Use VIIRS Day Night Band (DNB) radiances to add sub-pixel (~4x4km) variability to native (13x24km) OMI NO2 retrieval
Region H=Denver/Denver-Julesburg Basin
Native OMI pixel

## Slide 48
Sub-divide each OMI pixel into 4x8 subsectors
Use VIIRS Day Night Band (DNB) radiances to add sub-pixel (~4x4km) variability to native (13x24km) OMI NO2 retrieval
Region H=Denver/Denver-Julesburg Basin

## Slide 49
Compute mean DNB radiance for each 4x8 subsectors
Compute linear regression between pixel mean DNB radiance and OMI NO2 for each swath
Use linear regression to redistribute OMI NO2 over sub-pixels
Adjust mean of sub-pixel NO2 to original pixel NO2
Use VIIRS Day Night Band (DNB) radiances to add sub-pixel (~4x4km) variability to native (13x24km) OMI NO2 retrieval
Region H=Denver/Denver-Julesburg Basin

## Slide 50
Using VIIRS Day Night Band (DNB) radiances to add (~4x4km) sub-pixel variability to native (13x24km) OMI NO2 retrieval Region H: Denver/Denver-Julesburg on August 02, 2014

## Slide 51
The airborne Geostationary Trace gas and Aerosol Sensor Optimization (GEO-TASO) instrument flew on the NASA Falcon aircraft during the 2014 FRAPPE/DISCOVER-AQ field mission
GEO-TASO is test-bed for the NASA Tropospheric Emissions: Monitoring of Pollution (TEMPO) mission, which will make air quality measurements from geostationary orbit.
Current efforts:
Validation of high resolution OMI NO2 retrievals
during FRAPPE/DISCOVER-AQ

## Slide 52
Standard OMI/NO2 vs GEOTASO Slant Column Region H: Denver/Denver-Julesburg on August 02, 2014 (19:55Z)
8:00am (14Z) takeoff
1:00pm (19Z) takeoff
Standard OMI NO2 Slant Column
GEOTASO NO2 Slant Column
0.75x1016 mol/cm2 has been removed from OMI Slant Column to account for stratospheric NO2 contribution

## Slide 53
High resolution (4x4km) OMI/NO2 vs GEOTASO Slant Column Region H: Denver/Denver-Julesburg on August 02, 2014 (19:55Z)
1:00pm (19Z) takeoff
High Resolution OMI NO2 Slant Column
GEOTASO NO2 Slant Column
0.75x1016 mol/cm2 has been removed from OMI Slant Column to account for stratospheric NO2 contribution

## Slide 54
Pikeville KY
NOAA Shale Oil and Natural Gas Nexus (SONGNEX) field mission: (http://esrl.noaa.gov/csd/projects/songnex/)
Tentative Flight Plans
From Broomfield 6 flights:
Denver-Julesburg, Uintah, Upper Green River, San Juan
From Bismarck 2 flights:
Bakken
From Austin 3-4 flights:
Barnett, Eagle Ford, Haynesville, Permian
From Ohio (optional) 3 flights:
Marcellus
March 24 – April 28, 2015

## Slide 55
Airborne insitu, Geostationary Trace gas and Aerosol Sensor Optimization (GEO-TASO, Jim Leitch, Ball Aerospace) and Airborne Compact Atmospheric Mapper (ACAM, Scott Janz, NASA/GSFC) will be used to validate the spatially enhanced OMI NO2 retrievals during CalNex, DISCOVER-AQ, FRAPPE, and SONGNEX field missions.
Assimilation experiments will be conducted to assess the impact of spatially enhanced OMI NO2 retrievals on air quality within urban and oil and gas basins within regional air quality modeling systems (WRF-Chem, CMAQ)
brad.pierce@noaa.gov
Acknowledgement:
Funding for this work was provided by the NASA Air Quality Applied Science Team 2013 Oil&Gas Tiger Team Project (Anne Thompson, Lead)
Future Directions