## Slide 1
ES/AOS 535 Air Quality Modeling and Analysis February 11, 2016
R. Bradley Pierce
NOAA/NESDIS/CIMSS
Development
and applications of Air Quality Models
Real-time Air Quality Modeling System

## Slide 2
A Proposal to the NASA Langley Research Center 2000 Creativity and Innovation Program
Title: Regional Air Quality Modeling System (RAQMS)
Topic Area: Global Climate and Environmental Quality
Principle Investigator: R. Bradley Pierce (864-5817, r.b.pierce@larc.nasa.gov)
LaRC Co-Investigators: T. Duncan Fairlie (t.d.fairlie@larc.nasa.gov),
Jassim A. Al-Saadi (j.a.al-saadi@larc.nasa.gov), Jennifer R. Olson
(j.r.olson@larc.nasa.gov), James H. Crawford (j.h.crawford@larc.nasa.gov)
Doreen O. Neil (d.o.neil@larc.nasa.gov), Jack Fishman (j.fishman@larc.nasa.gov)
University of Wisconsin Co-Investigators: Donald R. Johnson (donj@ssec.wisc.edu),
Matthew H. Hitchman (matt@meteor.wisc.edu), Gregory J. Tripoli
(tripoli@meteor.wisc.edu)
EPA Co-Investigator: James J. Szykman (j.j.szykman@larc.nasa.gov )
Abstract: This proposed joint effort between LaRC and the University of Wisconsin-Madison (UW) aims to develop a meteorological and chemical modeling system for assimilating remote and in-situ observations of chemical composition, and provide predictions of air quality within any region of planet Earth. The combination of UW meteorological modeling capabilities and LaRC photochemical modeling expertise will yield a powerful capability that advances the science of air quality prediction using observations from new remote sensing platforms and will revolutionize weather forecasting by paving the way for air quality predictions. Developing a capability to assimilate meteorological and chemical observations within RAQMS will provide NASA with outreach opportunities as governmental agencies such as NOAA and EPA move toward operational prediction of air quality in the coming decades.

## Slide 3
Analysis/Forecast Cycle
Observations
Model
Forecast
Increment:
OBS-FX
Statistical
Blending
Analysis
FX IC
Current observations are combined with previous knowledge (first guess) to produce a forecast of the weather

## Slide 4
Schematic of an Operational
Numerical Weather Prediction (NWP) modeling system

## Slide 5
Schematic of an Operational
Numerical Weather Prediction (NWP) modeling system

## Slide 6
AIRS, and MODIS maps were produced with the Giovanni online data system [http://disc.sci.gsfc.nasa.gov/giovanni/]
Satellite Aerosol and Carbon monoxide measurements
Global distribution of carbon monoxide (CO)
From the Atmospheric Infrared Sounder (AIRS)
Global distribution of aerosol optical depth (AOD) from the Moderate Resolution Imaging Spectroradiometer (MODIS)
August 2006

## Slide 7
Challenge for O3 assimilation is separation of the stratosphere from troposphere to provide constraints on tropospheric analysis
AIRS and OMI maps were produced with the Giovanni online data system [http://disc.sci.gsfc.nasa.gov/giovanni/]
Satellite O3 measurements

## Slide 8
Schematic of an Operational
Numerical Weather Prediction (NWP) modeling system

## Slide 9
The primitive equations are a set of nonlinear differential equations that are used to approximate global atmospheric flow and are used in most atmospheric models. They consist of three main sets of equations:
Conservation of momentum: Consisting of a form of the Navier–Stokes equations that describe hydrodynamical flow on the surface of a sphere under the assumption that vertical motion is much smaller than horizontal motion and that the fluid layer depth is small compared to the radius of the sphere
A thermal energy equation: Relating the overall temperature of the system to heat sources and sinks
The Atmospheric Model
A continuity equation: Representing the conservation of mass.
Add continuity equations for each chemical species, as well as sources (emissions, photochemical and microphysical sources), and sinks (wet and dry deposion, photochemical loss) and you have RAQMS

## Slide 10
Online global chemical and aerosol assimilation/ forecasting system
UW-Madison sigma-theta hybrid coordinate model (UW-Hybrid) dynamical core
Unified stratosphere/troposphere chemical prediction scheme (LaRC-Combo) developed at NASA LaRC
Aerosol prediction scheme (GOCART) developed by Mian Chin (NASA GSFC).
Statistical Digital Filter (OI) assimilation system developed by James Stobie (NASA/GFSC)
Model Description

## Slide 11
Online global chemical and aerosol assimilation/ forecasting system
UW-Madison sigma-theta hybrid coordinate model (UW-Hybrid) dynamical core
Unified stratosphere/troposphere chemical prediction scheme (LaRC-Combo) developed at NASA LaRC
Aerosol prediction scheme (GOCART) developed by Mian Chin (NASA GSFC).
Statistical Digital Filter (OI) assimilation system developed by James Stobie (NASA/GFSC)
Model Description

## Slide 12
UW-Hybrid Equations
UW-Hybrid Vertical Grid
UW-Hybrid Conservation Properties

## Slide 13
Online global chemical and aerosol assimilation/ forecasting system
UW-Madison sigma-theta hybrid coordinate model (UW-Hybrid) dynamical core
Unified stratosphere/troposphere chemical prediction scheme (LaRC-Combo) developed at NASA LaRC
Aerosol prediction scheme (GOCART) developed by Mian Chin (NASA GSFC).
Statistical Digital Filter (OI) assimilation system developed by James Stobie (NASA/GFSC)
Model Description

## Slide 15
Online global chemical and aerosol assimilation/ forecasting system
UW-Madison sigma-theta hybrid coordinate model (UW-Hybrid) dynamical core
Unified stratosphere/troposphere chemical prediction scheme (LaRC-Combo) developed at NASA LaRC
Aerosol prediction scheme (GOCART) developed by Mian Chin (NASA GSFC).
Statistical Digital Filter (OI) assimilation system developed by James Stobie (NASA/GFSC)
Model Description

## Slide 17
“Remote Sensing of Tropospheric Pollution from Space” (BAMS June 2008 Cover Article)
  current capabilities for assimilation of composition measurements (RAQMS)
  role of trace gas measurements within the context of GEOSS
  national priorities for space-based measurements in the next decade (NRC Decadal Survey)
(Top) August 2006 O3 and CO columns from Realtime Air Quality Modeling System (RAQMS) chemical analyses. (Bottom) Comparisons for Houston and Huntsville IONS ozonesonde sites.
REMOTE SENSING OF TROPOSPHERIC POLLUTION FROM SPACE:
JACK FISHMAN, KEVIN W. BOWMAN, JOHN P. BURROWS, ANDREAS RICHTER, KELLY V. CHANCE,DAVID P. EDWARDS, RANDALL V. MARTIN, GARY A. MORRIS, R. BRADLEY PIERCE, JERALD R. ZIEMKE,JASSIM A. AL-SAADI, JOHN K. CREILSON, TODD K. SCHAACK, AND ANNE M. THOMPSON

## Slide 18
RAQMS Applications

## Slide 19
NOAA P3 Flights

## Slide 20
Schematic of an Operational
Numerical Weather Prediction (NWP) modeling system

## Slide 21
Continental
Background
Northeast
Corridor
Impacts on Continental Scale
Air Quality Prediction

## Slide 22
The effects of CO BCs are most important near the surface.
The effects of O3 BCs are most important above 4 km.
Significant implications for operational AQ forecasting
DC8 CO
DC8 O3
P3 CO
P3 O3

## Slide 23
Links between air quality and global climate change
Air Quality
Fourth Assessment Report of the Intergovernmental Panel on Climate Change, 2007
Notes: 23

## Slide 24
April 2008 Biomass Burning CO Emissions
Kazakhstan
Baykal
Thailand
Notes: 24

## Slide 26
Impacts of Kazakhstan/Baykal/Thailand wildfires
Impact of Kazakhstan/Baykal/Thailand wildfires on tropospheric aerosols extends into North America with potential US Air Quality impacts
Notes: 26

## Slide 27
April 22nd,2008
Trinidad Aeronet vs RAQMS AOD: April 2008
Biomass burning aerosols observed at Trinidad Head on April 22, 2008
Aerosol Robotic Network (AERONET)
is global network of Sun photometers
[Holben et al., 1998]

## Slide 28
The Front Range Air Pollution and Photochemistry Éxperiment (FRAPPÉ) field campaign took place from July 16 to August 18, 2014.
  FRAPPE was collaborative effort between the Colorado Department of Public Health
  and the Environment and NCAR.
The mission was closely coordinated with the NASA DISCOVER-AQ project, which agreed to conduct their final aircraft deployment in the Colorado Front Range.
  DISCOVER-AQ, a NASA Earth Venture program funded mission, stands for Deriving Information on Surface Conditions from Column and Vertically Resolved Observations Relevant to Air Quality.
Research aircraft and ground-based research mission to understand summertime air quality along the Colorado Northern Front Range Metropolitan Area (NFRMA)

## Slide 29
RAQMS Black and Organic Carbon (BCOC) Aerosol optical depth (AOD) Analysis
July-August, 2014

## Slide 30
RAQMS Black and Organic Carbon (BCOC) Aerosol optical depth (AOD) Analysis
12Z July 19, 2014

## Slide 31
RAQMS smoke (Black and Organic Carbon) Analysis
BAO July-August 2014
July 16-20, 2014

## Slide 32
RAQMS Smoke prediction (with MODIS AOD Assimilation)
RAQMS Smoke prediction (no MODIS AOD Assimilation)
RAQMS MODIS AOD ASSIM vs
NO ASSIM
July 16-20, 2014

## Slide 33
RAQMS Smoke prediction (with MODIS AOD Assimilation)
RAQMS MODIS AOD ASSIM vs
UW HSRL
July 16-20, 2014

## Slide 34
RAQMS Smoke prediction (with MODIS AOD Assimilation)
RAQMS MODIS AOD ASSIM vs
UW HSRL
July 16-20, 2014

## Slide 35
Distributed Regional Aerosol Gridded Observation Networks (DRAGON)-USA 2014 Colorado Front Range Urban Corridor
DRAGON
RAQMS
(DRAGON-USA, Brent Holben, NASA/GSFC)
http://aeronet.gsfc.nasa.gov/new_web/DRAGON-USA_2014_Colorado.html
July 16-20

## Slide 36
Distributed Regional Aerosol Gridded Observation Networks (DRAGON)-USA 2014 Colorado Front Range Urban Corridor
DRAGON
RAQMS
(DRAGON-USA, Brent Holben, NASA/GSFC)
http://aeronet.gsfc.nasa.gov/new_web/DRAGON-USA_2014_Colorado.html
July 16-20

## Slide 37
Schematic of an Operational
Numerical Weather Prediction (NWP) modeling system

## Slide 38
http://raqms-ops.ssec.wisc.edu/
Today’s Forecast

## Slide 39
http://raqms.ssec.wisc.edu/
RAQMS/WRF-Chem
PM2.5 forecast Feb 11, 2016
Today’s Forecast

## Slide 40
Questions?
Brad.pierce@noaa.gov