## Slide 1
Implementation of AIRS, IASI, and CrIS based stratospheric intrusion forecasting capability
into
IDEA-International
(Brad Pierce, NOAA/NESDIS)
With significant support from the CIMSS IMAPP/CSPP team
(James Davies, Kathy Strabala, Nadia Smith, Elisabeth Weisz, Rebecca Cintineo)
Air Quality Applied Sciences Team 5th Semi-Annual Meeting (AQAST 5)
June 4-6, 2013, University of Maryland, College Park

## Slide 2
Objective: Provide satellite based support to state and local air quality management for stratospheric intrusion (SI) related exceptional event analysis. (Gail Tonnesen and Pat Reddy POCs)
Tasks:
Development of a RAQMS public website with products adapted for SI forecasting in Western US. Gail Tonnesen and Pat Reddy will provide guidance during the development of this website and evaluate its effectiveness during Spring 2013 SI events.
Add capabilities to IDEA-I (http://cimss.ssec.wisc.edu/imapp/ideai_v1.0.shtml) within the International AIRS/MODIS Processing Package (IMAPP) to produce trajectory based SI forecasts initialized with real-time AIRS ozone retrievals.
Conduct retrospective nested high resolution RAQMS/WRF-CHEM SI forecasts for May 2010 and 2012 and provide an assessment of the influence of mesoscale circulations on SI to the EPA SI Working Group. (This task complements AQAST SI studies by Arlene Fiore using the AM3 model)
AQAST Tiger Team Project FY2013 (Brad Pierce, PI)
Satellite based support for Stratospheric Intrusion Exceptional Event Analysis
and
Secondary Visibility Standard Implementation Planning

## Slide 3
http://sunset.ssec.wisc.edu/idea-test2/
IDEA-I AIRS, CrIS, and IASI SI forecast capability is currently being beta tested at CIMSS using the UW-Madison Dual Regression retrieval
Refining initialization criteria
Extensive testing for June 6, 2012 Wyoming SI Exceptional Event Analysis
The Infusing Satellite Data Into Environmental Applications - International (IDEA-I) SI forecast is being developed under the Community Satellite Processing Package (CSPP)
CSPP supports the Direct Broadcast (DB) satellite community through the packaging and distribution of open source science software.
Funded by NOAA JPSS

## Slide 4
UW HS retrieval package V1.0
For AIRS, IASI and CrIS L1 to L2 Processing
Released under CSPP on 28 November 2012
Elisabeth Weisz, Bill L. Smith Sr., Nadia Smith, Kathy Strabala, et al.
Atmospheric Profile and Cloud Parameter Retrievals from Hyperspectral Infrared Radiances
IASI (nch=8461) on Metop-A, Metop-B
CrIS (nch=1305) on Suomi-NPP
AIRS (nch=2378) on Aqua
The UW hyper-spectral retrieval package, based on the Dual-Regression (DR) retrieval algorithm, is the only publicly available retrieval software package to convert hyper-spectral radiance measurements (Level 1) to retrieval (Level 2) products.

## Slide 5: Dual-Regression Retrieval Parameters
atmospheric temperature [K] at 101 pressure levels
atmospheric humidity [g/kg] at 101 pressure levels
atmospheric ozone [ppmv] at 101 pressure levels
atmospheric relative humidity [%] at 101 pressure levels
atmospheric dew point temperature [K] at 101 pressure levels
surface skin temperature [K]
surface emissivity at instrument spectral resolution
total precipitable water (vertically integrated from 100 hPa to surface) [cm]
precipitable water 1, 2, 3 (vertically integrated from 900 hPa to surface, 700 to 900, 300 to 700 hPa) [cm]
total ozone amount (vertically integrated) [dobson units]
lifted index [oC]
convective available potential energy [J/kg]
CO2 concentration [ppmv]
cloud top pressure [hPa]
cloud top temperature [K]
cloud optical thickness
effective cloud emissivity
cloud mask (values: 0 clear, 1 cloud)
Output Format: hdf5
http://cimss.ssec.wisc.edu/cspp/uwhsrtv_edr_v1.1.shtml
Used in SI
initialization
O3VMR (ppmv)
DPD (K)

## Slide 6
Basis for initialization point selection criteria
Plevs threshold: >500mb
O3VMR threshold: >0.08 to 0.10 (80-100ppbv)
Dewpnt-Tair threshold: <-15K
14 May, 2012
Upper left quadrant is stratospheric air;
dry air with high ozone

## Slide 7
On May 21, 2013, the State of Wyoming Department of Environmental Quality/Air Quality Division released a document entitled “Exceptional Event Demonstration Package for the Environmental Protection Agency Thunder Basin, Wyoming Ozone Standard Exceedance June 6, 2012” for public comment.
Following the public comment period, this document will be submitted to the US Environmental Protection Agencey (US EPA) to demonstrate that the surface ozone exceedances were due to an exceptional event associated with a stratospheric intrusion (SI).
“The Wyoming Department of Environmental Quality/Air Quality Division (WDEQ/AQD) has determined that a stratospheric intrusion created elevated ozone readings resulting in an 8-hour ozone standard exceedance at the Thunder Basin, Wyoming ozone monitor located in northeastern Wyoming on June 6, 2012” (Executive Summary)

## Slide 8
Two day’s prior to Wyoming SI exceptional Event
(6 initialization opportunities each day!)

## Slide 9
AIRS trajectory forecast showing descent into WY
Starting June 4
(two days before)

## Slide 10
Last frame of web animation @ 2012-06-07 00Z
Initialization points
Each “worm” is 6 hours of air parcel history
500 hPa GFS winds
AIRS trajectory forecast showing descent into WY
Starting June 4
(two days before)

## Slide 11
Archived gridded data netCDF file includes ozone retrieval swaths and GFS data fields
IASI 516 hPa ozone (ppmv) and 500mb stream lines, June 4, 2012

## Slide 12
CrIS 2150Z
AIRS 2100Z
IASI 1840Z
Ozone from IASI, AIRS, and CrIS can be viewed and compared in McIDAS-V
516 hPa Ozone and Cross-sections June 4, 2012

## Slide 13
Future Plans
Release IDEA-I SI forecast package to CSPP Beta users for testing in July, 2013
Maintain IDEA-I SI forecast capability at CIMSS for use by State and local AQ forecasters
Conduct retrospective case studies during 2013 SI events for evaluation by EPA SI Working Group

## Slide 14
http://www.esrl.noaa.gov/csd/projects/lvos.html
Las Vegas Ozone Study (LVOS)
Where: Angel Peak, Nevada
When: May - June 2013
NOAA ESRL CSD Tunable Optical Profiler for Aerosol and oZone (TOPAZ) lidar.
TOPAZ data provided by Andrew Langford (NOAA/ESRL)

## Slide 16
Extra Slides

## Slide 17
Training Set
Simulated Radiances
Retrieval
Radiances
AIRS L1B,
IASI L1C, CrIS SDR
Temperature, Moisture and Ozone profiles,
Surface and cloud parameters ….
Dual-Regression Retrieval
Regression Coefficients