## Slide 1
2017 NASA Health and Air Quality Applications Program Review, September 12-13, 2017, Reno, NV
Aura Chemical Reanalysis in support Air Quality Applications
PI Brad Pierce
(NOAA/NESDIS)
Presented by
Allen Lenzen
(UW-Madison, SSEC)
Contributions from
Monica Harkey
(UW-Madison, SAGE)
Notes: Electronic version at: ftp://ftp.ssec.wisc.edu/pub/raqms/Aura_Reanalysis/NASA_2017_Applied_Science_Program_Review_Pierce_Final.pptx

## Slide 2: Aura Chemical Reanalysis in support Air Quality Applications
Solicitation – ROSES 2013 Aura Science Team
Project Summary
  Utilize the Real-time Air Quality Modeling System (RAQMS) in conjunction with the NOAA Operational Gridpoint Statistical Interpolation (GSI) 3-dimensional variational data assimilation (DA) system to conduct a multi-year global chemical and aerosol reanalysis using NASA Aura and A-Train measurements.
Project Objectives
  Provide the air quality community with a multi-year global chemical and aerosol reanalysis using NASA Aura and A-Train measurements.
  Conduct regional chemical data assimilation experiments to quantify the influences in changes in NOx emissions on US air quality during the Aura period.
  Provide global 3 dimensional O3, CH4, N2O production and loss rates for next generation NOAA global forecast system.
  Collaborate with International, Federal, State and Local air quality management communities in the utilization of the Aura and A-Train measurements and reanalysis for air quality assessment activities.
|‌ 2
Notes: Same as last year, can go through rather quickly

## Slide 3
  FY16 funds (final year, $153,028) were received by NESDIS/STAR on July 19, 2016 due to delays in MOU approval by NOAA legal.
  CIMSS received FY16 funding from NESDIS/STAR on Sept, 15, 2016.
  NESDIS/STAR has requested a 1 year no-cost extension to complete the Aura Reanalysis project, which is currently scheduled to close on Sept 30, 2017.
Budget
Aura Chemical Reanalysis in support Air Quality Applications
Notes: Have spent 40% of the FY16 funds (CIMSS Year 3 proposal goes from 1 July 2016 to 30 June 2017).

## Slide 4: Applications Readiness Level (ARL)
|‌ 4
As of July 16, 2015
Started at ARL 3 (Proof of Application Concept) with real-time RAQMS Data assimilation
Reached ARL 4 (Initial Integration and Verification) upon successfully completing the RAQMS/GSI Data Denial experiments (September, 2016)
Reached ARL 5 (Validation in Relevant Environment) upon completion of 2010 RAQMS/GSI analysis (December 2016)
Currently at ARL 6 (Demonstration in Relevant Environment) based on finalizing 2006-2016 emissions constraints, MLS, OMI, AIRS, and MODIS assimilation procedures, and successful completion of the first four years of Aura Reanalysis.
Will reach ARL 7 by the end of requested 1-year no-cost extension with delivery of RAQMS Aura Reanalysis to DAAC.
Aura Chemical Reanalysis in support Air Quality Applications
Notes: Currently at Applications Readiness Level (ARL) 6 (Demonstration in Relevant Environment) will reach ARL 7 (Functional) with delivery to DAAC
PI is now getting “ebook” notifications of reporting, and has updated ARL

## Slide 5
Aura Chemical Reanalysis in support Air Quality Applications
Results and Milestones (Year 3)
  Completed first 4 years (2006-2009) of the 10 year Aura Reanalysis
  Conducted verification studies to assess the fidelity of the Aura Reanalysis through comparisons with airborne insitu measurements collected during NASA, NOAA and NSF field campaigns
  Completed CMAQ/GSI NOx emission adjustment experiments using offline CMAQ/GSI OMI NO2 assimilation constraints
Notes: This is the focus of the rest of the presentation, no need to read these, will walk through one at a time

## Slide 6
Aura Chemical Reanalysis in support Air Quality Applications
Results and Milestones (Year 3)
  Completed first 4 years (2006-2009) of the 10 year Aura Reanalysis
  Conducted verification studies to assess the fidelity of the reanalysis through comparisons with airborne insitu measurements collected during NASA, NOAA and NSF field campaigns
  Completed CMAQ/GSI NOx emission adjustment experiments using offline CMAQ/GSI OMI NO2 assimilation constraints
Notes: This is the focus of the rest of the presentation, no need to read these, will walk through one at a time

## Slide 7
Ziemke, et al. (2006), Tropospheric ozone determined from Aura OMI and MLS: Evaluation of measurements and comparison with the Global Modeling Initiative’s Chemical Transport Model, J. Geophys. Res., 111, D19303, doi:10.1029/2006JD007089.
Analyzed Tropospheric Ozone Column (TOC)
vs
OMI-MLS Tropospheric Ozone Residuals (TOR)
Aura Reanalysis captures seasonal variation but shows a systematic high bias relative to the OMI-MLS TOR

## Slide 8
Ziemke, et al. (2006), Tropospheric ozone determined from Aura OMI and MLS: Evaluation of measurements and comparison with the Global Modeling Initiative’s Chemical Transport Model, J. Geophys. Res., 111, D19303, doi:10.1029/2006JD007089.
ARCTAS
ARCTAS
Airborne measurements from NASA ARCTAS field campaign are used to verify Northern Hemisphere Aura Reanalysis TOC during July 2008

## Slide 9
NASA ARCTAS Cold Lake, AB Phase
ARCTAS Flight Tracks July 2008
>1DU High Bias
Aura Reanalysis shows excellent (<1%) agreement with airborne column
Notes: Aura Reanalysis overestimates observed ozone at ~900mb due to ozone production within wild fire plumes sampled during the July 2008 phase of the ARCTAS campaign (see extra slides)

## Slide 10
Ziemke, et al. (2006), Tropospheric ozone determined from Aura OMI and MLS: Evaluation of measurements and comparison with the Global Modeling Initiative’s Chemical Transport Model, J. Geophys. Res., 111, D19303, doi:10.1029/2006JD007089.
HIPPO
HIPPO
Airborne measurements from NSF HIPPO-I field campaign are used to verify Aura Reanalysis TOC over the Pacific Ocean during January 2009

## Slide 11
HIPPO-1 January 2009 O3 Verification
2.5DU
(10%) High Bias
HIPPO Flight Tracks January 2009
Aura Reanalysis shows 10% high bias relative to airborne column
~4DU

## Slide 12
<1DU (<2%) NH Bias
1.3 DU (6%) SH Bias
5DU (28%) Tropical Bias
Northern Hemisphere
Southern Hemisphere
Tropics
Tropical Pacific region (20N-20S) dominates the 10% high bias in Tropospheric ozone column
HIPPO-1 January 2009 O3 Verification

## Slide 13
<0.1x1018 mol/cm2
(7%) High Bias
HIPPO-1 January 2009 CO Verification
HIPPO Flight Tracks January 2009
Aura Reanalysis shows slight high global bias relative to airborne column
Notes: Note: RAQMS/GSI AIRS CO assimilation removes influence of apriori which accounts for most of the hemispheric differences in the AIRS CO column retrieval

## Slide 14
Northern Hemisphere
Southern Hemisphere
Tropics
Northern Hemisphere (>20N) has 13% low bias in CO column relative to airborne measurements
HIPPO-1 January 2009 O3 Verification
0.27x1018 mol/cm2
(13%) Low Bias
<0.1x1018 mol/cm2
(8%) High Bias
<0.1x1018 mol/cm2
(1.5%) Low Bias

## Slide 15
HIPPO-1 January 2009 BC Verification
HIPPO Flight Tracks January 2009
0.1x1015 mol/cm2
(83%) High Bias
Aura Reanalysis high bias relative to airborne column under low black carbon aerosol loadings

## Slide 16
HIPPO-1 January 2009 BC Verification
Northern Hemisphere
Southern Hemisphere
Tropics
0.1x1015 mol/cm2
(28%) High Bias
<0.1x1015 mol/cm2
(50%) High Bias
<0.1x1015 mol/cm2
(65%) High Bias
Mid tropospheric BC overestimates of 2-5x dominate overall high biases in BC column relative to airborne measurements under low aerosol loadings
Notes: AEROCOM models overestimate the BC concentrations in remote regions by a factor of five on average (Schwarz et al. 2010)

## Slide 17
Species
NH (>20N)
Tropics
SH (<20S)
All Pacific
O3
CO
BC
10% High Bias
2% High Bias
28% High Bias
6% High Bias
7% High Bias
13% Low Bias
8% High Bias
1.5% Low Bias
83% High Bias*
28% High Bias
50% High Bias
65% High Bias
*AEROCOM models overestimate the BC concentrations in remote regions by a factor of five on average (Schwarz et al. 2010)
HIPPO-1 January 2009 Verification Summary

## Slide 18
Aura Chemical Reanalysis in support Air Quality Applications
Results and Milestones (Year 3)
  Completed first 4 years (2006-2009) of the 10 year Aura Reanalysis
  Conducted verification studies to assess the fidelity of the reanalysis through comparisons with airborne insitu measurements collected during NASA, NOAA and NSF field campaigns
  Completed CMAQ/GSI NOx emission adjustment experiments using offline CMAQ/GSI OMI NO2 assimilation constraints
Notes: This is the focus of the rest of the presentation, no need to read these, will walk through one at a time

## Slide 19
Offline adjustment of area and point NOx emissions based on OMI Tropospheric NO2 column analysis increments
(NO2 lifetime too short to use assimilation to constrain tropospheric column amounts)
July 2011 average area emissions (NEI)
CMAQ/GSI NOx emission adjustment experiments

## Slide 20
Calculate monthly mean NO2 Jacobian (β) from a 15% NOX emission reduction perturbation experiment following Lamsal et al. 2011
Calculate monthly mean NO2 analysis increment using CMAQ/GSI OMI NO2 assimilation
  Lightning NOx sensitive background errors (to correct LNOx bias)
  NEI 2011 NOx sensitive background errors (to correct NEI emissions)
Adjust 2011 NEI NOx emissions using Jacobian and analysis increment
Lamsal, L. N., et al. (2011), Application of satellite observations for timely updates to global anthropogenic NOx emission inventories, Geophys. Res. Lett., 38, L05810, doi:10.1029/2010GL046476.
CMAQ/GSI NOx emission adjustment experiments

## Slide 21
July 2011 analysis increment
CMAQ/GSI NOx emission adjustment experiments
Analysis increment adjusts NO2 columns downward in urban areas
(with adjusted lightning NOX emissions)

## Slide 22
July 2011 OMI NO2
Transportation-related NOX emissions ~ 0.3 moles/sec
(~30% adjustment)
NOX emissions in urban areas ≥ 2 moles/sec
(~10% adjustment)
July 2011 NEI area-source emissions adjustment
CMAQ/GSI NOx emission adjustment experiments

## Slide 23
molecules/cm2
July 2011 average CMAQ (original emissions)
July 2011 average OMI NO2
R = 0.61
mean bias = -0.84 x 1015 molecules/cm2
CMAQ/GSI NOx emission adjustment experiments
OMI

## Slide 24
July 2011 average observed
mean bias = -0.46 x 1015 molecules/cm2
R = 0.66
July 2011 average OMI NO2
molecules/cm2
July 2011 average CMAQ (adjusted emissions)
CMAQ/GSI NOx emission adjustment experiments
OMI
CMAQ simulation with adjusted Lighting and NEI Emissions shows reduced low biases and increased correlations with OMI

## Slide 25
Ongoing activities
PI and Co-I are members of Aerosol and Atmospheric Composition Task Force for development of NOAA’s Next Generation Global Prediction System (NGGPS)
  Funded by NOAA Research Transition Acceleration Program (RTAP) for implementation of reduced troposphere/stratosphere chemistry algorithms into NGGPS.
  Aura Reanalysis will provide climatological regressions for NGGPS N2O and CH4 and ClOx and BrOx catalyzed stratospheric ozone loss
PI is Co-Lead (with Daniel Tong, GMU) of a multi-agency (NOAA, EPA, CDC) HAQAST Tiger Team for improved NEI NOx emissions based on CMAQ/GSI/OMI NO2 DA activities
  OMI based emissions adjustment approaches will be demonstrated within the NOAA NWS National Air Quality Forecasting Capability (NAQFC) and EPA/CDC fusion applications
Aura Chemical Reanalysis in support Air Quality Applications
Notes: Strong partnership with LADCO and Wisconsin DNR, LMOS 2017 mission concept arose from NASA Air Quality Applied Science Team (AQAST) meetings
NASA committed to providing Geostationary Trace gas and Aerosol Sensor Optimization (GeoTASO) airborne sensor (UVVIS spectrometer like TEMPO to measure O3, NO2, HCHO (formaldehyde)
Link to NOAA Operational global modeling/DA effort through NGGPS
Archived stratospheric halogen (ClOx/BrOx) ozone production from Aura Reanalysis will be used within NGGPS chemistry algorithm

## Slide 26
Aura Chemical Reanalysis in support Air Quality Applications
Application to Decision Making
The RAQMS Aura Reanalysis is the first complete global chemical and aerosol reanalysis that has been attempted within the US.
It follows the path lead by the European Monitoring Atmospheric Composition and Climate - Interim Implementation (MACC-II) project within the Copernicus Atmosphere Monitoring Service that is now operational at ECMWF.
The RAQMS Aura Reanalysis will provide comprehensive chemical and aerosol analyses for assessing global air quality and for providing lateral boundary conditions for regional air quality management such as State Implementation Planning (SIP) activites.
Notes: Strong partnership with LADCO and Wisconsin DNR, LMOS 2017 mission concept arose from NASA Air Quality Applied Science Team (AQAST) meetings
NASA committed to providing Geostationary Trace gas and Aerosol Sensor Optimization (GeoTASO) airborne sensor (UVVIS spectrometer like TEMPO to measure O3, NO2, HCHO (formaldehyde)
Link to NOAA Operational global modeling/DA effort through NGGPS
Archived stratospheric halogen (ClOx/BrOx) ozone production from Aura Reanalysis will be used within NGGPS chemistry algorithm

## Slide 27
Extra Slides

## Slide 28
All ARCTAS Cold Lake, AB DC8 Flights
Note: Significant wildfire sampling

## Slide 29
All ARCTAS Cold Lake, AB DC8 Flights
Note: Significant wildfire sampling

## Slide 30
All ARCTAS Cold Lake, AB DC8 Flights
Note: Significant wildfire sampling