## Slide 1: Determination of Greenhouse Gas Profiles from Ground-based Infrared Radiance Measurements
W. L. Smith Sr.1,2, L. Rochette3, R. B. Pierce4
1Hampton University – Hampton VA USA
2University of Wisconsin – Madison WI. USA
3LRTec – Quebec QC CA
4NOAA/NESDIS – Madison WI. USA
AERI (1990)
ASSIST (2008)
Ground-based
Spectral Coverage
Wavenumber (cm-1)
"Imaging Spectrometry XVII” 13 – 16 August 2012
San Diego California

## Slide 2: Radiative Processes
D
I
R
E
C
T

## Slide 3
FTS Measurement to Atmospheric Variables
Michelson Interferometer (FTS)
Interferogram
Radiance Spectrum
Vertical Sounding
Source
Fixed Mirror
Moving
Mirror
Beam
Splitter
Detector
Fourier Transformation
Numerical
Inversion
d1
d2
(d2-d1)
Radiance (mw/(m2-str-cm-1)
Brightness Temperature (°K)
Wavenumber (cm-1)

## Slide 4
Brightness Temperature/Radiance Spectrum
Radiance (mw/(m2-str-cm-1)
Wavenumber (cm-1)
Brightness Temperature (°K)
Wavenumber (cm-1)
O3
O3
H2O
H2O
H2O
H2O
H2O
H2O
CO2
CO2
CO2
CO2
N2O
N2O
N2O
N2O
CO
CO
CH4
CH4

## Slide 5: Jacobian (Radiance Sensitivity)
ΔRi = Σ(dRi/dQj) ΔQj
j
Where;
Qi = Temperature, H2O, O3, CO, CH4, and
N2O concentration, and Aerosol Extinction.

## Slide 6: Ground-based ASSIST Retrieval Sensitivity to Trace Gases
Brightness Temperature/Temperature Jacobian
Jacobian (°K/°K-km)
Wavenumber (cm-1)
Jacobian (°K/°K-km)
Altitude (km)
Wide spectral contribution
Sensitivity strong (>0.2) below 2-km

## Slide 7: Ground-based ASSIST Retrieval Sensitivity to Trace Gases
Brightness Temperature/Water Vapor Jacobian
Jacobian (°K/%-km)
Wavenumber (cm-1)
Jacobian (°K/%-km)
Altitude (km)
Moderate wide spectral contribution
Sensitivity strong (>0.2) below 3-km

## Slide 8: Ground-based ASSIST Retrieval Sensitivity to Trace Gases
Brightness Temperature/Ozone Jacobian
Jacobian (°K/%-km)
Wavenumber (cm-1)
Jacobian (°K/%-km)
Altitude (km)
Isolated moderate longwave spectral contribution
Sensitivity strong (>0.2) below 10-km

## Slide 9: Ground-based ASSIST Retrieval Sensitivity to Trace Gases
Brightness Temperature/Methane Jacobian
Jacobian (°K/%-km)
Wavenumber (cm-1)
Jacobian (°K/%-km)
Altitude (km)
Isolated moderate midwave contribution
Sensitivity strong (>0.2) below 4-km

## Slide 10: Ground-based ASSIST Retrieval Sensitivity to Trace Gases
Brightness Temperature/Nitrous Oxide Jacobian
Jacobian (°K/%-km)
Wavenumber (cm-1)
Jacobian (°K/%-km)
Altitude (km)
Weak isolated midwave + strong shortwave spectral contribution
Sensitivity strong (>0.2) below 2-km

## Slide 11: Ground-based ASSIST Retrieval Sensitivity to Trace Gases
Brightness Temperature/Carbon Monoxide Jacobian
Jacobian (°K/%-km)
Wavenumber (cm-1)
Jacobian (°K/%-km)
Altitude (km)
Isolated strong shortwave spectral contribution
Sensitivity strong (>0.2) below 6-km

## Slide 12: Ground-based ASSIST Retrieval Sensitivity to Trace Gases
Brightness Temperature/Carbon Dioxide Jacobian
Jacobian (°K/%-km)
Wavenumber (cm-1)
Jacobian (°K/%-km)
Altitude (km)
Weak longwave and shortwave spectral contribution
Sensitivity strong (>0.2) below 0.5 km

## Slide 13: Ground-based ASSIST Retrieval Sensitivity to Trace Gases
Brightness Temperature/Aerosol Jacobian
Jacobian (°K/%-km)
Wavenumber (cm-1)
Jacobian (°K/%-km)
Altitude (km)
Weak longwave and shortwave “window” spectral contribution
Sensitivity strong (>0.2) below 1-km

## Slide 14: Greenhouse Gas Physical Regression (PR) Retrieval Methodology
Qret = qo + (rm-ro)C
C = (R’TR’ + λETE)-1R’TQ’
q = atmospheric profiles (temperature, water vapor, etc.)
C = statistical covariance about the initial profile qo
ro = radiance calculated from the initial profile qo
Q & R = climatological ensemble of profiles & radiance spectra
( )’ = deviation from the initial conditions qo and ro
ETE = statistical covariance of spectral radiance noise
λ = scaler determined as that value which minimizes the
RMS difference between the retrieval calculated radiance
spectrum and observed radiance spectrum

## Slide 15
Statistical Data For C-Matrix
Year 2010 Global Product
3,110,400 Space/Time Samples
1-deg Resolution
Monthly Day 15, 0, 6 12, 18 GMT
T, H2O, O3, CO, CH4, N2O Profiles
Aerosol Extinction Profiles
CO2 uniformly mixed, randomly varied
Cloud Altitude/Optical Depth Profiles
Separated Into Seasonal/Regional Sets
http://www.esrl.noaa.gov/outreach/events/chemworkshop/pdf/Pierce_RAQMS.pdf

## Slide 16: Profile Regression Retrieval Errors
T
H2O
O3
CO
CH4
N2O
CO2
Aerosol

## Slide 17: Accounting for the Influence of Clouds
Cloud-Clearing Partly Cloudy Measurements (N* Method1)
  N* equation solves for clear radiance from partly clouded IFOVs
  Assumes that only the cloud fraction changes between two IFOVs
ti
t1
tj
tn
Rc(w)
Rc(w)
1 Smith, W. L. , 1968: An improved method for calculating tropospheric temperature and moisture from satellite radiometer measurements. Mon. Wea. Rev., 96, 387-396.
Time (UT)
Time (UT)

## Slide 18: Producing Clouded Radiance Retrieval
Cloud Stratification
  Stratifies C-matrix by cloud level (10- cloud levels + clear)
  Define optimal cloud-level as that one for which:
  RMSD [T(p,Pcld) - T(p,Rcc)] = Min
Procedure:
Calculate Rcc using the N* procedure outlined above.
Calculate T(p,Pcld) using the C-matrices for the 11 cloud altitude classes
For each cloud altitude class, compute the RMSD between T(p,Pcld) and T(p,Rcc)
Assume that the correct cloud class is that one for which RMSD [T(p,Pcld) - T(p,Rcc)] = Min
Set all profile values above the cloud level to be NaN (i.e., missing)

## Slide 19: June 22, 2010 Cloudy Case Study
Temperature
Mixing Ratio
Potential
Temperature
Relative
Humidity

## Slide 20: BIAS Corrections Using Forecast Model Profile
Problem: PR method uses a statistical training data set. Imperfect skill, due to lack of vertical resolution in radiances, leads to local bias in PR retrievals.
Solution: Calculate radiances from forecast model profile (FP) and perform PR retrieval using model radiances.
Statistical bias correction = FP – FP radiance retrieved FP
Bias
Corrected
Bias Correction removes statistical bias with respect to the model FP
RTVL
Corrected RTVL

## Slide 21: ASSIST Profile Results April 19 17 UTC – April 21, 00 UTC
Temperature ( 0 – 4 km)
Relative Humidity ( 0 – 4 km)
ASSIST - only
RAQMS
ASSIST w BIAS Correction

## Slide 22: ASSIST Profile Results April 19 17 UTC – April 21, 00 UTC
Ozone ( 0 – 4 km)
ASSIST - only
RAQMS
Carbon Monoxide( 0 – 4 km)
ASSIST w BIAS Correction

## Slide 23: ASSIST Profile Results April 19 17 UTC – April 21, 00 UTC
Methane ( 0 – 4 km)
ASSIST - only
RAQMS
Nitrous Oxide( 0 – 4 km)
ASSIST w BIAS Correction

## Slide 24
The retrieval procedure involves:
  Using an optimal estimation algorithm which incorporates a climatological covariance matrices for cloud height classes produced by a global dynamical chemistry model
  Obtaining the cloud free radiance spectra from cloud attenuated spectra using the well known “N* Method” used for operational processing of satellite data
  Defining the cloud height and proper cloud class for the statistical retrieval as that one in which the RMSD between the clouded radiance retrieval and the “clear sky radiance” retrieval is a minimum
  Correcting the retrieval for statistical bias using the difference between a real-time dynamical chemistry model model profile and the retrieval obtained from the radiance spectrum simulated from it
Retrieval Procedure Summary

## Slide 25
Retrieval Flow Chart
ASSIST Radiance
ASSIST Radiance
Profile Retrieval
NWP Profile
NWP Radiance
Clear Air
Radiance Threshold
Statistical Bias Correction
(NWP Profile – NWP Retrieval)
( If Internet Available )
Clear Column
Radiance
NWP Radiance
Profile Retrieval
Cloud Class
Determination
ASSIST Final
Profile Retrieval
RAQMS Regression
Statistics

## Slide 26: Cooperative Atmospheric Measurement program (CAMP)
ASSIST
(McKinney Texas Vs Lamont Oklahoma)
Lamont
Lamont
McKinney
McKinney
AERI
ASSIST

## Slide 27: McKinney Texas – June 25, 2012

## Slide 28: Temperature (FTS, FTS+BC, RAQMS)
McKinney FTS- only
McKinney FTS with BC
McKinney RAQMS
Lamont FTS- only
Lamont FTS + BC
Lamont RAQMS

## Slide 29: Relative Humidity (FTS, FTS+BC, RAQMS)
McKinney FTS- only
McKinney RAQMS
Lamont FTS - only
Lamont FTS with BC
Lamont RAQMS
McKinney FTS with BC

## Slide 30: Ozone (FTS, FTS+BC, RAQMS)
McKinney FTS- only
McKinney RAQMS
Lamont FTS- only
Lamont RAQMS
Lamont FTS with BC
McKinney FTS with BC

## Slide 31: Carbon Monoxide (FTS, FTS+BC, RAQMS)
McKinney FTS- only
McKinney RAQMS
Lamont FTS- only
Lamont RAQMS
Lamont FTS with BC
McKinney FTS with BC

## Slide 32: Methane (FTS, FTS+BC, RAQMS)
McKinney FTS- only
McKinney RAQMS
Lamont FTS- only
Lamont RAQMS
Lamont FTS with BC
McKinney FTS with BC

## Slide 33: Nitrous Oxide (FTS, FTS+BC, RAQMS)
McKinney FTS- only
McKinney RAQMS
Lamont FTS- only
Lamont RAQMS
Lamont FTS with BC
McKinney FTS with BC

## Slide 34: Carbon Dioxide (June 25, 2012)
AERI @ Lamont = 398.0 ppmv
ASSIST@ McKinney = 396.8 ppmv
JPL AIRS Retrievals
390.1 - 397.7 ppmv
395.2
390.1
393.1
397.7
394.2

## Slide 35: Retrieval Comparisons with Radiosondes (31)

## Slide 36
Summary
36
Ground-based FTS Provides excellent measurements of the Planetary Boundary Layer (PBL)
  Diurnal variation of temperature and moisture
  Trace gas profiles of O3 ,CO, CH4, and N2O
The retrieval procedure involves:
  Using optimal estimation for cloud 11 height classes
  Obtaining the cloud free radiance spectra from cloud attenuated spectra
  Defining the cloud height and proper cloud class for the statistical retrieval
  Correcting the retrieval for statistical bias using a dynamical chemistry forecast
An NGA Project is underway to validate ground based, airborne, and satellite trace gas measurements
  Emphasis being placed on the estimation of carbon dioxide
  The ground based spectral radiance measurements:
    ASSIST at McKinney Texas
    AERI at the DOE ARM CART-site in Lamont Oklahoma
Improved results to be obtained by combining ground based and satellite (Aqua AIRS, Metop IASI, and NPP CrIS radiance spectra for the thermodynamic and chemistry retrieval process