## Slide 1
Off-line Constraints on Urban NOx Emissions within NAM-CMAQ using TropOMI Tropospheric NO2 Retrievals
Brad Pierce
Space Science and Engineering Center*
University of Wisconsin-Madison, Madison, WI
and
Allen Lenzen*, Tommy Jasmin*, Pius Lee & Youhua Tang (NOAA), and Pieternel Levelt (KNMI)
LISTOS Airborne remote sensing retrievals: Scott Janz & Laura Judd (NASA)
LISTOS Ground based remote sensing retrievals: Jim Szykman, Luke Valin (EPA), Bob Swap (NASA)
AMS 2019 Joint Satellite Conference 28 September – 04 October 2019 Boston, MA
Data Providers

## Slide 2: Background
One of the key objectives for a Weather Ready Nation outlined in the NOAA Next Generation Strategic Plan is “Healthy people and communities due to improved air and water quality services”.
To support this objective, data assimilation capabilities need to be developed to exploit the next generation of satellite based air quality measurements.
This project focuses on developing capabilities to assimilate TROPOMI retrievals within the NWS regional air quality forecasting system (NAM-CMAQ)

## Slide 3
The TROPOspheric Monitoring Instrument (TROPOMI) is the satellite instrument on board the Copernicus Sentinel-5 Precursor (S5P) satellite launched on 13 October 2017.
  UV-VIS-NIR-SWIR push-broom grating spectrometer (270-495 nm, 675-775 nm, 2305-2385 nm).
  Nadir pixel 7x3.5 km2 for all spectral bands, with the exception of the UV1 band (7x28 km2) and SWIR bands (7x7 km2).
  S5P is a cooperative undertaking between ESA and the Kingdom of the Netherlands.
The objective of TROPOMI is to provide accurate and timely observations of key atmospheric species, for services on air quality, climate, and the ozone layer.
TROPOMI SWIR module

## Slide 4: Evaluating TROPOMI NO2 with Pandora: 10 instruments--June 2018-2019
Pandora data averaged over a  60-minute temporal window of the TROPOMI overpass with the horizontal bars representing the max/min over that temporal window and the coincidence TROPOMI tropospheric columns with cloud radiative fraction less than 20% with the vertical bars representing the reported precision. The dashed line is the 1:1 relationship and the solid line is the RMA linear fit.
Preliminary Results
Scatter around the best fit can be mostly attributed to mismatches in spatial representation of the different measurements and retrieval uncertainty
This low bias can be mostly removed by using a higher resolution NO2 profile shape in the retrieval (manuscript in prep)
No obvious seasonal or across-track dependency to the statistics
10 Pandora instruments installed/maintained through a EPA/NASA/state AQ agencies collaboration
Slide prepared by Laura Judd, NASA LaRC
Notes: In 2018, Pandoras were installed in 10 locations near NYC/LIS. Throughout the next year, there were 440 coincidences of Pandora data and TROPOMI data with cloud radiative fractions less than 20%.
Overall, the data are highly correlated with much of the scatter being attributed to mismatched spatial representivity between the two instruments. There is a persistant low bias by the TROPOMI product that is pretty well understood as a product of spatially coarse a priori from TROPOMI (1x1 deg TM5-MP a priori). If you use a higher resolution model to supply the profile shape, this low bias is mostly removed (see next slide). [FYI: GCAS/TROPOMI comparisons have very similar statistics but with a tighter correlation].
The bias does not appear to have a seasonal or pixel size (cross track position) dependency.

## Slide 5
Calculate monthly mean NO2 Jacobian (β) from a 15% NOX emission reduction perturbation experiment following Lamsal et al. 2011
Calculate monthly mean NO2 analysis increment using NAM-CMAQ/GSI TROPOMI NO2 assimilation
  NOx emission sensitive background errors (to correct NAM-CMAQ emissions)
Adjust NAM-CMAQ NOx emissions using Jacobian and average analysis increment
  Only adjust daytime emissions since TROPOMI does not provide nightime constraints
Lamsal, L. N., et al. (2011), Application of satellite observations for timely updates to global anthropogenic NOx emission inventories, Geophys. Res. Lett., 38, L05810, doi:10.1029/2010GL046476.
NAM-CMAQ/GSI NOx emission adjustment experiments
  NAM-CMAQ Beta for July-August 2018
Urban areas and transport corridors (b<1), rural areas (b>1)

## Slide 6
Calculate monthly mean NO2 Jacobian (β) from a 15% NOX emission reduction perturbation experiment following Lamsal et al. 2011
Calculate monthly mean NO2 analysis increment using NAM-CMAQ/GSI TROPOMI NO2 assimilation
  NOx emission sensitive background errors (to correct NAM-CMAQ emissions)
Adjust NAM-CMAQ NOx emissions using Jacobian and average analysis increment
  Only adjust daytime emissions since TROPOMI does not provide nightime constraints
Lamsal, L. N., et al. (2011), Application of satellite observations for timely updates to global anthropogenic NOx emission inventories, Geophys. Res. Lett., 38, L05810, doi:10.1029/2010GL046476.
NAM-CMAQ/GSI NOx emission adjustment experiments
  TropOMI Analysis Increments for July-August 2018
July-August, 2018 mean GSI analysis increment shows large reductions in urban areas.

## Slide 7
Calculate monthly mean NO2 Jacobian (β) from a 15% NOX emission reduction perturbation experiment following Lamsal et al. 2011
Calculate monthly mean NO2 analysis increment using NAM-CMAQ/GSI TROPOMI NO2 assimilation
  NOx emission sensitive background errors (to correct NAM-CMAQ emissions)
Adjust NAM-CMAQ NOx emissions using Jacobian and average analysis increment
  Only adjust daytime emissions since TROPOMI does not provide nightime constraints
Lamsal, L. N., et al. (2011), Application of satellite observations for timely updates to global anthropogenic NOx emission inventories, Geophys. Res. Lett., 38, L05810, doi:10.1029/2010GL046476.
NAM-CMAQ/GSI NOx emission adjustment experiments
  Delta NAM-CMAQ NOx emissions July-August 2018
Assimilation of TropOMI NO2 results in reductions in NOx emissions over major urban centers during July-August 2018

## Slide 8
Verification of NAM-CMAQ/GSI
NOx emission
adjustment experiments
Airborne remote sensing measurements during the 2018
Long Island Sound Tropospheric Ozone Study (LISTOS)

## Slide 9
Calculate monthly mean NO2 Jacobian (β) from a 15% NOX emission reduction perturbation experiment following Lamsal et al. 2011
Calculate monthly mean NO2 analysis increment using NAM-CMAQ/GSI TROPOMI NO2 assimilation
  NOx emission sensitive background errors (to correct NAM-CMAQ emissions)
Adjust NAM-CMAQ NOx emissions using Jacobian and average analysis increment
  Only adjust daytime emissions since TROPOMI does not provide nightime constraints
Lamsal, L. N., et al. (2011), Application of satellite observations for timely updates to global anthropogenic NOx emission inventories, Geophys. Res. Lett., 38, L05810, doi:10.1029/2010GL046476.
NAM-CMAQ/GSI NOx emission adjustment experiments
  Delta NAM-CMAQ NOx emissions July-August 2018
Assimilation of TropOMI NO2 results in (~20%) reductions in NOx emissions over NYC during July-August 2018

## Slide 10
Long Island Sound Tropospheric Ozone Study (LISTOS)
https://www-air.larc.nasa.gov/missions/listos/index.html
GCAS (Janz) LISTOS Flights: 07/02-08/29, 2018
GCAS NO2 Column 08/16/2018 PM
NAM-CMAQ (Control) NO2 Column 08/16/2018 PM
Geostationary Coastal and Air Pollution Events Airborne Simulator (GCAS, PI Scott Janz/NASA GSFC)
total column NO2 retrievals provided by Laura Judd (NASA/LARC)
NAM-CMAQ control NO2 column is significantly higher than GCAS

## Slide 11
Long Island Sound Tropospheric Ozone Study (LISTOS)
https://www-air.larc.nasa.gov/missions/listos/index.html
GCAS (Janz) LISTOS Flights: 07/02-08/29, 2018
GCAS NO2 Column 08/16/2018 PM
Geostationary Coastal and Air Pollution Events Airborne Simulator (GCAS, PI Scott Janz/NASA GSFC)
total column NO2 retrievals provided by Laura Judd (NASA/LARC)
NAM-CMAQ (TropOMI) NO2 Column 08/16/2018 PM
NAM-CMAQ TropOMI NO2 column is in better agreement with GCAS

## Slide 12
GCAS (Janz) LISTOS Flights: 07/02-08/29, 2018
Geostationary Coastal and Air Pollution Events Airborne Simulator (GCAS, PI Scott Janz/NASA GSFC)
total column NO2 retrievals provided by Laura Judd (NASA/LARC)
NAM-CMAQ control NO2 column is consistently significantly (7.22e15 mol/cm2) higher than GCAS

## Slide 13
GCAS (Janz) LISTOS Flights: 07/02-08/29, 2018
Geostationary Coastal and Air Pollution Events Airborne Simulator (GCAS, PI Scott Janz/NASA GSFC)
total column NO2 retrievals provided by Laura Judd (NASA/LARC)
NAM-CMAQ TropOMI NO2 column is consistently (29% reduction in high bias) in better agreement with GCAS

## Slide 14
Impact of NAM-CMAQ/GSI
NOx emission adjustment
on surface ozone predictions

## Slide 15
NAM-CMAQ surface ozone response to TropOMI offline NOx emission adjustment
Mean changes of + 2-4ppbv over Southern Long Island
Notes: NAM-CMAQ TropOMI data assimilation experiments conducted by Allen Lenzen (UW-Madison/SSEC)

## Slide 16
NAM-CMAQ surface ozone response to TropOMI offline NOx emission adjustment
Adjusted emissions result in an additional overestimate in 8hr averaged ozone relative to AIRNOW over NYC
Notes: NAM-CMAQ TropOMI data assimilation experiments conducted by Allen Lenzen (UW-Madison/SSEC)

## Slide 17
NAM-CMAQ surface ozone response to TropOMI offline NOx emission adjustment
Mean O3 changes of +/- 2-4ppbv in major urban areas over CONUS
Notes: NAM-CMAQ TropOMI data assimilation experiments conducted by Allen Lenzen (UW-Madison/SSEC)

## Slide 18
NAM-CMAQ surface ozone response to TropOMI offline NOx emission adjustment
Adjusted emissions result in neutral impacts for 8hr averaged ozone relative to AIRNOW over CONUS
Notes: NAM-CMAQ TropOMI data assimilation experiments conducted by Allen Lenzen (UW-Madison/SSEC)

## Slide 19
NAM-CMAQ surface ozone response to TropOMI offline NOx emission adjustment
Mean O3 changes of + 10-15 ppbv over LA-Long Beach
Notes: NAM-CMAQ TropOMI data assimilation experiments conducted by Allen Lenzen (UW-Madison/SSEC)

## Slide 20
NAM-CMAQ surface ozone response to TropOMI offline NOx emission adjustment
Adjusted emissions result in reduced biases in 8hr averaged ozone relative to AIRNOW over LA- Long Beach, CA
Notes: NAM-CMAQ TropOMI data assimilation experiments conducted by Allen Lenzen (UW-Madison/SSEC)

## Slide 21: Summary and Conclusions
An off-line approach to adjusting NAM-CMAQ NOx emissions has been demonstrated using TropOMI NO2 retrievals during July-August 2018
  Adjustment results in reductions in NAM-CMAQ NOx emissions within large urban centers
  Adjusted emissions result in improved agreement with GCAS NO2 columns over NYC during the LISTOS campaign
Surface ozone concentrations generally increase within large urban centers
  Adjusted emissions result in neutral impacts of 8hr averaged ozone predictions compared to AIRNOW measurements
  Some urban centers (NYC) show negative impacts while some urban centers (LA) show positive impacts
This work was supported by FY18 NOAA/NESDIS Office of Projects, Planning and Analysis (OPPA) Technology Maturation Program (TMP) Funding

## Slide 22
Extra Slides

## Slide 23
NAM-CMAQ surface ozone response to TropOMI offline NOx emission adjustment
Adjusted emissions result in neutral impacts for 8hr averaged ozone relative to AIRNOW over CONUS
Notes: NAM-CMAQ TropOMI data assimilation experiments conducted by Allen Lenzen (UW-Madison/SSEC)

## Slide 24: Improvement to TROPOMI with higher spatial resolution a priori NO2 profile shape from NAM-CMAQ
3 months of data
3 months of data
Preliminary results
Standard TROPOMI RPRO v1.2.2. v. Pandora
TROPOMI-NAMCMAQ v. Pandora
Slide prepared by Laura Judd, NASA LaRC
10 instruments July-August, 2018
Notes: You don’t need to show this unless you want to (or use it instead of the other scatter plot). I just wanted to share this so you see what I used the curtain data for last week!
TROPOMI-NAMCMAQ is the TROPOMI column with a recalculated AMF using the NAM-CMAQ a priori profile shape.
If you can think of a model data source where we could get more consistent profile shapes, let me know! I am very interested to continue something like this.