## Slide 1
CIMSS FX 20170504
Low pressure system over Ohio River Valley extending to Gulf bringing cirrus into Southern WI and clouds over Chicago
Note 2 hour time difference
WRF-CHEM at 12Z (7:00am CDT)
GOES-16 at 10Z (5:00am CDT)

## Slide 2
http://raqms.ssec.wisc.edu/o3_verification/ts/latest/WI/3800/550590019
RAQMS (red, 1x1 degree) underestimates SFC O3 (black) at Chiwaukee by 9.6ppbv (daytime, more significantly April 28-May 1)

## Slide 3
http://raqms.ssec.wisc.edu/o3_verification/ts/latest/WI/7620/551170006
RAQMS (red, 1x1 degree) underestimates SFC O3 (black) at Sheboygan by 7.8ppbv (daytime, more significantly April 28-May 1)

## Slide 4
7:00am CDT
Day 1
Midlevel
Clouds South of 42N
Lowlevel
Clouds North of 43.5

## Slide 5
10:00am CDT
Day 1
Midlevel
Clouds South of 42N
Lowlevel
Clouds diminishing
North of 44N

## Slide 6
1:00pm CDT
Day 1
Clear

## Slide 7
4:00pm CDT
Day 1
North North Easterly flow over Region
Clear

## Slide 8
7:00pm (Thursday) CDT
Initialization
Day 1 Loop
Initial Location of Milwaukee
And Chicago NOx emission Trajectories
Initialized every hour from 00Z-24Z

## Slide 9
7:00am CDT
Day 1
Dew point Depression (red is dry)

## Slide 10
10:00am CDT
Day 1
Dew point Depression (red is dry)

## Slide 11
1:00pm CDT
Day 1
Dew point Depression (red is dry)

## Slide 12
4:00pm CDT
Day 1
Dew point Depression (red is dry)
Flow out of NorthEast turning Northerly transports emissions to the SSW and South.
NAM shows small surface dewpoint depressions air over the region in the morning then becoming drier over land in the afternoon