## Slide 1: High Resolution WRF-CMAQ modeling during LISTOS
Ana Torres-Vazquez, Jon Pleim
Office of Research and Development
Atmospheric and Environmental Systems Modeling Division

## Slide 2
Long Island Sound Tropospheric Ozone Study (LISTOS)
LISTOS was a multi-agency collaborative field campaign organized by the Northeast States for Coordinated Air Use Management
(NESCAUM) with the goal to improve our understanding of ozone chemistry and transport from New York City to areas downstream, especially the Long Island Sound and adjacent Connecticut coastline.
Image credit: NASA Langley Research Center
Science Questions
How well does WRF-CMAQ model represent transport features like:
  the flow regimes that are conducive to high ozone on CT coast?
  land/sea breezes along the CT and Long Island coastlines?
  low level jets (LLJs)?
and their impacts to pollutant transport and production?
Can we improve model performance with modifications to physics or data assimilation?

## Slide 3: Modeling Approach
4km
1.33 km
Model Versions | Coupled WRF-CMAQ; WRFv4.1.1, CMAQv5.3.1
Initial Conditions for 12km simulation | NAM 12km Analysis 108km Hemispheric CMAQ
Run period | 12km: 2018 4km & 1.33km : May – Sept 2018.
Emissions | 2016ff projected forward to 2018; 1.33km domain had additional county-specific information.

## Slide 4: Modeling Approach
  Updates to meteorological modeling:
    Updated sea surface temperature using high resolution surface data: GHRSST (1 km).
    Surface data assimilation using UnRestricted Mesoscale Analysis (URMA) (2 km) through PX LSM soil moisture and temperature nudging
    Updated land-use, tree canopy and imperviousness information using 2016 NLCD-MODIS data
  Key aspects of emissions
    Onroad mobile sources – Run MOVES with county specific updated VMT, age distribution, temporal profile from 2017 (adjust for day of week for 2018 )
    Marine – hourly GPS ship data from 2017 (adjust for day of week for 2018)
Impervious surface
fraction for 1.33-km domain
Tree canopy fraction for 1.33-km domain

## Slide 5
GCAS captures NO2 sources and their transport in the early morning of August 6, 2018
12-13:58 UTC
14-15:53 UTC
Notes: Mention NYS MESONET

## Slide 6
GCAS captures NO2 sources and their transport in the early morning of August 6, 2018
Our 1.33km simulations replicates some of these sources at the surface but simulates different transport and timing regimes along the columns.
NO2
NO2
13 UTC
15 UTC
NO2 Vertical Column Density
13 UTC
15 UTC
NO2 Vertical Column Density
12-13:58 UTC
14-15:53 UTC
Notes: Mention NYS MESONET

## Slide 7: Surface-level wind flow
Summer-long flow is predominantly SSW, with NE and SE activity.
Measurements during the 21 exceedance events show predominant SSW flow.
Model captures general character of observed flow, but overestimates wind speeds and flow variance.
1-minute wind observations from ground stations managed by the Connecticut Department of Energy and Environmental Protection (CT DEEP).
Observations from the full summer
Observations from the 21 exceedance events
Modeled winds during the 21 exceedance days

## Slide 8: Surface-level wind flow
Summer-long flow is predominantly SSW, with NE and SE activity.
Measurements during the 21 exceedance events show predominant SSW flow.
Model captures general character of observed flow, but overestimates wind speeds and flow variance.
Model does not capture NNE land-breeze-like wind shift between 12 AM – 5 AM.
1-minute wind observations from ground stations managed by the Connecticut Department of Energy and Environmental Protection (CT DEEP).
12 AM – 5 AM Exceedance Event Observations versus Model

## Slide 9: Surface-level wind flow along the CT coast on July 10
1-min ozone
Wind Direction
Model does not simulate overnight land breeze processes along coastal CT stations.
Subsequently, residual ozone from the previous day was not fully cleared out.
At Greenwich: a delay in onset of on-shore breeze coincides with a delay in ozone production, which suggests importance of flow to adequate simulation of ozone.
At Madison: onset of ozone production preceded SW flow shift, suggesting localized production.
Model misses max. ozone concentrations at all stations.

## Slide 10: Surface-level wind flow along the CT coast on July 10
1-min ozone
Wind Direction
Breeze-ozone-NO2 relationships recreated by the model.
NO2
Model does not simulate overnight land breeze processes along coastal CT stations.
Subsequently, residual ozone from the previous day was not fully cleared out.
At Greenwich: a delay in onset of on-shore breeze coincides with a delay in ozone production, which suggests importance of flow to adequate simulation of ozone.
At Madison: onset of ozone production preceded SW flow shift, suggesting localized production.
Model misses max. ozone concentrations at all stations.

## Slide 11: Ozone LIDAR at Westport
Data courtesy of Tim Berkoff, NASA.
Ozone LIDAR data at Westport provides us with an encompassing snapshot of processes related to ozone production and ozone exceedances along the CT coast.
Potential evidence of:
Rapid growth within shallow surface layer
Localized low-level jets
…and a plume transporting high ozone concentrations over Westport.

## Slide 12
Data courtesy of Tim Berkoff, NASA.
Rapid growth within shallow surface layer
Model captures surface level growth, but it’s very similar to behavior higher along the column.
Plume transporting high ozone concentrations over Westport.
Timing of plume arrival later than observed.
** NOTE: there are discrepancies between LIDAR vertical column ozone values and those captured by the ozone sondes.

## Slide 13
Data courtesy of Tim Berkoff, NASA.
Potential evidence of localized low-level jets
** NOTE: there are discrepancies between LIDAR vertical column ozone values and those captured by the ozone sondes.
Ozone
Wind Speed
Wind Direction

## Slide 14: To summarize
The model captured prevailing wind flows and general high ozone concentrations over the region but struggled to adequately represent sea and land breezes and low-level jets, even at 1.33km grid lengths.
Evidence that transport issues are both local and regional.
There is evidence of this impacting the representation of NO2 and ozone.