## Slide 1
Visibility Algorithm Validation for 100% Delivery
Presented by R. Bradley Pierce

## Slide 2
ABI Visibility retrieval is average visibility over the depth of the planetary boundary layer (PBL)
Primary validation dataset is NWS Automated Surface Observing Systems (ASOS) raw (1 minute) extinction measurements Archived at NCDC Class
Secondary validation data sets include High Spectral Resolution Lidar (HSRL) and Cloud-Aerosol Lidar and Infrared Pathfinder Satellite Observations (CALIPSO) 550 nanometer extinction coefficients.
Product Overview
(Visibility)

## Slide 3: Example Product Output

## Slide 4: Example ASOS Visibility

## Slide 5: Example ASOS Visibility

## Slide 6: Visibility Requirements
Name | Output format for each coverage | Geographic Coverage (G, H, C, M) | Vertical Resolution | Horizontal Resolution | Mapping Accuracy | Measurement Range | Measurement Accuracy | Refresh Rate/Coverage Time Option (Mode 3) | Refresh Rate Option (Mode 4) | Data Latency | Product Measurement Precision
Visibility | NetCDF McIDAS | FD | N/A | 10km | 5 km | Clear (vis ≥ 30 km) Moderate (10 km ≤ Vis < 30 km) Low (2 km ≤ vis < 10 km); Poor (vis < 2 km) (under the conditions of clear up through clouds of only layer) | 80% correct classification | 60 min | 5 min | 806 sec | 1.5 categories
FD – Full Disk

## Slide 7: Visibility Product Qualifiers
Name | Geographic Coverage (G, H, C, M) | Temporal Coverage Qualifiers | Product Extent Qualifier | Cloud Cover Conditions Qualifier | Product Statistics Qualifier
Visibility | FD | Day | Quantitative out to at least 70 degrees LZA and qualitative at larger LZA | Clear conditions down to feature of interest associated with threshold accuracy | Over specified geographic area
FD – Full Disk

## Slide 8
Validation Approach

## Slide 9: Visibility Validation
Visibility product validation is performed with the following test data
  MODIS L1B 1KM calibrated and geo-located radiances
  MODIS L2 V5.1 Cloud Optical Thickness retrievals
  MODIS L2 V5.1 Aerosol Optical Depth retrievals
  Collocated ASOS harmonic mean 1-minute visibility measurements

## Slide 10: Visibility Validation: Details (1)
Method: Co-locate ABI visibility retrievals with ASOS visibility measurements obtained from harmonically averaged 1-minute ASOS extinction measurements and compare the categorical accuracy and precision with specifications
  Visibility accuracy specification: 80% correct classification
Approach: Compute categorical histograms for ASOS and ABI visibility retrievals

## Slide 11: Visibility Validation: Details (2)
Quantitative measures
- Percent correct classification, precision, Heike Skill Score, and false alarm rate
Validity criteria:
- 80% correct classification for co-located ASOS measurements

## Slide 12
Validation Results

## Slide 13
Visibility Validation Results
13
Histogram of ASOS & ABI Merged Aerosol and Fog categorical visibility classifications for 4165 coincident ASOS/MODIS
measurement pairs during May-June 2010.
Merged ABI V5 vs ASOS visibility May-June 2010
The merged visibility retrieval results in a 66.6% categorical success rate and an estimated precision of 0.57.
Notes: 13

## Slide 14: Visibility Validation Results
V5 Heidke Skill Score (Hit Rate)
Skill Score and False Alarm Rate (May-June, 2010)
V5 False Alarm Rate
Visibility Category | Merged retrieval
1 (Clear) | 0.324468
2 (Moderate) | 0.364389
3 (Low) | 0.666667
4 (Poor) | NA
Visibility Category | Merged retrieval
1 (Clear) | 0.261098
2 (Moderate) | 0.257462
3 (Low) | 0.0452322
4 (Poor) | NA
The V5 Visibility retrieval shows equivalent skill and false alarm rates for Clear and Moderate visibility classes and degrades for low visibility. No coincident poor visibility cases were found during the May-June 2010 validation period.
*Heidke Skill Score measures the fractional improvement relative to chance

## Slide 15: Visibility Validation Results
http://www.nws.noaa.gov/tdl/synop/wrfeval/vis_conus_heidke.gif
ABI Retrieval Score for Clear (>30km) and Moderate (10-30km) visibilities
Eta, WRF, GFS Model Output Statistics (MOS) validation for 5 visibility classes: <0.5 (0.8), 0.5-1.0 (0.8-1.6), 1.0-3.0 (1.6-4.8), 3-5 (4.8-8.0), >5 (8.0) miles (km)
MOS validation period: March 1, 2006, through May 31, 2006

## Slide 16
Accuracy | F&PS | Visibility Algorithm
Percent correct classification | 80% | 66.6%
Statistics (Visibility categorical accuracy and precision). MODIS clear sky down to feature of interest data (May-June 2010)
Preliminary estimates show that the algorithm meets precision requirements but does not meet the accuracy requirements
Visibility Validation Results: Summary
Precision | F&PS | Visibility Algorithm
RMS categorical error | 1.5 | 0.57

## Slide 17
Visibility Error Budget
Consider May-June 2010 Co-located ABI visibility retrievals at ASOS stations as “truth”
Introduce range of errors to each predictor
Compute average percentage error in visibility classification as a function of (+/-) percentage error for individual predictors

## Slide 18
Visibility Error Budget
Results
The ABI visibility retrieval is most sensitive to errors in 2m Temperature (t2m) and Temperature at the top of the PBL (tpbltop) during May-June 2010
A +/- 2% (4 %) error in 2m Temperature alone would result in a categorical accuracy
of 89% (78%) for the May-June 2010 coincident ASOS/MODIS pairs.

## Slide 19
Visibility Error Budget
Results
Comparison of GFS 2m Temperature and ASOS Dry Bulb Temperature (K) for coincident ASOS/MODIS pairs during May-June 2010 shows that actual biases are ~2K (less than 1%) with rms errors on the order of 4K (1.3%)

## Slide 20: Summary
The GOES-R ABI visibility algorithm provides a new capability for estimating boundary layer visibility from space that complements current surface measurements
The Heidke Skill Scores for Clear and Moderate visibility are comparable to MOS estimates for Low and Poor visibility categories and provide information about aerosol driven visibility reductions
The GOES-R AWG visibility algorithm is very sensitive to errors in the 2m Temperature and Temperature at the top of the PBL – a >4% error in 2m Temperature alone would result in the ABI visibility retrieval not meeting performance requirements.