LiDAR Point Processing

April 29, 2011 LiDAR Point Data

Continental Mapping Consultants

Report Generated June 25, 2011

LAS Format

Horizontal average point spacing:

Horizontal Units = UTM 15N Meters

Raw Data—0.324m cross track, 0.509m down track, 6.06 points/m (CMC quote)

Raw Data—0.356115m (derived from ArcGIS 3D Analyst PFI)

Ground—1.085962m (derived from ArcGIS 3D Analyst PFI)

Vertical Accuracy:

Vertical Units = NAVD88 Geoid 09 Meters

Overall—0.090m (95% cl), Bare Earth—0.069m (95% cl)

Assess LiDAR Coverage & Sample Density

Point File Information (PFI)—3D Analyst Toolbox

Ground Points	(meters)

Average Point Spacing—1.085962m

| File Name | Point Count | Point Spacing | Z Min | Z Max |
| --- | --- | --- | --- | --- |
| LAS1 | 1299741 | 1.054155 | 246.34 | 282.72 |
| LAS2 | 1072732 | 1.121999 | 238.36 | 265.17 |
| LAS3 | 1228823 | 1.071893 | 238.39 | 272.7 |
| LAS4 | 1154087 | 1.095800 | 238.73 | 266.71 |

Raw Data (meters)

Average Point Spacing—0.356115m

| File Name | Point Count | Point Spacing | Z Min | Z Max |
| --- | --- | --- | --- | --- |
| LAS1 | 2689436 | 0.366409 | 250.36 | 307.22 |
| LAS2 | 2634466 | 0.360997 | 248.72 | 316.11 |
| LAS3 | 2675979 | 0.346292 | 237.96 | 273.78 |
| LAS4 | 2060852 | 0.374674 | 242.96 | 279.30 |
| LAS5 | 3027469 | 0.342037 | 257.12 | 294.97 |
| LAS6 | 3022558 | 0.345635 | 246.28 | 292.06 |
| LAS7 | 3064535 | 0.343259 | 236.37 | 270.27 |
| LAS8 | 3018477 | 0.342430 | 243.20 | 283.41 |
| LAS9 | 2393870 | 0.379531 | 257.06 | 281.43 |
| LAS10 | 2986742 | 0.347698 | 238.11 | 275.21 |
| LAS11 | 3393069 | 0.326215 | 237.70 | 279.47 |
| LAS12 | 2814094 | 0.356988 | 246.69 | 283.37 |
| LAS13 | 2556462 | 0.362218 | 253.91 | 278.36 |
| LAS14 | 2372122 | 0.383648 | 237.63 | 272.53 |
| LAS15 | 3148467 | 0.324808 | 237.82 | 282.79 |
| LAS16 | 2020793 | 0.395004 | 242.55 | 278.58 |

LAS to Multipoint

3D Analyst Toolbox Parameters--

File Name: GROUND

Folder: Ground LAS

Output: Feature Dataset

Average Point Spacing: 1.086 (Derived from Point File Information)

Input Return Values: Any Return

Output Coordinate System: UTM NAD83 15N

File Name: RAW_LAST_RETURN

Folder: RAW LAS

Output: Feature Dataset

Average Point Spacing: 1.086 (Derived from Point File Information)

Input Return Values: Last Return

Output Coordinate System: UTM NAD83 15N

Point to Raster

Point to Raster Tool Parameters—

(NOTE: Does not produce highest quality but allows for fast results)

For Point Density Return:

RAW_LAST_COUNT

Input Features: RAW_LAST_RETURN

Value Field: OID (ignored)

Output Raster Dataset: RAW_LAST_COUNT

Cell Assignment Type: COUNT

Cellsize: 2 (<4x average point spacing of 0.356115m)

Comment: Shows flight paths and overlap, not very useful

For Point Density Return:

GROUND_ALL_COUNT

Input Features: GROUND_RETURN

Value Field: OID (ignored)

Output Raster Dataset: GROUND_ALL_COUNT

Cell Assignment Type: COUNT

Cellsize: 6 (<4x average point spacing of 1.086m)

Comment: Comparison of cellsize size assignment from 5 – 8.4 m determined that 6m returns a finer image with least compromise of empty cells

For Canopy Area:

RAW_LAST_Z

Input Features: RAW_LAST_RETURN

Value Field: SHAPE.Z

Output Raster Dataset: RAW_LAST_Z

Cell Assignment Type: RANGE

Cellsize: 2 (4x average point spacing of 0.356115m)

Comment: Displays areas of vegetation cover

For Rough Digital Elevation Model:

GROUND_ALL_SHAPEZ

Input Features: GROUND

Value Field: SHAPE.Z

Output Raster Dataset: GROUND_ALL_SHAPEZ

Cell Assignment Type: RANGE

Cellsize: 6 (<4x average point spacing of 1.086m)

Comment: Woohoo now we’re getting somewhere

For an even rougher DEM:

GROUND_ALL_Z_MEAN

Input Features: GROUND

Value Field: SHAPE.Z

Output Raster Dataset: GROUND_ALL_Z_MEAN

Cell Assignment Type: MEAN

Cellsize: 6 (<4x average point spacing of 1.086m)

Comment: Not a good representation, very rough

Building Terrains

A terrain dataset is a multi-resolution, TIN-based surface built from measurements stored as features in a geodatabase. They're typically made from LiDAR, sonar and photogrammetric sources. Terrains reside in the geodatabase, inside feature datasets with the features used to construct them. (ESRI Resource Center)

Considerations:

LiDAR coverage extent (covers Aztalan study area)

Number of points & density (GROUND—1.086m, 6.06 points/m)

Output raster resolution (0.5m or smaller, 1.0m did not provide details)

Output raster extent (tiled, can mosaic according to need)

Output raster format (TIFF or JPEG for general, non-GIS users)

Process:

Load Multi-points into feature dataset

Create Feature Dataset

Horiz Coordinate: UTM83 15N

Vertical Coordinate: NAVD88

Use LAS to Multipoint tool from ArcGIS 3D Analyst toolbox

Add hydro break lines to feature dataset