Data Specifications for 3D Imagery Project for

Aztalan State Park

T07N R14E Sections 16, 17, 20 & 21

Town of Aztalan, Jefferson County, Wisconsin

Supplemental to the 3-D representation of the study area, but equally as important is the detailed spatial analysis of an archaeological site, therefore high-density data specifications are requested to provide finest resolution of the study area.

Survey Extents:

Coordinate System—UTM NAD83, Zone 15N, meters

Primary Study Area (1000 acres):

| NORTHING |  | EASTING |  | CORNER |
| --- | --- | --- | --- | --- |
| 4777249.23683000 |  | 838214.45190000 |  | NE |
| 4777364.64614000 |  | 835760.40147900 |  | NW |
| 4775551.04389000 |  | 835822.71046700 |  | SW |
| 4775636.91532000 |  | 838240.18688000 |  | SE |

Secondary Study Area (7500 acres):

| NORTHING |  | EASTING |  | CORNER |
| --- | --- | --- | --- | --- |
| 4778923.97683000 |  | 838215.95434900 |  | NE |
| 4778733.31577000 |  | 831807.98173600 |  | NW |
| 4773983.16949000 |  | 831985.88369300 |  | SW |
| 4774177.24792000 |  | 838276.96562400 |  | SE |

See Map 1: Aztalan Study Area Extent Map for details (attached)

Time of Survey:

Data collection is to occur during leaf-off conditions with no snow cover between the dates of March 18 and April 30, 2011.

Collection Specifications:

  - Average point spacing—0.5 to 0.7 meter (or better)

  - Vertical Accuracies—15 cm RMSE (or better)

  - Horizontal Accuracies—0.5 meter (or better)

Deliverables:

The following is to be delivered with ten (10) weeks following the data collection:

    - Raw data (point cloud) data as either ASCII or LAS format

    - Bare earth DEM in ESRI GRID format—1-m resolution

    - Black & White Orthoimagery—0.5-ft resolution

    - First and Last Returns

    - Return Intensity Data

    - Data collection reports and spatial metadata

    - Tile Size: 2000 m x 2000 m (PLSS Section)

    - Provided on DVD in the following projection:

UTM, Zone 15N, meters

Horizontal Datum: NAD83 (97)

Vertical Datum: NAVD88

Other Deliverables (if available):

  - 3-D Modeling

  - Digital Terrain Model (DTM)

  - Shaded Relief Model

  - Triangular Irregular Network (TIN)

  - High-quality fly-through visualization

  - Earthwork profile

Map 1: Aztalan Study Area Extents